## Slide 1: Assessment of aerosol plume dispersion products and their usefulness to improve models between satellite aerosol retrieval and surface PM2.5
Chowdhury Nazmi1,2, Barry Gross1,2 , Yonghua Wu2, Fred Moshary1,2
1Department of Electrical Engineering, The City College of NY
2NOAA-Cooperative Remote Sensing Science and Technology Center
The 14th Annual CMAS Conference, October 5-7, 2015

## Slide 2: Motivation
Relative size of
Particulate Matter
Human Health is strongly affected by the ambient concentration of Fine Particulate Matter (PM2.5)
EPA Guidelines have been developed to address these issues.
Surface sampling is quite expensive and existing networks are very limited.
Satellites provide column integrated information that can potentially be used to estimate PM2.5.
Wide range of factors such as aerosols variability, meteorology and the vertical structure of aerosols affect the PM2.5-AOD relationship.

## Slide 3: How can Remote Sensing extract PM2.5?
PM2.5 - AOD relationship illustration
Total column integrated aerosol optical depth (AOD) measurements can be connected to surface PM2.5 using a simple linear model.1
Strongly depends on aerosol properties, PBL height, meteorological conditions, presence of different aerosols of different mass/optical properties, aloft plumes (smoke) etc.
Many attempts have been made to connect surface PM2.5 measurements to column AOD, but it is expected that any simple relationship does not work in the presence of aloft plumes or mixed aerosol types. 3
1 Zhang et al., 2014
2Al-Saadi et al., 2005; Hoff et al., 2009
3 Engel-Cox et al., 2004

## Slide 4: Proposal
Most operational satellite algorithms for AOD do not have a way of identifying/quantifying the existence of aloft plumes such as smoke.
This makes the use of satellite AOD’s risky and therefore the use of complementary smoke tools is very important as a way of better utilizing satellite AOD
Some tools that can theoretically identify smoke events/plumes include
  CCNY LIDAR
  GOES ASDTA Smoke product
  NAAPS aerosol model
Our proposal is to see if these tools can help detect and compensate for the presence of smoke events and exploring if the Smoke Index can be used in a pre-processing mode to filter smoke cases and as an extra input to modify existing PM2.5 estimators including multivariable regressions and NN.

## Slide 5: Instruments and datasets used
Ground-based multi-wavelength elastic-Raman scattering LIDAR:
  Detects Aloft plume days
MODIS(AQUA/TERRA Satellite) Level 2 Aerosol Product:
  Detects Aerosol Optival Depth(AOD)
  “Optical_Depth_Land_And_Ocean” parameter is used which is “Aerosol Optical Thickness” at 0.55 µm for both Ocean (best) and Land (corrected) with best quality data (QA Confidence Flag = 3)
  Spatial resolution of a 10x10 1-km (at nadir)-pixel array.
  New York City Department of Environmental Conservation (NYCDEC):
    PM2.5 concentration data
    15 urban and 5 non-urban PM2.5 station data were available
    Provides PM2.5 concentration of every hour of a day
    ASDTA(Automated Smoke Detection and Tracking Algorithm) Smoke Product:
      Semi-quantitative retrieval of column average smoke concentration (µg/m3)
      Spatial resolution: 0.15 degree, Temporal Resolution: Hourly
      NAAPS (Navy Aerosol Analysis and Prediction System) Global Aerosol Model:
        Outputs: Smoke, Sulfate, SO2, Dust and Sea-Salt mass concentration profile at different altitudes
        Need to convert from Concentrations to AOD
  1X1 degree spatial resolution, 24 vertical levels, forecasts every 6 hour intervals
  Time Frame Used: Summer 2010-2012

## Slide 6
Hourly PM2.5 vs Satellite AOD
y= 25x+5.9
R=0.5968
rmse=18.39
PM2.5 concentration data collected for available 15 urban and 5 non-urban NY stations from NYDEC for summer 2010-2012.
AOD data at PM2.5 station locations are collected from MODIS AQUA/TERRA for summer 2010-2012.
PM2.5 vs AOD plotted for all 20 PM2.5 station locations at MODIS hours.
Note low slope and fairly high offset

## Slide 7
LIDAR (Light Detection and Ranging) Imagery for plume detection
NOAA CREST LIDAR can be used to detect existence of plumes.
Direct integration of the extinction coefficient can be used to estimate the plume AOD as well as the resulting PBL AOD
Plumes can easily be > 50% of total AOD.

## Slide 8: Evidence of Smoke Event contamination at CCNY
LIDAR can be used to study the effect of plumes on potential linear behavior between satellite AOD and surface PM2.5
When filtering out plume cases, a better linear correlation factor as well as a much improved slope and RMSE are observed
As expected, poor correlation is seen when only the smoke plume cases are studied.
No Filter
Filtered out aloft plume days
Aloft plume days
y=26x+4.5
R=0.6056
rmse=20.35
y=36x+1.9
R=0.6732
rmse=17.63
y=13x+9.3
R=0.3377
URBAN Stations

## Slide 9
Plume transport algorithms are not expected to have very good spatial accuracy.
Therefore, using it to determine the smoke content of a single pixel is not recommended.
A more conservative approach is to use an extended domain and estimate the smoke likely hood based on statistics.
The smoke contamination of each event is quantified as:
Smokiness=average smoke AOD in the domain * fraction of smoky pixels in the domain
A CDF distribution allows us to develop a long term climatology of “smokiness” within a given domain.
From this, we can study the PM2.5 vs AOD as a function of the degree of “smokiness”.
Focusing on summer where best connection between AOD and PM2.5 expected and smoke plume contamination is most frequent.
Fraction of smoky pixels
=(valid # of pixels)/(total # of pixels)
Quantifying high plume contamination cases with ASDTA

## Slide 10
Filtering based on average smokiness of entire NY
y= 45x-1.9
R=0.7754
rmse=12.82
Filter out
Smokiness>=0.016
y= 25x+5.9
R=0.5968
rmse=18.39
No Filter

## Slide 11
Filtering based on average smokiness of entire NY
Correlation
RMSE
Slope
Intercept

## Slide 12
Reducing domains to 20km boxes Urban Cases Only
y=28x+0.73
R=0.8722
rmse=14.25
Filter out
Smokiness>=0.018
No Filter
y=26x+4.5
R=0.6056
rmse=20.35
Note that when the domain size shrinks, the CDF is skewed to
higher value which is reasonable since it is easier to fill a smaller cell with smoke
In addition , we see that the CDF is consistent for different regions (urban or nonurban)
which is reasonable for transported smoke.

## Slide 13
Reducing domains to 20km boxes Urban Cases Only
Significant improvement seen as the smoke Indicator decreases.
If too small, not enough points left.
Correlation
RMSE
Intercept
Slope

## Slide 14
NAAPS Global Aerosol Model
ALOFT Smoke AOD
TOTAL Smoke AOD
PBL Smoke AOD
Interestingly
PBL Smoke ~ Aloft Smoke

## Slide 15
Filtering out contaminated cases using
NAAPS Aloft Smoke AOD as smoke indicator
NAAPS Aloft Smoke AOD<0.013
No Filter
y= 25x+5.9
R=0.5968
rmse=18.39
NAAPS Aloft smoke AOD

## Slide 16
Filtering out contaminated cases using
NAAPS Aloft Smoke AOD as smoke indicator
Correlation
RMSE
Slope
Intercept

## Slide 17
NAAPS Smoke Indicator comparison
Correlation
RMSE
Slope
Intercept

## Slide 18
NAAPS & ASDTA Smoke Indicator comparison
URBAN CASES
Correlation
RMSE
Slope
Intercept

## Slide 19: Conclusions / Future Work
In general, we have demonstrated that by applying either ASDTA or NAAPS smoke index, there is a general improvement in the resultant relationship between satellite AOD and station PM2.5 as the SI decreases.
In particular, the Correlation and slope increases as the smoke index becomes lower and the RMSE and y-intercept decreases which is consistent with removal of smoke from inorganic aerosol conditions.
This implies that the SI can be used in a pre-processing mode to filter smoke cases.
In the future, we plan to add the SI as an additional factor to more complex processing approaches such as NN’s to improve PM2.5 estimations.
Also, we will transition from MODIS AOD to VIIRS AOD products including an assessment of the different resolution (6km EDR and .75km pixel.)
We will also look at other smoke tools such as OMI’s Absorbing Index and the VIIRS smoke mask and look for correlations and best combinations to use between all of these products.