## Slide 1
Further Steps for Improving Soil NOx Estimates in CMAQ
Quazi Ziaur Rasool, Rui Zhang, Benjamin Lash, Daniel S. Cohan
Rice University, Houston, TX
*Adapted from Cooter et al., 2012

## Slide 2: Why study soil NOx?
NOx contributes to:
  Ozone and PM formation
  Net cooling of the climate
  N deposition and acid rain
Soil NOx ~ 19% of Global NOx Budget (Vinken et al. 2014)
Large underestimations and uncertainties in Soil NOx inventories
[Source: Vinken et al., ACP 2014]
6.2
9
9.6
10
12.9
Extrapolated
Conservative
OMI
Top-down

## Slide 3: Formation of Soil NO
Biotic (Nitrification-Denitrification):
  Microbial action on soil N
  All sources of N can be converted to NO3--N
Abiotic (Chemo-denitrification):
  non-enzymatic conversion of NO2− or NO3−
  low pH; higher NH4+ ,NO2−, reduced metal, organic matter and moisture
NH4+ NH2OH HNO NO NO2-
NO NO2- NO3-
[Source: Pilegaard, Phil Trans R Soc B 2013
and Medinets et al., Soil Bio & Biochem 2015]
(NH4+-N + NO3--N + Organic N)
Chemo-denitrification
Org-N
Microbial Nitrification
Microbial Denitrification
  Affected by soil pH, moisture, Temp.; N availability & Vegetation type
Fe2+ ; H+
NO
Mineralization

## Slide 4
[Source: Hudman et al, ACP 2012]
Berkeley Dalhousie Soil NO Parameterization (BDSNP) vs. standard Yienger & Levy scheme in CMAQ
Features | Yienger-Levy | BDSNP
Land surface model | No LSM to be based upon | Uses GEOS-Chem LSM
Soil temperature (T) | Soil T = f (Air temp) | Soil T from GEOS-Chem LSM
Soil Moisture (θ) | Poor soil moisture data | Soil moisture from GEOS-Chem LSM
Response to Soil Moisture (θ) | Accounts for rainfall instead of soil moisture | Accounts for soil moisture, rain-induced pulsing after drought
Deposition | Not accounted for | Takes N deposition in to account
Emission response | Overestimated in wet soil Weak correlation in dry soil | Non-linear response to T & θ, sophisticated emission response

## Slide 5
Uses biomes from CMAQ fine-resolution LSM (Pleim-Xiu)
North American or global biome emission factors
Uses EPIC dynamic daily fertilizer fields in place of fixed
Created a stand-alone (offline) version
  Allows rapid creation of soil NO inventories and testing of sensitivities to fertilizer application, input parameters, etc.
  Uses meteorological fields but not photochemical model
  Requires assumptions for N-deposition to soils
Enhancements to BDSNP

## Slide 6
Soil NO Flux = A’(Biome, Soil Nitrogen (Deposition, Fertilizer)) x f(T) x g(θ) x
Pulse(Dry Period) x Canopy Reduction
BDSNP Soil NO scheme implemented in CMAQ v5.0.2
Biome Emission Factors
(LU/LC + climate zones)
(Steinkamp and Lawrence, 2011)
Old: GEOS-Chem LSM
New: Pleim-Xiu LSM from CMAQ (NLCD40 land use category - option of Global and North American emission factors )
Deposition
Inline BDSNP: Deposition from CMAQ
Offline BDSNP:
Uses deposition fields from benchmarked run
Fertilizer
Old: Potter (2010) for 1994-2001
New: Daily EPIC simulation for 2011
Soil N = Biome N + Deposition N + Fertilizer N
Meteorology (WRF) and
Land Surface Model (Pleim Xiu)
Soil Temperature (T) and Soil Moisture (θ) for emission response
Antecedent dry period length for Pulse Emission Factor
Radiation/wind/pressure for Canopy Reduction Factor
Soil NO Emission Rate
Potter or EPIC Fertilizer N pool data

## Slide 7: Soil biome/Land Use Dataset Comparison
GEOS-Chem Biome map (0.25° x 0.25°)*
CMAQ MODIS NLCD40 biome map (12 km)*
Previous BDSNP (inline with GEOS-Chem)
24 Land use categories - MODIS LU/LC classification
Too coarse for regional modeling
Current BDSNP (inline with CMAQ / offline)
MODIS 24 Land use types regrouped (from NCLD 40 category LU/LC map)
Köppen-Geiger climate zone definition (Kottek et al., Meteorol. Z. 2006), re-gridded to 12 km grid size
(Warm)
(Cold)
*Both based on global emission factors Stienkamp & Lawrence, ACP 2011

## Slide 8: Flexibility to use different biome emission factors
GEOS-Chem biomes with global S&L* CMAQ NLCD biomes with global S&L*
CMAQ NLCD biomes with
North American S&L*
*S&LSteinkamp, J. and Lawrence, M. G. (2011) Improvement and evaluation of simulated global biogenic soil NO emissions in an AC-GCM. Atmospheric Chemistry and Physics, 11(12), 6063–6082. doi:10.5194/acp-11-6063-2011
East US- more broadleaf forest (higher biome emission factor) than other parts of world
Midwest- Croplands in other regions like Asia emit higher NO than in US

## Slide 9
Total daily soil N (= NH4+-N + NO3--N + Organic N ) pool input into BDSNP
[Weighted sum as per grid crop fraction]
Dynamic Fertilizer & Control Scenarios input:
EPIC outputs as CMAQ inputs
[Source: Cooter et al., Biogeosciences 2012 and FEST-C User manual]
EPIC
Grid-wise Crop types cultivated (Crop fraction file consistent with NLCD LU/LC)
Grid-wise daily soil N (classified as separate NH4+-N , NO3--N , Organic N pools)
+

## Slide 10
Environmental Policy Integrated Climate (EPIC) model
Fertilizer Application Rate estimates-
  USDA Agricultural Resource Management Survey database
  Validated with fertilizer sales rate
Heat Unit Scheduling (HUSC), plant nutrient stress drive fertilizer timing
[Source: Cooter et al., Biogeosciences 2012]

## Slide 11: Impact of EPIC vs. Potter Fertilizer Data on Soil NO
Fertilizer
Application (kgN/ha)
Control (Potter)
EPIC
Difference in Soil NO (g/s) (EPIC - Potter)*
EPIC - Potter
*Averaged over July 2011, and based on NLCD biome map with global emission factors from S&L 2011

## Slide 12: Sub-domain soil NO (monthly mean)
BDSNP (Potter with Old Biome) - YL
(EPIC with New Biome) – (Potter with Old Biome)
Chart: Sub-domain soil NO (Monthly mean, July 2011)
| MidWest | NE | SE | South (TX, OK) | NW | SW
YL | 1961.28 | 289.44 | 495.936 | 559.872 | 438.048 | 594.432
BDSNP (Potter with Old Biome) | 3870.72 | 521.856 | 915.84 | 1632.96 | 1226.88 | 1667.52
BDSNP (EPIC with New Biome) | 4492.8 | 673.056 | 1468.8 | 1797.12 | 1339.2 | 1503.36
NW
SW
NE
SE
Mid-West
South
NW
SW
NE
SE
Mid-West
South

## Slide 13: Impact of different soil NO schemes on NO2 column (Monthly mean)
BDSNP (Potter with Old Biome) - YL
(EPIC with New Biome) – (Potter with Old Biome)

## Slide 14: Impact of different soil NO schemes on MDA8 Ozone (Monthly Mean)
BDSNP (Potter with Old Biome) - YL
(EPIC with New Biome) – (Potter with Old Biome)

## Slide 15: Aggregated metrics for model performance (3 cases inline with CMAQ)
Daily Avg. PM2.5 (July 2011)
PM2.5 (Daily) Observed data from IMPROVE sites1
Ozone Observed data from EPA’s AIRS AQS (Air Quality System) network2
Aggregated performance metrics for sites showing higher sensitivities between 3 cases (including sites exceeding EPA standard in case of Daily max. 8-hr ozone)
MDA8 Ozone (July 2011)
1http://www3.epa.gov/airquality/airdata/
2http://views.cira.colostate.edu/fed/Datasets/Default.aspx
Chart: Correl. coeff. ~ 0.6 (For all 3 cases)
| NMB (%) | NME (%)
YL | -4.8088 | 14.4559
BDSNP (Potter with Old Biome) | 2.2193 | 10.683
BDSNP (EPIC with new (global) Biome) | -1.2823 | 14.7039
Chart: Correl. Coeff. ~ 0.7 (For all 3 cases)
| NMB (%) | NME (%)
YL | -28.5192 | 34.6374
BDSNP(Potter with Old Biome) | -26.9013 | 33.878
BDSNP (EPIC with new (global) Biome) | -26.4425 | 33.5695

## Slide 16: Conclusions
BDSNP updates: Finer-scale representation of soil NO dependence on land use, soil conditions, and N availability
Finer resolution results in higher sensitivity of soil NO to biome emission factors
New BDSNP predicts higher soil NO due to dynamic fertilizer data and fine resolution biomes
Non-linear trend in soil NO with soil parameters and meteorology
Slight decrease in NMB for ozone and PM
Need closer inspection of performance in regions with largest soil NO changes

## Slide 17: Acknowledgements
NASA AQAST TIGER Soil NOx Project funding
Ellen Cooter, Jesse Bash (US EPA)

## Slide 18: Extra Slides

## Slide 19: Inline BDSNP: Three WRF-BEIS-CMAQ simulation cases
YL - EPA standard configuration with YL95 soil NO scheme
BDSNP (Potter with old Biome) – BDSNP soil NO scheme with GEOS-Chem soil biome classification and Potter at al. (2010) fertilizer data
BDSNP (EPIC with new Biome) – BDSNP soil NO scheme with NCLD40 Global soil biome and EPIC fertilizer data

## Slide 20: Monthly Mean (July 2011) Soil NO
YL
BDSNP (Potter with Old Biome)
BDSNP (EPIC with New Biome)

## Slide 21: Monthly mean(July 2011) MDA8 O3
YL
BDSNP (Potter with Old Biome)
BDSNP (EPIC with New Biome)

## Slide 22: Monthly mean(July 2011) Daily Avg. PM 2.5
YL
BDSNP (Potter with Old Biome)
BDSNP (EPIC with New Biome)

## Slide 23: Impact of different soil NO schemes on Daily Avg. PM 2.5 (Monthly mean)
BDSNP (Potter with Old Biome) - YL
(EPIC with New Biome) – (Potter with Old Biome)

## Slide 24: Effect of varying Fertilizer and Biome inputs on soil NO (based on Monthly mean estimates for July 2011)
Chart: Change in Sub-domain Soil NO (tonnes/day)
| MidWest | NE | SE | South (TX, OK) | NW | SW
(New NLCD 40 Global Biome) - (Old GEOS-Chem Biome) | -5.184 | 24.8832 | 168.48 | 2.592 | -38.88 | -75.168
(EPIC ) - (Potter) | 251.424 | 98.496 | 80.352 | 80.352 | 49.248 | 10.368
(New NLCD40 NAM Biome) - (New NLCD40 Global Biome) | -88.128 | -7.776 | -12.96 | -49.248 | -15.552 | -85.536