## Slide 1: Aerosol from Organic Nitrogen in the Southeast United States
Office of Research and Development
National Exposure Research Laboratory, United States Environmental Protection Agency
CMAS Conference, 5 October 2015
Havala O. T. Pye,1,*
Deborah J. Luecken, 1 Lu Xu, 2 Christopher M. Boyd, 2 Nga L. Ng,2 Kirk Baker,3
Benjamin R. Ayres,4 Jesse O. Bash, 1 Karsten Baumann,5 William P. L. Carter,6
Eric Edgerton,5 Juliane L. Fry, 4 William T. Hutzell, 1 Donna Schwede, 1 and Paul B. Shepson7
1National Exposure Research Laboratory, US Environmental Protection Agency
2Georgia Institute of Technology
3Office of Air Quality Planning and Standards, US Environmental Protection Agency
4Reed College
5Atmospheric Research and Analysis, Inc.,
6Center for Environmental Research and Technology, University of California at Riverside
7Purdue University
*pye.havala .AT. epa.gov

## Slide 2: Particle-phase organic nitrogen (pON)
Organic nitrogen (ON)
  Forms in the gas phase when VOCs react with OH/NO or the nitrate radical (NO3)
  Has uncertain fate (photolysis, partitioning to the particle, hydrolysis, or deposition) with implications for NOx and ozone
In the particle phase, ON is an important component of PM in California, Colorado, the Southeast United States, as well as other locations
Carlton et al., SOAS white paper
Southern Oxidant and Aerosol Study (SOAS)
1 June to 15 July 2013
Centreville, AL SEARCH network site
Regionally representative
NO2 column density
Notes: A major source of oranic nitrates is reaction in the gas phase of VOCs with OH/NOx …..

## Slide 3: Organic aerosol in the Southeast
Xu et al. 2015 PNAS
Less oxidized-oxygenated organic aerosol (LO-OOA)
Factor resolved in ambient AMS data (Xu et al. 2015 PNAS)
Second largest contributor to brown carbon absorption (after biomass burning) (Washenfelder et al. 2015 GRL)
Similar to b-pinene + NO3 laboratory-based factor (Boyd et al. 2015 ACP)
Correlates with organic nitrate functional groups in the particle (R=0.81)
Includes SOA from monoterpenes + NO3 and isoprene and other minor contributions
Notes: Today we are going to focus on LO-OOA as a proxy for SOA from organic nitrates

## Slide 4: Traditional BVOC+NO3 OA model (CMAQ v5.1)
+ NO3
+ OH
Isoprene
Emission
SV_ISO1
SV_ISO2
AISO1
AISO2
Monoterpenes
Emission
SV_TRP1
SV_TRP2
ATRP1
ATRP2
oligomers
Monoterpenes: Carlton et al. 2010 ES&T
Isoprene: v5.1 unpublished
+ NO3
+ OH
+ Ozone
Notes: CMAQ has included SOA from pathways that would include nitrate functional groups for quite some time

## Slide 5: Revised organic nitrogen SOA model (CMAQ v5.1 saprc07tic aero6i)
Aerosol Organic Nitrate
Gas organic nitrate
deposition
Photolysis or chemical reaction
deposition
BVOC + NO3
BVOC + OH, NO
NOx
Hydrolysis
HNO3
+
Organic
HNO3
deposition
Benefits
Interaction of aerosol system with gas system (implications for NOx, ozone)
Provides more opportunities for evaluation
b
a
Notes: In saprc07tic aero6i we have revised the SOA scheme to include SOA from explicit biogenic organic nitrates

## Slide 6: What is hydrolysis?
Hydrolysis is a reaction with water in the particle
The organic product of hydrolysis is likely an alcohol (-ONO2 replaced with -OH)
Converts organic nitrogen (aka organic nitrates, alkyl nitrates, AN) to HNO3 thus serves as a NOx sink
Rate is likely a function of acidity and type of nitrate group (primary, secondary, tertiary)
Two different implementations of hydrolysis in CMAQv5.1
cb05e51 (Pleim presentation)
Similar to CB6r3, CAMx v6.1 approach
Particle-NTR  HNO3, t = 6 hrs
No tracking of particle-phase NTR
saprc07tic with aero6i (this work)
Particle-phase biogenic organic nitrates converted to nonvolatile SOA and HNO3
Timescale of 3 hours (30 hours as a sensitivity)
Optimal timescale is faster than cb05e51, but applies to a smaller subset of organic nitrates
Notes: Hydrolysis is a critical component of our SOA model and Jon mentioned this morning that hydrolysis improved the vertical profile of alkyl nitrates in CMAQ

## Slide 7: Semivolatile BVOC-nitrates
Organic Nitrate | Parent VOC | Surrogate Structure | Molec. Wt. [g/mol] | O:C | OM/ OC | Vapor Pressure [Pa] at 298 K | Saturation concentration C* [mg/m3] at 298K | Lifetime against particle-phase hydrolysis
MTNO3 | Mono-terpenes (excl. a-pinene) | C10H17O5N | 231 (Fry et al. 2009) | 0.5 | 1.9 | 1.3x10-4 (Fry et al. 2009) | 12 (calculated from pvap) | 3 hrs (Boyd et al. ACP 2015 for tertiary monoterpene nitrates)
ISOPNN | isoprene | C5H10O8N2 | 226 (Rollins et al. 2009) | 1.6 | 3.8 | 9.7x10-5 (Rollins et al. 2009) | 8.9 (Rollins et al. 2009) | 3 hrs (Boyd et al. ACP 2015 for tertiary monoterpene nitrates)
ISOPNN only has nocturnal (from reaction with NO3) sources and is primarily composed of dinitrates
MTNO3 has both daytime (from RO2+NO) and nighttime (from NO3) sources and both single and dinitrates

## Slide 8: NO3 is the dominant ON source
MTNO3 Production
* CIMS signal is one subset of MTNO3
*
Notes: RO2 fate:
Night: 40% RO2, 60% HO2
Day: 50% HO2, 10% RO2, 40% NO

## Slide 9: Monoterpene-ON SOA > Isoprene-ON SOA
Monoterpene-ON SOA
Isoprene-ON SOA
Hydrolysis Product
All units: mg m-3
thydrolysis=3 hr

## Slide 10: Regional BVOC SOA increases
Base Biogenic SOA (v5.1 aero6)*
Increase over Base
All units: mg m-3
thydrolysis=3 hr
* Base biogenic SOA: Semivolatile SOA and oligomers from monoterpenes, isoprene, sesquiterpenes following Carlton et al. 2010 and IEPOX SOA following Pye et al. 2013.

## Slide 11: OC predicted at CTR June 2013
Base v5.1-beta
Revised w/ thydrolysis=30 hr
Revised w/ thydrolysis=3 hr
Local Hour
OC mgC/m3
Observations
CMAQ
Observations
CMAQ
Bias in OA vs AMS: -23%
(-1.26 mg/m3)
Bias in OA vs AMS: -35%
(-1.93 mg/m3)
Local Hour
Local Hour

## Slide 12: Faster hydrolysis more consistent with observations
Increasing the hydrolysis rate increases the magnitude of modeled LO-OOA

## Slide 13: Faster hydrolysis more consistent with observations
Faster hydrolysis improves the speciation of LO-OOA
Increasing the hydrolysis rate increases the magnitude of modeled LO-OOA

## Slide 14: Faster hydrolysis more consistent with observations
Faster hydrolysis improves the speciation of LO-OOA
Increasing the hydrolysis rate increases the magnitude of modeled LO-OOA
Faster hydrolysis improves the magnitude of gas-phase alkyl nitrates (AN)

## Slide 15: 25% NOx emission reduction leads to 9% OA reduction
mg/m3

## Slide 16: Conclusions
Gas-phase mechanisms should couple with aerosol-phase mechanisms to provide a realistic depiction of monoterpene+NO3 chemistry (allows for removal of NOx from the system)
Model predictions of ANs and LO-OOA are more consistent with observations when particle-phase hydrolysis is relatively fast (3 hours vs 30 hours)
Updates described here (fast hydrolysis) will be available in v5.1 saprc07tic aero6i
NOx emission reductions in the Southeast are expected to reduce SOA
Notes: Monoterpenes are predicted to account for the majority of particle-phase organic nitrates at CTR
New pathways product more SOA than standard
Hydrolysis decreases gas-phase SANs, increases modeled HNO3 and LO-OOA, but does not substantially increase particle organic N

## Slide 17
Office of Research and Development
National Exposure Research Laboratory, United States Environmental Protection Agency

## Slide 18: Acknowledgements
The authors thank Kristen Foley, Jon Pleim, Rohit Mathur, Kathleen Fahey, Rob Pinder, Ron Cohen, and Steve Brown for useful discussion.
The authors thank CSC for emission processing, Shaojie Song for GEOS-Chem simulations, William Brune for OH observations, Tran Nguyen and Paul Wennberg (NSF grant AGS-1240604) for CIMS data, and William Brown for ceilometer data.
The authors also thank the SOAS field team including Ann Marie Carlton.
SEARCH is sponsored by Southern Company and EPRI. Georgia Tech was supported by NSF Grant 1242258 and US EPA STAR RD-83540301 and R835410. JLF acknowledges EPA STAR 83539901. PBS acknowledges EPA STAR R835409.
This work has been submitted for publication and is currently under review.

## Slide 19: Updates to CMAQ saprc07tic
Base: Xie et al. 2013 ACP expanded isoprene chemistry available in CMAQ v5.0.2
saprc07 base (Carter 2010 AE)
10 isoprene nitrates (isoprene+NO3 follows Rollins et al. 2009 ACP)
1 lumped nitrate for sources other than isoprene
Updates in CMAQ v5.1 for saprc07tic_ae6i ONLY:
Tracking of monoterpene nitrates (excluding a-pinene)
Tracking of isoprene dinitrates
Vapor pressure-based partitioning of monoterpene nitrates and isoprene dinitrates
Hydrolysis of particle phase organic nitrates with two assumptions:
  10% tertiary nitrate (30 hour lifetime)
  100% tertiary nitrate (3 hour lifetime)
Updates to gas-phase deposition
Other minor changes