## Slide 1
Constraining Condensed-Phase Kinetics of Secondary Organic Aerosol Components from Isoprene Epoxydiols
Theran Riedel, Ying-Hsuan Lin, Zhenfa Zhang, Kevin Chu, Joel Thornton, William Vizuete, Avram Gold, and Jason Surratt
Dept. of Environmental Sciences and Engineering
The Gillings School of Global Public Health
University of North Carolina at Chapel Hill
CMAS Conference
October 5, 2015

## Slide 2: isoprene epoxydiols (IEPOX) and SOA
Aerosol Phase
“tracers”  aerosol products from IEPOX that contribute to SOA mass
~50% of isoprene  IEPOX (rural)
~500 Tg/year isoprene
  even at low conversion (urban) lots of
potential mass to aerosols
Gas Phase

## Slide 3: IEPOX-tracer formation
Gaston et al., ES&T 2014; Riedel et al., ES&TL 2015
Eddingsaas et al., JPCA 2010; Cole-Filipiak et al., ES&T 2010; Piletic et al., PCCP 2013
khet = Sa/4
k  9e-4 M-2 s-1
k  2e-4 M-2 s-1
k = ??
k = ??
k = ??
k = ??
Recent interest in explicit modeling of SOA formation due to model-measurement deviations
  GAMMA: McNeill et al., ES&T 2012
  CMAQ: Pye et al., ES&T 2013; Karambelas et al., ES&TL 2014
Need for more constraints on SOA formation kinetics
  experiments and modeling

## Slide 4: IEPOX chamber SOA experiments
10 m3 teflon chamber
RH: < 5%
aerosol seed: (NH4)2SO4 + H2SO4
IEPOX injected: 600 ppbv
seed injection
and stabilization
IEPOX
injection
Filter
collection
SOA
Total SOA growth: 170 g m-3

## Slide 5: IEPOX-tracer quantification
GC/MS: 2-methyltetrols, C5-alkene triols, 3-MeTHF-3,4-diols, IEPOX-dimer
LC/ESI-MS : IEPOX-OS, IEPOX-dimerOS
other SOA
“other SOA”  IEPOX-SOA products not quantified through offline measurements

## Slide 6: explicit chamber-SOA modeling
0-D time-dependent box model
Model run time = experiment duration
Initialize model with:
  chamber measured seed aerosol [Sa] and [mass]
  E-AIM calculated seed aerosol composition
    [SO42-], [HSO4-], [H2O], [H+]
Explicitly track:
  IEPOX(g), IEPOX(aq)
  2-methyltetrols, organosulfate, C5-alkene triols, 3-MeTHF-3,4-diols, IEPOX dimer, IEPOX dimer organosulfate, other SOA
  [SO42-], [HSO4-]
Vary model aqueous rate constants to minimize difference between model output and filter measurements

## Slide 7: explicit chamber-SOA modeling
IEPOX(g) IEPOX(aq)
2-methyltetrol
dimer
organosulfate
C5-alkene triol
3-MeTHF-3,4-diol
dimer OS
H+, SO42-
H+, H2O
H+
H+
H+, IEPOX
H+, IEPOX
other SOA
H+
volatile products
SOA yield (SOA) < 1, so invoke volatile product formation

## Slide 8: model output

## Slide 9: model output

## Slide 10: model-estimated rate constants
k  9e-4 M-2 s-1
k  2e-4 M-2 s-1
Notes: -Repeated 5 times varying the amount of IEPOX injected.

## Slide 11: molar SOA yield (SOA)
Riedel et al., ES&TL 2015: SOA = 0.1 – 0.12
Notes: -means that per mole about 8% of IEPOX

## Slide 12: atmospheric-type simulation
Total predicted SOA mass = 0.37 g m-3
Initialize with:
500 pptv IEPOX
ammonium bisulfate aerosol
250 m2/cm3 aerosol Sa
50% RH
6-hour processing time
2-methyltetrols 288 ng/m3
IEPOX-OS 52 ng/m3
C5-alkene triols 25 ng/m3
3-MeTHF-3,4-diols 7.4 ng/m3
IEPOX-dimer 0.1 ng/m3
IEPOX-dimerOS 0.1 ng/m3
other SOA 0.6 ng/m3

## Slide 13: atmospheric-type simulation
Look Rock, TN (Budisulistiorini et al., ACP 2015)
Yorkville, GA (Lin et al., ES&T 2012)
tracers = 482.8 ng m-3
study mean (ng m-3)
Total predicted SOA mass = 0.37 g m-3
tracers = 724.5 ng m-3

## Slide 14: final thoughts
estimated formation rate constants for IEPOX-SOA tracers that have yet to be constrained by bulk measurements
  agreed well with experimentally obtained estimates
  (2-methyltetrols and IEPOX-OS)
can be extended to other SOA production systems (i.e., -pinene)
important to test that current understanding can account for SOA production in simple systems
recently this work submitted to ACPD

## Slide 15: acknowledgements
83540401
UNC Surratt Group
Jason Surratt
Ying-Hsuan Lin
Matthieu Riva
Sri Hapsari Budisulistiorini
Xinxin Li
Maiko Arashrio
Tianqu Cui
Weruka Rattanavaraha
Kevin Chu
UNC Gold Group
Avram Gold
Zhenfa Zhang
Funding:
University of Washington
Joel Thornton
Cassandra Gaston
NSF: CHE 1404644 and 1404573
Texas Commission on Environmental Quality

## Slide 16: the end… thanks!

## Slide 17: junk slides

## Slide 18: model output: titration of aerosol sulfate
Low-NOx isoprene oxidation (IEPOX formation) with acidified ammonium sulfate seed aerosol from Surratt et al., ES&T, 2007
Model output (this study):

## Slide 20
Recent interest in explicit modeling of SOA formation due to model-measurement deviations
  GAMMA: McNeill et al., ES&T 2012
  CMAQ: Pye et al., ES&T 2013; Karambelas et al., ES&TL 2014
Need for more constraints on SOA formation kinetics
  experiments and modeling