## Slide 1: Top-Down Constraints on Emissions of NH3, NOx, and SO2 during the 2013 NOAA SENEX Campaign
M. J. Alvarado1, C. R. Lonsdale1, E. Winijkul1, C. M. Brodowski1, K. E. Cady-Pereira1, D. K. Henze2, S. Capps2,*
1Atmospheric and Environmental Research
2Univerisity of Colorado – Boulder
*Now At Drexel University
With thanks to the SENEX science team
(A. Neuman, J. Nowak, J. Holloway, T. Ryerson, A. Middlebrook, J. Jimenez, J. Fry)
SEARCH Science Team (S. Shaw, K. Bauman, C. Blanchard)
and Environment and Climate Change Canada (C. McLinden, M. Shephard)
Copyright 2016, Government sponsorship acknowledged.

## Slide 2: NH3, SO2, and NOx are key PM2.5 precursors
NH3 + HNO3NH4NO3
2 NH3 + H2SO4(NH4)2SO4
Increase incidence of cardiovascular and respiratory diseases
Increase number of CCN
SO2, NOX emissions decreasing due to controls but NH3 increasing
Approach: Use model-based top-down approaches to constrain emissions
Identify emission-related errors in baseline model runs (this talk)
  Use chemical families (e.g., NHx = NH3(g) + NH4(p)) to reduce impact of chemistry errors, then separate meteorology from emission errors
Future Work:
  Lagrangian models (e.g., WRF-STILT, Nehrkorn et al., 2010)
  CMAQ Adjoint (Hakami et al., 2007)

## Slide 3: Using Satellites to Investigate NH3 Sources
TES NH3 transects over Bakersfield in CalNex suggested a x2 underestimate in afternoon due to diurnal cycle errors (Lonsdale et al., ACPD, 2016)
2012 CrIS NH3 is consistent with CalNex TES results.
Some evidence of a transport error on June 17 – flow along slope not correct?

## Slide 4: NOAA SENEX Campaign (June-July 2013)
SEARCH Network
CrIS NH3
OMI NO2
NOAA P-3 Aircraft

## Slide 5: CMAQ Modeling Configuration
Files provided by US EPA to follow their SENEX configuration
Eastern US Grid
  12 km horizontal
  35 vertical layers
WRF 3.6.1
  CUMULUS: Kain-Fritsch
  MICROPHYSICS: Morrison 2-moment
  RADIATION: AER’s RRTMG
  PBL SCHEME: ACM2
  SURFACE LAYER: Pleim
  LAND-SURFACE: Pleim-Xiu
CMAQ v5.0.1
  SAPRC07tc gas chemistry
  AERO6 aerosols
  Aqueous chemistry
NEI 2011 Emissions
  Scenario 2013_ef_v6_13g_s07_hg
  No Bi-Di NH3 Flux
  No Lightning NOx

## Slide 6: Difficulties Using NH3 RVMR with CMAQ
CrIS NH3 RVMR (ppb)
CMAQ NH3 RVMR (ppb)
Slope = 0.12
r2 = 0.20
CMAQ NH3 profiles concentrated at surface.
CrIS sensitivity is at higher altitudes than TES
Using RVMR (Shephard et al., 2011) thus leads to spuriously low CMAQ values
Instead focus on NH3 surface gradients
Raw CMAQ
CrIS
CMAQ RVMR

## Slide 7: Feed lot NH3 emissions overestimated in AL
CrIS Surface NH3
CMAQ Surface NH3
CMAQ – NOAA P3 NH3
06/11/13
(Tuesday)
06/22/13
(Saturday)

## Slide 8: NH3 errors not just due to partitioning

## Slide 9: SEARCH NHx daily averages
CTR
MNB = -30%
MANGE = 39%
r2 = 0.47
Slope = 1.07
Data: Daily averages of continuous NH3(g) and NH4(p) at SEARCH sites
Daily NHx generally underestimated (MNB = +1 to -30%)
A few days at Yorkville have dramatic underestimates
YRK
MNB = +1.1%
MANGE = 41.5%
r2 = 0.13
Slope = 0.29
JST
MNB = -11%
MANGE = 23%
Slope = 0.93
r2 = 0.56
BHM
MNB = -19%
MANGE = 52%
Slope = 0.71
r2 = 0.29
Alabama
Georgia
Rural
Urban

## Slide 10: High NHx event at Yorkville?
June 1 – July 15 Daily Averages
High NH3 at Yorkville from poultry feed lots (broilers) to the ESE (Saylor et al., Atmos. Environ, 2010).
Observed sustained winds from ESE (100o ± 20o) for 3-day period.
Modeled wind direction much more variable, with afternoons generally from N.
NH3(g)
Obs.
CMAQ
NH4(p)
Obs.
CMAQ

## Slide 11: Aircraft SOx over Alabama and Georgia shows combination of emission and transport errors

## Slide 12: June 11 SOx: CMAQ underestimates point source, gets location of EC Gaston power plant plume wrong

## Slide 13: June 11 SOx: CMAQ underestimates point source, gets location of EC Gaston power plant plume wrong

## Slide 14: SEARCH daily SOx observations
CTR
MNB = -10%
MANGE = 40%
r2 = 0.23
Slope = 0.70
Data: Daily averages of continuous SO2(g) and SO4(p) at SEARCH sites
Daily SOx generally accurate except:
  At JST (missing or underestimated local source?)
  For a few days at CTR
Alabama
Georgia
Rural
Urban
YRK
MNB = +8%
MANGE = 35%
r2 = 0.41
Slope = 1.13
BHM
MNB = +8%
MANGE = 45%
r2 = 0.25
Slope = 1.05
JST
MNB = +119%
MANGE = 125%
r2 = 0.20
Slope = 2.65

## Slide 15: High SOx event at Centreville?
Hourly SO2 data shows two peaks from SW:
8 AM, June 25
2 PM, June 26
SO2 point sources to SW (NEI 2011):
Lowman Power Plant (4,300 tpy)
Barry Power Plant (11,644 tpy)
Chunchula Gas Plant (1,447 tpy)
Georgia Pacific Pulp and Paper (1,971 tpy)
Model winds from SSE and WSW, respectively, during events.
BUT measured winds from SW in other periods didn’t have same high SO2 levels.
June 1 – July 15 Daily Averages
Centreville Wind Rose, June 26-30
Centreville Wind Rose, June 6-10
SO2(g)
Obs.
CMAQ
SO4(p)
Obs. (continuous)
Obs. (daily teflon)
CMAQ

## Slide 16: SEARCH daily NOy suggests NOx overestimate
Data: Daily averages of continuous NOy compared with total modeled NOy from CMAQ (including NO3(p)) at SEARCH sites
Large overestimates of NOy at all locations
  r2 higher at rural sites than urban
CTR
MNB = +70%
MANGE = 71%
r2 = 0.63
Slope = 1.88
Alabama
Georgia
Rural
Urban
YRK
MNB = +173%
MANGE = 173%
r2 = 0.74
Slope = 2.43
BHM
MNB = +184%
MANGE = 185%
r2 = 0.17
Slope = 1.71
JST
MNB = +173%
MANGE = 174%
r2 = 0.27
Slope = 2.01

## Slide 17: Aircraft NOy also suggest NOx overestimate, but not as severe as at SEARCH sites or on weekends?
Tuesday
Saturday
Wednesday

## Slide 18: June 11 NOy: NOy overestimate consistent with NOx emission overestimate in Birmingham

## Slide 19: June 11 NOy: Possible contribution from errors in transport of EC Gaston Power Plant plume

## Slide 20: OMI NO2 doesn’t show strong overestimate for Atlanta or Birmingham
Area | OMI NO2*
Atlanta | +1%
Birmingham | -19%
Charlotte | -21%
Nashville | -21%
Louisville | -6%
Fayetteville | -49%
Miami | +39%
Offshore Louisiana | +47%
*Mean of (CMAQ-Obs)/CMAQ

## Slide 21: Summary
NH3
  CrIS and NOAA P-3 observations show NH3 emissions from feed lots in northern Alabama are lower than in the 2011 NEI
  But NHx at SEARCH sites is generally underestimated (MNB = +1% to -30%), including a high NHx event at Yorkville missed in CMAQ due to errors in wind direction
SO2
  SOx errors seem more consistent with transport errors rather than emission errors, except at the Jefferson Street SEARCH site
NOx
  SEARCH NOy observations suggest NOx emissions in NEI 2011 are overestimated (MNB = 70-180%)
  P3 aircraft also sees mean NOy overestimates over Georgia and Alabama, but with MNB of 12-52%
  But CMAQ (without lightning NOx) underestimates OMI NO2 columns over Birmingham by 20%

## Slide 22: Acknowledgements
    NOAA CPO AC4 Program Grant Numbers NA13OAR4310060 and NA14OAR4310129
NOAA CSD and SENEX science team (A. Neuman, J. Nowak, J. Holloway, T. Ryerson, A. Middlebrook, J. Jimenez, J. Fry)
SEARCH Science Team (S. Shaw, K. Bauman, C. Blanchard)
Environment and Climate Change Canada (C. McLinden, M. Shephard)
EPA (K. Baker, H. Pye)
UNC CMAS Center (B.H. Baek, Z. Adelman)

## Slide 23: Backup Slides

## Slide 24: Better emissions with TES NH3
Largest changes western US and Mexico
Used GEOS-Chem adjoint with TES NH3 profiles, averaging kernels and error covariances to optimize model
Optimized GC shows better agreement with AMoN network measurements
Zhu et al., 2013, JGR

## Slide 25: Why switch to CrIS?
 | TES | CrIS
Satellite | AURA | NPP
Available Data | July 2004-present | October 2011-present
Resolution | 0.06 cm-1 | 0.625 cm-1
Footprint | 5x8 km rectangle | 14 km diameter circle
Repeat cycle | Once every 16 days | Daily
Equatorial crossing | 1:30 am and 1:30 pm | 1:30 am and 1:30 pm
Noise in NH3 window | 0.09 – 0.12 K | 0.03 – 0.06 K
TES is past its design lifetime, taking little new data, and has low spatial coverage
CrIS could monitor global NH3 with high spatial coverage for many more years (>2022)

## Slide 26: NH3 signal from TES and CrIS
Simulated spectra and NH3 signal
18 ppbv at surface
Detectability is ~1 ppbv under ideal conditions
But thermal contrast also plays a role
TES
CrIS

## Slide 27: CrIS microwindows and constraints
Lower spectral resolution of CrIS required different microwindows.
A priori and constraints from TES (Shephard et al., 2011)
  Polluted, Moderately polluted, and Unpolluted profiles
A priori selected based on signal to noise ratio (SNR) and thermal contrast

## Slide 28: TES and CrIS Sensitivity to NH3
Both instruments most sensitive to NH3 between 950 and 600 mbar
TES is more sensitive to amounts lower in the atmosphere
1 piece of information or less: DOFS<1.0
Collapse all information to a single point: RVMR
  Easier to compare with in situ measurements, models and other instruments
TES
CrIS

## Slide 29: CrIS NH3 Retrieval: Simulated Spectra
Notes: Doubled NH3 emissions in GEOS-Chem to generate “true” profiles
Profiles fed into RT model and CrIS noise added to get simulated spectrum.
Test ability of retrieval to reproduce the “true” profiles

## Slide 30: CrIS California Monthly Average NH3

## Slide 31: June 11 NOy: NOy overestimate consistent with NOx emission overestimate in Birmingham

## Slide 32: CMAQ NH3 profile very concentrated near surface
NOAA P3
Aircraft
CMAQ

## Slide 33: CMAQ seems well-mixed in PBL based on CO
NOAA P3
Aircraft
CMAQ