## Slide 1: Predicting the Impact of a Wood-Stove Change-Out Program on Ambient Particle Levels in Utah Valleys
Nancy Daher, Ph.D.
Christopher Pennell
Utah Division of Air Quality

## Slide 2: Overview
Three non-attainment areas
Confined topography
Susceptible to strong wintertime inversions
Exceedances of 24-hr PM2.5 NAAQS during wintertime inversions
Notes: Wasatch Front: width,max= ~18 miles, Length = 120 mi
Elevation ~ 2200 m (7200 ft) above valley floor
Cache valley, Length = 37.3 miles, W = 12.4 miles, elev = 9700 ft

## Slide 3: Overview
Three non-attainment areas
Confined topography
Susceptible to strong wintertime inversions
Exceedances of 24-hr PM2.5 NAAQS during wintertime inversions
NP Lareau et al. AMS 2013
Notes: Wasatch Front: width,max= ~18 miles, Length = 120 mi
Elevation ~ 2200 m (7200 ft) above valley floor
Cache valley, Length = 37.3 miles, W = 12.4 miles, elev = 9700 ft

## Slide 4: Overview
Three non-attainment areas
Confined topography
Susceptible to strong wintertime inversions
Exceedances of 24-hr PM2.5 NAAQS during wintertime inversions
Notes: Wasatch Front: width,max= ~18 miles, Length = 120 mi
Elevation ~ 2200 m (7200 ft) above valley floor
Cache valley, Length = 37.3 miles, W = 12.4 miles, elev = 9700 ft

## Slide 5: Overview
Wintertime PM2.5
Residential Wood Combustion (RWC) accounts for 13-21% of wintertime PM2.5 in Utah’s non-attainment areas
Chart: 
| RWC | Other
Hawthorne | 16.2 | 83.8
Chart: 
| RWC | Other
 | 21.1506 | 78.8494
Chart: 
| RWC | Other
 | 12.787 | 87.213
Wintertime PM2.5

## Slide 6: Overview
Chart: PM2.5
| Wood smoke | Ammonium sulfate | Ammonium nitrate | Urban/Industrial source | Ammonium chloride/road salt | Road dust | Vehicular emissions
 | 0.16199 | 0.094945 | 0.34277 | 0.06833 | 0.16741 | 0.027374 | 0.13718
PMF results winter 2014-2015
Chart: 
| RWC | Other
Hawthorne | 16.2 | 83.8
Chart: 
| RWC | Other
 | 12.787 | 87.213
Chart: 
| RWC | Other
 | 21.1506 | 78.8494
Wintertime PM2.5

## Slide 7: Objective
Determine the Impact of a Wood-Stove Change-out Program
Existing
wood-burning devices
EPA-certified
wood-burning devices

## Slide 8: Approach
Base Run
Baseline residential wood-burning inventory
Sensitivity Run
Modified inventory
Wood-burning devices replaced by EPA-certified ones
Source Apportionment Modeling
Source Apportionment Modeling
CAMx6.3+PSAT
Notes: 2014 NEI back-casted to 2011. Emissions calculated using EPA RWC new tool (for 2014 NEI)
This assumes a complete and immediate replacement
purely a sensitivity run

## Slide 9: Model Configuration: CAMx6.3
1.33 km (201 x 90)
Two-way Nesting
4 km (180 x 186)
Notes: Two‐way nesting propagates information both up‐ and down‐scale across all grids.

## Slide 10: Model Configuration: CAMx6.3
41 vertical layers
Two-way nesting
Cb6r2 aerosol scheme
Boundary/Initial conditions from MOZART
SMOKE3.6.5 emissions processor
WRF meteorology processor (University of Utah)
CAMx-PSAT source apportionment tool
4 km (180 x 186)
1.33 km (201 x 90)
Notes: Emissions: using EPA new tool for WS; back-projected to 2011
cb6r2: mechanism 2; No halogen chemistry
Two‐way nesting propagates information both up‐ and down‐scale across all grids.
Advection solver: PPM
Chemistry: EBI
Dry deposition: zhang
Horiz. Diffusion: k theory

## Slide 11: Modeling Episode: Wintertime Inversion

## Slide 12: Model Modifications
WRF Model Modifications* - Land use/cover - Snow cover fields
CAMx Model Modifications/Set up - Snow cover adjustment - Zeroing out of ozone deposition velocity - kvpatch
Improved Nitrate Simulation
*University of Utah, Eric Crosman & Chris Foster
Improved Inversion Simulation
Notes: improved land use, snow cover and snow albedo characterizations that more closely represent field observations.
Modifications to the NLCD 2011 dataset included reducing the areal extent of the Great Salt Lake to reflect the lake state at that time as well as changing the characteristics of a number of land use classifications (e.g., urban and barren land) to more closely match albedo observations obtained during PCAPS.
Snow cover obtained from North American Mesoscale (NAM) reanalysis was also modified to better match observations

## Slide 13: Base Case Model Performance: Primary OC
Kvpatch
Enhance nighttime mixing
Simulated boundary layer
Observed boundary layer
Notes: improve the turbulent coupling between the surface and the lower boundary layer
WRF: MYJ PBL scheme

## Slide 14: Base Case Model Performance: Primary OC
Urban STN sites

## Slide 15: Base Case Model Performance: PM2.5
Hawthorne/Lindon: - urban
Logan:
-rural
Notes: HW, LN 2 urban sites, each representing a non-attainment area
logan, primarily an agricultural community; not nearly as urbanized as HW and LN
Distinct air basin

## Slide 16: PSAT: Source Regions/Groups
Source Regions
20 Source Regions:
1-
2-
3-
4-
5-
Source Groups
Three groups: Group 1: Residential wood combustion (RWC) emissions Group 2: Non-RWC low-level emissions Group 3: Point sources
Tracer Species
Primary PM species: - Primary Organic Aerosol (POA) - Elemental Carbon (PEC)
- Fine crustal material (FCRS)
- Other fine PM (FPRM)
20 source regions

## Slide 17: Absolute Drop in RWC (µg/m3)
Jan. 7
PM2.5 > 50 ug/m3
Percent Drop in modeled PM2.5
Jan. 7
PM2.5 > 50 ug/m3

## Slide 18: Absolute Change in Ambient PM2.5 (µg/m3)
Apply % drop in PM2.5 modeled to PM2.5 measured

## Slide 19: PMF vs. CAMx-PSAT
Compare Base Case to PMF results (receptor-based technique)
Determine RWC contribution relative to measured PM2.5
PSAT: January 2011
PMF: Winter 2014-2015
Urban
Semi-rural
Notes: BR due to poorer model performance at this site

## Slide 20: Findings
Change-out program has a limited air quality benefit
Generally good agreement between CAMx & PMF for primary RWC at urban sites
Overall good model performance for OC/PM2.5
Important implications for developing emissions control strategies
Notes: Results help inform similar efforts aiming at investigating the impact of a WS change-out program

## Slide 21: Acknowledgements
Gail Tonnesen
University of Utah: Dr. Erik Crosman, Dr. John Horel & Chris Foster
Ramboll Environ: Gary Wilson & Chris Emery

## Slide 22
Thank You

## Slide 24: Percent Reduction in Emissions
 | CO | NOx | PM2.5 | SO2 | VOCs
Salt Lake | 37.3% | 15.6% | 21.4% | 16.4% | 35.8%
Utah | 37.8% | 17.8% | 22.0% | 14.2% | 38.2%
Cache | 35.3% | 18.8% | 20.0% | 10.4% | 37.3%
Entire State | 38.4% | 18.7% | 22.0% | 12.8% | 40.2%

## Slide 25: EPA RWC Estimation Tool
NEI 2011 tool
Appliance Fraction
Derived from the U.S. Department of Commerce, "American Housing Survey for the United States: 2005" and certified stoves were grown at an EPA estimated 1% per year.
Burn Rate
Based on USDA Forest Service Midwest or Great Plain state surveys performed in the 1990s. Rates were then adjusted to account for efficiencies in EPA certified stoves. County climate zones were also applied to further adjust burn rates.
NEI 2014 tool
Appliance Fraction
American Housing Survey + Energy information administration residential energy combustion survey
Logistic regression that estimates the likelihood of whether or not a home uses a wood-burning appliance. Uses demographic variables to predict the proportion of homes in each county that uses each appliance (home type; urban/rural setting; number of heating degree days; appliance type; burn type)
Burn Rate
Estimated using regression analysis based on each unique combination of home type, urban/rural setting, appliance type and burn type

## Slide 26
Appliance type | Efficiency (%)
Uncertified freestanding cordwood stove | 54
Certified non-catalytic cordwood stove | 65
Certified catalytic cordwood stove | 70
Pellet Stove | 75
Uncertified cordwood fireplace insert | 49
Certified non-catalytic cordwood insert | 60
Certified catalytic cordwood insert | 65
Pellet insert | 70
Cordwood fireplace | 18

## Slide 27: Difference in cords burned between EPA 2011NEIv2 tool & DAQ Survey
 | Fireplaces | Inserts | Stoves
All areas | 9.2% | -49.8% | -40.1%
Box Elder | -36.8% | -20.7% | 30.0%
Cache | -33.6% | -48.7% | -10.8%
Davis | -38.0% | -61.3% | -50.4%
Salt Lake | 59.3% | -53.9% | -55.0%
Tooele | -11.8% | -28.4% | -16.8%
Utah | -4.3% | -26.7% | -27.9%
Weber | -29.5% | -70.2% | -29.2%

## Slide 28: Emissions Calculation
Notes: Occupied housing units: American Community Survey (2014)
Appliance fraction: American Housing Survey + Energy information administration residential energy combustion survey
50 unique appliance fractions
Wood density: US Forest Service, Timber Products Output, 2005
Burn rate: estimated using regression analysis based on each unique combination of home type, urban/rural setting, appliance type and burn type

## Slide 29
Observed boundary layer
Simulated boundary layer

## Slide 30: KVPATCH Application
KVPATCH preprocessor applied to:
Enhance nighttime mixing over urban areas
Enhancement over user-specified surface layer depth
Day-by-day basis
Weak trough
Set depth = 200 m
Notes: Increase dispersion by increasing the diffusivity coefficient that is estimated by WRF
Applies landuse-dependent minimum Kv values to layers below user-specified height.
enhance mixing below convective clouds
The cloud patch extends the daytime PBL Kv profile through capping cloud tops as a means to prohibit artificial collapse of the boundary layer when convection develops and to include convective venting to the free troposphere.
Applies minimum Kv values to layers below a user-defined height based on input landuse fields and surface layer stability within that depth

## Slide 31: KVPATCH Application
KVPATCH preprocessor applied to:
Enhance nighttime mixing over urban areas
Enhancement over user-specified surface layer depth
Day-by-day basis
Set depth = 600 m
Notes: Increase dispersion by increasing the diffusivity coefficient that is estimated by WRF
Applies landuse-dependent minimum Kv values to layers below user-specified height.
enhance mixing below convective clouds
The cloud patch extends the daytime PBL Kv profile through capping cloud tops as a means to prohibit artificial collapse of the boundary layer when convection develops and to include convective venting to the free troposphere.
Applies minimum Kv values to layers below a user-defined height based on input landuse fields and surface layer stability within that depth

## Slide 32: Base Case Model Performance: Crustal Material

## Slide 33: Base Case Model Performance: Primary OC
Meas. PM2.5 = 49.1 µg/m3
Meas. PM2.5 = 65.4 µg/m3

## Slide 34: Absolute Change in POA
Jan. 2
PM2.5 < 25 ug/m3
Jan. 7
PM2.5 > 50 ug/m3

## Slide 35: Residential Wood-combustion Source Estimates: Base Case
Jan. 2
PM2.5 < 25 ug/m3
Jan. 7
PM2.5 > 50 ug/m3

## Slide 36: Sensitivity Analysis

## Slide 37: Model Performance: Total PM2.5

## Slide 38: Sensitivity Analysis