## Slide 1
Carey Jang, U.S.EPA/Air Quality Modeling Group
Zac Adelman & Dongmei Yang, UNC-CH, Institute of Environment
Dustin Zhu, South China Univ. of Technology, China
Shuxiao Wang and Jia Xing, Tsinghua Univ.
CMAS Conference, RTP, NC, October 25, 2016
Development and Applications of Next-Generation Integrated Air Quality Decision Support System (ABaCAS)
Science
Policy
Actions
Cost/Benefit & Attainment
ABaCAS
Air Pollution
(PM2.5 & O3)
Emissions Control & Cost
Health & Economic
Benefit
AQ
Benefit & Attainment

## Slide 2: Outline
Development of Next-Generation Integrated AQ Decision Support System: “ABaCAS”
  “ABaCAS ”: Air Benefit and Cost and Attainment Assessment System
    An international collaborative project supported by DOS, EPA, China MEP, Taiwan EPA and Energy Foundation
    Developed jointly by a team of U.S. and international scientists
    Built upon EPA’s new-generation modeling assessment tools: SMAT-CE, RSM/CMAQ, and BenMAP-CE.
Recent Development & Applications:
  “Streamlined ABaCAS-SE” : Integrated assessment of AP control cost and AQ, health/economic & attainment benefits to support policy analysis
  International Applications : China YRD & PRD cases, Western USA case, (other Asian and USA cases under development)
ABaCAS

## Slide 3
Control
& Cost
Estimate
Real-time
Air Quality
Benefit
Air Quality
Attainment
Assessment
Health &
Economic
Benefit
Integrated
Cost/Benefit
& Attainment
Assessment
ABaCAS : Air Benefit and Cost & Attainment Assessment System
Integrated AQ Decision Support System (http://www.abacas-dss.com)

## Slide 4: “ABaCAS”: Air Benefit and Cost & Attainment Assessment System
An integrated AQ Decision Support System
Developed for “Scientists” and “Policy Makers”

## Slide 5: “ABaCAS-SE ” (Streamlined Edition”) (2015-2016)
Cost estimate ($$)
Health Benefit ($$)
Attainment (DVs)
AQ Benefit (ug/m3)
Benefit ($$)/Cost ($$)
> 12 ug/m3 (non-attainment)
ICET script
BenMAP-CE script
SMAT-CE script
RSM-VAT script
ICET
BenMAP-CE
SMAT-CE
ABaCAS-SE Master Script
RSM-VAT
BenMAP-CE
ABaCAS-SE
Control Strategy
B
Control Strategy
C
……………
Control Policy Scenarios
Control Strategy
A
Streamlined Assessment
Notes: spatial field: A Spatial Field refers to air pollution estimates made at the center of each grid cell in a specified modeling domain. For example, MATS might calculate ozone design values for each grid cell in the modeling domain. Several types of Spatial Fields can be calculated for ozone and PM.
利用环境监测数据、模型数据（主要是CMAQ模拟的结果）作为模型输入，并利用优化的数理统计技术对大气复合污染状况进行模拟，实现对环境空气质量标准的达标评估。其中包括point estimate和spatial field estimate。

## Slide 6: “ABaCAS-SE” (Streamlined Edition, 2015): Developed for Policy-Making and Analysis
ABaCAS-SE “YRD 2017 case”:
5~10 minutes to complete a run
ABaCAS-SE

## Slide 7: ABaCAS-SE：China YRD/Shanghai Case Study
China National Air Pollution Control Plan (2013) | 
Region | Annual PM2.5
BJ-TJ-Hebei | 25% ↓
YRD/Shanghai (Yangtze River Delta) | 20% ↓
PRD/Guangzhou | 15% ↓
Beijing | 60 ug/m3
Other Cities (333 cities) | 10% ↓ (PM10)
RSM/CMAQ
AQ Response to Emissions Control
BenMAP-CE
Health and Economic Benefits
AQ Attainment
SMAT-CE
AQ Attainment in YRD:
2017: PM2.5 20% ↓
2030: Attain China NAAQS
Emissions Control & Cost
ICET

## Slide 8
2010
2017
2030
Chart: 
| WET | ESP | WET+FGD | ESP+FGD | ESP+CFB | ESP+LNB | FGD+LNB | ESP+FGD+LNB | ESP+FGD+LNB+SCR | HED+FGD+LNB+SCR
2010 | 9614879.72 | 33987138.62 | 223736.43 | 195949865.16 | 8455768.87 | 23132291.26 | 2282023.41 | 82938763.19 | 114341239.25 | 0
Chart: 
| WET | ESP | WET+FGD | ESP+FGD | ESP+CFB | ESP+LNB | FGD+LNB | ESP+FGD+LNB | ESP+FGD+LNB+SCR | HED+FGD+LNB+SCR
2017 | 0 | 3148377.19 | 0 | 0 | 2055847.72 | 18640967.73 | 10586744.63 | 79579849.77 | 407141980.32 | 105265260.29
2017 | 0 | 3148377.19 | 0 | 0 | 2055847.72 | 18640967.73 | 10586744.63 | 79579849.77 | 407141980.32 | 105265260.29
Chart: 
| WET | ESP | WET+FGD | ESP+FGD | ESP+CFB | ESP+LNB | FGD+LNB | ESP+FGD+LNB | ESP+FGD+LNB+SCR | HED+FGD+LNB+SCR
2030 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 430621713.64 | 164385982.21
ESP+FGD+LNB+SCR
HED+FGD+LNB+SCR
AP Control Measures Considered in YRD
Chart: Power generation share
| 2010 | 2017 | 2030
GRATE | 0.017569 | 0.014257 | 0
Sub-Critical <100MW | 0.039052 | 0.016136 | 0
Sub-Critical 100-300MW | 0.045031 | 0.034148 | 0.021275
Sub-Critical ≥300MW | 0.51026 | 0.38693 | 0.26074
Super Critical | 0.1428 | 0.10829 | 0.072454
Ultra Super Critical | 0.045342 | 0.25807 | 0.22149
Fluidized Bed Combustion | 0.026683 | 0.021654 | 0
IGCC | 0 | 0 | 0.043217
Oil-fired | 0.016413 | 0 | 0
Gas-fired | 0.065235 | 0.052938 | 0.038365
Nuclear | 0.04748 | 0.058253 | 0.103
Hydro | 0.039432 | 0.041569 | 0.050651
61%
21%
18%
18%
39%
43%
28%
34%
38%
Conventional
coal-fired power
Advanced
coal-fired power
New and clean energy
(PI: Prof. Shuxiao WANG, Tsinghua Univ., June 2014)
Control
Energy
Infrastrure
2030

## Slide 9: ICET: International Control Cost Estimate Tool
2. Selections of regions,
pollutants, and Sectors
3. Calculations of
control cost & analysis
Provide control Technology cost

## Slide 10
Emission reductions to attain the air quality goals
  YRD: By 2017, the PM2.5 concentrations decrease by 20% on the basis of 2012 levels. Attaining the Ambient Air Quality Standard by 2030.
2012
2017
2030
Shanghai
Jiangsu
Zhejiang
Emissions/ 104 t
(PI: Prof. Shuxiao WANG, Tsinghua Univ., June 2014)
RSM Control Policy Factors

## Slide 11
Base
”RSM/CMAQ” in “ABaCAS-SE”: PM2.5 YRD: Base vs. Control (2010 vs. 2017)
Control

## Slide 12: ”RSM/CMAQ” in “ABaCAS-SE” YRD 2017 case: PM2.5 Source Contribution

## Slide 13: ”SMAT-CE” in “ABaCAS-SE”: PM2.5 Attainment YRD Base vs. Control (2013 vs. 2017)
Base
Control

## Slide 14
”SMAT-CE” in “ABaCAS-SE”: PM2.5 Attainment YRD Base vs. Control (2013 vs. 2017)

## Slide 15: ”SMAT-CE” in “ABaCAS-SE” YRD 2017 case: PM2.5 Attainment (Reduction)

## Slide 16: ”BenMAP-CE” in “ABaCAS-SE” YRD 2017 Case: Mortality (Lives Saved)
”BenMAP-CE” in “ABaCAS-SE” YRD 2017 Case: Valuation ($$ Saved)

## Slide 17: “ABaCAS-SE”: China YRD 2017 case (vs. 2011) Developed for supporting policy-making & analysis
ABaCAS-SE “YRD 2017 case”:
5~10 minutes to complete a run
ABaCAS-SE
Benefit/Cost =
~12.5

## Slide 18: China Pearl River Delta (PRD) Ozone Case Study
RSM/CMAQ
BenMAP-CE
SMAT-CE
Benefit/Cost
(PI: Prof. ZHU Yun, SCUT)

## Slide 19: Western U.S. Case Study (ABaCAS-SE)
CMAQ (no-RSM)
BenMAP-CE
SMAT-CE
Benefit/Cost
(PI: UNC-Chapel Hill)

## Slide 20
  Fully functional “ABaCAS website” (abacas-dss.com) and on-line user manuals & quick start guides
  Enhanced “ABaCAS-SE” and “no-RSM” option
  International control cost estimate tool (ICET)
  Single Source Impact Analysis (SSIA) for PM2.5 & O3
  New analytical & supporting tools: Model-VAT & Data Fusion Tool (under development)
  Integrated AQ & climate assessment: GCAM-ABaCAS (plan for 2016-2017)
New & Ongoing Development of ABaCAS System (2016 – 2017)

## Slide 21
“ABaCAS” Website (www.abacas-dss.com)

## Slide 22
“ABaCAS System” & Tools: Overview &UG

## Slide 23
“ABaCAS”: Online User Manuals

## Slide 24
“ABaCAS Download”: System Package (free)

## Slide 25
“ABaCAS” Conferences/Workshops

## Slide 26
Model-VAT:
Multi-Scale Model Visualization & Analysis Tool
H-CMAQ
GOES-Chem
User-Friendly V/A & Eval. Tool for Photochemical & Dispersion Models
CMAQ
(SCICHEM, AERMOD, CAMx,
Combined CMAQ/AERMOD underway)
Combined

## Slide 27
Health/Econ. Benefit
AQ Benefit
AQ benefit/Cost
assessment
“GCAM-ABaCAS”: Conceptual Framework
Integrated Climate-AQ Benefit/cost Assessment
Climate & AQ co-benefit/cost Assessment
ABaCAS
Control cost
RSM/CMAQ
SMAT-CE
BenMAP-CE
Climate/AQ Policies
Air Pollutant
Emissions
Reduction
ICET
GCAM
Radiative Forcing & Global mean temp
Social Cost of Carbon
(CPP, Paris Agreement, etc.)
Input Data
Output Data
GHG
Emissions
Reduction
Global Change
Assessment Model
Attainment Benefit
Climate benefit/Cost
assessment
Development Plan for 2016-2017, PI: Prof. Jia Xing, Tsinghua Univ.

## Slide 28
Emission Control
Health & Economic.
Benefit
Air Quality Attainment
PM 2.5
O3
Summary
Effective AQ management requires scientifically sound assessment tools for supporting and attaining AQ goals
“ABaCAS” can serve as an international decision support community tool for air pollution cost/benefit and attainment assessment
Scientists and policy-makers Need to work closely together with to lead to a successful application for AQ attainment
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 29: “ABaCAS” Contributors
USA:
  EPA: Carey Jang, Charles Fulcher, Neal Fann, Brian Timin, Kirk Baker, Scott Voorhees, Dale Evarts, Tyler Fox, etc.
  UNC-IE: Adel Hanna, Zac Adelman, Dongmei Yang, etc.
  Univ. of Tennessee: Joshua Fu, Xinyi Dong, Jian Sun, etc.
International:
  Tsinghua Univ.: HAO Jiming, WANG Shuxiao, XING Jia, etc.
  South China Univ. of Technology: ZHU Yun, LONG Sicheng, etc.
  Taiwan CJC Univ.: LAI, H.C., WU Pei-Chi, etc.
  Sponsors/Partners: DOS, Energy Foundation, China MEP, Taiwan EPA, Clean Air Alliance of China, Clean Air Asia, etc.

## Slide 30
USEPA/Office of Air Quality Planning & Standards
Univ. of North Carolina – Institute of Environment
ABacAS Demo Booth (4-5 pm, Tue., 10/25)
Notes: Because of the limited time, we can not introduce all. Some slides are listed behind as appendix. ///(forward and back)here it is/// Thanks for your attention; and thanks very much for the EPA team’s help again.

## Slide 31: YRD 2030 Case Study (ABaCAS-SE)
RSM/CMAQ
BenMAP-CE
SMAT-CE
Benefit/Cost = 9.3
(5~10 minutes to run)

## Slide 32
“ABaCAS Publications”: Recent Published Paper

## Slide 33: 2015 ABaCAS Conference/Training Workshop (Guangzhou, 6/23-35)
2016 ABaCAS Conference/Training Workshop (Shanghai, 6/14-16)

## Slide 34: “ABaCAS”: Air Benefit and Cost & Attainment Assessment System
New Tool: Model-VAT (2016)

## Slide 35
  Fully functional “ABaCAS website” (abacas-dss.com) and on-line user manuals & quick start guides
  Enhanced “ABaCAS-SE” and “no-RSM” option
  International control cost estimate tool (ICET)
  Single Source Impact Analysis (SSIA) for PM2.5 & O3
  New analytical & supporting tools: Model-VAT & Data Fusion Tool (under development)
  Integrated AQ & climate assessment: GCAM-ABaCAS (plan for 2016-2017)
New & Ongoing Development of ABaCAS System (2015 – 2016)

## Slide 36: Single-Source Impact Analysis (SSIA): PM 2.5 & O3
    Feature:
    Fuse results of “Dispersion” (e.g., AERMOD) & “Grid ” (e.g., CMAQ) model
  1. “Dispersion Model”:
    Provide SSIA of Primary PM2.5
    (local or near-source impact)
  2. “Photochemical Grid Model”:
    Provide SSIA of Secondary PM2.5
    (regional or downwind impact)
Example of fused results of
“Dispersion Model” (AERMOD) and
“Grid Model” (CMAQ)
Grid
(CMAQ)
Fused
Dispersion (AERMOD)

## Slide 37
“ABaCAS Website”: Chinese Version

## Slide 38
Chart: PM2.5 concentraton (μg/m3)
| Beijing | Tianjin | Hebei | JJJ
2012 PM2.5 monitoring value | 89.5 | 96 | 108.4 | 106
2017 PM2.5 predicted value | 65.3 | 80.2 | 74.2 | 75.6
ABaCAS Application in JJJ
Health Endpoint (Age Range) | Beijing | Tianjin | Hebei
COPD (0-99) | 596 | 230 | 2073
Lung Cancer (0-99) | 1017 | 393 | 3495
Ischemic heart disease (25-99) | 568 | 222 | 1876
Stroke (25-99) | 1201 | 475 | 3651
Total | 3382 | 1320 | 11096
Health Benefit (GBD Avoided Death): BenMAP-CE
- Effects of China Air Pollution Control Action Plan (2012-2017)
RRF
Chart: Emissions
| 2012 | 2017 | 2012 | 2017 | 2012 | 2017 | 2012 | 2017 | 2012 | 2017 | NH3 Emission/kt | PM2.5 Emission/kt | SO2 Emission/kt | VOC Emission/kt | NOx Emission/kt
Beijing | 52.18 | 55.83 | 62.68 | 50.54 | 184.15 | 146.74 | 358.83 | 340.14 | 398.44 | 319.09
Tianjin | 45.41 | 48.59 | 113.44 | 83.07 | 287.57 | 168.11 | 297.4 | 278.9 | 387.79 | 239.16
Hebei | 627.47 | 671.4 | 861.92 | 653.87 | 1085.59 | 731.57 | 1349.55 | 1140.69 | 1589.87 | 1172.19
27.1%
16.5%
31.5%
28.7%
27.2%
12.3%
32.8%
24.1%
-7.0%
Reductions
(Profs. WANG Shuxiao and XING Jia, Tsinghua Univ., 2016)
Notes: 38

## Slide 39: “ABaCAS-China” Project Team
China:
  Tsinghua Univ.: HAO Jiming, WANG Shuxiao, XING Jia, etc.
  South China Univ. of Technology: YE Daiqi, ZHU Yun, XIE Junping, etc.
  Zhejiang Univ.: CEN Kefa, GAO Xiang, LUO Kun, CHEN Linghong, etc.
  Chinese Academy of Environmental Sciences: CHAI Fahe, GAO Jian, etc.
  Chinese Academy of Environ. Planning: LEI Yu, XUE Wenbo, etc.
  Shanghai Academy of Sciences: CHEN Changhong, Li Li, etc.
  Shanghai EMC: FU Qingyan, WANG Qian, etc.
  Sponsors/Partners: Energy Foundation, Clean Air Alliance of China, Clean Air Asia, etc.
USA:
  EPA: Carey JANG, Dale Evarts, Jeremy Schreifels, Scott Voorhees, etc.
  Univ. of North Carolina: Zac Adelman, Limei RAN, Dongmei YANG, etc.
  Univ. of Tennessee: Joshua FU, Xinyi DONG, Jian SUN, etc.

## Slide 40: “ABaCAS-China” Project Team
China:
  Tsinghua Univ.: HAO Jiming, WANG Shuxiao, XING Jia, etc.
  South China Univ. of Technology: YE Daiqi, ZHU Yun, XIE Junping, etc.
  Zhejiang Univ.: CEN Kefa, GAO Xiang, LUO Kun, CHEN Linghong, etc.
  Chinese Academy of Environmental Sciences: CHAI Fahe, GAO Jian, etc.
  Chinese Academy of Environ. Planning: LEI Yu, XUE Wenbo, etc.
  Shanghai Academy of Sciences: CHEN Changhong, Li Li, etc.
  Shanghai EMC: FU Qingyan, WANG Qian, etc.
  Sponsors/Partners: Energy Foundation, Clean Air Alliance of China, Clean Air Asia, etc.
USA:
  EPA: Carey JANG, Dale Evarts, Jeremy Schreifels, Scott Voorhees, etc.
  Univ. of North Carolina: Zac Adelman, Limei RAN, Dongmei YANG, etc.
  Univ. of Tennessee: Joshua FU, Xinyi DONG, Jian SUN, etc.

## Slide 41
Emission
Control
AQ
Benefit
Health
Benefit
Identify and compare cost of alternative control strategies
Assess air quality benefit and attainment of emissions control
Emission Control & Cost
Health & Economic
Benefit
AQ
Benefit & Attainment
Assess health and Environ.
benefit of emissions control
CoST-CE
RSM/CMAQ & SMAT-CE
BenMAP-CE
Effective AQ Management Requires Scientifically Sound Benefit/Cost & Attainment Assessment Tools

## Slide 42: “ABaCAS”: Air Benefit and Cost & Attainment Assessment System
An integrated AQ Decision Support System
Developed for “Scientists” and “Policy Makers”

## Slide 43
Provide Emissions Control Cost Analysis and Estimate
BenMAP-CE
SMAT-CE
CoST-CE
RSM/CMAQ
Provide Health Impacts and Economic Benefits Estimate
Provide Real-time Air Quality
Response of Emissions Control
Provide Attainment Test/Demo for
PM2.5 & O3 Non-attainment Areas
Please visit ABaCAS website for more information:
http://www.abacas-dss.com
ABaCAS : Air Benefit and Cost & Attainment Assessment System

## Slide 44
ABaCAS
CoST-CE
RSM/CMAQ
BenMAP-CE
SMAT-CE
Cost-effective Control Strategy Development
Health & Air Quality Benefit Assessment
Cost/Benefit Analysis & Optimization
Air Quality Attainment Assessment
Control Cost
Estimate
Air Quality
Benefit
Attainment
Test/Demo
Health & Env.
Benefit
“www. abacas-dss.com”
An Integrated Air Quality Management and Decision Support System

## Slide 45
Please visit ABaCAS website for more information:
http://www.abacas-dss.com
Provide Emissions Control Cost Analysis and Estimate
BenMAP-CE
SMAT-CE
CoST-CE
RSM/CMAQ
Provide Health Impacts and Economic Benefits Estimate
Provide Real-time Air Quality
Response of Emissions Control
Provide Attainment Test/Demo for
PM2.5 & O3 Non-attainment Areas
Applications of ABaCAS in China

## Slide 46: BenMAP-CE: Environmental Benefit Mapping & Analysis (Community Edition)
Provide Health Impacts & Economic Benefits Estimate:
Developed by USEPA and International ABaCAS team to estimate health & environmental impacts and economic benefits due to changes in AQ
BenMAP-CE
(2012-2014)
BenMAP-CE
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 47
Baseline
Control
AQ Benefit
1st Step: AQ Data
Setup

## Slide 48
AQ Benefit (gridded)
Health Impact &
Incidence Estimate
2nd Step: Health
Impact
Estimate
Population-weighted

## Slide 49
3rd Step: Aggregation, Pooling, Valuation, Uncertainty Analysis
Health & Economic
Benefits Estimate
(Aggregated & Pooled)
Incidence (gridded)
“Spatial” Aggregation &
“Multi-study” Pooling (uncertainly analysis)

## Slide 50: RSM: Response Surface Model
Provide Real-time AQ Response of Emissions Control:
Developed by USEPA & international ABaCAS team to provide real-time response of AQ concentrations to changes in emissions
RSM/CMAQ
(2011-2015)
RSM-VAT
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 51
Cost/Benefit Analysis
Decision Support System
Modeling Framework
CMAQ
Air Quality Model
BenMAP
Health Benefits Model
Decision-maker/Analyst
Policies
Impacts
Emissions Control
Air Quality Benefit
Health
Benefit
Air Quality
Emissions
Air Pollution Abatement Cost Tool
Community Multi-scale Air Quality Model
Benefit Mapping Tool
  Air Benefit & Control Assessment (ABaCAS)
CoST
Cost Analysis Tool
Integrated
Assessment
RSM
Response Surface Model

## Slide 52
Emission Source groupings
PP: Power Plant IND: Industry
TRA: Transportation DOM: Domestic
(1) Wang et al., Env. Sci. & Tech., 2011; (2) Xing et al., ACP, 2011; (3) Zhao et al., submitted ES&T., 2014
RSM/CMAQ Application in East China
Base
Control
China RSM
Regional control
Local control
Regional contribution of PM2.5 can be more important than
local contribution in Beijing
50% reduction of SO2, NOx & PM
Beijing
PM2.5
Control
Policy
Factor
Notes: 52

## Slide 53: CoST-CE: Control Strategy Tool (Prototype)
Provide Control Cost Analysis and Estimate : A prototype under development to give an estimate of control cost and link to RSM/CMAQ & BenMAP for cost/benefit assessment
CoST-CE
(2014-2015)
China Pollution Abatement Cost Model
Database & Optimization Model
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 54
CoST-CE: Prototype
Selections of regions,
pollutants, and technology
Calculations of
control cost & analysis

## Slide 55: SMAT-CE: Software for Model Attainment Test
Developed by U.S.EPA and international “ABaCAS” team to perform attainment assessment for EPA’s national rules and/or SIPs on PM2.5, O3, and visibility
SMAT-CE
(Community Edition)
(2013-2015)
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 56
Annual PM2.5
(12 ug/m3)
SMAT-CE: Attainment Test (U.S.A)
2018
Daily PM2.5
(35 ug/m3)
Ozone
(75 ppb, MD8hr)
2011
2018
2011
2018
2011
> 12 ug/m3 (non-attainment)
> 35 ug/m3 (non-attainment)
> 75 ppb (non-attainment)

## Slide 57: SMAT-CE: Status/Progress
    Software for Model Attainment Test- Community Edition
User-Friendly GUI framework
Streamlining operations & reports
    Fully functional for annual & daily PM2.5, O3, visibility attainment test
    Open-source program with user-friendly framework & GUI
    Increased computational efficiency by 2~3 times faster than MATS
    Developed “Data Viewer” w/ GIS mapping/data analysis capabilities
    Developed a pilot “SMAT-Asia” module
    Developed (1) “BenMAP” benefit module and (2) “Single Source Impact Analysis” (SSIA) module

## Slide 58: “SMAT-Asia” Prototype Development
“SMAT-Asia”: a customized version for Asia based on “SMAT-CE”
Modified GUI & data inputs/functions to accommodate different monitor data structure & technologies in Asia (e.g., optional PM2.5 species)
USA
|
USA
China
Taiwan
China YRD/Shanghai Pilot Study
Monitor Data
Model Data
Attainment Test
Shanghai
Shanghai

## Slide 59: Single-Source Impact Analysis (SSIA) in SMAT-CE
    Feature:
    Fuse results of “Dispersion” (e.g., AERMOD) & “Grid ” (e.g., CMAQ) model
  1. “Dispersion Model”:
    Provide SSIA of Primary PM2.5
    (local or near-source impact)
  2. “Grid Model”:
    Provide SSIA of Secondary PM2.5
    (regional or downwind impact)
Example of fused results of
“Dispersion Model” (AERMOD) and
“Grid Model” (CMAQ)
Grid
(CMAQ)
Fused
Dispersion (AERMOD)

## Slide 60: “ABaCAS”: Air Benefit and Cost & Attainment Assessment System
An Integrated AQ Decision Support & Assessment System
Developed for “Scientists” and “Policy Makers”

## Slide 61: “ABaCAS-SE ” (Streamlined Edition”) (Prototype: 2014-2015)
Cost ($$)
Health Benefit ($$)
Attainment (DVs)
AQ Benefit (ug/m3)
Benefit ($$)/Cost ($$)
> 12 ug/m3 (non-attainment)
CoST-CE script
BenMAP-CE script
SMAT-CE script
RSM-VAT script
CoST-CE
BenMAP-CE
SMAT-CE
Standalone ABaCAS
(Scientists)
Streamlined ABaCAS
(Policy-Makers)
ABaCAS Master Script
RSM-VAT
BenMAP-CE
ABaCAS-SE
Notes: spatial field: A Spatial Field refers to air pollution estimates made at the center of each grid cell in a specified modeling domain. For example, MATS might calculate ozone design values for each grid cell in the modeling domain. Several types of Spatial Fields can be calculated for ozone and PM.
利用环境监测数据、模型数据（主要是CMAQ模拟的结果）作为模型输入，并利用优化的数理统计技术对大气复合污染状况进行模拟，实现对环境空气质量标准的达标评估。其中包括point estimate和spatial field estimate。

## Slide 62: ABaCAS-SE：China YRD Case Study
National AP Control Plan | 
Region | Annual PM2.5
JJJ/Beijing | 25% ↓
YRD/Shanghai | 20% ↓
PRD/Guangzhou | 15% ↓
Beijing | 60 ug/m3
Other major cities (333 个) | 10% ↓ (PM10)
RSM/CMAQ
AQ Response to Emission Control
BenMAP-CE
Health and Economic Benefits
(PI: Prof. Shuxiao WANG, Tsinghua Univ., 2015)
AQ Attainment
SMAT-CE
AQ Attainment in YRD:
2017: PM2.5 20% ↓
2030: Attain China NAAQS
Emissions Control & Cost
CoST-CE

## Slide 63: “ABaCAS-SE” (Streamlined Edition, 2014-2015):: Developed for Policy-Making and Analysis
ABaCAS-SE “YRD 2017 case”:
5~10 minutes to complete a run
ABaCAS-SE

## Slide 64: ”CoST-CE” in “ABaCAS-SE” YRD 2017 Case Study

## Slide 65
”CoST-CE” in “ABaCAS-SE”: Emissions & Cost YRD: Base vs. Control (2010 vs. 2017)

## Slide 66: ”RSM/CMAQ” in “ABaCAS-SE”: PM2.5 YRD: Base vs. Control (2010 vs. 2017)

## Slide 67
”RSM/CMAQ” in “ABaCAS-SE”: PM2.5 YRD: Base vs. Control (2010 vs. 2017)

## Slide 68: ”RSM/CMAQ” in “ABaCAS-SE” YRD 2017 case: PM2.5 Source Contribution

## Slide 69: ”SMAT-CE” in “ABaCAS-SE”: PM2.5 Attainment YRD Base vs. Control (2013 vs. 2017)

## Slide 70
”SMAT-CE” in “ABaCAS-SE”: PM2.5 Attainment YRD Base vs. Control (2013 vs. 2017)

## Slide 71: ”SMAT-CE” in “ABaCAS-SE” YRD 2017 case: PM2.5 Attainment (Reduction)

## Slide 72: ”BenMAP-CE” in “ABaCAS-SE” YRD 2017 Case: Mortality (Lives Saved)
”BenMAP-CE” in “ABaCAS-SE” YRD 2017 Case: Valuation ($$ Saved)

## Slide 73
”BenMAP-CE” in “ABaCAS-SE” YRD 2017 Case: Mortality (Lives Saved)
”BenMAP-CE” in “ABaCAS-SE” YRD 2017 Case: Valuation ($$ Saved)

## Slide 74: ”Benefit/Cost” in “ABaCAS-SE” YRD 2017 Case: Benefit/Cost Analysis (Ratio=~11)

## Slide 75: YRD 2030 Case Study (“CoST-CE” in ABaCAS-SE)

## Slide 76: YRD 2030 Case Study (ABaCAS-SE)
RSM/CMAQ
BenMAP-CE
SMAT-CE
Benefit/Cost =~ 9
(5~10 minutes to run)

## Slide 77
“ABaCAS”
Website
(abacas-dss.com)
“ABaCAS”
System Overview
“ABaCAS”
System Package
(free download)

## Slide 78
Continue to upgrade/improve ABaCAS system and sub tools and expand international applications
Develop a pilot “ABaCAS-SE” study in a selected U.S. region
Incorporate “Extended RSM” (ERSM/CMAQ) into RSM-VAT
Develop an international control strategy tool (iCoST) linking to RSM/CMAQ & a “climate co-benefit” module
Develop a “Model-VAT” tool to provide multi-model, multi-scale data visualization and analysis
Develop a standalone “Data Fusion” (DF) tool to fuse monitoring and model data (spatial field)
Initiate ABaCAS pilot projects for PM2.5 & O3 assessment in Asia (Thailand, Philippines, South Korea, Taiwan, etc.)
Plan to provide ABaCAS training workshops in Asia (December 2015 in Bangkok & June 2016 in Shanghai)
Next Steps & Work Plan
Emission Control
Health & Economic
Benefit
Air Quality Attainment
PM 2.5
O3
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 79
Carey Jang, U.S. EPA, Jang.carey@epa.gov
Blue Skies for our Children !
THANK YOU! 谢谢!

## Slide 80: ABaCAS Applications in Taiwan
S-1 | Control-1 | Cost-1 | Health-1
S-2 | Control-2 | Cost-2 | Health-2
. . . | . . . | . . . | . . .
RSM/CMAQ
BenMAP-CE
ABaCAS-Taiwan
AQ
assessment
Emissions control cost & strategies
Emissions scenarios & strategies
Real-time AQ response to emission changes
Health & economic benefit using local data
Health & Economic benefit
PI:
Prof. H.C. Lai,
Chang Jung C. Univ.
Control Cost & Analysis
TECAS

## Slide 81
CoST
RSM/CMAQ
BenMAP
SMAT
Emissions
Control & Cost
AQ Benefit
Attainment
Health/Economic Benefit
“abacas-dss.com”
$$ (cost)
Tons (emis)
AQ (benefit)
Tons (emis)
$$ (benefit)
AQ (benefit)
AQ (benefit)
$$ (cost)
$$ (benefit)
$$ (cost)
ABaCAS-SE
Cost/Benefit

## Slide 83: “ABaCAS” Team
USA:
  EPA: Carey Jang, Dale Evarts, Jeremy Schreifels, Scott Voorhees, Charles Fulcher, Neal Fann, Brian Timin, Kirk Baker, Tyler Fox, etc.
  UNC-IE: Adel Hanna, Limei Ran, etc.
  Univ. of Tennessee: Joshua Fu, Xinyi Dong, Jian Sun, etc.
International:
  Tsinghua Univ.: HAO Jiming, WANG Shuxiao, WU Yue, etc.
  South China Univ. of Technology: YE Daiqi, ZHU Yun, XIE Junping, etc.
  Zhejiang Univ.: CEN Kefa, GAO Xiang, LUO Kun, CHEN Linghong, etc.
  Sponsors/Partners: Energy Foundation, Clean Air Alliance of China, Clean Air Asia, etc.

## Slide 84
Emission Control
Health & Economic.
Benefit
Air Quality Attainment
PM 2.5
O3
Summary
Effective AQ management requires scientifically sound assessment tools for supporting and attaining AQ goals
“ABaCAS” can serve as a key decision support community tool for air pollution cost/benefit and attainment assessment in Asia
Need to work closely together with Asian scientists and policy makers to lead to a successful application for AQ attainment in Asia
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences

## Slide 85
New PM2.5 standards and attainment requirements provide a unique opportunity for “ABaCAS-SE” and “SMAT-CE” applications in Asia
Propose to expand pilot projects for “ABaCAS-SE” and “SMAT-CE” applications for PM2.5 (& O3) attainment assessment in Asia (Taiwan, Thailand, South Korea, etc.)
Plan to provide ABaCAS training workshops in Asia (likely mid December 2015 in Bangkok)
Work Plan (2015-2016)
PM 2.5
O3
Notes: Comment: This is an important slide, but needs to be improved. Consider to use animations to highlight the key features & differences