## Slide 1: How do we improve the treatment of atmospheric photochemistry in future air quality models?
Deborah Luecken (USEPA)
From discussions with:
Havala Pye, Bill Hutzell, Golam Sarwar, Kathleen Fahey (US EPA)
Dick Derwent (rdscientific) , Bill Carter (UC Riverside), Harvey Jeffries (UNC)
Ajith Kaduwela (UC Davis, CARB), and many others
Office of Research and Development
NERL/CED
CMAS Annual Meeting
Chapel Hill, NC, September 24, 2016

## Slide 2: Atmospheric chemistry in AQMs must account for robust integration across media/phases and address many issues
Aerosol formation: mechanistic and parameterized
Extensible aqueous chemistry and deposition
Extended, customized Mechanistic Gas phase chemistry: Organic and inorganic
* * *
* * * *
*
*
O . *
Surface reactions (parameterized)
Strengthen linkages and consistency across scales/application
Customize mechanisms to facilitate linkages
Improve two-way information flow
CMAQ is working to:
This is the part I’m going to focus on
this morning

## Slide 3: What I’m going to talk about
Difficulties representing atmospheric chemistry in Air Quality Models
Why it is important to find a better and more consistent way to create these mechanisms
A prototype for developing the types of mechanisms we need for future applications

## Slide 4: The problem with modeling atmospheric photochemistry is that there are so many organics
~ 80% of VOC emissions can be treated with only 50 VOCs (Simon et al., Atmos. Poll. Res., 2010)
For a VOC with n carbons
= 60.5 x
=10 x Number of VOCs
Need ~ 50,000,000 species and 0.5 billion reactions
 | SAPRC07 | CB6
# species | 173 | 118
# reactions | 464 | 297
What we use right now
(Aumont et al., Atmos. Phys. Chem. 2005)
Number of Distinct VOCs produced
Number of reactions required

## Slide 5: Ways to treat 50,000,000 VOCs in Air Quality Models
Example: n-butane
CH3-CH2-CH2-CH3
CH3-C-CH3
|
CH3
By molecular structure i.e. CB05
By reactive species, i.e. SAPRC07
NC4H10
CH3-CH2-CH2-CH3
“Representative species” i.e. CRI
ALK3
CH3-CH2-CH2-CH3
CH3-S-CH3
CH3-CH2-OH
CL-CH=CH-Cl
OH + NC4H10  RN13O2
RN13O2 + NO  MEK + HO2 + NO2
RN13O2 + NO  CCHO + C2H5O2 + NO2
ALK3 + OH  0.695*xHO2 + 0.236*xTBUO + 1.253*RO2C + 0.07*RO2XC + 0.07*zRNO3 + 0.026*xHCHO + 0.445*xCCHO + 0.122*xRCHO + 0.024*xACETONE + 0.332*xMEK + 0.983*yROOH + 0.017*yR6OOH -0.046*XC
Can get very large (i.e. computationally expensive)
Depends on how you define “representative”
CH3-CH2-
PAR
CH2-
CH3
CH3
CH3
CH3
CH3
Not real species
Not real reactions
Loss of information
More condensed
More explicit
PAR + OH  0.870*XO2 + 0.130*XO2N + 0.110*HO2 +
0.060*ALD2 – 0.110*PAR + 0.760*ROR + 0.050*ALDX

## Slide 6: See Bill Carter’s talk at 2014 CMAS for more details……
Development of Gas-Phase Atmospheric Chemical Mechanisms
Overview
Mechanism development objectives, evaluation, levels of detail
SAPRC mechanisms: components, versions, updates
Recommendations and thoughts on the future
William P. L. Carter
University of California, Riverside, CA
October 27, 2014

## Slide 7: Problems common to all condensed chemical mechanisms
Difficult to modify
  Hard to keep at state-of-the-science
  Hard to adapt to secondary aerosol formation, new species
Rely largely on developer’s judgement
  Lack of transparency, documentation
Hard to evaluate/compare
  Can’t measure condensed species
  Naming conventions differ
  Unclear protocol for evaluation
wouldn’t it be great if we could fix these?

## Slide 8: Does it really matter how the mechanism represents VOCs?
Mean Bias and root mean square error in modeled ozone compared to monitored data, binned by observed values, daily 8-hr maximum ozone, over continental US, for July 1-14, 2011.
Vastly different mechanisms give similar predictions for current ozone
CRI (early version)
CB05 (e51)
CB6
SAPRC07

## Slide 9
CB05 and SAPRC07 even give similar response to emission controls (here for a 25% NOx reduction)
But they can give different concentrations of intermediate species.
The importance of having more detail in intermediate species will have implications when we look beyond ozone, NOx, organic and primary PM
~no points here
or here
Fractional difference in H2O2: CB05-SAPRC07T
0.40
0.20
0.
-0.2
-0.40

## Slide 10
Other studies show the same thing: similar ozone formation, but (sometimes large) differences in intermediates
(Knote et al., Atmos. Env., 2014)
Median ozone: +/- 5% ppb
Median OH: +/- 40%
Median H2O2: +/- 25%

## Slide 11
MEK + HCHO +MGLY
isoprene
+OH,O2
+HO2
ISOPOOH
+OH
+OH, NO2
MPAN
Decomp, hn
isoprene nitrates
HCHO + MACR + MVK + C5-aldehydes
+ HCHO, MVK, MACR
Rxn with O2 or decomp
Why intermediates matter when predicting SOA from isoprene +OH
+RO2
HCHO, MVK,MACR
+SO4-2
+NO3-
+OH
MAE
HMML
+NO3-
acid
+H2O
acid
IEPOX
AISO1
AISO2
oligomer
+SO4-2
+NO3-
ISOPO2 +
SV_ISO1
SV_ISO2
+NO
large route for SOA from isoprene
minor route for SOA from isoprene
Chemistry described in Pye et al., ES&T, 2013
Where we have information on SOA formation, we should use it!
+OH / NO or HO2
GLY + HCHO +MGLY
Notes: Dependence on NOx, NO2, water, acidity, sulfate….

## Slide 12: Differences in intermediates can influence secondary organic aerosol formation
Ratio of HOx to NO importance CB6/SAPRC07 - hourly value at 11 AM
Blue indicates where CB6 has higher throughput via HO2
orange indicates where SAPRC07 has higher throughput via HO2
Ratio of 14-d avg SOA concentrations CB6/SAPRC07
Differences in OH, HO2 and NO/HO2 ratios can make a large difference in SOA predictions
..and more SOA
..and more SOA

## Slide 13: Another example of differences: vertical profiles of alkylnitrates compared to aircraft data in DISCOVER-AQ (Baltimore)
Measurements
CB05e51
CB6
CRI
4 km
3 km
2 km
1 km
Alkyl nitrate predictions depend on mechanism you choose (factor of 5 difference here!)

## Slide 14: Errors in alkylnitrates can propagate to errors in criteria pollutants and deposition
(Pye et al., ES&T, 2015)
Example of semi-mechanistic description for biogenic nitrate SOA formation
Alkyl nitrates
VOC
NO2
Ozone
aldehydes, acids, hydroperoxides, etc.
aerosols
Organic nitrogen dry deposition
+NO
+HO2, RO2
Organic nitrogen wet deposition
+ OH, Cl, hn
Peroxy radical
+O3
aldehydes
Nitrooxy-peroxy radical
+NO3
removal
(impact on nitrogen deposition discussed in Schwede CMAS presentation 2014)

## Slide 15
The techniques that we have used in the past to create chemical mechanisms for Air Quality Models work well for ozone (what they were developed for), but don’t work so well for predicting concentrations of other species that will be important for future applications
Emerging pollutants
Aerosol components
Scale appropriate (i.e. urban global, surface stratosphere)

## Slide 16: Prototype for future mechanisms
Highly detailed chemical mechanism with documentation
Automated series of condensation rules dependent on application
Mechanism for remote atmospheres
Mechanism for ozone and PM regulatory applications
Mechanism when individual VOCs and organic aerosol components are available
Compare back for consistency
New research findings
Mechanism for specialized applications, i.e. oil and gas applications
Mechanisms for different applications are consistent, documented, and (relatively) easily generated (and updated)

## Slide 17: Components of the prototype: New research findings
New research findings
New data continually being updated and evaluated and is readily available, but we need a way to use it in models
http://iupac.pole-ether.fr/
Other examples of sources:
http://jpldataeval.jpl.nasa.gov/
http://kinetics.nist.gov/kinetics/index.jsp

## Slide 18: Components of the prototype: detailed mechanisms
Highly detailed chemical mechanism with documentation
Techniques are available for doing this but need more resources (and consistency!)
Master Chemical Mechanism (http://mcm.leeds.ac.uk/MCMv3.3.1/home.htt)
SAPRC07 Mechanism Generation System
Bernard Aumont’s Automated Generator
(Aumont et al., Atmos. Phys. Chem. 2005)

## Slide 19: Components of the prototype: condensation techniques
Some proposals on how to do this but need more innovative ideas and input, more automation and resources, community “buy in”
Automated series of condensation rules dependent on application
Average of absolute change in O3 for scenarios at various degrees of condensation for SAPRC-07
Greg Yarwood (Ramboll ENVIRON): Test of protocol for condensation of alkane chemistry in MCM to Carbon Bond mechanism (emulating MCM in CB6)
(Carter presentation, CMAS, 2014)
Increased degree of condensation
Change in ozone
Carter “lumped process” derivations for SOA
“Morpho” representation of detailed chemistry
alkane
CH3-CH2-CH2-CH3

## Slide 20: Possible Futures for chemical mechanisms
Door number 1: Keep using the mechanisms that we have
  hope nothing bad happens
Door number 2: Continue using techniques we have, but try to keep patching them up
  updating mechanisms whenever some university/Agency has resources
  pursue a partially-mechanistic SOA formation route.
Door number 3: Step back and rethink how we develop mechanisms
  invest seriously in a better way to do this, so that different mechanisms/models are consistent, transparent and flexible for our future needs.