## Slide 1: IMPROVING AIR QUALITY MODELING PERFORMANCE AND CAPABILITIES IN BOGOTÁ, COLOMBIA
Jorge E. Pachón*, Boris Galvis, María Paula Pérez,
Jhonathan Ramírez, Luisa Castro, Cesar Palacios
Universidad de La Salle, Centro Lasallista de Investigación y Modelación Ambiental CLIMA
Bogotá, Colombia
Barron Henderson, Robert Nedbor-Gross
University of Florida, Gainesville, FL, USA
15th Annual CMAS Conference, Chapel Hill, NC, October 24-26, 2016

## Slide 2: INFORMATION ABOUT BOGOTA
Population (2014) approximately 8 million
Area: 1587 km2
2,600 m.a.s.l.
Motorization rate (avg): 130 vehicles per 1000 inhabitants.
Air quality monitoring network operates since 1997. Records of PM10, PM2.5, CO, NOx, SO2, O3.
frequent thermal inversions led to bad air quality

## Slide 3: AIR QUALITY IN BOGOTA
PM10 (ug/m3)
PM2.5 (ug/m3)
O3 (ppb)
Chart: PM2.5
| 2012 | 2013 | 2014 | 2015
 | 13.3725 | 14.361 | 18.9506 | 17.28
Chart: PM10
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
 | 68 | 71 | 57 | 59.1 | 59 | 51.63 | 47.6 | 47.9 | 52 | 44
 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
only 1 station

## Slide 4
02/02/16 11am
02/02/16 10am
01/02/16 1pm
01/01/16 9am
haze produced by wildfires and strong stagnant conditions in January 2016
why are we interested in air pollution in Bogota?

## Slide 5: BACKGROUND
In 2012, Bogotá implemented a CMAQ based air quality (AQ) modeling system.
The model performed satisfactorily but needed adjustments on meteorology predictions and emission inventories.
In the last years, our efforts have focused on improving modeling results and capabilities with the following activities:
  Updating emission inventories for mobile, point and area sources
  Improving estimates of resuspended particle matter from paved and unpaved roads - see Perez et al., APR 2016
  Adjusting mobile source emission factors to consider fleet turnover and changes in fuel characteristics – see Ramirez´s poster on 10/24 at 4.10pm
  Using different terrain databases to improve meteorological performance – see Nedbor-Gross´ talk on 10/26 at 4.50pm
  Developing an emission pre-processor compatible with the photochemical model – see Perez´s poster on 10/24 at 4.10pm

## Slide 6
UPDATING OF EMISSION INVENTORIES
Emission from mobile, point, and area sources were updated from the base year (2008) to the modeling years (2012 - 2014).
TEMPORAL AND SPATIAL DISAGREGGATION
Emissions were disaggregated hourly to 1x1 km in a inner domain of 64x64 km including Bogota and surroundings.
1
SELECTION OF MODELING EPISODE
Based on the analysis of air quality records, two modeling periods were chosen: Feb. 15 (±10 days for dry period) and Oct. 15 (±10 days for wet period) 2012. JFM and OND in 2014.
EMISSION REDUCTION STRATEGIES
Emissions reduction strategies in 2020/2030 were tested for mobile, point and area sources to identy the most cost-effective program.
IMPLEMENTATION OF WRF-CMAQ
WRF and CMAQ were implemented for the modeling episode and in four domains, the inner one including Bogota and surroundings. ICs and BCs from global models.
2
3
4
5

## Slide 7: UPDATING EMISSION INVENTORIES
MOBILE
RESUSPENDED
DUST
AREA
WILDFIRES
Mobile sources contribute with >90% of NOx, CO, CO2
emissions and direct and indirect PM10 emissions.
Chart: 
| PM2.5 | PM10 | NOx | SO2 | CO | CO2 | VOC
Industrial | 307.44 | 1281 | 3275 | 2036 | 812 | 1619573 | 2828
Commercial | 67.6 | 130 | 67 | 190 | 2529 | 36022 | 105
Mobile Off-road | 149.15 | 157 | 5159 | 159 | 4520 | 769623 | 0
Mobile On-road | 1087 | 1202 | 45297 | 1228 | 241527 | 9164014 | 26096
Resuspended Dust | 8413 | 48478 | 0 | 0 | 0 | 0 | 0
Gas stations | 0 | 0 | 0 | 0 | 0 | 0 | 23786
Notes: Jhonathan, por favor señalar donde encuentro los archivos para editar la grafica en Excel, verificar que éstas sean las emisiones 2014. incluir PM2.5 en la tabla y totalizar

## Slide 8: MOBILE SOURCE EMISSIONS
VP: passenger vehicles; CC: trucks and pick-ups; T: taxis; M: motorcycles;
MB: microbus; B: bus; TM: Transmilenio (BRT); ESP: school and tourism buses; C: trucks
Buses and trucks contribute with more than 60% of PM emissions.
Chart: Hora del día hábil
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
1 | 0.0097126 | 0.005693 | 0.0041206 | 0.0042458 | 0.008147 | 0.031075 | 0.061215 | 0.050515 | 0.051254 | 0.049982 | 0.050275 | 0.048996 | 0.049258 | 0.05039 | 0.058647 | 0.066635 | 0.065243 | 0.0675 | 0.063449 | 0.057495 | 0.054095 | 0.042999 | 0.03052 | 0.018538
2 | 0.011998 | 0.0069679 | 0.0051594 | 0.0072118 | 0.015894 | 0.041784 | 0.061888 | 0.058631 | 0.050036 | 0.048746 | 0.047773 | 0.048646 | 0.049922 | 0.050559 | 0.051012 | 0.050241 | 0.052364 | 0.057456 | 0.057693 | 0.059282 | 0.05562 | 0.050524 | 0.039023 | 0.02157
3 | 0.010059 | 0.0061996 | 0.0050024 | 0.0067267 | 0.015595 | 0.03527 | 0.068029 | 0.068531 | 0.059485 | 0.053709 | 0.048213 | 0.04568 | 0.049248 | 0.050287 | 0.053784 | 0.054475 | 0.055114 | 0.059603 | 0.058849 | 0.053892 | 0.049961 | 0.042741 | 0.031203 | 0.018345
4 | 0.0077214 | 0.0045258 | 0.0032758 | 0.0033753 | 0.0064768 | 0.026814 | 0.057442 | 0.05723 | 0.053908 | 0.055687 | 0.056682 | 0.057829 | 0.057826 | 0.058864 | 0.060189 | 0.059047 | 0.06024 | 0.064163 | 0.058997 | 0.054063 | 0.050234 | 0.041931 | 0.028742 | 0.014737
5 | 0.006673 | 0.0041082 | 0.0033139 | 0.0044568 | 0.010437 | 0.043145 | 0.069318 | 0.066436 | 0.054452 | 0.052832 | 0.053233 | 0.050591 | 0.051816 | 0.052771 | 0.056965 | 0.05125 | 0.057014 | 0.065266 | 0.057864 | 0.0487 | 0.049858 | 0.043595 | 0.033464 | 0.01244
6 | 0.0049347 | 0.0032735 | 0.002918 | 0.0033879 | 0.0061253 | 0.022806 | 0.052797 | 0.050396 | 0.051004 | 0.056631 | 0.058103 | 0.057595 | 0.060236 | 0.061371 | 0.061034 | 0.062312 | 0.058501 | 0.062041 | 0.060287 | 0.060074 | 0.058254 | 0.045605 | 0.032376 | 0.0079371
7 | 0.012614 | 0.0077747 | 0.0062733 | 0.0084356 | 0.019557 | 0.025488 | 0.054356 | 0.05407 | 0.053767 | 0.05711 | 0.053767 | 0.053471 | 0.055252 | 0.057445 | 0.052655 | 0.053992 | 0.056457 | 0.062187 | 0.058992 | 0.05656 | 0.044662 | 0.040712 | 0.031397 | 0.023006
8 | 0.0092705 | 0.0063904 | 0.0055104 | 0.0077449 | 0.017429 | 0.026296 | 0.055495 | 0.061983 | 0.060859 | 0.05775 | 0.057638 | 0.058882 | 0.058033 | 0.057824 | 0.055933 | 0.057988 | 0.058536 | 0.061922 | 0.054872 | 0.046601 | 0.042489 | 0.036475 | 0.028623 | 0.015457
9 | 0.0089156 | 0.005495 | 0.0044338 | 0.0059621 | 0.013823 | 0.036928 | 0.059296 | 0.065855 | 0.059686 | 0.056412 | 0.054981 | 0.053761 | 0.05371 | 0.051067 | 0.055033 | 0.055201 | 0.056798 | 0.061177 | 0.057796 | 0.050904 | 0.047025 | 0.03919 | 0.030292 | 0.01626
10 | 0.0096079 | 0.0059216 | 0.0047781 | 0.006425 | 0.014896 | 0.017257 | 0.045001 | 0.062536 | 0.065911 | 0.05961 | 0.05988 | 0.059501 | 0.059146 | 0.055616 | 0.061598 | 0.059058 | 0.059444 | 0.060901 | 0.05302 | 0.050815 | 0.045729 | 0.038383 | 0.027443 | 0.017523
11 | 0.0057522 | 0.0038158 | 0.0034014 | 0.0039491 | 0.00714 | 0.04696 | 0.061403 | 0.06447 | 0.059382 | 0.05279 | 0.052587 | 0.055109 | 0.056853 | 0.054814 | 0.053792 | 0.058217 | 0.060238 | 0.062805 | 0.055769 | 0.050125 | 0.04982 | 0.04054 | 0.031016 | 0.0092519
12 | 0.012341 | 0.0076061 | 0.0061373 | 0.0082526 | 0.019133 | 0.024935 | 0.055894 | 0.070956 | 0.061113 | 0.055872 | 0.052601 | 0.052312 | 0.054054 | 0.056199 | 0.051513 | 0.052821 | 0.055233 | 0.05683 | 0.059378 | 0.050075 | 0.043693 | 0.039829 | 0.030716 | 0.022507
Chart: Hora del día festivo
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
1 | 0.022864 | 0.018865 | 0.018984 | 0.017707 | 0.01102 | 0.012343 | 0.02558 | 0.034076 | 0.040296 | 0.049393 | 0.059008 | 0.065806 | 0.069616 | 0.070811 | 0.063431 | 0.059984 | 0.059744 | 0.061752 | 0.062588 | 0.056621 | 0.048216 | 0.036076 | 0.024463 | 0.010755
2 | 0.026203 | 0.021882 | 0.020274 | 0.01993 | 0.016197 | 0.019669 | 0.025838 | 0.033087 | 0.037169 | 0.044619 | 0.052216 | 0.056107 | 0.056609 | 0.059432 | 0.058816 | 0.061835 | 0.06244 | 0.064462 | 0.062767 | 0.060947 | 0.055889 | 0.041523 | 0.027195 | 0.014895
3 | 0.024637 | 0.020059 | 0.01905 | 0.019679 | 0.015601 | 0.021527 | 0.032901 | 0.035844 | 0.036408 | 0.041254 | 0.045638 | 0.048074 | 0.048397 | 0.051384 | 0.066445 | 0.064236 | 0.065286 | 0.069282 | 0.064773 | 0.062557 | 0.05797 | 0.044282 | 0.02898 | 0.015737
4 | 0.022864 | 0.018865 | 0.018984 | 0.017707 | 0.01102 | 0.012343 | 0.02558 | 0.034076 | 0.040296 | 0.049393 | 0.059008 | 0.065806 | 0.069616 | 0.070811 | 0.063431 | 0.059984 | 0.059744 | 0.061752 | 0.062588 | 0.056621 | 0.048216 | 0.036076 | 0.024463 | 0.010755
5 | 0.017905 | 0.014063 | 0.014629 | 0.014491 | 0.01157 | 0.020979 | 0.036405 | 0.044104 | 0.050396 | 0.056681 | 0.062574 | 0.070766 | 0.07252 | 0.070055 | 0.069323 | 0.058863 | 0.054368 | 0.059435 | 0.058189 | 0.048837 | 0.040972 | 0.027061 | 0.016702 | 0.0091121
6 | 0.017905 | 0.014063 | 0.014629 | 0.014491 | 0.01157 | 0.020979 | 0.036405 | 0.044104 | 0.050396 | 0.056681 | 0.062574 | 0.070766 | 0.07252 | 0.070055 | 0.069323 | 0.058863 | 0.054368 | 0.059435 | 0.058189 | 0.048837 | 0.040972 | 0.027061 | 0.016702 | 0.0091121
7 | 0.017905 | 0.014063 | 0.014629 | 0.014491 | 0.01157 | 0.020979 | 0.036405 | 0.044104 | 0.050396 | 0.056681 | 0.062574 | 0.070766 | 0.07252 | 0.070055 | 0.069323 | 0.058863 | 0.054368 | 0.059435 | 0.058189 | 0.048837 | 0.040972 | 0.027061 | 0.016702 | 0.0091121
8 | 0.019442 | 0.016958 | 0.016259 | 0.01668 | 0.014271 | 0.022782 | 0.03095 | 0.035554 | 0.040307 | 0.046717 | 0.054789 | 0.06159 | 0.062932 | 0.067 | 0.066058 | 0.062686 | 0.061698 | 0.061494 | 0.059449 | 0.055071 | 0.048119 | 0.039048 | 0.025683 | 0.014464
9 | 0.024637 | 0.020059 | 0.01905 | 0.019679 | 0.015601 | 0.021527 | 0.032901 | 0.035844 | 0.036408 | 0.041254 | 0.045638 | 0.048074 | 0.048397 | 0.051384 | 0.066445 | 0.064236 | 0.065286 | 0.069282 | 0.064773 | 0.062557 | 0.05797 | 0.044282 | 0.02898 | 0.015737
10 | 0.024637 | 0.020059 | 0.01905 | 0.019679 | 0.015601 | 0.021527 | 0.032901 | 0.035844 | 0.036408 | 0.041254 | 0.045638 | 0.048074 | 0.048397 | 0.051384 | 0.066445 | 0.064236 | 0.065286 | 0.069282 | 0.064773 | 0.062557 | 0.05797 | 0.044282 | 0.02898 | 0.015737
11 | 0.017905 | 0.014063 | 0.014629 | 0.014491 | 0.01157 | 0.020979 | 0.036405 | 0.044104 | 0.050396 | 0.056681 | 0.062574 | 0.070766 | 0.07252 | 0.070055 | 0.069323 | 0.058863 | 0.054368 | 0.059435 | 0.058189 | 0.048837 | 0.040972 | 0.027061 | 0.016702 | 0.0091121
12 | 0.024637 | 0.020059 | 0.01905 | 0.019679 | 0.015601 | 0.021527 | 0.032901 | 0.035844 | 0.036408 | 0.041254 | 0.045638 | 0.048074 | 0.048397 | 0.051384 | 0.066445 | 0.064236 | 0.065286 | 0.069282 | 0.064773 | 0.062557 | 0.05797 | 0.044282 | 0.02898 | 0.015737
Temporal mobile profiles - weekday
Temporal mobile profiles - weekend
Chart: 
| SITP | Transit | Freight | Motorcycle | Taxi | Passenger | Pick-up | Tourism
N° Vehiculos | 8994 | 6648 | 105333.39 | 422242 | 52179 | 949134.1568 | 429704 | 42827
Chart: 2014
| CO2 | CO | NOx | VOC | PM2.5 | SO2
VP | 0.36856 | 0.18434 | 0.090587 | 0.10085 | 0.063307 | 0.47067
CC | 0.2123 | 0.13106 | 0.093895 | 0.091924 | 0.079853 | 0.22556
T | 0.080714 | 0.1363 | 0.20407 | 0.36553 | 0.019873 | 0.045275
M | 0.15281 | 0.40915 | 0.078361 | 0.30413 | 0.12257 | 0.19806
MB | 0.033162 | 0.029954 | 0.10623 | 0.035817 | 0.22005 | 0.01179
B | 0.045314 | 0.010434 | 0.17349 | 0.020517 | 0.13864 | 0.0094147
TM | 0.009931 | 0.0024322 | 0.040141 | 0.0047959 | 0.032233 | 0.0020712
ESP | 0.010404 | 0.0057969 | 0.054845 | 0.0073888 | 0.043871 | 0.0027311
C | 0.086799 | 0.090526 | 0.15837 | 0.06905 | 0.27959 | 0.034427
Notes: Jhonathan, por favor señalar donde encuentro los archivos para editar la grafica en Excel, incluir PM10
Profe: En el Dropbox en noveno entregable subi un Excel “graficas total emisiones todas las fuentes”

## Slide 9: Mobile PM2.5
Spatial and temporal desaggregation - PM
Resuspended PM10
Notes: Jhonathan, Luisa, la animacion de las emisiones es mucho mas rapida en mobiles que resuspendido, homogenizarlas
Ya estan homogeneizadas

## Slide 10: MODELING DOMAIN
Equatorial Mercator Projection |  |  |  |  |  | 
 | Origin (km) |  | Resolution(km) |  | #Cells | 
Domain | X | Y | Δx | Δy | X | Y
d01 | 251759.250 | -1578187. | 27 | 27 | 179 | 154
d02 | 2123759 | 158812.062 | 9 | 9 | 94 | 76
d03 | 2522759.5 | 413813.469 | 3 | 3 | 82 | 67
d04 | 2622759.250 | 483812.062 | 1 | 1 | 64 | 64
Emissions: d04 from local estimation; d01, d02 and d03 from EDGAR
WRF - ICs, BCs from GFS-NCEP, using the default physics options for WRF
CMAQ – d01: ICs, BCs from GEOS-Chem; d02,d03,d04: ICs from GEOS-Chem; BCs from parent domain
Vertical structure: 29 layers
Notes: MaPaula, verificar que la información sea correcta

## Slide 11: Modeling results in 2012 - Ozone
Ozone
Good Agreement
Model
Obs
United States NAAQS: 70 ppb
Ozone is well predicted, but not a problem.

## Slide 12: Modeling results in 2012 – PM10
PM10 “Fixed”
PM10 “Fixed”
Use of adjustment factors
Model
Obs
Coarse particles needs refinement

## Slide 13: What did we learn from AQ modeling?
Chart: PM2.5
| On road | Off road | Comerciales | Industriales | Vias | Const. Edificaciones | Const & Mantenimiento vias | Canteras | Desgaste de frenos y llantas
PM2.5 | 0.12543 | 0.00752 | 0.0061802 | 0.028069 | 0.7525 | 0.029896 | 0.00091424 | 0.039404 | 0.010079
PM emissions from mobile and point sources are not enough to explain ambient PM concentrations observed in the city (PM10 average 52 ug/m3, PM2.5 average 20 ug/m3 for 2014).
Resuspended dust emissions might account for such missing PM fraction. Prior to 2012 no emission inventory in the city had accounted for resuspended dust.
10,938 ton/yr
Chart: 
| Mobile | Point
 | 1520.9141 | 1468
3,000 ton/yr
Resuspended roads
Resuspended building
Tire and break wear
Notes: Barron, do we have a graph that shows PM concentrations modeled without RPM? So that we can show low levels of ambient PM?

## Slide 14: What did we learn from AQ modeling in 2012?
The first inventory of resuspended dust emissions resulted in overestimation of PM concentrations for the 2012 modeling year.
SO2, CO and NO2 emission inventories also resulted in overestimation of ambient concentrations in 2012.
SO2 OCT
PM10 OCT
NO2 OCT
CO OCT
Notes: Problema con el perfil nocturno night bias, no se hizo el promedio de 3 capas

## Slide 15: IMPROVING EMISSION ESTIMATES
PM underestimation
PM
overestimation
Include resuspended dust emissions
Adjust
resuspended dust emissions
SO2 overestimation
CO
Overestimation
NO2 overestimation
Adjust EFs for SO2
Adjust EFs for CO
Adjust EFs for NO2
Determine dust loadings (Cs)
Interpolate Cs to all roads
Estimate EFs from EPA AP-42, Chap. 13
Construct dust emission inventories
Revise Cs interpolation
Assign temporal variabilty to RPM
Apply mitigation factors
MOVES
Vehicular fleet age and activity (AADT)
Speed bins
Passenger vehicles and public buses renovation
Lower sulfur content in fuels
Stricter controls for VOC emissions
New EFs estimated considering:

## Slide 16: RESUSPENDED DUST ADJUSTMENT
Avg
0.59
Natural mitigation factor adjustment for re-suspended particulate
matter emission inventory
Source | Period | 2014 Hourly based fractions |  | Time invariant | Effective reduction
 |  | p(x,t) | h(x,t) | fx | 
Paved Roads | JFM | 0.87 | 1.0 | 0.62 | 0.41 Emission reduction over the year for both sources
 | OND | 0.86 |  |  | 
Unpaved Roads | JFM | 0.91 | 0.96 |  | 
 | OND | 0.91 | 0.93 |  | 
2012 project 60% adjustment factors
Recently Published International Database (~60%)
This Project Local Database (~60%)
see more at Perez et al., APR, 2016
Notes: MaPaula, reemplzar la figura de la derecha, creo tu tienes una donde no se ve el corte

## Slide 17: MOVES IMPLEMENTATION
MAIN RESULTS
MAIN CHALLENGES
Fleet equivalence between Colombia and US (type, size, power, emission control technologies, driving patterns).
New EFs reflect reflect changes in fuel quality and fleet turnover.
Tire and break wear emissions
PM EFs take into account vehicle age
see more at Ramirez´s poster on 10/24 at 4.10pm
Chart: Emission inventory 2012 vs 2014
| CO2/1000 | CO/100 | NOx/10 | VOC/10 | PM2.5 | SO2
2,012 | 10458.2212 | 8664.4547 | 6653.9508 | 9188.5495 | 1163.2183 | 14109.1493
2014 | 13438.6466 | 3009.6938 | 5331.2743 | 3490.6481 | 1340.1473 | 1859.7068
CO and SO2 chages due to new EFs

## Slide 18: MODELING RESULTS – 2014
AVG 66.9 ug/m3
AVG of modeling values observed at air quality stations; MAX of modeling values across the whole domain
MAX 128 ug/m3
PM10
OND
Quantile-quantile plots for a24 PM10 with observations on the x-axis and model concentrations on the y-axis
PM10 slightly high biased in OND
AVG 31.8 ug/m3
MAX 67.5 ug/m3
OND
PM2.5
PM2.5 is slightly high biased for low concentrations, but the bias increases for higher concentrations
Notes: Robbie,
Q-Q plot for PM10 only for January and October, update with JFM and OND. Do these results include three-layer modeling average?
Answer: I updated the QQ plots wth full JFM and OND. Yes, they include the 3-layer averaging
MAX in spatial plots differ from MAX Q-Q plots??
Answer: The maxes differ because the spatial plots are time means and the QQ plots have all of the a24 values for each day.

## Slide 19: MODELING RESULTS
AVG 1.64 ppb
MAX 15.9 ppb
SO2
OND
SO2 is slightly low biased
AVG 14.3 ppb
MAX 178 ppb
OND
AVG of modeling values observed at air quality stations; MAX of modeling values across the whole domain
Quantile-quantile plots for a24 NOx with observations on the x-axis and model concentrations on the y-axis
NOx
High bias for Nox
probably overestimation of emissions
Notes: Robbie,
Add spatial plot for 2014
Answer: Spatial plots added.
Q-Q plot for PM10 only for January and October, update with JFM and OND. Do these results include three-layer modeling average?
Answer: I updated the QQ plots wth full JFM and OND. Yes, they include the 3-layer averaging
MAX in spatial plots differ from MAX Q-Q plots??
Answer: The maxes differ because the spatial plots are time means and the QQ plots have all of the a24 values for each day.

## Slide 20: MODELING RESULTS – O3
JFM
AVG 34.6 ppb
AVG 27.8 ppb
MAX 37.5 ppb
MAX 28.1 ppb
2014
OND
Larger O3 concentrations in JFM
AVG of modeling values observed at air quality stations; MAX of modeling values across the whole domain
Quantile-quantile plots for mda8 O3 with observations on the x-axis and model concentrations on the y-axis
The simulation shows strong performance for both periods, with a slight high bias for the both periods. Bias increase for large concentrations.
Notes: Robbie,
Add spatial plot for 2014
Answer: Spatial plots added.
Q-Q plot for PM10 only for January and October, update with JFM and OND. Do these results include three-layer modeling average?
Answer: I updated the QQ plots wth full JFM and OND. Yes, they include the 3-layer averaging
MAX in spatial plots differ from MAX Q-Q plots??
Answer: The maxes differ because the spatial plots are time means and the QQ plots have all of the mda8 values for each day.

## Slide 21: HEALTH IMPACT ESTIMATION
X
Tot pop: 7’759,974
X
Fuente(SDP, 2010) – Tasas brutas de mortalidad 2005-2010
Fuente (SDP, 2010) – Proyección de población por UPZ 2014
52% pop>30
RR
All-cause mortality
6% (4-8%)
increase
10 ug/m3 PM2.5
(Krewski et al, 2009)
X
RR
Respiratory diseases
4% (1.3-6.7%)
increase
10 ppb O3
(Jerrett et al, 2009)

## Slide 22: Cost of air pollution in Bogota in 2014
Deaths from all cause by PM2.5 represent 1.1% of the Bogota's GDP.
VSL for Colombia expressed as WTP per person: $574,321.51 USD projected from (Castillo et al., 2010).
Pollutant |  | Estimated mortalities | (WTP USD in million)
PM2.5 (Krewski et al, 2009) | All-cause mortality | 1746 (1195-2270) | $1,002.765 ($686.314 - $1,303.710)
 | Respiratory | 629 (298-934) | $361.248 ($171.148 - $536.416)
 | Cardiovascular | 1050 (838 -1248) | $603.038 ($481.281 - $716.753)
O3 (Jerrett et al, 2009) | Respiratory | 152 (51-249) | $87.297 ($29.290 - $143.006)
Notes: MaPaula, por favor completar este cuadro y la información restante

## Slide 23: CONCLUSIONS
In the last years, we have significantly improved Bogota’s air pollutant emission estimates considering resuspended dust and changes in fuel quality and vehicle fleet renovation.
The implementation of CMAQ have become a great opportunity to revise emission estimates and adjust them to the proper level.
CMAQ represents a great potential to optimize costs / benefits related with air pollution in Bogota.

## Slide 24: RESEARCH NEEDS IN BOGOTA
Chemical compostion of ambient and resuspended PM. Unknown sources: erosion, break and tire wear, surface abrassion, dust.
Reconciliation of high and low resolution emission inventories, especially NOx and CO.
Determination of the PBL mixing depth to solve night-time biases.
PM forecasting system and set up early warnings to protect public health.

## Slide 25: AKNOWLEDGMENTS
This project has been funded under different contract and agreements awarded to Universidad de La Salle: contract 1467 of 2013 awarded by Secretaría de Ambiente de Bogotá; contract 241 of 2015 awarded by Colciencias; collaboration agreement 5224377 of 2015 between Ecopetrol and ULS.
We thank all the organizations and people that have contributed in different ways to this project.

## Slide 26: THANKS!
QUESTIONS?