## Slide 1: Comparing Extreme Events Simulated by WRF Using USGS and NLCD Land Use Data Sets
Stephany Taylor1,2, Tanya Spero1 and Megan Mallard1
1US EPA National Exposure Research Laboratory, Research Triangle Park, NC
2North Carolina Agricultural and Technical State University, Greensboro, NC
15th Annual CMAS Conference
October 26, 2016

## Slide 2: Motivation
Extreme weather events have catastrophic impacts on society.
Climate change can alter frequency and intensity of extreme events.
Need to simulate extreme events with confidence.
Currently using USGS land use for regional climate modeling.
Want to update to NLCD land use
  Better representation in US, especially at higher resolution
  Better alignment with configuration used at EPA for AQ modeling
  Using NOAH LSM in WRF
  NLCD not tested with NOAH
Is there an impact on simulating extreme events in WRF by changing from USGS to NLCD?

## Slide 3: Methodology
WRFV3.8 with downscaling physics/nudging options (Spero et al. 2016)
Two continuous runs: Oct 1987 – Dec 1990 (analyzed 1988-1990)
  USGS 24-category land use
  NLCD/MODIS 40-category land use
108-36-km North American domain, focus on 36-km CONUS
Comparisons to:
  North American Regional Reanalysis (NARR), 32-km
  Climate Prediction Center (CPC) precipitation reanalysis, 0.25-deg
NLCD
USGS

## Slide 4
Midwest Drought/Heat Wave 1988 >5,000 Deaths $40B damages
NC Severe Storm Outbreak May 1-6, 1989 $1B damages
Hurricane Hugo Sept. 21-22, 1989 >100 Deaths >$7B damages
Texas/Arkansas Flooding May 11-19, 1990 >$1B damages 13 Deaths
Tropical Storm Marco
Oct. 10-13, 1990 $57M damages 7 deaths
Deep Freeze Dec. 21-26, 1989 ~$5B agricultural/crop damages

## Slide 5
Accumulated Precipitation (mm) Comparisons for Drought Case June 1988
Both LU data runs:
Have similar precip. patterns.
Over predict precip. over SE and northern US border.
Under estimate rainfall across NM and central TX.
USGS over saturates southern MO and KY.
NLCD over estimate precip. over northern MO.
NLCD matches better to CPC data over northern NY.

## Slide 6: Average Soil Temperature and Moisture in the Top Layer for July and August 1988 Drought Case
Notes: Both LU simulations:
Over estimate temperatures/soil dryness over NV/UT.
Under predicts temperatures and over predicts soil moisture across the NE.
NLCD drier than USGS across NE, lower MS River Valley and GA coastline.
USGS drier than NLCD near central TX.

## Slide 7
Severe Storms May 1-6, 1989
GOES 7 Infrared Satellite Image

## Slide 8: Severe Storms May 1-6, 1989 Accumulated Precipitation (mm)
GOES 7 Infrared Satellite Image.
Both LU simulations:
  Under estimates precip.
USGS has a wider precip. pattern over TX/OK and the Carolinas.
NLCD matches CPC better over New England.

## Slide 9: Hurricane Hugo Sept. 21-22, 1989
GOES 7 Infrared Satellite Image

## Slide 10: Hurricane Hugo Sept. 21-22, 1989 Accumulated Precipitation
Both LU categories have precip. discontinuity over the Appalachian Mountains.

## Slide 11: Deep Freeze Dec. 21-26, 1989

## Slide 12: Deep Freeze Dec. 21-26, 1989 2-meter Temperature (K)
Both LU simulations have similar temperature patterns.
USGS matches NARR better over southern TX.
NLCD matches NARR better over NC.

## Slide 13: Flooding Event May 11-19, 1990
Flooding of the Trinity, Red and Arkansas rivers resulted in 13 casualties and $1.0 billion in damages.

## Slide 14: Flooding May 11-19, 1990 Accumulated Precipitation (mm)
Both LU runs substantially misrepresent precip. coverage for this flooding event.
USGS has more precip. coverage over the SE.
NLCD matches CPC better across the NE.

## Slide 15: Tropical Storm Marco Oct. 10-13, 1990
Tropical Storm Marco Track
GOES 7 Visible Satellite Image

## Slide 16: Tropical Storm Marco Oct. 10-13, 1990 Accumulated Precipitation (mm)
USGS correctly estimates precip. over west coastal FL.
NLCD has better precip. coverage over eastern NC.

## Slide 17: Summary
NLCD soil moisture tends to be drier than USGS over eastern U.S. across all case studies.
Similar precipitation patterns for all events, regardless of LU.
  Usually USGS has “wider” precip. than NLCD.
  USGS often better for high precip. events in SE.
  NLCD tends to be better for precip. in NE.
Warmer temperatures in NLCD than USGS, especially in the SE.
  Disclaimer: The views expressed in this presentation are those of the authors and do not necessarily represent the views or policies of the U.S. Environmental Protection Agency.

## Slide 18
Supplemental material
WRF Parameterizations used:
  Noah Land Surface Model
  WRF single moment 6-class microphysics scheme
  Rapid radiative transfer model for global models for short and longwave radiation scheme
  MM5 Monin-Obukhov similarity surface scheme
  Yonsei University planetary boundary layer scheme
  Kain-Fritsch cumulus scheme
Run Time: Oct. 1987-Dec. 1990
REFERENCE:
Spero, T., Chris Nolte, J. Bowden, M. Mallard, AND J. Herwehe. The Impact of Incongruous Lake Temperatures on Regional Climate Extremes Downscaled from the CMIP5 Archive Using the WRF Model. Journal of Climate. American Meteorological Society, Boston, MA, 29(2):839-853, (2016).