## Slide 1: NOX emissions, isoprene oxidation pathways, and implications for surface ozone in the Southeast United States
Katherine (Katie) Travis
CMAS 2016: 10/26/16
Co-authors: D. J. Jacob, J. A. Fisher, P. S. Kim, E. A. Marais, L. Zhu, K. Yu, C. C. Miller, R. M. Yantosca, M. P. Sulprizio, A. M. Thompson, P. O. Wennberg, J. D. Crounse, J. M. St. Clair, R. C. Cohen, J. L. Laughner, J. E. Dibb, S. R. Hall, K. Ullmann, G. M. Wolfe, I. B. Pollack, J. Peischl, J. A. Neuman, and X. Zhou
This work was supported by the NASA Earth Science Division and by STAR Fellowship Assistance Agreement no. 91761601-0 awarded by the US Environmental Protection Agency (EPA). It has not been formally reviewed by EPA. The views expressed in this presentation are solely those of the authors.
Notes: Good afternoon. Today I am going to talk about ‘Nox emissions, isoprene oxidations pathways, and implications for surface ozone in the Southeast US. I would like to thank my advisor Daniel Jacob, and the Jacob group working on this project at Harvard, as well as the PI’s from the SEAC4RS field campaign whose data I will discuss in this work. I would also like to thank my funding from both the NASA Earth Science Division and the EPA Star Fellowship program.

## Slide 2: The Southeast US Is One of the Most Difficult Regions to Model for Surface Ozone
Monthly Mean Surface O3
2001
Fiore et al, 2009
CASTNET Observations
Multi-model Mean
Blame has included isoprene chemistry, isoprene emissions, dry deposition etc.
Notes: Mainly CAMX and CMAQ, 134-150 sites
21 global
and hemispheric chemical transport models - HTAP

## Slide 3: SEAC4RS (Aug-Sep 2013) Provided an Unprecedented Dataset to Investigate Air Quality in the Southeast US
SEAC4RS Flight Tracks from DC8 Aircraft
Data Used for this Study Include:
  Thomas Ryerson, NOAA: NOy, NO, NO2, O3
  Ron Cohen, Berkeley: NO2
  Paul Wennberg, Caltech: isoprene oxidation products
  Jack Dibb, UNH: HNO3
  Sam Hall, NCAR: J-values

## Slide 4: GEOS-Chem Incorporates State-of-the-Science Understanding of O3-NOx-VOC Chemistry
0.25ox0.3125o resolution over North America.
Emissions:
  Biogenic from MEGAN (Guenther et al., 2012).
    See Zhu et al, 2016 (ACPD)
  Soil NOx from Hudman et al (2012).
  Lightning NOx according to Murray et al. (2012).
  Anthropogenic emissions from EPA’s NEI 2011v1.
Chemistry:
  Chemistry from Mao et al. (2013).
    With bromine chemistry (Parrella et al., 2012).
  Improved treatment of low- and high- NOx pathways to incorporate recent lab studies.
Physical processes:
  Faster deposition of isoprene oxidation products (Nguyen et al, 2015).
1
Notes: To study O3 in the southeast, I am using the GEOS-Chem chemical transport model. O3 in surface air from this model is show for the campaign on the right. We use assimilated meteorology from NASA, with 47 vertical layers, 0.25 degree horizontal resolution, and 88 advected tracers. We take biogenic emissions from the MEGAN inventory. Lightning Nox is constrained by observations of lightning flashes from the Lightning Imaging Sensor (LIS) and the Optical Transient Detector (OTD) satellite instruments.
Bromine sources include sea-salt aerosol, photolysis, and oxidation of short-lived bromocarbons. Decreases global mean tropospheric OH by 4%. Improves our ability to simulate 19th century O3 and seasonality. Decreases tropospheric O3 bruden by 6%,
The lightnign Nox emitted in the model for a given grid cell is distributed vertically between the surface and convective cloud top height following standard profiles for marine, tropical, midlatitude storms etc. 1-7% below 2km.
Note SENEX and SEAC4RS
Emissions:
  Biogenic from MEGANv2.1 (Guenther et al, 2010)
  Hourly anthropogenic emissions from EPA’s NEI08 for 2010
  Daily fire emissions from the Quick Fire Emissions Database (QFED) (Darmenov et al, 2013)
Chemistry
  Initial chemistry from Mao et al, 2013
  Improved treatment of isoprene RO2 isomerization (Crounse et al, 2011; Stavrakou et al, 2010; Peeters et al, 2014)
  Reduced NO2 recycling from isoprene nitrates (Lee et al, 2014)
  Reduced yields of MVK/MACR (Liu et al, 2013)
  Added gas-phase source of HONO (Li et al, 2014)
Physical processes:
  Fast deposition of isoprene oxidation products
  Aqueous uptake of soluble isoprene oxidation products
  Fast photolysis of carbonyl nitrates (Muller et al, 2014)
  Daily fire emissions from the Quick Fire Emissions Database (QFED) (Darmenov et al, 2013)
Aircraft. Aircraft emissions are from the AEIC inventory [Stettler et al., 2011] (new development).
Ships. Global shipping emissions are from ICOADS, as implemented in GEOS–Chem by Lee et al. [2011]. Shipping emissions of NOx are processed by the PARANOX module of Vinken et al. [2012] to account for ozone and HNO3 production in the plume.
Open Fires. Emissions from open fires for individual years are from the GFED2 inventory with 3-hourly, 8-day, or monthly resolution [van der Werf et al., 2009] or from the GFED3 inventory with 3-hourly, daily, or monthly resolution [Giglio et al., 2010; van der Werf et al., 2010; Mu et al. 2011].
Lightning. Lightning NOx emissions are computed with the algorithm of Price and Rind [1992] as a function of cloud top height, and are scaled globally as described by Murray et al. [2012] to match OTD/LIS climatological observations of lightning flashes. Biogenic VOCs. Biogenic VOC emissions in GEOS–Chem are from the MEGAN v2.1 inventory of Guenther et al. [2012] as implemented by Barkley et al. [2011].
Soils. Biogenic soil NOx emissions are from Hudman et al. [2012] (new development).
  Reduced yields of MVK/MACR (Liu et al, 2013)
  Added gas-phase source of HONO (Li et al, 2014)
  Biogenic from MEGANv2.1 (Guenther et al, 2010)
  Anthropogenic from NEI08 for 2010 from EPA with annual scale factors
  Daily fire emissions from QFED Chemistry
  Base chemistry from Mao et al, 2013
  Improved treatment of isoprene RO2 isomerization (Crounse et al, 2011, Stavrakou et al, 2010, Peeters et al, 2014)
  Reduce NO2 recycling from isoprene nitrates by 50% (Lee et al, 2014)
  Reduce yields of MVK/MACR (Liu et al, 2013)
Physical processes:
  Fast deposition of isoprene oxidation products
  Aqueous uptake of IEPOX to form SOA (Pye et al, 2013)
  Fast photolysis of carbonyl nitrates (Muller et al, 2014)

## Slide 5: NOx and Ozone are Overestimated in the Original GEOS-Chem Simulation
SEAC4RS PI
Jack Dibb: HNO3, Thomas Ryerson: O3, NO, NO2
PBL is 60% too high for NOx and 12ppb too high for ozone.
NEI11v1 (Gg N)
Notes: Two fundamentally different methods have been compared: chemiluminescence (NO-O3 chemical reaction and emission of radiation from the nitrogen dioxide product) and laser-induced fluorescence (absorption of radiation by nitric oxide and then reradiation at different wavelengths by the excited nitric oxide).

## Slide 6: Reducing NEI11v1 by 50% Improves Agreement with SEAC4RS NOy and O3
SEAC4RS PI
Jack Dibb: HNO3
Thomas Ryerson: O3, NO, NO2
Many studies find that NEI mobile NOx is overestimated –
  Castellanos et al, 2011; Fujita et al, 2012; Yu et al, 2012; Brioude et al, 2013; Anderson et al, 2014.
We scale NEI11v1 by 50% by reducing industry and mobile NOx by 60%.
NEI11v1
Notes: The uncertainty in this scaling factor due to the presence of soil NOx is 30-60%.
If I didn’t scale industry, I would need a 50-90%
We reduce the overall NOx budget by 41%.
Two fundamentally different methods have been compared: chemiluminescence (NO-O3 chemical reaction and emission of radiation from the nitrogen dioxide product) and laser-induced fluorescence (absorption of radiation by nitric oxide and then reradiation at different wavelengths by the excited nitric oxide).
The model's treatment of emissions from aging vehicles is one likely contributor; the NEI overestimate of NOx emissions could indicate that engines produce less NOx and catalytic converters degrade more slowly than assumed by MOVES2010. MOVES2010 likely fails to capture dependence of NOx emissions on vehicle age accurately. Similarly, Bishop et al. (2012) shows that 1% of the vehicle fleet could emit as much as 15% of total NOx emissions, indicating that misrepresen- tation of the attributes of these outliers in emissions inventories could have significant effects on the estimated emissions. Incorrect emissions apportionment to the diesel portions of the on- and off- road fleets would lead to significant errors in the ratio of CO to NOx emissions. Incorrect emission factors are also another possible source of error. Lindhjem et al. (2012) found that the use of MOVES2010 emissions factors increased NOx emissions by 50% in comparison to those found in the previous EPA model, MOBILE6.

## Slide 7: Spatial Variability Shows No Significant Biases
r=0.71
Mean model bias for ozone is +2 ppb, 9% for NOx
NOx and O3 Concentrations Below 1.5 km
SEAC4RS PI
Thomas Ryerson: O3, NO, NO2
O3, ppb
NOx, ppb
Observed NOx
Model NOx
Model O3
Observed O3
Notes: The highest observed ozone (>75 ppb) was found in air influenced by agricultural burning along the Mississippi River and by outflow from Houston over Louisiana. GEOS-Chem does not capture the extreme values and this probably reflects a dilution effect (Yu et al., 2016).
MS, AL, GA
Get citation on Ag fires

## Slide 8: Simulation with Scaled NOx Successfully Captures Isoprene Oxidation Pathways From SEAC4RS
RO2
ISOPRENE + OH 
HPALD
NO
ISOPN
HO2
ISOPOOH
Isom.
SEAC4RS PI
Paul Wennberg:
ISOPN, ISOPOOH, HPALD
‘High NOx pathway’
See Fisher et al, 2016 (ACP) for more on ISOPN
Notes: Say that the yield of isoprene nitrates matters.
Mao et al, 2013 - this is attributed to a lower and reversible yield of isoprene nitrates, increasing the ozone production efficiency per unit of nitrogen oxides (NOx ≡NO+NO2).
The bias for HPALD is within the uncertainty of the kinetics and measurement. Our HPALD source is based on the ISOPO2 isomerization rate constant from Crounse et al. (2011).
A theoretical calculation by Peeters et al. (2014) suggests a rate constant that is 1.8× higher, which would reduce the model bias for HPALD and ISOPOOH and increase boundary layer OH by 8%.
GEOS-Chem overestimates ISOPOOH by 74% below 1.5 km. Recent work by St. Clair et al. (2015) found that the reaction rate of ISOPOOH + OH to form IEPOX is approximately 10% faster than the rate given by Paulot et al. (2009b), which would further reduce the model overestimate. It is likely that after these changes the GEOS-Chem overestimate of 15 ISOPOOH would be within measurement uncertainty. For both ISOPOOH and HPALD, GEOS-Chem captures much of the
spatial variability (r = 0.8 and 0.7, respectively).
5% from other minor pawthw
We successfully capture the fate of ISOPO2 that leads to O3.
We underestimate HPALD by a factor of 2.
  Isomerization rate is uncertain by 50% (Crounse et al, 2011)
  OH reaction rate is uncertain by +/- 35% (Wolfe et al, 2012)
ISOPOOH is overestimated – formation rate is uncertain by +/- 16%.
ays

## Slide 9: Reductions in NOx Have a Smaller Impact Due to Spatial Segregation of Emissions
More details in:
Yu, K. et al, ACP (2016)
Notes: High NOx pathway would just be 62% with original Nox, 13% change in high NOx pathway

## Slide 10: We Add New Constraints on NOx Using Measurements of Deposition
Wet deposition of NO3-
NOx = NO + NO2
NO2 + OH + M HNO3
Very
soluble
H+ ,NO3-
Dry deposition of HNO3
Measured by the National Atmospheric Deposition Program
Measured during Southern Oxidant and Aerosol Study June-July 2013
“ What Goes Up Must Come Down”

## Slide 11: Wet Deposition Supports National Scaling of NEI11
Observations (kg N ha-1 month-1)
Model (kg N ha-1 month-1)
US Nitrate Wet Deposition
August-September 2013
Reduced NOx (Bias = 7%)
Original NOx (Bias = 63%)
Nitrate
((kg N ha-1 month-1)
0.0 0.1 0.2 0.3 0.4
Southeast US: Bias = 8%, r=0.71
CONUS: Bias =7%, r= 0.76
Notes: *Midwest: 66% reduced to 7%, *Southeast: 71% reduced to 8%
The National Atmospheric Deposition Program has measured acids, nutrients since 1978.
250 sites, with monthly data in mg NO3-/L.

## Slide 12: Ozone Production Efficiency (OPE) Provides Constraint on Efficiency of Ozone Formation
Without scaling, OPE = 14.7 which means ozone would be produced less efficiently than observed.
Southeast US
Notes: NOz = NOy – NOx

## Slide 13: How well can we constrain US NOx emissions with OMI NO2?
OMI NO2
(BEHR)
OMI NO2
(NASA v2.1)
GEOS-Chem
with reduced
NOx emissions
-18% vs. BEHR
-11% vs. NASA
Low bias in GEOS-Chem is due to upper troposphere, not surface emissions
With original NEI emissions, Bias = +26-31%
Aug-Sep 2013 data with GEOS-Chem shape factors

## Slide 14: Free/upper troposphere makes major contribution to OMI NO2 tropospheric column in summer
25-40%
of column
GEOS-Chem low bias in upper troposphere is caused by NO/NO2 chemistry; insufficient convection of HOx precursors HCHO and CH3OOH?
Current OMI retrievals may have large AMF errors
Mean SEAC4RS NO2 profiles
Mean NO/NO2 ratio
65-80%
of column
[NO]/[NO2] ≈ k7/(k5[O3])
SEAC4RS PI
Thomas Ryerson: NO2
Ron Cohen: NO2
Notes: Current retrievals of satellite NO2 data do not properly account for this elevated pool of upper tropospheric NO2, so that the reported tropospheric NO2 columns are biased high.
K7 = NO2 photolysis
K5 = NO + O3
The upper troposphere above 8 km contributes 32–49% in the aircraft observations and 23% in GEOS-Chem.

## Slide 15: Discrepancy Remains Between Surface & Upper PBL O3
O3
Remaining uncertainties are potential O3 sinks and boundary layer mixing.
40ppb
48ppb
Altitude, km
O3, ppb
Median Ozonesonde
PI. Anne Thompson
Notes: Median ozone for CASTNET

## Slide 16: Conclusions
NEI11v1 for NOx is biased high across the US by as much as a factor of 2.
Emissions from industrial and mobile sources must be 30-60% lower than NEI values.
Evidence for this comes from (1) SEAC4RS observations of NOx and its oxidation products, (2) NADP network observations of nitrate wet deposition fluxes.
The OPE in the boundary layer is well reproduced.
There may be large errors in satellite NO2 columns due to the presence of upper tropospheric NO2. Observations show departure from photochemical steady-state.
MDA8 surface ozone is still biased against the CASTNET observations by approximately 8ppb.
ktravis@fas.harvard.edu
Travis, K. R., Jacob, D. J. et al. Why do models overestimate surface ozone in the Southeast United States?, ACP, 2016 (in press).
Notes: Emissions include scaling

## Slide 17: Additional Papers from SEAC4RS
Organic nitrates: Fisher, J. A. et al.: Organic nitrate chemistry and its implications for nitrogen budgets in an isoprene- and monoterpene-rich atmosphere: constraints from aircraft (SEAC4RS) and ground-based (SOAS) observations in the Southeast US, Atmos. Chem. Phys., 16, 5969–5991, doi:10.5194/acp-16-5969-2016, 2016.
Formaldehyde: Zhu, L. et al.: Observing atmospheric formaldehyde (HCHO) from space: validation and intercomparison of six retrievals from four satellites (OMI, GOME2A, GOME2B, OMPS) with SEAC4RS aircraft observations over the Southeast US, Atmos. Chem. Phys. Discuss., doi:10.5194/acp-2016-162, in review, 2016.
Aerosols: Kim, P. S., Jacob, D. J. et al.: Sources, seasonality, and trends of southeast US aerosol: an integrated analysis of surface, aircraft, and satellite observations with the GEOS-Chem chemical transport model, Atmos. Chem. Phys., 15, 10411–10433, doi:10.5194/acp-15-10411-2015, 2015.
SOA: Marais, E. A. et al.: Aqueous-phase mechanism for secondary organic aerosol formation from isoprene: application to the southeast United States and co-benefit of SO2 emission controls, Atmos. Chem. Phys., 16, 1603–1618, doi:10.5194/acp-16-1603- 2016, 2016.
Model Resolution: Yu, K. et al.: Sensitivity to grid resolution in the ability of a chemical transport model to simulate observed oxidant chemistry under high-isoprene conditions, Atmos. Chem. Phys., 16, 4369–4378, doi:10.5194/acp-16-4369- 2016, 2016