## Slide 1: 24-Hour PM2.5 Attainment Modeling - Fairbanks
Mark Hixson
10-23-2017

## Slide 2: Attainment Modeling for a State Implementation Plan (SIP)
Fairbanks air quality
Moderate SIP development
  Emissions Inventory
  Meteorology
  CMAQ
  Attainment Demonstration
Post-SIP challenges

## Slide 3: Overview of Fairbanks, Alaska
Fairbanks North Star Borough
97,000 residents
Fairbanks and North Pole
Second largest city in Alaska

## Slide 4: Air Quality
Carbon Monoxide
  Designated 1990
  8-hour CO standard of 9 ppm
  Attainment 2001
  Largely motor vehicle emissions driven
PM2.5
  2006 24-hr PM2.5 standard revised to 35 µg/m3
  Designated in 2009 with 43 µg/m3
  Attainment deadline 2015
  Largely wintertime wood smoke contributions
Severe cold, inversions, and stagnation
Notes: SOB registered 43 ug/m3 at time of designation

## Slide 5: Fixed Monitor Sites 2009-2013
Notes: SOB 1998
NPE 2008
NCORE 2009
NPFS 2012

## Slide 6: 24-hour PM2.5 Trends Through 2014

## Slide 7: PM2.5 Speciation
Chart: Winter PM2.5 for high concentration days 2006-2010 Fairbanks State Office Building
Q4_Q1_top25_06-10 | 18.277 | 4.3365 | 8.0527 | 6.0463 | 6.5372 | 1.1262 | 55.6241

## Slide 8: PM2.5 Sources
Chart: 
| Wood Smoke 60-80% | Sulfate 7-21% | Diesel 0-11% | ammoniumn nitrate 3-11%
Sales | 80 | 21 | 7 | 3
Positive Matrix Factorization (PMF)
Chemical Mass Balance (CMB)
Woodsmoke dominates1 (50-80%)
Sulfate sources also a concern (10-20%)
1 The Fairbanks, Alaska PM2.5 Source Apportionment Research Study Winters 2005/2006-2012/2013, and Summer 2012, Tony J. Ward, Ph.D., December 2013

## Slide 9: Modeling Domain & Episodes
200x200 cell domain (WRF, SMOKE, CMAQ)
1.33km grid cell spacing
38 vertical layers (0,3.8, 6.4, 10.9m, …)
January 23 – February 10 & November 2 – 17, 2008

## Slide 10: Meteorological Modeling
Weather Research Forecasting Model (WRF) v3.1
Conducted to focus on extreme cold conditions by Penn State
Temperature and wind speed biased high
Largest error in wind direction
Complicated by frequency of calm conditions
Drainage flows/settling unrepresented

## Slide 11: Home Heating Data Gathering
Home Heating Surveys
  2006, 2007 and 2010 – ongoing
  Specialized 2013, 2016 surveys
Home Heating Energy Model
  Instrumented home study
  Variables: temperature, building size, hour of day, heating devices, weekday/weekend
  Outputs: Hourly energy usage
Local fuel and device testing

## Slide 12: Home Heating Emissions Modeling
Energy-driven emissions
  Device efficiencies
  Wood moisture content
Zip-code specific device mixture
Parcel-based gridding
Maintained gridded, hourly input through SMOKE
Vertical allocations (simple plume rise)

## Slide 13: Onroad Mobile Sources
Cold Weather Vehicle Testing
Parking Lot Surveys
Plug-in Block Heaters
DMV Registration
Transportation Modeling
Photo reproduced from (ffg/flickr)

## Slide 14: Mobile Source Modeling
EPA’s MOtor Vehicle Emissions Simulator (MOVES) 2010a
  Configured local activity and population inputs
  SMOKE-MOVES processing of inputs
    WRF modeled meteorology
    Customized LINUX scripting environment
    Generated SMOKE-ready rate lookup tables for running, starting, and evaporative emission rates
    Applied emission benefits for vehicle plug-ins
Generated local spatial and temporal surrogates for SMOKE

## Slide 15: Point Sources
Facilities provided information
  Emission units
  Stack parameters
  Control devices
  Fuel properties
Baseline used actual emissions
Projections used either potential to emit (PTE) or actual

## Slide 16: Nonroad, Aircraft, Rail, Other Area
Non-road mobile sources
  EPA’s NONROAD 2008 model
  Spatial surrogates
  Aircraft - Emission and Dispersion Modeling System
  Rail – local activity and EPA’s AP-42 emission factors
Other Area – commercial cooking

## Slide 17: Photochemical Modeling
Meteorology from WRF v3.1
Sparse Matrix Operator Kernel Emissions (SMOKE) model version 2.7.5b
Community Multiscale Air Quality (CMAQ) model version 4.7.1
Baseline 2008 episodes: January, November 2008
Projected and control 2015, 2019 episodes

## Slide 18: Model Performance
Chart: MFB
| 0.10348608022242767
PM25 | 0.30586
OC | 0.38643
EC | 0.56101
SO4 | 0.88471
NO3 | 0.54623
NH4 | 0.81855
OTHER | 0.81366
goal
criteria

## Slide 19: Control Scenarios
Summary of Modeled Control Measures and Applicable Years |  | 
Modeled Control Measure | Year(s) for Which Measure Applies | Control Inventory Year(s)
ARA Hydronic Heater Retrofit Program | 2012 | 2015, 2019
FNSB Wood Stove Change Out Program | 2011 and later | 2015, 2019
State Standards for New Home Heating Devices | 2016 and later | 2019
State-Coordinated Wintertime Dry Wood Use Program | 2016 and later | 2019
Expansion of Natural Gas Availability | 2016 and later | 2019
Control measures addressed home heating PM2.5
No precursor controls pursued
  NOx and VOC demonstrations
  RACM/RACT no feasible SO2 or NH3

## Slide 20: Speciated Model Attainment Test (SMAT)
Scenario Name | Organic Carbon (RRF) | Elemental Carbon (RRF) | SO4 (RRF) | NO3 (RRF) | Other Primary Particulate (RRF) | Future Design Value (µg/m3)
2015 Baseline (PTE) | 0.96 | 0.90 | 1.00 | 0.97 | 1.80 | 43.2
2015 Control Package (PTE) | 0.85 | 0.82 | 1.00 | 0.92 | 1.80 | 40.1
2015 Control Package (Actual) | 0.85 | 0.80 | 1.00 | 0.91 | 0.92 | 39.6
SMAT determines future design values (FDV) using Relative Response Factor (RRF)
44.7 µg/m3 DV 2006-2010
39.6 µg/m3 result is still well above 35 µg/m3
Attainment was deemed impracticable as a result

## Slide 21: Unmonitored Area Analysis 2015

## Slide 22: Attainment Challenges
North Pole Fire Station Design Value 4x NAAQS
Modeling meteorology
Sulfate chemistry
Alternative, cheap, reliable, clean heating sources

## Slide 23: Serious SIP Challenges
Chart: Year
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006
24 hour PM 2.5 NAAQS | 65.5 | 65.5 | 65.5 | 65.5 | 65.5 | 65.5 | 65.5
State Office Building 24 hour Design Value | 43 | 39 | 40 | 40 | 43 | 39 | 41 | 44 | 50 | 47 | 46 | 41 | 40 | 35.3667 | 37.1
NCORE 24 hour Design Value | 44.6667 | 39.7333 | 39.2667 | 34.8333 | 33.5667
NPFS 24 hour Design Value | 139.4333 | 123.8333 | 105.5667
NPE 24 hour Design Value | 45.3
 | 35.5 | 35.5 | 35.5 | 35.5 | 35.5 | 35.5 | 35.5 | 35.5 | 35.5 | 35.5 | 35.5
Notes: Design values have been steadily above the current standard since it was established. Recently regulatory monitoring in the town of North Pole where the Flint Hills refinery was located have shown drastically higher concentrations.

## Slide 24: Thank You!
Cindy Heil (ADEC)
Alice Edwards (ADEC)
Barbara Trost (ADEC)
Dea Huff (ADEC)
Alex Edwards (ADEC)
Jim Conner (FNSB)
Ron Lovell (FNSB)
Tom Carlson (Sierra)
Bob Dulla (Sierra)
Wen Zhang (Sierra)
Robert Crawford (Rincon Ranch)
Brian Gaudet (Penn State)
Smith Lake Fairbanks, AK

## Slide 25: Questions?
Fire Station Monitor North Pole, AK