## Slide 1
Implications of burned area approaches in emission inventories for modeling wildland fire pollution in the contiguous U.S
Shannon Koplitz, Chris Nolte, and George Pouliot
USEPA
Disclaimer: The views of the author expressed herein do not necessarily state or reflect those of the United States Government.
Taken during descent into Seattle on September 1, 2017
August 29, 2017
Regional smoke layer?
flames

## Slide 2: Wildland fires in the U.S. – a complex landscape
Wildland fires can account for more than 30%* of total U.S. PM2.5 emissions.
* Based on NEI 2011
Photo: Saul Young/New Sentinel
Tennessee 2016
California 2013
Photo: Hoover Volunteer Fire Department (accessed from CNN.com)
Texas 2017
Colorado 2012
Photo: @PatrickSandusky (accessed from www.businessindsider.com)
Photo: Dan Bartletti, Los Angeles Times (accessed from www.soperwheeler.com)

## Slide 3: Fire emissions in global and regional models are estimated from four key variables
To estimate emissions E of chemical species s in grid cell i,j:
Burned area is usually quantified independently of the other three parameters, and can be estimated a variety of ways.
Es,i,j = BAi,j x FLi,j x CCi,j x EFs
Burned area (i.e. fire size and location)
Fuel load (i.e. how much biomass is there)
Combustion completeness (i.e. how much of the available biomass actually burns)
Emission factor per unit carbon combusted

## Slide 4: Burned area estimates for the U.S. can vary by more than 2x between inventories

## Slide 5: Burned area estimates for the U.S. can vary by more than 2x between inventories
Decent agreement in western U.S.

## Slide 6: Burned area estimates for the U.S. can vary by more than 2x between inventories
Agreement between burned area products varies widely by region.
2011
Large differences in southern U.S.

## Slide 7: Burned area estimates for the U.S. can vary by more than 2x between inventories
Agreement between burned area products varies widely by region.
2011
Large differences in southern U.S.
What does this mean for modeling wildland fire pollution in the U.S.?

## Slide 8: Objective
To connect uncertainty in wildland fire emissions to modeled PM2.5 and ozone concentrations, in order to provide context for projecting and interpreting the air quality impacts of future wildland fire activity at regional and national scales.

## Slide 9: Objective
To connect uncertainty in wildland fire emissions to modeled PM2.5 and ozone concentrations, in order to provide context for projecting and interpreting the air quality impacts of future wildland fire activity at regional and national scales.
Implement three different wildland fire emission inventories – NEI, FINN, and GFED4s - into CMAQ (v5.1, 36km horizontal resolution).
Attribute changes in PM2.5 and ozone during one full year (2011) of atmospheric conditions to each inventory by subtracting out results from a “no fire” simulation.
Characterize spatial and temporal differences in modeled PM2.5 and ozone resulting from the use of each inventory.
Tasks

## Slide 10: Emissions generally align with burned area patterns

## Slide 11: Modeled fire pollution varies by 300% nationally
GFED4s estimates of PM2.5 are generally more consistent with NEI than FINN, but ozone estimates are much higher.
0.85 µg m-3
0.33 µg m-3
0.93 µg m-3
0.28 ppb
0.22 ppb
0.74 ppb
Modeled Enhancements in PM2.5 and April-Sep MDA8 Ozone

## Slide 12: Modeled fire pollution varies by 300% nationally
GFED4s estimates of PM2.5 are generally more consistent with NEI than FINN, but ozone estimates are much higher.
0.85 µg m-3
0.33 µg m-3
0.93 µg m-3
0.28 ppb
0.22 ppb
0.74 ppb
Modeled Enhancements in PM2.5 and April-Sep MDA8 Ozone

## Slide 13: Individual fires demonstrate potential benefits of high spatial and temporal resolution
High spatial and temporal resolution allow FINN to potentially capture acute pollution episodes from individual fires.
GFED4s appears to miss the Wallow Fire

## Slide 14: PM2.5 from wildland fires is comparable to contributions from other anthropogenic sectors
As emissions from other sectors decrease, wildland fires will become an increasingly important source of PM2.5 for much of the country.
(This work)
*EGU emissions went down by over 70% between 2005 and 2016.
µg m-3
PM2.5 from other Sectors in 2005*
FINN
NEI
GFED4s
(Caiazzo et al 2013)
PM2.5 from Wildland Fires in 2011

## Slide 15: Summary
Differences in burned area estimates lead to large spatial and temporal differences in wildland fire emissions across inventories.
Modeled wildland fire PM2.5 and ozone pollution varies by 300% nationally for 2011 due only to the inventory used.
At seasonal and regional scales, results using GFED4s agree more closely with those produced with NEI, but for individual fire events FINN is better able to capture higher frequency changes in fire pollution levels compared to GFED4s.
Constraining estimates of burned area/wildland fire emissions will become increasingly important as emissions from other sectors decrease, and as fire activity changes in response to future climate.

## Slide 16: Extra Slides

## Slide 17: Modeled fire pollution varies by 300% nationally
0.85 µg m-3
0.33 µg m-3
0.93 µg m-3
0.28 ppb
0.22 ppb
0.74 ppb
Modeled Enhancements in PM2.5 and April-Sep MDA8 Ozone
Additional NAAQS Exceedances Compared to No Fire Case
GFED4s estimates of PM2.5 are generally more consistent with NEI than FINN, but ozone estimates are much higher.

## Slide 18: Estimation methods include top-down and bottom-up approaches
Different approaches can lead to significant variability in space and time between burned area estimates.
Inventory | Method to estimate burned area
Global Fire Emissions Database (GFED) | Satellite-derived burn scars (MODIS)
Fire Inventory from NCAR (FINN) | Satellite-derived active fire detections (MODIS) combined with MODIS land cover product (VCF)
Monitoring Trends in Burn Severity (MTBS) | Satellite image processing (LANDSAT)
National Interagency Fire Center (NIFC) | Fire incident reports (federal and state data)
National Emission Inventory (NEI) | NOAA Hazard Mapping System (includes active fires from MODIS, AVHRR, GOES), perimeters from MTBS, incident reports
Table modified from Larkin et al. 2014

## Slide 19
µg m-3
NEI - FINN
NEI – GFED4s
GFED4s - FINN
OMI Aerosol Index
Smoke from the Wallow Fire is visible in OMI Aerosol Index data from June 2011.

## Slide 20
µg m-3
NEI - FINN
NEI – GFED4s
GFED4s - FINN
OMI Aerosol Index
Despite the high modeled PM2.5 from Flint Hills in NEI during April 2011, no corresponding signal is evident in the OMI AI data.
The Flint Hills burn signal is strong in the NEI compared to other inventories

## Slide 21: The Flint Hills burn signal is strong in the NEI compared to other inventories
NEI fire emission estimates rely heavily on HMS fire detections and average MTBS perimeters by land cover type – efforts to assess potential biases incurred from this approach are ongoing.
µg m-3
NEI - FINN
NEI – GFED4s
GFED4s - FINN
OMI Aerosol Index

## Slide 22: Regional differences in fire pollution seasonality are reflected in all three inventories
Prescribed burning peaks in southern U.S. during winter-spring
Monthly Wildland Fire OC Emissions by Region

## Slide 23: Regional differences in fire pollution seasonality are reflected in all three inventories
Prescribed burning peaks in southern U.S. during winter-spring
Monthly Wildland Fire OC Emissions by Region
Monthly Wildland Fire PM2.5 by Region
Relatively higher modeled pollution levels compared to local emissions in NE and MW

## Slide 24: Heat flux assumptions affect plume rise and smoke transport downwind
In NEI:
HFLUX = Burned Area x Fuel Load

## Slide 25: Heat flux assumptions affect plume rise and smoke transport downwind
In NEI:
HFLUX = Burned Area x Fuel Load
No fuel loading information carried directly with FINN or GFED, instead we scaled by PM2.5 emissions:
HFLUX = PM2.5 x Heat Content x Global Average Fuel Load/PM2.5
(From Wiedinmyer et al. 2011)

## Slide 26: Heat flux assumptions affect plume rise and smoke transport downwind
In NEI:
HFLUX = Burned Area x Fuel Load
No fuel loading information carried directly with FINN or GFED, instead we scaled by PM2.5 emissions:
HFLUX = PM2.5 x Heat Content x Global Average Fuel Load/PM2.5
We also tested scaling FINN HFLUX by the median HFLUX/PM2.5 value from the NEI 2011 data:
HFLUX = PM2.5 x Median HFLUX/PM2.5

## Slide 27: Heat flux assumptions affect plume rise and smoke transport downwind
Using median HFLUX/PM2.5 derived from NEI to scale FINN HFLUX results in roughly double the fire-related surface PM2.5 enhancements near emitting areas, with some reductions in far field transport.
In NEI:
HFLUX = Burned Area x Fuel Load
No fuel loading information carried directly with FINN or GFED, instead we scaled by PM2.5 emissions:
HFLUX = PM2.5 x {Heat Content x Global Average Fuel Load/PM2.5}
We also tested scaling FINN HFLUX by the median HFLUX/PM2.5 value from the NEI 2011 data:
HFLUX = PM2.5 x Median HFLUX/PM2.5
8.1e7
2.2e9
Wildland Fire PM2.5 with FINN

## Slide 28: Emissions generally align with burned area patterns
Strong Flint Hills signal in NEI
FINN lower (in general) in the west
Small fire correction greatly increases GFED4s emissions