## Slide 1: AQ impact study for increase in Shale Gas Productions since 2011
Pius Lee1, Jeff McQueen2, Ivanka Stajner2, Daniel Tong1, Li Pan1, Youhua Tang1, Hyuncheol Kim1, and Barry Baker1
1NOAA/Air Resources Laboratory
2NOAA/National Weather Service
16th CMAS, Oct 23-25 2017

## Slide 2
Source: U.S. Energy Information Administration, Form EIA‐23L, Annual Report of Domestic Oil and Gas Reserves; U.S. Department of Energy, Office of Fossil Energy,
Natural Gas Imports and Exports
Production and imports
Trillion cubic feet
Proved
Natural gas proved reserve reserves
Trillion cubic feet
Natural gas production
Natural gas imports
16th CMAS, Oct 23-25 2017

## Slide 3: Shale Oil and Gas due to Marcellus Play
Marcellus Play is generally considered to be able to produce dry natural gas : > 95% CH4
(Cox-Colvin 2017 ) www. coxcolvin.com /the-marcellus-and-utica-shale-
natural-gas-play-what-are-the-issues/
16th CMAS, Oct 23-25 2017
Notes: 1500 wells increase per year
Source EIA

## Slide 4
2014 Energy Information Administration on Shale Plays
Source: eia.gov/todayinenergy
16th CMAS, Oct 23-25 2017

## Slide 5
Chart: Gas Production (Million Cubic Feet)
| Texas | Pennsylvania | Oklahoma | Wyoming | Louisiana | Colorado | West Virginia | New Mexico | Ohio | Arkansas | North Dakota | Utah | Alaska | Kansas | California
2011 | 7112863 | 1310592 | 1888870 | 2159422 | 3029206 | 1637576 | 394125 | 1237303 | 78858 | 1072212 | 97102 | 457525 | 356225 | 309124 | 250177
2012 | 7475495 | 2256696 | 2023461 | 2022275 | 2955437 | 1709376 | 539860 | 1215773 | 84482 | 1146168 | 172242 | 490393 | 351259 | 296299 | 246822
2013 | 7633618 | 3259042 | 1993754 | 1858207 | 2360202 | 1604860 | 741853 | 1171640 | 166017 | 1139654 | 235711 | 470863 | 338182 | 292467 | 252310
2014 | 7985019 | 4257693 | 2331086 | 1794413 | 1960813 | 1643487 | 1067114 | 1229519 | 512371 | 1122733 | 326491 | 454545 | 345310 | 286480 | 238988
2015 | 7880530 | 4812983 | 2499599 | 1793716 | 1776800 | 1704836 | 1318822 | 1244811 | 1014848 | 1010274 | 471504 | 423300 | 343534 | 285236 | 231060
2016 | 6985576 | 5263973 | 2468312 | 1602701 | 1861187 | 1703277 | 1375108 | 1230493 | 1466854 | 826917 | 504672 | 367251 | 343629 | 249524 | 211451
Source:
Source: usenergydevcorp.com and Energy Information Administration (EIA)
16th CMAS, Oct 23-25 2017

## Slide 6
Chart: 
| Texas | Pennsylvania | Louisiana | Colorado | West Virginia | Ohio | North Dakota | Utah | California
2011 | 95014 | 44500 | 19137 | 28813 | 52498 | 34931 | 188 | 6075 | 1580
2012 | 139368 | 61815 | 19318 | 43792 | 51629 | 31966 | 526 | 7603 | 4240
2013 | 140087 | 62922 | 19345 | 46141 | 51646 | 31647 | 451 | 8121 | 4356
2014 | 140964 | 61838 | 18802 | 46883 | 50097 | 30804 | 423 | 8300 | 4183
2015 | 142292 | 67621 | 18660 | 46876 | 53060 | 31060 | 398 | 8537 | 4211
2016 | 142368 | 68536 | 18382 | 46322 | 47938 | 26599 | 462 | 8739 | 4209
Number of production wells
16th CMAS, Oct 23-25 2017

## Slide 7
Cost cutting in fracking range of 10-30% in past decade
(1) Longer horizontal drills;
(b) Improved geo-steering accuracy;
(3) Minimized steel casing and liner;
(4) Clustered up drill-heads for multi-pad drilling;
(e) Experimenting lower cost proppants;
(6) Multiple-pad drilling usually resulted in a smaller emission
Increased efficiency => reduction in emission
Multiple-pad drilling => smaller emission since
centralized controls and abatement measures
16th CMAS, Oct 23-25 2017

## Slide 8
 | Well numbers |  |  | Million cubic feet |  | 
Year | 2011 | 2016 | 2016/2011 | 2011 | 2016 | 2016/2011
Texas | 95,014 | 142,368 | 1.50 | 7,112,863 | 6,985,576 | 1.02
Pennsylvania | 44,500 | 68,536 | 1.54 | 1,310,592 | 5,263,973 | 4.02
Louisiana | 19,137 | 18,382 | 0.96 | 3,029,206 | 1,861,187 | 0.61
Colorado | 28,813 | 46,322 | 1.61 | 1,637,576 | 1,703,277 | 1.03
West Virginia | 52,498 | 47,938 | 0.91 | 394,125 | 1,375,108 | 3.49
Ohio | 34,931 | 26,599 | 0.76 | 78,858 | 1,466,854 | 18.60
North Dakota | 188 | 462 | 2.46 | 97,102 | 504,672 | 3.85
Utah | 6,075 | 8,739 | 1.44 | 457,525 | 367,251 | 0.79
California | 1,580 | 4,209 | 2.66 | 250,177 | 211,451 | 0.76
Ʃ | 282,736 | 363,555 | 1.29 | 14370035 | 19741365 | 1.38
Variation of state-wide top production rate and well-numbers between 2011 to 2016
16th CMAS, Oct 23-25 2017

## Slide 9
Adjustment factor applied to NEI2011 oil and gas area source sector
16th CMAS, Oct 23-25 2017

## Slide 10
Species scaled to reflect enhanced emission from
increased oil and gas exploration/production due to fracking
CMAQ species | Species category | Activities attributed to emission
NOx +HONO | Nitrogen oxides | Compression, drilling, transportation
ALD, ALD2 | And other higher aldehydes | Processing and drilling
Alkane, alkene | Paraffin and Olefin & HC | Product and processing
XYL TOL TERP | VOC | Product and processing
Benzene | And other aromatics | Product and transportation
SO2, SULF | Sulfur compounds | Product and processing
PEC | Elemental carbon (soot) etc | Processing, drilling and compression
PMFINE | Other emitted particulate | Processing, compression, transportation
16th CMAS, Oct 23-25 2017
Notes: MPAS (Model for Prediction Across Scales) Voroni (hexagonal meshes using c-grid staggering

## Slide 11
Score: PROD vs. O_n_Gas_refreshed for July 10-22 2017
Daily Maximum 8 h average O3
Oil_n_Gas refreshed emission helped reduced O3 under-prediction
MD8A O3 Case |  | obs | mean | bias | rmse | correlation
CONUS (52200) | Base | 41.7 | 42.8 | 1.1 | 9.00 | 0.75
 | O_n_G |  | 43.5 | 1.8 | 9.11 | 0.76
Northeast (7900) | Base | 38.7 | 41.6 | 2.9 | 8.62 | 0.78
 | O_n_G |  | 42.4 | 3.7 | 9.01 | 0.78
Southeast (8500) | Base | 38.8 | 43.7 | 4.89 | 8.95 | 0.75
 | O_n_G |  | 44.4 | 5.58 | 9.21 | 0.77
Up Middle (11180) | Base | 41.5 | 42.5 | 0.96 | 7.10 | 0.81
 | O_n_G |  | 43.5 | 1.93 | 7.31 | 0.82
Low Middle | Base | 41.8 | 45.7 | 3.91 | 9.82 | 0.71
(5145) | O_n_G |  | 46.4 | 4.64 | 10.02 | 0.72
Rocky M. | Base | 48.4 | 46.0 | -2.43 | 8.93 | 0.71
(7600) | O_n_G |  | 46.7 | -1.78 | 8.56 | 0.73
Pacific Coast | Base | 47.5 | 43.8 | -3.63 | 11.48 | 0.75
( 7260) | O_n_G |  | 44.0 | -3.48 | 11.48 | 0.75
16th CMAS, Oct 23-25 2017

## Slide 12
Score: PROD vs. O_n_Gas_refreshed for July 10-22 2017
Oil_n_Gas refreshed emission helped reduced PM2.5 under-prediction
Daily average PM2.5
24 h PM2.5 Case |  | obs | mean | bias | rmse | correlation
CONUS (35600) | Base | 11.2 | 11.9 | 0.69 | 12.75 | 0.72
 | O_n_G |  | 13.1 | 1.88 | 13.54 | 0.72
Northeast (5980) | Base | 8.3 | 9.06 | 0.73 | 4.59 | 0.57
 | O_n_G |  | 9.29 | 0.96 | 4.67 | 0.59
Southeast (4400) | Base | 9.0 | 10.71 | 1.71 | 5.15 | 0.55
 | O_n_G |  | 11.12 | 2.12 | 5.63 | 0.55
Up Middle (6100) | Base | 9.0 | 12.15 | 3.13 | 5.82 | 0.60
 | O_n_G |  | 12.61 | 3.58 | 6.18 | 0.62
Low Middle | Base | 9.5 | 10.74 | 1.26 | 5.02 | 0.54
(2780) | O_n_G |  | 11.39 | 1.91 | 5.58 | 0.56
Rocky M. | Base | 13.5 | 12.98 | -0.54 | 16.94 | 0.79
(5750) | O_n_G |  | 15.56 | 2.04 | 17.75 | 0.78
Pacific Coast | Base | 14.7 | 13.23 | -1.51 | 18.34 | 0.71
( 8530) | O_n_G |  | 15.20 | 0.46 | 19.46 | 0.71
16th CMAS, Oct 23-25 2017

## Slide 13
Standard Deviation
Standard Deviation
Standard Deviation
Correlation
Correlation
Taylor diagram for Base and O_n_G simulation between July 10-September 28 2017
hourly O3 hourly PM2.5
O_n_G
O_n_G
16th CMAS, Oct 23-25 2017
Notes: MPAS (Model for Prediction Across Scales) Voroni (hexagonal meshes using c-grid staggering

## Slide 14
Large plays: Barnett, Eagle Fort & Haynesville (TX) and Marcellus (PA)
Behavior is rather different between the various shale plays;
NEI2011 already accounted for that, therefore locale-spec scaling OK
Focus on the exceptional productive Marcellus Play
Large reserve as well as dry gas;
Good prospects for additional Marcellus-like plays: e.g. Mancos CO.
Sporadic wet gas signature -- Courtesy Prof. Russ Dickerson:
UMD flights had detected coal-bed associated emissions;
Nation wide Oil and Gas production trend: levelling off
Large reserves in multiple locations but price incentive is low;
Oil and Gas production can be a long term phenomenon;
State-specific scaling for Shale Play as Oil_n_Gas area source
July 20-Sep28 sensitivity run advantageous to capture concentrations;
Exceedance forecast improved;
However the over-prediction in O3 elsewhere was exacerbated
O_n_G configuration with CMAQ5.2 is considered for NAQFC
Scale shale play production as oil/gas sector
16th CMAS, Oct 23-25 2017