## Slide 1: Significantly Reduced Health Burden from Ambient Air Pollution in the U.S. Under Emission Reductions from 1990 to 2010
16th CMAS Conference
10/24/2017
Yuqiang Zhang1, J. J West2, Rohit Mathur3, Jia Xing4, Christian Hogrefe3, Shawn Roselle3, Jesse Bash3, Jonathan Pleim3, Chuen-Meei Gan3, David C. Wong3
1ORISE Fellowship Participant at US EPA, RTP, NC 27711, USA
2UNC-CH, NC 27599, USA
3US EPA, RTP, NC 27711, USA
4Tsinghua University, Beijing 100084, China

## Slide 2
Introduction
“Air Quality Improves as America Grows”
Annual PM2.5 decreased by 42% from 2000 to 2016.
MDA8 O3 decreased by 22% from 1990 to 2016;
EPA (2017):
Our Nation's Air: Status and Trends Through 2016

## Slide 3
Introduction
Ambient air pollution and human health
Exposure to PM2.5 and O3 has been associated with both morbidity (e.g. asthma exacerbation) and mortality (e.g. death from cardiovascular and respiratory diseases as well as lung cancer).
  Estimated 88,400 adults deaths attributable to PM2.5 exposure, and 11,700 adults deaths attributable to O3 exposure in 2015 by Global Burden of Disease(GBD) (Cohen et al., 2017).
What are the trends in air pollution mortality, due to changes in ambient air pollution?

## Slide 4
Objectives
Quantify the annual mortality burden of ambient PM2.5 and O3 in the continental U.S. from 1990 to 2010, based on long-term air quality model simulations by coupled WRF-CMAQ (Gan et al., 2015, 2016);
Analyze contributions of changes in air pollutant concentration, population, and baseline mortality to the overall trend;
Innovations:
  Estimate the mortality burden annually, with annual baseline mortality and population data;
  Analyze the inter-annual variability in mortality estimates.

## Slide 5
Methods
Model simulation: Coupled WRF-CMAQ model
Horizontal resolution of 36 × 36 km covering the Continental U.S. (CONUS);
With a self-consistent U.S. emission inventory from 1990 to 2010 developed by Xing et al., 2013;
Boundary conditions are obtained from 108 × 108 km WRF-CMAQ hemisphere simulation (Xing et al., 2015, Mathur et al., 2017);
Simulation period covering 1990 to 2010;
Model evaluations for aerosol and O3 have been reported in previous studies (Gan et al., 2015, 2016; Astitha et al, 2017).
Gan et al., 2016

## Slide 6
Methods
For baseline mortality rates (y0):
Calculated y0 for individual counties using baseline incidence rates and population from CDC-Wonder database, and then regrid to the 36 km grid.
∆Mort = y0 x AF x Pop
Health Impact Function
∆Mort: mortality burden for PM2.5 or O3;
y0: baseline mortality rates;
AF: attributable fraction;
Pop: Exposed population, ages > 25 yrs
For attributable fraction (AF):
PM2.5: Integrated Exposure–Response (IER) model (Burnett et al., 2014)
O3: log-linear model from Jerrett et al., (2009).
For exposed population (Pop):
Annual data at county-level from the US CDC from 1990 to 2010
Notes: CDC: Centers for Disease Control and Prevention
For the AF, they are both depending on the air pollution concentration;

## Slide 7
Results
In U.S., for PM2.5 , the population-weighted average decreased by 39%, and regional average decreased by 29%;
For O3, both decreased by 9%;
Both the PM2.5 and O3 decreases were attributed to the significant emission reductions.
Chart: µg/m3
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Popweighted Avg | 17.61 | 17.42 | 17.06 | 16.32 | 16.79 | 15.54 | 15.77 | 15.06 | 15.1 | 15.04 | 15.12 | 14.76 | 13.27 | 13.56 | 13.03 | 13.13 | 12.59 | 12.91 | 12.21 | 10.9 | 10.73
Regional Avg | 9.07 | 8.97 | 8.98 | 8.56 | 9.03 | 8.25 | 8.58 | 8.19 | 8.16 | 8.49 | 8.48 | 8.08 | 7.35 | 7.55 | 7.17 | 7.55 | 7.94 | 7.9 | 7.2 | 6.51 | 6.45
Annual average PM2.5
U.S. air quality trends from 1990 to 2010
Chart: ppbv
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Popweighted Avg | 58.96 | 59.57 | 56.84 | 57.07 | 57.83 | 59.03 | 56.19 | 56.09 | 59.31 | 58.28 | 56.6 | 56.94 | 55.93 | 54.93 | 52.6 | 55.94 | 54.54 | 55.36 | 53 | 51.19 | 53.57
Regional Avg | 55.02 | 54.66 | 53.45 | 52.5 | 54.71 | 54.53 | 53 | 52.01 | 54.95 | 54.38 | 54.18 | 53.41 | 52.69 | 52.55 | 49.76 | 52.33 | 51.8 | 51.84 | 49.47 | 48.77 | 49.99
April to September average of daily maximum 1hr O3

## Slide 8
Results
Decrease by 53%, from 123,700 deaths yr-1 in 1990 (95%CI, 70,800-178,100), to 58,600 deaths yr-1 (95%CI, 24,900-98,500) in 2010.
Interannual variability is small (coefficient of variation, CV, of 4% ).
PM2.5 mortality burden from 1990 to 2010
Chart: PM2.5
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Mortality Burden | 123734.8 | 121982 | 119709.3 | 117824.8 | 119252.8 | 111990 | 112404.2 | 106224.6 | 103898.4 | 106769.8 | 105716.7 | 100212.9 | 90312.41 | 90440.89 | 83231.12 | 82684.02 | 77560.6 | 77076.04 | 73074.28 | 60456.5 | 58580.09
Notes: 1. However, they use uniform 22, 30 ppbv for the east and west backgournd o3 concentration. The background O3 should be higher in both the east and the west, larger than 32 ppbv. So they underestimate the background and then overestimate the O3 health burdens

## Slide 9
Results
Concentration change only: -36% from 1990 to 2010;
Mortality rates change only: -45% from 1990 to 2010;
Population change only: 40% from 1990 to 2010;
PM2.5 mortality burden from 1990 to 2010
Chart: PM2.5
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Mortality Burden | 123734.8 | 121982 | 119709.3 | 117824.8 | 119252.8 | 111990 | 112404.2 | 106224.6 | 103898.4 | 106769.8 | 105716.7 | 100212.9 | 90312.41 | 90440.89 | 83231.12 | 82684.02 | 77560.6 | 77076.04 | 73074.28 | 60456.5 | 58580.09
Concentration change only | 123735 | 122723 | 121474 | 117094 | 120261 | 113225 | 114957 | 110837 | 109996 | 111579 | 112275 | 109354 | 99683 | 101747 | 98181 | 98669 | 95565 | 97612 | 92775 | 80665 | 78907
MortalityRates change only | 123735 | 120224 | 117021 | 117422 | 113911 | 111834 | 108805 | 105041 | 102030 | 101550 | 98692 | 94985 | 92898 | 89574 | 84460 | 82270 | 77979 | 74545 | 73910 | 70097 | 68272
Population change only | 123735 | 126629 | 129025 | 131348 | 133420 | 135662 | 137908 | 140093 | 142428 | 144700 | 146340 | 148698 | 150958 | 153401 | 155626 | 158465 | 161467 | 164546 | 167757 | 170955 | 173503
Total Mortality burden: -53%
Notes: 1. However, they use uniform 22, 30 ppbv for the east and west backgournd o3 concentration. The background O3 should be higher in both the east and the west, larger than 32 ppbv. So they underestimate the background and then overestimate the O3 health burdens

## Slide 10
Results
Increase by 13%, from 109,000 (95%CI, 3,700-17,500) deaths yr-1 in 1990 to 12,300 deaths yr-1 (95%CI, 4,100-19,800) deaths yr-1 in 2010 ;
Interannual variability is larger (CV of 12%).
O3 mortality burden from 1990 to 2010
Chart: O3
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Mortality Burden | 10903 | 11545 | 10355 | 11226 | 11816 | 12651 | 11403 | 11590 | 13981 | 13499 | 12471 | 12732 | 12208 | 11760 | 9999 | 13039 | 11863 | 12716 | 11834 | 10379 | 12275
Notes: 1. However, they use uniform 22, 30 ppbv for the east and west backgournd o3 concentration. The background O3 should be higher in both the east and the west, larger than 32 ppbv. So they underestimate the background and then overestimate the O3 health burdens

## Slide 11
Results
O3 mortality burden from 1990 to 2010
Chart: O3
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Mortality Burden | 10903 | 11545 | 10355 | 11226 | 11816 | 12651 | 11403 | 11590 | 13981 | 13499 | 12471 | 12732 | 12208 | 11760 | 9999 | 13039 | 11863 | 12716 | 11834 | 10379 | 12275
Concentration change only | 10903 | 11155 | 9868 | 9939 | 10348 | 10918 | 9534 | 9434 | 11028 | 10540 | 9702 | 9882 | 9389 | 8827 | 7664 | 9332 | 8583 | 9081 | 7818 | 6888 | 8128
MortalityRates change only | 10903 | 11077 | 11022 | 11711 | 11685 | 11665 | 11835 | 11988 | 12250 | 12234 | 12122 | 12131 | 12137 | 12230 | 11908 | 12667 | 12205 | 12435 | 13326 | 13000 | 13076
Population change only | 10903 | 11142 | 11322 | 11494 | 11670 | 11851 | 12032 | 12196 | 12341 | 12483 | 12586 | 12753 | 12891 | 13030 | 13187 | 13360 | 13538 | 13707 | 13869 | 14022 | 14142
Concentration change only: -25% from 1990 to 2010;
Mortality rates change only: 20% from 1990 to 2010;
Population change only: 30% from 1990 to 2010.
Total Mortality burden: 13%
Notes: 1. However, they use uniform 22, 30 ppbv for the east and west backgournd o3 concentration. The background O3 should be higher in both the east and the west, larger than 32 ppbv. So they underestimate the background and then overestimate the O3 health burdens

## Slide 12
Results
Mortality burden change from 1990 to 2010 by states
For PM2.5, New York has the largest decreases (-8,500 deaths yr-1), followed by California (-6,100 deaths yr-1), and Pennsylvania (-5,500 deaths yr-1);
For O3, the largest increases in CA (360 deaths yr-1), followed by Texas (230 deaths yr-1), and Arizona (140 deaths yr-1).
PM2.5 O3

## Slide 13
Results
Compared with previous studies
Chart: (a)
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015
This study | 123.7348 | 111.99 | 105.7167 | 82.684 | 58.5801
Cohen et al., 2017 | 106.2 | 107.2 | 106.2 | 100 | 83.4 | 88.4
Fann et al., 2012 | 130
Punger & West, 2013 | 73.26
Giannadaki et al., 2017 | 52
Chart: (b)
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015
This study | 6.9 | 8.2 | 8.5 | 8.7 | 7.9
Cohen et al., 2017 | 7.5 | 9.2 | 10.6 | 11.1 | 11.2 | 11.7
This study with pre-industrial | 9.412 | 11.219 | 11.932 | 12.402 | 11.916
Fann et al., 2012 | 19
Punger&West, 2013 | 23.968
Our results are comparable to previous studies;
The PM2.5 mortality burden trends were larger than Cohen et al. (2017), mainly caused by the overestimation of the PM2.5 concentration decrease trends (Gan et al., 2016).

## Slide 14
Conclusion
Annual PM2.5 decreased by 39%, and summertime O3 decreased by 9%;
The PM2.5 mortality burdens decreased by 53%, from 123,700 deaths yr-1 in 1990 to 58,600 deaths yr-1 in 2010, mainly caused by the decreasing PM2.5 concentration and baseline mortality rates;
The O3 mortality burdens increased by 13%, from 10,900 deaths yr-1 in 1990 to 12,300 deaths yr-1 in 2010, mainly caused by the increases of the baseline mortality rates and population changes.

## Slide 15
Acknowledgements
Thanks for the funding sources NASA Health Air Quality Applied Science Team #NNX16AQ80G. This work was also supported in part by MOST National Key R & D program in China (2016YFC0207601).
Y.Z. was supported in part by the Internship/Research Participation Program at Office of Research and Development, US Environmental Protection Agency (EPA), administered by the Oak Ridge Institute for Science and Education through an interagency agreement between the US Department of Energy and the US EPA.
Although this work has been reviewed and approved for publication by the US EPA, it does not reflect Agency’s views and policies.

## Slide 16
Thanks for your attention!
Questions and Comments?

## Slide 17
Extra slides

## Slide 18
Introduction
Ambient air pollution and human health
Recent studies have assessed the global (Forouzanfar et al., 2015; Forouzanfar et al., 2016; Lelieveld et al., 2015; Silva et al., 2016) or national (Fann et al., 2012; Punger and West, 2013) burden of disease attributable to air pollution.
Few studies have focused on the mortality burden trends
  Cohen et al. (2017) quantified both PM2.5 and O3 mortality burden at global and regional scale from 1990 to 2016 at 5-yr interval;
  Wang et al. (2017) quantified the PM2.5 mortality burden from 1990 to 2010 in the Northern Hemisphere using Hemispheric scale CMAQ;
  Fann et al. (2017) quantified the PM2.5 all-cause mortality burden in US from 1980 to 2010 using geographic kriging PM2.5 from observation

## Slide 19
Methods
For O3
Use Log -linear model: RR = expβ∆X
RR = 1.040 (1.1013-1.067) per 10 ppbv O3 increases from Jerrett et al., 2009;
β: Concentration response factor
(3) ∆X = X2(1990-2010) – X1 (Threshold concentration)
For PM2.5
Use Integrated Exposure–Response (IER) model: RR equals to
z = ambient PM2.5 concentration;
zcf = counterfactual conc. = Uniform(5.8,8.8)
For attributable fraction (AF):
∆Mort = y0 x AF x Pop
∆Mort: mortality burden for PM2.5 or O3;
Y0: baseline mortality rates;
AF: attributable fraction = (RR – 1)/RR;
Pop: Exposed population, ages > 25 yrs
Health Impact Function
Notes: Model evaluation for the major air pollutants and meteorology variables are presented in several previous studies.
Why NH4 is poor—check the reference
Underestimating N—Check Wyat’s paper

## Slide 20
Methods
For exposed population (ages > 25yrs):
∆Mort = y0 x AF x Pop
∆Mort: Health burden for O3 or PM2.5;
Y0: baseline mortality rates;
AF: attributable fraction = (RR – 1)/RR;
Pop: Exposed population, ages > 25 yrs
Chart: U.S. Pop > 25 yrs
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
US Population > 25yrs | 156815904 | 160163552 | 162775600 | 165241072 | 167659552 | 170190112 | 172742016 | 175090400 | 177195888 | 179232656 | 180725104 | 183110640 | 184998144 | 186866960 | 188957312 | 191279072 | 193725136 | 196094672 | 198463168 | 200752640 | 202517600
Notes: 2000 2010

## Slide 21
Methods
For baseline mortality rates:
∆Mort = y0 x AF x Pop
∆Mort: Health burden for O3 or PM2.5;
Y0: baseline mortality rates;
AF: attributable fraction = (RR – 1)/RR;
Pop: Exposed population, ages > 25 yrs
Notes: 2000 2010

## Slide 22
Methods
The baseline mortality rates for cause-specific death related with PM2.5, including chronic obstructive pulmonary disease (a), lung cancer (b), ischemic heart disease (c) and stroke (d), and the Respiratory diseases (e) related with O3. The bottom whiskers, bottom border, middle line, top border and the top whiskers of the boxes, indicate the 5th, 25th, 50th, and 75th, 95th percentiles, respectively, across all counties; The red circles are the national-level rate. Baseline mortality rates are shown for 1990-1998 after they are corrected to ensure comparability between ICD9 and ICD10 codes.
Baseline mortality rates
Notes: Model evaluation for the major air pollutants and meteorology variables are presented in several previous studies.
Why NH4 is poor—check the reference
Underestimating N—Check Wyat’s paper

## Slide 23
U.S. emission trends from 1990 to 2010
Xing et al., 2013
Use a consistent framework across years to develop U.S. emissions estimates from 1990 to 2010.
Emissions for major air pollutants are greatly decreasing, except for NH3, the increase of which is mainly caused by the activity of livestock and agriculture.

## Slide 24
Results
O3 decreases significantly in the east and west, > 0.5 ppbv yr-1;
The decreases are slow or insignificant in the middle;
PM2.5 decreases in the Northeast, but no significant changes in the west.
6-month average of daily maximum 1hr O3
Annual average PM2.5
U.S. air quality trends from 1990 to 2010

## Slide 25
Methods
∆Mort = y0 x AF x Pop
Background O3 (1850):
From an ensemble of 14 global chemistry–climate models (ACCMIP; Silva et al., 2013)
O3 higher in the eastern and western U.S., large than 30 ppbv; lower in the middle, larger than 28 ppbv
Notes: Model evaluation for the major air pollutants and meteorology variables are presented in several previous studies.
Why NH4 is poor—check the reference
Underestimating N—Check Wyat’s paper

## Slide 26
Results
Trends for the absolute contribution of the three factors
Chart: O3
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
MortRates change only | 0 | 174 | 119 | 808 | 782 | 762 | 932 | 1085 | 1347 | 1331 | 1219 | 1228 | 1234 | 1327 | 1005 | 1764 | 1302 | 1532 | 2423 | 2097 | 2173
Concentration change only | 0 | 252 | -1035 | -964 | -555 | 15 | -1369 | -1469 | 125 | -363 | -1201 | -1021 | -1514 | -2076 | -3239 | -1571 | -2320 | -1822 | -3085 | -4015 | -2775
Population change only | 0 | 239 | 419 | 591 | 767 | 948 | 1129 | 1293 | 1438 | 1580 | 1683 | 1850 | 1988 | 2127 | 2284 | 2457 | 2635 | 2804 | 2966 | 3119 | 3239
Chart: PM2.5
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
MortRates change only | 0.2 | -3510.8 | -6713.8 | -6312.8 | -9823.8 | -11900.8 | -14929.8 | -18693.8 | -21704.8 | -22184.8 | -25042.8 | -28749.8 | -30836.8 | -34160.8 | -39274.8 | -41464.8 | -45755.8 | -49189.8 | -49824.8 | -53637.8 | -55462.8
Concentration change only | 0.2 | -1011.8 | -2260.8 | -6640.8 | -3473.8 | -10509.8 | -8777.8 | -12897.8 | -13738.8 | -12155.8 | -11459.8 | -14380.8 | -24051.8 | -21987.8 | -25553.8 | -25065.8 | -28169.8 | -26122.8 | -30959.8 | -43069.8 | -44827.8
Population change only | 0.2 | 2894.2 | 5290.2 | 7613.2 | 9685.2 | 11927.2 | 14173.2 | 16358.2 | 18693.2 | 20965.2 | 22605.2 | 24963.2 | 27223.2 | 29666.2 | 31891.2 | 34730.2 | 37732.2 | 40811.2 | 44022.2 | 47220.2 | 49768.2
Notes: 1. However, they use uniform 22, 30 ppbv for the east and west backgournd o3 concentration. The background O3 should be higher in both the east and the west, larger than 32 ppbv. So they underestimate the background and then overestimate the O3 health burdens

## Slide 27
Results
Mortality burden relative change from 1990 to 2010 by states
For PM2.5, New York has the largest decreases (-8,500 deaths yr-1), followed by California (-6,100 deaths yr-1), and Pennsylvania (-5,500 deaths yr-1);
For O3, the largest increases in CA (360 deaths yr-1), followed by Texas (230 deaths yr-1), and Arizona (140 deaths yr-1).
PM2.5 O3