## Slide 1
Preliminary Evaluation of the CMAQ v5.3 Beta Release
K. Wyat Appel, Christian Hogrefe, Kristen Foley, George Pouliot, Robert Gilliam, Benjamin Murphy, Havala Pye, Jesse Bash, Jon Pleim, Sarwar Golam, Shawn Roselle, Rohit Mathur and the CMAQ Development Team
Computational Exposure Division
National Exposure Research Laboratory
Office of Research and Development
U.S. Environmental Protection Agency
23 October 2018
Community Modeling and Analysis System Conference
Chapel Hill, NC

## Slide 2
CMAQv5.3β – Release and Major Updates
Release schedule
  Beta version released October 2018: https://github.com/USEPA/CMAQ
  Final version planned release in June 2019: www.epa.gov/cmaq
  Instrumented models – DDM, Sulfur tracking (available w/ final release)
New features
  Aerosols
    AERO7
    Increased monoterpene SOA (Pye et al. 2015 ES&T, Xu et al. 2018 ACP), uptake of water onto hydrophilic organic aerosol (Pye et al. 2017 ACP), and reorganization of anthropogenic SOA (M. Qin)
  Gas Chemistry
    Minor updates to CB6r3 (ClNO3 reaction added; first-order O3 depletion)
    Full halogen chemistry – included in optional detailed mechanism
    Dimethyl sulfide (DMS) chemistry – optional detailed mechanism
  Deposition
    Updated M3Dry deposition scheme
    Surface Tiled Aerosol and Gaseous Exchange (STAGE) deposition scheme added

## Slide 3
CMAQ Inputs and Configuration
All simulations are CONUS annual simulation for 2016
MCIP from the same 2016 WRF simulation used in all simulations
Same 2016 emissions used in all simulations
 | CMAQv5.2.1 | CMAQv5.3β
Boundary Conditions | V5.2.1 Hemispheric CMAQ | V5.3 Hemispheric CMAQ
Chemical Mechanism | CB6r3 | CB6r3
Aerosol Module | AERO6 | AERO7
Deposition scheme | M3Dry | M3Dry; STAGE
Bi-directional Ammonia | No | No
Wind-blown Dust | No | No
Lightning NO | Yes | Yes

## Slide 4
MDA8 O3 – CMAQv5.2.1 vs v5.3β
Lower O3 in CMAQv5.3β due primarily to science updates in dry deposition and boundary conditions
AQS
CMAQv5.2.1
CMAQv5.3b M3Dry (No Bidi)
CMAQv5.2.1
CMAQv5.3b M3Dry (No Bidi)

## Slide 5
MDA8 O3 – CMAQv5.2.1 vs v5.3β (Jan- Apr)
O3 lower across the entire domain in the CMAQv5.3β simulation for January - April

## Slide 6
MDA8 O3 – CMAQv5.2.1 vs v5.3β :
Change in Bias (Jan – Apr)
The decrease in O3 results in higher bias for almost all sites as CMAQ underestimates MDA8 O3 in the winter and spring in 2016

## Slide 7
MDA8 O3 – CMAQv5.2.1
AQS
CMAQv5.2.1
CMAQv5.2.1

## Slide 8
MDA8 O3 – CMAQv5.3β w/ M3Dry Bidi
AQS
CMAQv5.2.1
CMAQv5.3b M3Dry w/ bidi
CMAQv5.2.1
CMAQv5.3b M3Dry w/ bidi

## Slide 9
MDA8 O3 – CMAQv5.3β w/ STAGE Bidi
AQS
CMAQv5.2.1
CMAQv5.3b M3Dry w/ bidi
CMAQv5.3b STAGE w/ bidi
CMAQv5.2.1
CMAQv5.3b M3Dry w/ bidi
CMAQv5.3b STAGE w/ bidi

## Slide 10
MDA8 O3 – CMAQv5.3β w/ v5.2.1 BCs
AQS
CMAQv5.2.1
CMAQv5.3b M3Dry w/ bidi
CMAQv5.3b STAGE w/ bidi
CMAQv5.3b M3Dry w/ bid and v5.2.1 BCs
CMAQv5.2.1
CMAQv5.3b M3Dry w/ bidi
CMAQv5.3b STAGE w/ bidi
CMAQv5.3b M3Dry w/ bid and v5.2.1 BCs

## Slide 11
MDA8 O3 – CMAQv5.2.1 vs v5.3β (May – Sep)

## Slide 12
MDA8 O3 – CMAQv5.2.1 vs v5.3β (May - Sep)
O3 lower across most of the domain in the CMAQv5.3β simulation for May - September

## Slide 13
MDA8 O3 – CMAQv5.2.1 vs v5.3β :
Change in Bias (May – Sep)
The lower O3 in the CMAQv5.3β simulation results in generally lower bias in the eastern U.S. and higher bias in much of the western U.S. in the summer

## Slide 14
PM2.5 – CMAQv5.2.1 vs v5.3β
Higher PM2.5 in CMAQv5.3β primarily due increased SOA in AERO7

## Slide 15
PM2.5 – CMAQv5.2.1 vs v5.3β (Jun – Sep)
Consistently higher PM2.5 in the summer w/ CMAQv5.3β

## Slide 16
PM2.5 – CMAQv5.2.1 vs v5.3β (Jun – Sep)

## Slide 17
PM2.5 – CMAQv5.2.1 vs v5.3β (Jun – Sep):
Change in bias

## Slide 18
CMAQv5.2.1 vs v5.3β (Jun – Sep)
Organic Carbon
Non-Carbon Organic Matter

## Slide 19
PM2.5 – M3Dry Bidi vs No Bidi (Seasonal):
Change in Bias
Winter
Spring
Summer
Fall

## Slide 20
PM2.5 – v5.3β STAGE Bidi vs M3Dry Bidi (Jan-Jun)
STAGE bidi results in moderately higher total PM2.5 versus M3Dry bidi for January - June

## Slide 21
Summary
Ozone
  Lower O3 with CMAQv5.3β
    due primarily to changes in the representation of dry deposition in v5.3β
    both M3Dry and STAGE reduce O3
    reduction in O3 greater with M3Dry than STAGE
      updates in M3Dry O3 deposition to snow planned before final release of v5.3 to improve wintertime O3
  BCs created using v5.3β (M3Dry) hemispheric CMAQ simulation contribute to lower O3 (vs BCs using v5.2.1)
    largest in the winter and fall
  Perform hemispheric CMAQ simulation with STAGE to provide BCs to regional CMAQ simulation
    provide consistent deposition scheme
    expect improve performance in cooler months
Total PM2.5
  Higher PM2.5 in the summer w/ CMAQv5.3β
    result of increased SOA production with AERO7
  Similar PM2.5 outside of the summer with AERO7
  M3Dry has a mixed effect on total PM2.5
    largest impact in the southeastern U.S. and the San Joaquin Valley in California
  Results of new STAGE deposition scheme will be presented by Jesse Bash (Wed 9:10am, Dogwood Room)

## Slide 22
Acknowledgements and Disclaimer
CMAQ Development Team and Others
  Jesse Bash
  Kathleen Fahey
  Bill Hutzell
  Deborah Luecken
  Benjamin Murphy
  Jon Pleim
  Havala Pye
  Limei Ran
  Golam Sarwar
  Donna Schwede
  David Wong
  Robert Gilliam (Meteorology)
  George Pouliot (Emissions)
  Chris Nolte (Code integration)
The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. Environmental Protection Agency.

## Slide 23
Extra Slides

## Slide 24
PM2.5 – M3Dry Bidi vs No Bidi (Annual):
Change in Bias