## Slide 1: Hemispheric-CMAQ Application and Evaluation for 2016
Presented by: Barron H. Henderson
OAQPS AQMG: P Dolwick, C Jang, C Misenis, N Possiel, B Timin
OAQPS EIAG: A Eyth, J Vukovich
ORD: R Mathur, C Hogrefe, G Pouliot, KW Appel
General Dynamics IT: Kathy Brehme
Notes: Henderson, Dolwick, Jang, Eyth, Vukovich, Mathur, Hogrefe, Pouliot, Possiel, Timin, Appel

## Slide 2: Outline
Overview
Global model versions and options
Emissions
  Natural
  Anthropogenic
CMAQ Results and Evaluation
Seasonal Average Ozone
Sonde Evaluation
CASTNet Evaluation
Tropospheric Ozone Assessment Report Databases
Satellite Qualitative
I won’t show results from GEOS-Chem results, but I will occasionally reference the performance from GEOS-Chem in the 2011 EPA modeling platform and preliminary 2016 GEOS-Chem.

## Slide 3: Hemispheric CMAQ
v5.2.1 (IPV, dust, halogens)
8 month spinup period
Polar stereographic (~1x1 deg)
44 Layers up to 50mb
Weather Research and Forecasting
Version 12.0.1
1-year spinup period
2x2.5 degree w/ half polar cells
72 vertical layers up to 0.01mb
  ~38 up to 50mb
Goddard Earth Observing System (v5) “forward product”
Layer 25 (~ 600 mb)
Hourly O3 : 3/26 – 4/04/11
GEOS-Chem

## Slide 4: Natural Emissions
Biogenics (plants and soils):
  BOTH: Model of Emissions of Gases and Aerosols from Nature (MEGAN) v2.1
  H-CMAQ North America Biogenic Emission Inventory System (BEIS)
Wild and Prescribed Fires:
  GEOS-Chem: 2011: GFED or 2-16: FINN v1.6
  H-CMAQ: FINN v1.5 and over US 2016 platform
Lightning:
  GEOS-Chem with Lee Murray updates
  H-CMAQ GEIA climatological averages by latitude & season
Inline Dust:
  GEOS-Chem: DEAD w/ current parameters
  HCMAQ: Inline CMAQ algorithm
Sea Salt: similar in-line schemes
Dimethyl Sulfide
  GEOS-Chem in-line
  H-CMAQ not in present run
  Relevant for aerosols and haze
More in Vukovich et al. Wednesday at 3:30pm in Grumman

## Slide 5: Anthropogenic Emissions
Global
EDGAR-HTAP base year 2010
  BOTH interpolated to 2014 by CEDS sector/country scalars
  GEOS-Chem uses RETRO VOC
  HCMAQ uses Pouliot sector-based speciation
Shipping:
  HCMAQ: EDGAR-HTAP and 2016fe platform within Continental US modeling domain
  GEOS-Chem: ARCTAS SO2, ICOADS CO, and over Europe from EMEP
Aircraft:
  HCMAQ: EDGAR-HTAP
  GEOS-Chem: AEIC
Regional
US: 2016fe Platform
Canada: EC 2013 interpolated
Mexico
  Mobile 2016 MOVES
  Other scaled from 2008
Asia (non-China): MIXv1
China: Tsinghua University (THU)
  Lower sulfate than CEDS
  Lower NOx than CEDS
  Similar trends in power sector
  Differences in metals where THU applies government required controls
More in Vukovich et al. Wednesday at 3:30pm in Grumman

## Slide 6: Results and Evaluation
CMAQ-Only
Seasonal Averages for Ozone
Sonde and CASTNet Evaluation
TOAR Qualitative Evaluation

## Slide 7: Ozone Surface and about 5km Spring
Surface
0.5 sigma or ~500hPa or 5km
Northern Hemisphere Spring (March April May, MAM) concentrations are relatively low with clear transport in the mid-troposphere seen most strongly in the southern latitudes
Beijing

## Slide 8: Ozone Surface and about 5km Summer
Surface
0.5 sigma or ~500 hPa or ~5km
Northern Hemisphere Summer (June-July-August, JJA) concentrations are higher both at the surface and aloft., but the transport patterns are less clearly defined than spring.
Beijing

## Slide 9: Evaluation Networks
WOUDC
  In domain sites: 29; launches: 1315
  Many in NA and W EU
  Averaging samples w/in CMAQ sigma levels
CASTNet
  Large scale simulations will not capture small-scale gradients
  Not all CASTNet sites are rural
In-service Aircraft for Global Observing System (IAGOS)
  333 grid cells covered
  3156 ascents or descents
Notes: Thanks to

## Slide 10: WOUDC Sondes: by Site (all Times)
Observations
H-CMAQ
Ratio
-1 degrees
82 degrees
(80, 120) percent
<3/2 x
>2/3 x
>1/2 x
<2x
Sorted by latitude and averaged across launches
Near tropopause bias that is strongest in the northern latitudes
Notes: There appears to be a near tropopause bias that is strongest in the northern latitudes

## Slide 11: WOUDC Sondes: by Time (all Sites)
Observations
H-CMAQ
Ratio
Jan 1, 2016
Dec 31, 2017
(80, 120) %
<3/2 x
>2/3 x
>1/2 x
<2x
Near tropopause bias is strongest in the spring.
WRF-CMAQ demonstrates increased downward mixing in March/April, but it appears muted compared to the sondes.
The mid troposphere (600-400 hPa) sondes have a maximum in that is not present in CMAQ.
Notes: The

## Slide 12: IAGOS Flights
Focusing on east (Japan) for Asian outflow
Missing Apr, Jul, and Oct flights
Captures a few prominent upper air features
Tends to be high biased
Over the continent, tends to be higher biased

## Slide 13: IAGOS Flights
Focusing on west (Hawaii) for incoming air
Missing Mar-Jul, and Oct flights…
Captures several key features
Mixed performance

## Slide 14: CASTNet Monitors: All Year
CASTNet monitors are not all rural, but they are frequently used as a proxy. Here we evaluate hourly ozone.
15LST has an r=0.67
Performance at these monitors is within ±7.5 ppb at most monitors.
There is a west-east bias divide
Notes: CASTNet monitors are not all rural, but they are frequently used as a proxy

## Slide 15: CASTNet Diurnal Performance
Plots show count of monitor-days with bias as a function of hour of day or day of year
Hour of day all year
0-5LST over the year
11-17LST over the year
Obs
Mod
Bias
Bias 11-17LST
Bias 00-05LST
Monitor-Hours
Monitor-Days
Monitor-Days
Notes: Monitor-Hours

## Slide 16: Summary
Compares well to sondes in the mid troposphere
  appears to have a near tropopause low-bias
  low bias northward of 50 degrees Dec-May
  performing similarly to GEOS-Chem used for the 2011 platform
Routine aircraft measurements show mixed results.
Performs best in JJA compared to CASTNet
  Most data is within 10 ppb of observations
  Clear West-East bias gradient
TOAR evaluation suggests similar results with better performance at rural than urban monitors
Compared to current test of GEOS-Chem v11-02* were less biased.
  H-CMAQ was low-biased while GC was high-biased compared to sondes
  Testing GC version (v12.0.1), considering meteorology
*w/FINN fires and 2016 lightning

## Slide 17: Next Steps
Provide boundary conditions for regional scale modeling.
Continue to evaluate, particularly for aerosols.
Estimate Ozone contributions from
  Natural (global) sources
  Anthropogenic
    International sources
    Domestic sources

## Slide 18: Appendix

## Slide 19: CASTNet Monitors: Spring
Spring (MAM) has a low-bias
15LST r=0.63
Majority of monitors within ±7.5 ppb
The west-east gradient is less strong than for the whole year

## Slide 20: CASTNet Monitors: Summer
Summer (JJA)
15LST has an r=0.66
Majority of monitors within ±7.5 ppb.
The west-east bias gradient is most strongly present in the summer.