## Slide 1
huiying.luo@uconn.edu
AirMG Group led by Dr. Astitha: airmg.uconn.edu
Dynamic evaluation of WRF-CMAQ PM2.5 simulations over the Contiguous United States for the period 2000-2010
Huiying Luo1, Marina Astitha1, Christian Hogrefe2,
Rohit Mathur2, and S. Trivikrama Rao1,3
1University of Connecticut
2US Environmental Protection Agency
3North Carolina State University

## Slide 2
Scope and Objectives
Analyze and interpret features embedded in PM2.5 observations and model outputs
Assess the model’s ability to reproduce changes/trends in observed PM2.5 concentrations
Improve confidence in model’s use for policy analysis
How well can we capture changes in PM2.5 induced by variations in meteorology and/or emissions over a decade?

## Slide 3
Data
Coupled 2000-2010 WRF-CMAQ (vers. 5.0.1) with 36-km grid cells over the USA (Gan et al. 2015; Xing et al. 2013)
AQS (100), 2000-2010
Min coverage each year: 30%
Observations:
  Daily total PM2.5 spanning 2000-2010 are retrieved from U.S. EPA’s Air Quality System (AQS).
  SO4, NO3, NH4, OC, EC, and Cl with the total PM2.5, are retrieved from both Chemical Speciation Network (CSN) and Interagency Monitoring of Protected Visual Environments (IMPROVE) networks. Only 1 CSN and 1 IMPROVE site on the map are used here for illustrative purposes.
Also a CSN site
IMPROVE site

## Slide 4
Methodologies
Power spectrum
Total PM2.5 with its BL component
PM2.5
BL
SY
PM2.5 BL
    Synoptic Forcing (SY): shorter-term component attributable to weather-induced variations
    Baseline Forcing (BL): longer-term component attributable to seasonality, emissions policy, inter-continental transport, and trend components
1. Kolmogorov-Zurbenko (KZ) filter
is the long-term component of
: window length
: number of application of the moving average
- Scale separation of 29 days
Selection of and depends on:
Timescales of interest (Synoptic scale)
Desired degree of separation
Data structure (Sampling frequency)
(Rao et al., 1994, 1995, 1997; Eskridge el., 1997; Hogrefe et al., 2003)

## Slide 5
Decomposition of total PM2.5 with EMD
Multiple improvements to address mode mixing as well as other problems and the most recent version of Improved Complete Ensemble Empirical Mode Decomposition with Adaptive Noise (Improved CEEMDAN) is used (Wu and Huang, 2009; Yeh et al., 2010; Torres et al., 2011; Colominas et al., 2014).
An IMF must satisfy:
the number of extrema (maxima and minima) and zero-crossings must be equal or differ at most by one;
the local mean, defined as the mean of the upper and lower envelopes, must be zero.
Signal is decomposed to multiple Intrinsic Mode Functions (IMFs) and a residual trend through sifting processes (Huang et al., 1998):
2. Empirical Mode Decomposition (EMD)
Methodologies
A unique technique that enables model evaluation at multiple time scales that is intrinsic to the PM time series.

## Slide 6: PM2.5 Density scatter
MW(30) NE(13) S(9) SE(29) SW(7) W(12)
Operational Evaluation
Model behavior depends on locations.
Largely underestimates PM2.5 total in SW and W regions. Need for speciated PM2.5 to identify the causes of these discrepancies.
Cooler seasons (Q1 and Q4) have a bimodal distribution, which represents the spatial variations from eastern to western US as shown in regional scatter plots.
Binned every 2 μg/ m3.
Q1 Q2 Q3 Q4

## Slide 7: Evaluation of 11 years daily PM2.5 and BL (2000-2010)
Operational Evaluation
Model simulations and observations are highly correlated in MW
Difficulty in simulating BL for some sites in CA and near large water bodies
Overall overestimation in eastern and underestimation in western CONUS.
R RMSE Bias
PM2.5
BL

## Slide 8
Trend analysis (2000-2010)
A general decreasing trend of BL mean and 98th percentile can be seen from both observations and CMAQ for most locations. The increasing trends (noted in orange and red in 1st, 2nd col.) are not statistically significant.
The decreasing is underestimated (red in last col.) in W, SW and Florida, while overestimation occurs in MW and NE.
Significant trends (p< 0.05) are circled.
μg/m3/yr
BLmean
98th pct
OBS CMAQ Bias

## Slide 9
Obs
CMAQ
CMAQ agrees with the magnitude and trends of observed 98th percentiles of PM2.5 in MW, NE, and SE.
98th percentiles are underestimated in SW and W regions and overestimated in the S.
The notable decreasing trend in the W seen in observations is not captured by the model.
Trend analysis (2000-2010)

## Slide 10
(Quarter mean)
CMAQ agrees with observations in the sign of the trends for all regions and seasons but varies in magnitude.
CMAQ shows more trend variability in SE and less variability in MW and W.
CMAQ underestimates the decreasing trend at the 90th percentile in SW and W, while it overestimates the trend in NE and S.
Trends in cooler seasons (Q1, Q4) are more challenging to simulate than warmer seasons.
μg/m3/yr
μg/m3/yr
Trend analysis (2000-2010)

## Slide 11
How well is CMAQ representing a 5-yr change?
Sites in W, SW and near large water bodies exhibit larger errors.
RMSE is lower when we look at the 5-yr change, esp. in regions close to the coast.
Percentage of systematic error (RMSEs) in RMSE is much larger than that of unsystematic error (RMSEu = 100 - RMSEs) in 98th percentile, which points to feasible improvement in CMAQ’s ability to simulate exceedances in total PM2.5.
98th percentile Conc. Absolute Change
(%)
(%)

## Slide 12: Quabbin Summit, MA (RURAL, IMPROVE) Total PM2.5
Obs CMAQ
Mean cycle (days)
Peak cycle (days)
EMD analysis with speciated PM2.5

## Slide 13: Quabbin Summit, MA (RURAL, IMPROVE) Total PM2.5
EMD analysis with speciated PM2.5
Very clear annual cycles of PM2.5 exist in both obs and CMAQ, but they are out of phase by up to six months.
Mean cycle (days)
Obs CMAQ
The residual (trend) indicates the overestimation of magnitude of trend component by CMAQ.

## Slide 14
SO4
NO3
Cl
OC
EC
TS Annual cycle Trend
Quabbin Summit, MA (IMPROVE)
Overestimated magnitude
Overestimated magnitude and trend
Problematic*
Varies
Shifted nearly half year
Overestimated magnitude and trend
Overestimated magnitude, cycle
Overestimated magnitude
Good
Good
Obs CMAQ
Mean cycle (days)
EMD analysis with speciated PM2.5

## Slide 15: Reno, NV (urban - AQS, CSN) Total PM2.5
Obs CMAQ
The underestimation can be partially explained by missing the extreme wildfire events such as the 2008 California Wildfires.
Mean cycle (days)
EMD analysis with speciated PM2.5

## Slide 16: Reno, NV (AQS, CSN)
Underestimated magnitude
SO4
NO3
NH4
OC
EC
TS Annual cycle Trend
Shifted
Underestimated magnitude, shifted
Underestimated excl. 05-07, shifted
Underestimated excl. 05-07, shifted
Underestimated trend
Underestimated mag. and trend
Underestimated magnitude
Underestimated magnitude, varies
Underestimated magnitude, varies
Obs CMAQ
Mean cycle (days)
EMD analysis with speciated PM2.5

## Slide 17
Summary and Future Work
For daily PM2.5, the longer-term baseline component and the annual extreme (98th pct.) are overestimated in the eastern United States and underestimated in the west.
A universal decreasing trend in PM2.5 10th, 50th, 90th and 98th percentiles can be seen from both observations and CMAQ. The notable decreasing trend in the 98th percentile that was observed in the West is not captured by the model.
Percentage of the 98th percentile’s systematic error (83.5%) is much larger than that of unsystematic error (16.5%), which suggests that CMAQ’s ability to simulate exceedances in total PM2.5 could be improved.
EMD decomposition enables model evaluation at multiple time scales that is intrinsic to the PM time series. Our preliminary analysis shows CMAQ dose not simulate the magnitude or phase of PM2.5 annual cycles well. However, CMAQ is capable of simulating the trend well, even if the magnitude of the trend component is less accurate.

## Slide 18
Acknowledgements
The views expressed in this presentation are those of the authors and do not necessarily represent the views or policies of the U.S. Environmental Protection Agency.
Part of this work was supported by the Electric Power Research Institute (EPRI) Contract #00-10005071, 2015-2017 (MA and HL)