## Slide 1
17th Annual CMAS Conference, UNC-Chapel Hill
October 24, 2018
Mechanistic representation of soil nitrogen emissions in CMAQ
Quazi Z. Rasool1*, Jesse O. Bash2, and Daniel S. Cohan1
1 Department of Environmental Science and Engineering, UNC- Chapel Hill
*formerly at Department of Civil engineering, Rice University
2Computational Exposure Division, NERL, US Environmental Protection Agency

## Slide 2: Outline
Motivation: Importance of soil nitrogen emissions to air quality
Methods and results
  Parametric modeling of soil NO
  Mechanistic modeling of soil N oxide emissions (NO, HONO, N2O)
  WRFv3.7-CMAQv5.1 with FEST-C v1.2 simulation for May and July 2011*
Future work & conclusions
* Appel et al. (2017), GMD
Notes: Introduce biochar

## Slide 3
NH3
NH4+
NO2-
NO3-
Nitrification
Denitrification
Org N
Microbial or active N
Surface nutrient runoff
Organic N
Immobilization
Mineralization
Atmosphere
Soil
Plant N uptake
Leaching
Soil Nitrogen cycling : sources and emissions
N sources/inputs
Fertilization
Deposition
Natural fixation
Adapted from Fowler et al. (2013), Pilegaard (2013), Su et al.(2011)
Volatilization
N2O HONO
NO
GHG
Ozone & PM2.5
hν
NO OH
Ozone & PM2.5
Health Risks
PM2.5
Volatilization

## Slide 4: Reactive soil N in air quality models
Parametrized NO emissions and soil-atmosphere exchange of NH3
  HONO and N2O typically neglected
NO and NH3 influence ozone and particulate matter
Soil NO ~ 20% of global NOx budget
Large underestimations and uncertainties in traditional scheme
  No deposition, poor representation of soil moisture, lack of spatial heterogeneity
Updated parameterized approach
Vinken et al. (2014), Bash et al. (2013), Hudman et al. (2012)

## Slide 5: Motivation
Soil nitrogen emissions altered by increasing fertilizer use
Decline in fossil fuel NOx, increasing soil NOx contribution
Inconsistent treatment of N species in soils and fluxes
  Bi-directional scheme for ammonia but not other species
  NO parameterized; HONO ignored
  Nitrification and denitrification not represented
Reduce uncertainties of soil N emissions and air quality predictions

## Slide 6: YL algorithm vs BDSNP (Default soil NOx scheme in CMAQ) (Updated soil NOx scheme)
Yienger and Levy (1995), Hudman et al. (2010), Hudman et al. (2012)

## Slide 7
Environmental Policy Integrated Climate (EPIC) agricultural model
(Cooter et al., 2012)
Wet Dep
Dry Dep
Org N pool
NH3 emission
NH3 deposition
Notes: HUSC to Schedule Vegetable Plantings, Predict Harvest Dates and Manage Crops
Temperature controls the development of many organisms that don’t have complex thermoregulatory systems. This allows us to predict the development of different organisms by accurately using development or phenology models which are based on the accumulation of heat units (i.e. degree days) during a growing season.

## Slide 8: Current implementation of EPIC in CMAQ as part of FEST-C for estimating bi-directional NH3
NH3 bi-directional exchange scheme
Soil NH4+ and H+
Nitrification, Volatilization
Soil properties
Meteorology & Land surface model (WRF)
Land use data
EPIC
Crop fertilization
Fertilizer timing
Ag soil management
Background soil NH4+ and H+
Net soil NH3
Chemical Transport Model (CMAQ)
Physical and chemical processes in the atmosphere
Deposition
Anthropogenic emissions
Pollutants
(Ozone, PM, etc.)

## Slide 9
NH3
NH3
NH4+
N2
N2O
NO
NO N2O
N2
NO N2O HONO
NO2-
NO3-
HNO3
HNO3
Atmosphere
Soil
HNO2
H+
NO2
NO2
H+
Fertilizer, Deposition, Biome
Adapted from Su et al., 2011; Pilegaard, 2013 and Medinets et al., 2015
N (-3)
N (+5)
Nitrification
Denitrification
Org N
NO
N2O
Reactive N cycling schematic
(Parametrized vs Mechanistic)
Org N
Total N
NO
Parametrized
Mechanistic

## Slide 10: Mechanistic soil N scheme: DAYCENT
Simulates all terrestrial ecosystems
Widely calibrated and validated for:
  Crop yield, soil C, NO3-, soil T and water content, N2O
More complex mechanistic models available
  Advantage: Bi-directional exchange between soil and atmosphere
  Disadvantage: Very few validations and extensive computational requirement
(Necpálová et al., 2015; Butterbach-Bahl et al., 2013; Parton et al., 2001)

## Slide 11: Integration of EPIC and DAYCENT in CMAQ for soil N emissions
Soil NH4+, NO3-, Organic N & C
Soil properties
Mechanistic soil N scheme
NH3 bi-directional exchange scheme
DAYCENT soil N gas sub-model
HONO emission from nitrification
Meteorology & Land surface model (WRF)
Land use data
EPIC
Crop fertilization
Fertilizer timing
Ag soil management
Non-Ag soil N and C
Soil N emissions (NH3, NO, HONO)
Chemical Transport Model (CMAQ)
Physical and chemical processes in the atmosphere
Deposition
Anthropogenic emissions
Pollutants
(Ozone, PM, etc.)

## Slide 12: Mechanistic soil N scheme : Overview
Meteorology,
canopy structure,
biome/vegetation coverage
(LAI and bulk stomatal resistance),
deposition coefficients
Length of dry period before rain
Soil
moisture
Soil temperature
DayCENT - Nitrification and Denitrification algorithm
Sub-grid
NLCD40 biomes
Pulsing events
Agricultural
(EPIC)
Wang et al. canopy reduction factor
Nitrification |  |  | Denitrification | 
NO | HONO | N2O | NO | N2O
Mechanistic scheme
1
2
1
Canopy reduction factor applies to all NO and HONO emissions
2
Pulsing factor applies only to nitrification NO and HONO
Soil NH4 , NO3, C
Oswald et al.
f(Soil water holding capacity,
biome specific optimum NO:HONO)
Soil
pH
Gas diffusivity
Soil organic N and C
Agricultural
(EPIC)
Non-Agricultural
(Schimel and Weintraub et al.)
N Deposition
Soil organic N and C
- Non-agricultural (Xu et al.)

## Slide 13: Organic to inorganic N transformation in mechanistic soil N scheme
Non-agricultural1 soil organic
C and N data
(Xu et al.)
Microbial (i.e. active) N
NH4
Nitrification
NO, HONO, N2O
NO3
Mineralization2
Immobilization2
Denitrification
N2
NO, N2O
DAYCENT N emission sub-model
1Also includes non-US agricultural areas
2Schimel and Weintraub Algorithm for Non-Agricultural and
EPIC algorithm for Agricultural regions
Microbial biomass C:N
Agricultural soil organic
C and N data
(EPIC)
soil composition,
organic residue C:N,
inorganic N available
Biome, geographical location
soil T
and moisture
O2 available,
bulk density, tillage

## Slide 14: Updates in CMAQ : parameterized and mechanistic
Features in CMAQ | Parameterized | Mechanistic
Species emitted | Nitric oxide (NO), NH3 | NO, NH3, HONO, N2O
Approach* | BDSNP equations for NO | DayCENT submodel representing nitrification, denitrification, and mineralization
Variables considered | Total soil N, soil T, soil moisture, rainfall, and biome type | Soil water content (irrigated and unirrigated), T, NH4+, NO3−, gas diffusivity, and labile C by soil layer
Soil N data source | EPIC (agricultural soil only) | EPIC for agricultural soil Microbial biomass C, N, and properties for non-agricultural
*CMAQ bi-directional for NH3 (Bash et al., 2013) in both
Notes: DAYCENT and EPIC model both based on CENTURY ecosystem model
CENTURY simulates cycling of reactive N (along with other nutrients) between soil, vegetation, atmosphere and water
EPIC differs from DAYCENT since:
  EPIC has been implemented on a regional scale in CMAQ and,
  NH3 Bi-directional feedback implemented in EPIC-CMAQ framework
  (Cooter et al., 2012)
EPIC does not give how much of NO and N2O each came from nitrification and denitrification
N sub model of DAYCENT addresses that mechanistically based on
  soil water content (WFPS), temp, soil NH4+ and NO3− concentrations, gas diffusivity and labile C availability at various soil layers
  (Parton et al 1998; Del Grosso et al., 2000; Parton et al., 2001)
Soil HONO still not addressed in current biogeochemical models

## Slide 15: Comparison of Soil NO and HONO across schemes
YL
BDSNP
Mechanistic*
May 2011 July 2011
*Only Mechanistic scheme shows both NO and HONO
Soil NO and HONO emissions in ng-N/m2/s

## Slide 16: Soil N2O emission estimate from Mechanistic scheme
May 2011
July 2011
Soil N2O emissions in ng-N/m2/s

## Slide 17: Observed maximum summertime soil NO (monthly avg.) compared across schemes
Chart: Maximum soil NO (ng-N m−2 s−1)
| Iowa | Montana | South Dakota | Texas | Colorado
Observed NO | 18 | 12 | 10 | 43 | 10
Mechanistic May NO + HONO | 17.1 | 7.8 | 11.7 | 52.5 | 7.9
Mechanistic July NO + HONO | 13 | 14.2 | 10 | 45 | 11.5
YL May NO | 8.2 | 7.1 | 8 | 15 | 9.7
YL July NO | 11.4 | 12.9 | 13.9 | 15.9 | 15.3
BDSNP May NO | 20.1 | 9.8 | 18.4 | 54.1 | 18.6
BDSNP July NO | 41.7 | 42.3 | 54.6 | 60.3 | 33.2
Iowa fertilized fields (Williams et al., 1992) Montana fertilized fields (SCHIAMACHY NO2 derived) (Bertram et al., 2005) South Dakota fertilized fields (Williams et al., 1991)
Texas grasses and fields (both fertilized) (Hutchinson and Brams, 1992) Colorado natural grasslands (Parrish et al., 1987; Williams et al., 1991; Martin et al., 1998)
Notes: Iowa fertilized fields (Williams et al., 1992)
Montana fertilized fields* (Bertram et al., 2005)
South Dakota fertilized fields (Williams et al., 1991)
Texas grasses and fields (both fertilized) (Hutchinson and Brams, 1992)
Colorado natural grasslands (Parrish et al., 1987; Williams et al., 1991; Martin et al., 1998)

## Slide 18: Relative contribution of soil NOx to total NOx across schemes
YL
BDSNP
Mechanistic
Mechanistic scheme shows:
Eastern U.S. has lower soil NOx than expected
Regions with high soil NOx contribution: Agricultural plains (N Dakota to Texas) & West U.S.
Soil NOx is not more than 10-13% of total NOx <- Higher fossil fuel NOx concentrated in urban and industrial locations
BDSNP showed highest soil NOx contributing 25-33% to total NOx
May 2011 July 2011

## Slide 19
Total NOx (Mechanistic – YL)
Soil NO + HONO (Mechanistic – YL)
Impact of Mechanistic scheme on soil NO and HONO emissions and total NOx concentration
May
July

## Slide 20: Impact of Mechanistic scheme on OH, O3, PM and PM NO3
May
July
OH (Mechanistic – YL)
Max. daily 8-hr O3 (Mechanistic – YL)
PM2.5 total (Mechanistic – YL)
PM2.5 NO3 (Mechanistic – YL)

## Slide 21: Reduction in bias in predicted NOx concentrations with mechanistic scheme
Centerville
(CTR)
(BHM)
(JST)
(YRK) Yorkville
Gulfport (GFP)
Pensacola (OLF)
South Eastern Aerosol Research and
CHaracterization (SEARCH) Network, 2011

## Slide 22: Tropospheric NO2 column change (Mechanistic – YL) @ OMI overpass time
Regions in black show depreciated model performance and red shows improved

## Slide 23: Tropospheric NO2 columns across schemes compared to OMI observations
Mechanistic scheme improves trop. NO2 estimates for sensitive regions in West U.S.
Inconsistency in May and July for CA <-overestimation and spatial heterogeneity in OMI estimates in July (Lamsal et al., 2014)
Midwest agricultural plains NO2 underestimated

## Slide 24: Reduced bias in O3 and PM2.5 nitrate in Mechanistic Scheme
Mean Bias (MB) relative to AQS O3 observations
May 2011
July 2011

## Slide 25: Future work and scope
Extend bi-directional approach to N species beyond NH3
Necessitates field measurements to understand HONO, soil-plant canopy N exchanges
Representation of farming practices in mechanistic models, impact on NO, HONO
  Excess nutrient management on farms (Livestock manure)
  Biochar
  Nitrification inhibitors, tillage, controlled irrigation, injection of fertilizer
Creating offline version of the mechanistic model
Account for previously ignored sources of soil N and transformation process
  Rock weathering and Bio-crusts -significant fraction of global terrestrial N
  Unexplored mechanisms like Anammox
  (Anaerobic ammonium oxidation, where NH4+ and NO2− form N2)

## Slide 26: Conclusions
Key enhancements in mechanistic absent in parametric
  Consistent representation across N species
  Mechanistic representation of actual soil processes
  Extended to non-agricultural soil types
Improved OMI NO2 predictions overall with mechanistic, underestimates in Midwest
BDSNP overestimates NOx , O3 and PM2.5 relative to YL
Mechanistic scheme improves NOx , O3 and PM2.5 estimates relative to parametric

## Slide 27: Disclaimer: The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. EPA.
Office of Research and Development
National Exposure Research Laboratory , Computational Exposure Division
Office of Research and Development
National Exposure Research Laboratory, Computational Exposure Division
Notes: Disclaimer may be placed elsewhere in the presentation (such as the title slide or the “final” slide); however, it should be clearly legible.

## Slide 28: Acknowledgements
CED, NERL at US EPA for the opportunity as a visiting researcher
NASA Air Quality Applied Sciences Team
NASA grant NNX15AN63G (via UAH)
Dr. Ellen Cooter (US EPA), Dr. Rui Zhang (CSU)

## Slide 29: Air quality modeling and soil N emissions
Biogenic emissions
Vegetation VOCs
Soil NO and NH3
Meteorology & land surface model (WRF)
Land use data
Chemical transport model (CMAQ)
Physical and chemical processes in the atmosphere
Anthropogenic emissions
Pollutants
(Ozone, PM, etc.)
Adapted from Saylor and Hicks (2016)
Deposition

## Slide 30: Yienger-Levy (YL) default soil NO scheme in CMAQ: Overview
Soil temperature
Rainfall
Biome specific base emissions
(non-agricultural,
non-growing season)
YL wet and dry soil NO algorithm
Biome classification
NLCD40
Pulsing events
Leaf and stomatal
area index (LAI, SAI)
Canopy reduction
Yienger and Levy Soil NO emission
Growing season emissions
(base grassland + fertilizer)
Rainfall
(if original YL);
Soil moisture
(if PX-LSM)

## Slide 31: YL pulsing term
YL Pulsing multiplier

## Slide 32: Berkley Dalhousie Soil NOx Parametrization (BDSNP) scheme : Overview
Meteorology,
canopy structure,
biome/vegetation coverage
(LAI and bulk stomatal resistance), and
deposition coefficients
Length of dry period before rain
Soil
moisture
Soil temperature
BDSNP soil NO algorithm
MODIS24 mapping
to sub-grid NLCD40 biomes
Pulsing events
Biome specific background NO emission factor
Fertilizer and deposition N (EPIC)
Wang et al. canopy reduction factor
BDSNP
Soil NO emission

## Slide 33: Soil Biome / Land Cover Dataset Enhancements
GEOS-Chem (0.25° x 0.25°)
CMAQ (12 km x 12 km)
GEOS-Chem
24 MODIS land cover categories
Too coarse for regional modeling
CMAQ
Mapped 40 NLCD categories from Pleim-Xiu to 24 MODIS categories
Köppen-Geiger climate zones
Sub-grid fractionation of biomes
Rasool et al. (2016), Geosc. Model Dev.

## Slide 34
Environmental Policy Integrated Climate (EPIC) agricultural model
Fertilizer quantity: USDA Agricultural Resource Management Survey database, validated with fertilizer sales data
Fertilizer timing: Determined by plant nutrient stress
Can simulate varied agricultural practices (e.g., tillage, fertilizer type)
Fertilizer Emission Scenario Tool for CMAQ (FEST-C) incorporates EPIC simulated agricultural soil N into CMAQ runs
(Cooter et al., 2012)
Notes: HUSC to Schedule Vegetable Plantings, Predict Harvest Dates and Manage Crops
Temperature controls the development of many organisms that don’t have complex thermoregulatory systems. This allows us to predict the development of different organisms by accurately using development or phenology models which are based on the accumulation of heat units (i.e. degree days) during a growing season.

## Slide 35: Current implementation of EPIC in CMAQ as part of FEST-C for estimating bi-directional NH3
Bash et al. (2013)
Bi-directional Ammonia exchange scheme

## Slide 36: Impact of Potter vs EPIC Fertilizer Data on Soil NO
Fertilizer
Application (kgN/ha)*
Potter
EPIC
Difference in BDSNP
Soil NO (g/s)*
EPIC - Potter
*Averaged over July 2011

## Slide 37
Seasonality in BDSNP soil NO estimates

## Slide 38
Total NOx (BDSNP – YL)
Soil NO (BDSNP – YL)
Impact of BDSNP scheme on soil NO emission and total NOx concentration
May
July

## Slide 39: Impact of BDSNP scheme on OH, O3, PM and PM NO3
May
July
OH (BDSNP – YL)
Max. daily 8-hr O3 (BDSNP – YL)
PM2.5 total (BDSNP – YL)
PM2.5 NO3 (BDSNP – YL)

## Slide 40: Sensitivity of BDSNP to different inputs
Rasool et al. (2016) GMD
CMAQ biome
New fertilizer data
North American emission factors

## Slide 41: Biochar as soil amendment
Crop residues
Manure
Organic waste
Energy crop residue
(grass, willow, wooden chips)
Pyrolysis
(~ 500℃)
Biochar (Solid residue)
Biomass (C)
Bio-fuel and Syngas (CO+H2)
Energy sector Transportation
Industry
Residual heat
Soil
Potential benefits of biochar
C sequestration
Reduces nutrient runoff
Mitigating GHGs and air pollutants
Alters soil pH and moisture
Adapted from Lehmann (2007)

## Slide 42: Potential air quality benefits of biochar-aided soil NO emission reductions
Studies differ on whether biochar reduces soil NO by 47-67% (Nelissen et al, 2014) or not at all (Xiang et al., 2015)
Impact on O3
Impact on PM2.5
Pourhashem et al. (2017) ES&T
July 2011 impacts using BDSNP, Ozone is Max. 8-hr Daily Avg.

## Slide 43: DAYCENT: scope for application in CMAQ
DAYCENT and agro-ecosystem EPIC model used in CMAQ for agricultural NH3 use same C-N mineralization scheme: CENTURY model
CENTURY extensively validated like its daily version i.e. DAYCENT
Mechanistic models face limitation for validation of gaseous N emissions critical to air quality
CMAQ provides opportunity to apply DAYCENT to estimate soil N oxide emissions and then validate their impact on atmospheric chemistry
Compare NO and HONO emissions estimates and associated estimates of tropospheric NO2 column, ozone, and PM2.5 with those obtained from CMAQ using the YL and BDSNP parametric schemes

## Slide 44
From: The Potential Role for a Nitrogen Compliance Policy in Mitigating Gulf Hypoxia
Appl Econ Perspect Policy. 2016;39(3):458-478. doi:10.1093/aepp/ppw029
Appl Econ Perspect Policy | Published by Oxford University Press on behalf of the Agricultural and Applied Economics Association 2016. This work is written by US Government employees and is in the public domain in the US.
USDA NASS, 2012
Excess nitrogen (Livestock manure management)
Notes: Figure 1 County average excess nitrogen per harvested cropland acre
44

## Slide 45
In ppb
Mean Bias for Ozone and NOx concentration relative to AQS observations

## Slide 46
Reduced bias in NOx in Mechanistic Scheme
Mean Bias (MB) relative to AQS NOx observations
May 2011
July 2011

## Slide 47
Reduced bias in O3 in Mechanistic Scheme
Mean Bias (MB) relative to CASTNET O3 observations
May 2011
July 2011

## Slide 48
Reduced bias in PM2.5 nitrate in Mechanistic Scheme
Mean Bias (MB) relative to IMPROVE PM NO3 observations
May 2011
July 2011

## Slide 49
Mean Bias for Ozone concentration relative to CASTNET observations
In ppb

## Slide 50
In μg/m3
Mean Bias for PM2.5 NO3 concentration relative to IMPROVE and CSN observations

## Slide 52: Soil moisture (m3/m3) on a monthly mean basis (May and July 2011) for CONUS
http://www.cpc.ncep.noaa.gov/products/analysis_monitoring/regional_monitoring/palmer/2011/