## Slide 1: Evaluation of the CMAQ Model Performance during Persistent Cold Air Pool Events
Xia Sun1, Heather A. Holmes1, Kirk R. Baker2, and Cesunica E. Ivey3
Atmospheric Sciences Program, Department of Physics, University of Nevada, Reno, NV
U.S. Environmental Protection Agency, Research Triangle Park, NC
Chemical and Environmental Engineering, University of California, Riverside, CA
Oct 22 2018, Chapel Hill, NC
17th Annual CMAS Conference

## Slide 2: Persistent Cold Air Pools (PCAPs)
Topographic depression with cold air
During wintertime in mountain areas
Model Challenges
Difficult to replicate the multiday stagnant conditions (Baker et al. 2011)
Complex terrain
Chemistry during PCAPs (Baasandorj et al. 2017)
Notes: Snow at Christmas, less radiation, more chance ; mountain diurnal wind system, cold temperature, less radiation, cloudiness, and high background pm2.5 during pcaps make it different than non-pcaps

## Slide 3: Persistent Cold Air Pools (PCAPs)
(Yu et al. 2016)
Total number of the occurrences of PCAPs ≥3 days during 1979 to 2012
Notes: NARR, a VCP is identifed if 65% of a temperature profle in the
lowest 1.5 km above ground level (AGL) has a lapse rate of
2.5∘C km−1 or less and the 10-m wind speed is 3.0 m s−1
or less. Our results will be meaningful

## Slide 4: The Persistent Cold Air Pool Study （Utah, 2010-2011, PI: C. David Whiteman)
(Sun et al. 2018, under review)
Valley heat deficit:
CAPs are accompanied by high PM2.5

## Slide 5: WRF Model Configurations (v 3.7)
d01: 12km, d02: 4km
NAM, 12 km, 6hr reanalysis with 3hr forecasting dataset
NLCD 40-class land use
41 vertical layers
Four Dimensional Data Assimilation
Notes: First layer around 12 m, acm2 run extra 10 days for the soil nudging scheme

## Slide 6: WRF Model Configurations
Microphysics: Thompson scheme
Longwave radiation: RRTM
Shortwave radiation: Dudhia
Convective precipitation: Kain-Fritsch 2
NAM_ACM2, NAM_YSU,NAM_MYJ
Pleim-Xiu LSM ran extra 10 days for its soil nudging scheme
Jan1-Jan31, 2011, 7 days segmental run with spin up time of 1 day
Notes: First layer around 12 msNo-temperature or moisture nudging in the diagnosed PBL, wind nudging applied at all levels. Temperature and wind nudging strength was 3.0*10-4 s-1; moisture 1.0*10-5 s-1.

## Slide 7: Valley Heat Deficit (H22) and PBLH
H22 (MJ m-2)
Strong PCAPs
Underestimated H22
NAM_ACM2 produced the highest PBLH
At the NCAR sounding site (40.60º N, 111.93º E)
Notes: Ncar site

## Slide 8: Vertical Profiles (2011/01/02 1700 MST)
For this sounding:
WRF did not capture the inversion at 2km MSL
Overestimated water vapor mixing ratio near the ground
Higher simulated wind in the low levels
Notes: Higher surface temperature ,Higher latent heat flux,

## Slide 9: CMAQ Model Configurations (v 5.2)
Meteorology: WRF v 3.7
Emissions: 2011 National Emission Inventory
Mechanism: cb6r3_ae6_aq
--CB6, revision 3 gas-phase mechanism
--sixth-generation CMAQ aerosol mechanism with
sea salt and speciated PM Other
--aqueous phase chemistry
Notes: Kirk Baker provided the emissions

## Slide 10: PM2.5 Spatial Variation
NAM_YSU
NAM_MYJ
OBS
NAM_ACM2
units=µg/m3
coverage limit=75%

## Slide 11: PM2.5 Statistics
>16
12
8
4
0
Higher ME and RMSE in the region impacted by PCAPs (NAM_ACM2)
RMSE - µg/m3
>24
18
12
6
0
ME - µg/m3

## Slide 12: PM2.5 Confusion Matrix
False Alarm Ratio
Critical Success Index
Probability of Detection
NAM_ACM2
Accuracy (%) = 88.5
CSI(%) =4.1
POD(%) =4.2
FAR(%) =45.2
NAM_MYJ
Accuracy (%) = 88.5
CSI(%) =6.2
POD(%) =6.5
FAR(%) =46.7
NAM_YSU
Accuracy (%) = 88.3
CSI(%) =7.0
POD(%) =7.6
FAR(%) =53.0
Notes: Bias <- round((false_alarm+hit_exceed)/(miss_exceed+hit_exceed),1)

## Slide 13: Speciated PM2.5 (CSN)
Large underestimation of NH4 and NO3-
Notes: Possible chemical mechanisim may not be accurate enought

## Slide 14: Time series (Hawthorne site)
24-hour averages
Daily variation of NOx was well captured
Lower O3 during CAP pollution episodes
Notes: It has the most measurements

## Slide 15: Time series (Hawthorne site)
24-hour averages
Overestimated SO2
PM2.5 daily trend was captured but underestimated the peaks during strong PCAPs

## Slide 16: Diurnal Variations-NOx
Non-PCAPs
PCAPs
High NOx observed during nighttime
Peak at 4 pm simulated by model
Notes: Consistent NOx source or the lack of NOx removal in the residual boundary layer at night); model increase fast for the nox built up in the evening hours

## Slide 17: Diurnal Variations-O3
Non-PCAPs
PCAPs
Ozone diurnal variation during non-PCAPs was well simulated.
Overestimation of nighttime ozone during PCAPs might be due to underestimation of NOx or be chemistry related

## Slide 18: Diurnal Variations-SO2
Non-PCAPs
PCAPs
Consistent overestimation of SO2

## Slide 19: Diurnal Variations-PM2.5
Non-PCAPs
PCAPs
Overestimation of PM2.5 in the afternoon during non-PCAPs, associated with EC and OC
Underestimated PM2.5 at nighttime during PCAPs, associated with underestimated NOx, chemistry, and meteorology uncertainties

## Slide 20: Diurnal Variations-Speciated PM2.5
Non-PCAPs
PCAPs
Notes: Significant increase from ammonium and nitrate, slightly enhanced EC, oc doesn’t vary too much in pcaps.

## Slide 21: Stacked Plots (Hawthorne site)
Non-PCAPs
PCAPs
Notes: No need to add emissions in this case

## Slide 22: Conclusions
WRF did not capture some of the inversions during PCAPs
CAMQ underestimated PM2.5 during PCAPs
NH4NO3 was underestimated and OC was overestimated for speciated PM2.5
Simulated and obs avg. daytime surface sensible heat fluxes during Jan1 to Jan 9 2011 in Salt Lake Valley

## Slide 23
THANKS!