## Slide 1
Younha Kim1, Jung-Hun Woo1*, Bok Haeng Baek2, Jinseok Kim1, Jinsu Kim1, Youjung Jang1, Minwoo Park1, Yungyeong Choi1, Eunji Lee1, Hyunjin Park1
Development of an Integrated Assessment Model for Korea :
The GHGs and Air pollutants Unified Information DEsign System for Environment(GUIDE)
2018 CMAS Conference
1 Konkuk University, Seoul, Korea
2 University of North Carolina, Chapel Hill, USA
Notes: Good morning Everyone. I appreciate for the opportunity to share my recent work with you this morning.
I'm Jinseok Kim from Kunkuk University in South Korea. Today, I am presenting this work in behave of Dr. Kim.
This morning I would like to share our recent development of an integrated Assessment model called GUIDE which stands for Green House Gases and Air Pollutants Unified Information Design System for Environment in Korea. This model is consisted of three major parts. The first one is the cost-benefit decision making system, the second one is the air quality modeling system and then last one is information service platform that integrates all the output from both systems and allows users to understand this complex system between cost-benefit, and air quality control strategy results. This last information service platform is currently under the development. This morning I am going to focus on showing the air quality modeling system outcomes we recently completed.

## Slide 2
Background
2
Source : IEA, 2016
Top 10 GHGs emitting countries in 2014
CO2 Emission Trend in Northeast Asia
Source : World bank
1st. China
5th. Japan
7th. Korea
Notes: Before I show you our results, I want to briefly cover our motivation of this GUIDE modeling system development.
As you can see in this figure, over the last 60 years, GHG emissions have increased.
There are major Green House Gases contributors in the world including China, US and India, and Korea ranks the 7th place. Last two decades, Korea has been making a great efforts to reduce these green house gases to comply with the IPCC’s future RCP and also Korea introduced the GHG reduction plan from INDC of Paris Agreement.
While we are working on the Climate Changes, we also have been facing the serious air quality issues in local level.

## Slide 3
Background
3
fine particulate matter
(NASA KORUS-AQ Campaign)
PM10: 166 ug/m3
2013, Dec 5th
PM10: 35 ug/m3
2013, Dec 6th
Han river in Seoul
Recent Air Pollution issue in Seoul Metropolitan Area
NIER/NASA, 2017
Primary vs.
Secondary
Composition
P. Orgarnic 8%
Chloride 1%
Black
Carbon
8%
Local vs.
Transboundary
Contribution
Notes: Seoul, the capital of Korea, has recently faced atmospheric environmental problems. As you see the pictures in this slide, local air quality issues like PM2.5 has been causing many concerns on human health impacts. Although Korea has been working hard to reduce our own emissions from various major emissions sources like large stationary point sources, onroad mobile sources. We have been facing the air quality impacts from our neighbor countries like China, North Korea, and other countries next to South Korea.
To understand these regional air quality issues, last 2017, Korea government had completed the collaborative research air quality field campaing with NASA, it is called “KOR-US”. Based on this campaign study with NASA, we have found out that almost 34% of high PM2.5 episode are caused by China and 9% by North Korea. And also this secondary organic aerosol among PM2.5 is about 34%, sulfate, nitrate and ammounium are 16%, 24% and 14%, respectively.
So, to understand this complex air quality issues and come up with a better control strategies, we have been working on developing this integrated, assessment model, GUIDE modeling system.

## Slide 4
Objective of GUIDE System
4
The GHGs and Air pollutants Unified Information DEsign System for Environment
(GUIDE)
이 그림이 어제 캐리 장 박사가 소개했던
한국에서 개발되고 있는 한국형 Integrated Assessment Model 의 체계도입니다.
저는 여기에서 Air Quality Model 개발 및 작성을 담당하고 있고, 오늘 프리젠테이션에서는 이 부분을 포커스 하여 발표하도록 하겠습니다.. 등의 내용으로~~
이 전 슬라이드가 왠지 외국인들이 한번에 딱 캐취하기가 좀 복잡할 수도 있을 것 같아서. 이것도 혹시 모르는 플랜B로 간직해봐바. 백박사님과 물론 의논 해야 겠지만^^
Notes: This figure shows the GUIDE model development framework.
The GUIDE model is consisted of three major groups. The Group of objective 2 on the left is the group that develops the economic and energy projection model and the cost-benefit decision making model.
and the Group of objective 1 on the right is the group that conducts the inventory development and the study to create the Air quality module.
The Group of Objective 3 is currently working on combining these developments into one platform.

## Slide 5
5
GUIDE Model
Objective 1
: Integrated Emissions Inventory &
Policy Supporting Air Quality Model
Policy Supporting Air Quality Model
Source-Receptor
(RSM-VAT)
Integrated GHGs-AP Inventory
Activity
Emis. Factors
Control Tech.
Met. Model
Air Quality Model
Emissions Model
Integrated GHGs and AP Emissions Inventory
Objective 1
Objective of GUIDE System
Notes: In this presentation, I will be focusing on showing the design of the Integrated Emissions Inventory and Policy Supporing Air Quality Modeling syste. It includes the construction of RSM (Respose Surface Model), a policy-supporting air quality modeling system in GUIDE models.

## Slide 6
Policy Supporting Air Quality Model
6
Baseline
NOx/SO2/PM
50% Control
Examples of utilizing RSM and VAT.
(East China)
Simulation of the SMOKE-CMAQ system about 200 times according to the reduced emission scenarios by region/sector to generate the Response Surface Model (RSM) and visualization of the system using the Visualization Analysis Tool (VAT).
Real-time(near-realtime) atmospheric chemical transport information integrated into decision making system.
(Jiming Hao et al., 2017)
Objective: Integrated Emissions and Atmospheric Transport Model
우선적으로 SMOKE와 CMAQ을 활용한
Notes: Since many of you already heard about the RSM model from yesterday’s talks from Dr. Carey Chang from U.S. EPA and Professor Jia Xing from Tinghua university in China, I won’t go into the detail. In this study, we have adopted the RSM module from ABaCAS to develop the real-time air quality modeling results for Group 2 decision making model under the GUIDE system.
In our study, we have identified a total of 120 control factors for the RSM model. They are based on by regions, by pollutants and by emission sectors. Based on these 120 control factors, we have initially simulated around 200 RSM scenarios CMAQ modeling runs.
To create the RSM, we have simulated about SMOKE-CMAQ system about 200 times according to the reduced emission scenarios by region and sector to generate the air quality input dataset for Response Surface Model (RSM) and the visualization analysis tool called VAT

## Slide 7
7
RSM* Design for “GUIDE”
*Response Surface Modeling
  Region, pollutants, and sector
  17 Regions
  8 Pollutants
  7 Sectors
Region | Pollutant | Sector
Seoul | CO | Power(POW)
Busan | CO2 | Industry(IND)
Daegu | NH3 | Mobile(MOB)
Incheon | NOX | Residential/commercial(RES)
Gwangju | SO2 | Agriculture(AGR)
Daejeon | PM10 | Other(OTH)
Ulsan | PM2.5 | Solvent(VOC)
Sejong | VOC | Boundary condition(BC)
Gyunggi-do |  | 
Gangwon-do |  | 
Chungcheongbuk-do |  | 
Chungcheongnam-do |  | 
Jeollanam-do |  | 
Jeollabuk-do |  | 
Gyeongsangbuk-do |  | 
Gyeongsangnam-do |  | 
Jeju |  | 
Objective: Integrated Emissions and Atmospheric Transport Model
Region-Sector Control Factors : ~119 Factors + Boundary Condition
= 120 Factors
Notes: The RSM design for the GUIDE model is as follows.
Korea is divided into 17 regions, and There are a total of 8 pollutants (CO, CO2, NOx, Ammonia and so on) with a total of 7 sectors like power, industry, mobile, residential, agriculture and the Solvent VOC sector. SMOKE processing is drived by utilizing the sectors classified as above.
So, we have created a total of 119 factors by region and sector with boundary conditions to consider the impacts from our neighbor countries like China and North Korea.

## Slide 8
8
Chemical Transport Modeling System(SMOKE-CMAQ-RSM) Modeling Framework
*Latin Hypercube Sampling
Base Scenario Emission was created using KORUSv2.1 Emission Inventory and SMOKE-Asia Emission Processing System. (The KORUS emission inventory was developed in support of the KOREA-NASA KORUS-AQ aircraft field campaign.)
Using Latin Hypercube Sampling(LHS), 120 control scenarios were created and modeled.
The generated 120 scenario CMAQ results were applied to RSM.
Objective: Integrated Emissions and Atmospheric Transport Model
Emission Inventory
(KORUSv2.1)
LHS* method Scenario
(~120 Scenario)
KORUS E.I. :
Younha Kim
Oct. 24th 2pm presentation
Real time CMAQ-RSM
Results
(~120 Scenario)
Notes: This is the modeling framework for creating the SMOKE-CMAQ-RSM. Base Scenario Emission was created using KORUSv2.1 Emission Inventory th rough SMOKE-Asia Emission Processing System. If you are interested in how the emissions inventories are created for this 2017 KOR-US field campaingns, please check out the Dr. Younha Kim’s presentation tomorrow at 2pm.
And we also used the Latin Hypercube Sampling(LHS) to develop a total of intial 120 control scenarios for RSM.
The generated 120 scenario CMAQ results were applied to RSM.

## Slide 9
9
*Response Surface Modeling
Chemical Transport Model | CCTM in CMAQ v4.7
 | (U.S. CMAS)
• chemical mechanism | SAPRC-99 aero3
Emissions | 
• anthropogenic emission model | SMOKE-Asia (Woo et al., 2009)
• emissions inventory | CREATEv3.0 (Woo et al., 2018) (KORUSv2.1)
Meteorological Model | WRF (U.S. NCAR)
Period | January, April, July, October, 2013
Domain | • Extent :
 | Domain 1 (East Asia) Domain 2 (South Korea)
 | • Grid resolution (domain):
 | 27 ⅹ27km2(174 x 128) 9 ⅹ9km2(67 x 82))
 | • N. of vertical layer: 30
Domain
Meteorological data
-cloudiness-
Chemical Transport Modeling System(CMAQ-RSM) Modeling Framework
Objective: Integrated Emissions and Atmospheric Transport Model
Notes: For our Chmical Transport Modeling system, we used the CMAQ v4.7 with Chemical Mechanism SAPRC99.
Emissions were processed using SMOKE-Asia with KORUS v2.1 inventory which is based on the latest East Asia region emissions inventory called CREATE v3.0.
The meteorological model was WRF. To represent the seasonality of air quality, we modeled January, April, July, October. A total of four month with 10 sinup days.
The one in the redbox is the 27km by 27km modeling domain and the smaller black box around South Korea is 9km * 9km modeling domain.

## Slide 10
a)
b)
c)
Comparison between CMAQ simulation results and actual data for the High Ozone Season (July)
(a: Rural Area NO2, b: Metropolitan Area NO2,
c: Metropolitan Area O3)
Comparison of the simulated concentration of ozone and the measured concentration of atmospheric measurement network
Objective: Integrated Emissions and Atmospheric Transport Model
CMAQ Base Modeling Evaluation
Notes: Before we start the CMAS-RMS control scenario simulations, we peformed the complete CMAQ based modeling evaluations. These plots are showing the NOx and ozone simulation results in July.
The R square of NOx is about 0.6, but the R square of ozone is more than 0.7.
Based on these evaluations, I concluded that the performance of CMAQ was reasonable.

## Slide 11
11
RSM Base Scenario [PM2.5]
Result
Notes: The results of the RSM are shown as follows.
This figure is the result of RSM for PM2.5, which shows the Base Scenario.
As we expected, the high concentration area in the Red Box are shown around the industry complex or megacity area.

## Slide 12
12
RSM 50% Reduction Scenario [PM2.5]
Result
Notes: The following shows the results when all emissions are reduced by 50%. As you can see that the concentration of PM2.5 in the high concentration area are significantly reduced compared with the base scenario shown in the previous slide.

## Slide 13
13
RSM 50% Increase Scenario [PM2.5]
Result
Sensitivity
Notes: The following shows the results when all emissions are increased by 50%. You can see that the high PM2.5 concentrations are occurred near those metropolitan and megacity regions
With this RSM visualization tool, you can see the response of the PM2.5 concentration changes while adjusting the emission amount in real time.

## Slide 14
A : Base Scenario; B : All sector 30% reduction; C : All sector 20% reduction;
D : Power 17%, Industry 32%, Mobile 28%, Residential 23% reduce (Recommend policy in Korea);
E : Solvent VOC 20% increase, the others 30% reduction;
F : Solvent VOC 20% increase, the others 20% reduction;
RSM Results (△PM2.5) [Base-Scenario] : △Reduction(+)
Result
(A)
(B)
(C)
(E)
(F)
(D)
Notes: The following are the results of testing base scenarios and reduction scenarios using RSM.
The meaning of each graph is shown below.
Graph A is the base case. there is no concentration of PM2.5 that is reduced or increased.
Graphs B and C are scenarios that reduce all emissions by 30% and 20%. Even if korea reduce the amount of emissions uniformly across all regions, we can see that the responses from each region are different.
Graph D shows the result of applying the desired PM2.5 reduction policy from 2017 to 2022 planned in Korea.
I'll tell you about more detail about this in the next slide.
Graph E and F show the results when the emissions of Solvent VOC Sector, the source of VOC, are increased while the emissions of the remaining sectors are decreased.
The results of Graphs E and F show that it is important in Korea to regulate VOC emissions to reduce PM2.5 concentration.

## Slide 15
15
Result
Recommended policy in Korea for PM2.5
(A)
(B)
(C)
(D)
Targeted PM2.5 in A region:
8ug/m3 Reduction
(A) : Power 17%, Industry 32%, Mobile 28%, Residential 23% Reduction
(B) : (A) + Solvent VOC 10% Reduction
(C) : (A) + Solvent VOC & Agriculture Sector 10% Reduction
(D) : (A) + Solvent VOC 20% Reduction
Notes: We also analyzed the current policy using RSM.
Graph A is the one from the previous slide and the concentration of PM2.5 that is reduced base on the Korea’s PM2.5 policy.
The goal of this policy is to cut down the PM2.5 concentration in region A by 8 ug/m3.
However, we have derived the RSM result that it is difficult to achive the target with the current policy alone.
So, we have reduced the VOC emission from Solvent sector by 19% in Graph B, and Solvent VOC and Agriculture 10% reduction in Graph C, and finally recuded the Solvent VOC 20% in Graph D to see whether we can achieve the goal.
While Graph B and C did not meet the goal in region A, Graph D showed that reducing the solvent VOC sector by 20% will allows us to meet the requirement of current policy goal.
Using RSM in this way allows decision makers to consider what policies need to be implemented to achieve their goals.

## Slide 16
16
①Weight control function for each sector and region
②Select results button in map, graph, and table format
③Base year/Control year comparison, Delta result selection radio button
④2D/3D selection button
⑤Animation on/off button
⑥Display of 2D concentration line results
⑦Show graph legend
Display results of RSM model in real time according to user input change
Provides atmospheric model results in three forms ; MAP, CHART and DATA (Benchmarking from ABaCAS)
GUIDE-RSM : Displaying map results [2D/3D] : Under Development
Development of “GUIDE” Prototype
Notes: The resulting RSM results are being applied to the GUIDE system for information service platform.
The above figure is a prototype of informationve service platform system in the GUIDE system.

## Slide 17
17
After implementing the input and output sections of the health benefits model as a separate prototype -> platform integration
Output the results of the health benefit model in the form of maps using tables, graphs and GIS
Health Benefit Model : Under Development
Development of “GUIDE” Prototype
Notes: The following is the Health Benefit model developed by the Group of objective 2.
Likewise, these results are being applied to the GUIDE system by the Group of objective 3 .

## Slide 18
Development of “GUIDE” Prototype
18
Display the results of decision support by scenarios in graphs, cumulative ben diagrams, etc.
Integrate the results of the input elements of the decision making model and output the entire result as a report
Scenario 1
Policy Selection
Technology Selection
Constraints
Cost benefits
RSM
Health benefits
Diagram
Graph
Report
Final GUIDE Decision Making Model : Future Design
Notes: Finally, combining these studies to develop the Decision Making Model GUIDE is a comprehensive goal.

## Slide 19
Summary & Future Work
19
To improve the fine particle pollution in Korea, it is necessary to consider the secondary formation.
Complete SMOKE-CMAQ-RSM modeling for 120 control scenarios.
Successfully implemented the RSM model based on the 120 control scenarios CMAQ results.
Summary
Future Work
Increase the number of scenarios to improve the accuracy of RSM.
Full integration with “cost-health benefit” module to estimate the air quality & health benefits over the cost of control strategy.
Full integration with information service system.
Notes: finally, summary and future work.
We are Created 120 control factors considering 17 regions, 7 sectors, and Boundary condition.and Complete SMOKE-CMAQ-RSM modeling for 120 scenarios.
in conclusion, To improve the fine particle pollution in Korea, it is necessary to consider the secondary formation.
Future work is as follows.

## Slide 20
Thank you

## Slide 21
Intercomparison of CMAQ & RSM Concentration