## Slide 1
Jia Xing1, Dian Ding1, Shuxiao Wang1, Bin Zhao1,4, Carey Jang2, Yun Zhu3, Jiming Hao1
1 School of Environment, Tsinghua University, Beijing, China
2 Office of Air Quality Planning & Standards, US EPA, RTP, NC, USA
3 South China University of Technology, Guangzhou, China
4 University of California, Los Angeles, CA, USA
22 Oct 2018, 17th Annual CMAS Conference, Friday Center, UNC-Chapel Hill
Representing the nonlinear responses of tropospheric ozone and fine particulate matter to precursor emission changes
Notes: 1
两控区
2018/10/22
大气处
1

## Slide 2: Nonlinear-Relationship between Emission and pollution
Emissions
O3
PM2.5
Pollution

## Slide 3: Nonlinear-Relationship between Emission and pollution
Emissions
O3
PM2.5
Pollution
Nonlinear

## Slide 4: A promising method to address that issue
Ambient Concentration
Emission ratio
0
1
“real atmosphere”
Sensitivity (e.g., DDM)
Source Apportionment (e.g., ISAM)
RSM
base
Response Surface Model (RSM)
——a meta-model built upon multi-“Brute Force” model simulations, to explore the response relationship between emission changes and air quality responses

## Slide 5: Development of the RSM
NOx emission ratio
PM2.5 response surface
SO2 emission ratio
Baseline
Primary emission
Air quality
1.Control
factors
Source A- NOx/industry
Source B- NMVOC/mobile
…
2.Emission
scenarios
Source A
Source B
Source C
3.CMAQ
simulation
4.Statistical
results
Latin Hypercube Sample (LHS)
Hammersley quasi-random Sequence Sample (HSS)
RSM
Mperk
RSM-VAT

## Slide 6: Development of the Extended-RSM (ERSM)
Region 1
Region 2
Region i
Region n
…
…
RSM
RSM
RSM
RSM
Precursor
Precursor
Precursor
Precursor
+
Transport
Transport
Transport
+
Transport
RSM_TT
Indirect effects
Xing et al., ES&T, 2017
local chemistry (CM) associated with the change in its precursor levels at the receptor region
regional transport (TP) of the pollutant from the source region to the receptor region
interregional effects (IND) among multiple regions, representing the impacts on the contribution from one source region by other source regions (new in ERSMv2.0)

## Slide 7: improved Performance in the latest ERSM v2.0
“True” response
ERSMv1.0
ERSMv2.0
PM2.5 response to changes in emissions
X-scale: NH3
Y-scale: NOx
X-scale: NH3
Y-scale: SO2
Improvement under large reduction condition

## Slide 8: Overview of the RSM evolution
pf-RSM
How to further reduce the number of cases required in RSM?

## Slide 9: The prior knowledge of pollutant responses to emissions
The isopleths of 1-h maxima O3 response to changes of NOx/VOC emissions
(established based on 30 Brute-Force CMAQ runs, monthly average, July 2005)
Urban site (in Beijing city)
Rural site (in Miyun, northern Beijing)
(Xing J. et al. ACP, 2011)
VOC-limited
NOx-limited
Pollution concentrations contributed by its sources and sinks through a series of atmospheric processes in which the nonlinear behavior contributes to the nonlinearity in the responses of concentrations to precursor emissions

## Slide 10: The prior knowledge of pollutant responses to emissions
High Ozone(>70ppb)
Low Ozone(<30ppb)
Beijing
Shanghai
Guangzhou
Similar responsive functions can be expected across regions and time

## Slide 11: Design of RSM with polynomial functions
NOx
VOC
Original training samples
VOC
NOx
Prior knowledge
Regression-based
RSM (Traditional)
NOx
VOC
Ozone response
regression
VOC
NOx
Fewer samples
Fitting-based RSM
(pf-RSM)
fitting
(Xing J. et al. ACP, 2018)
the prior knowledge was characterized as a series polynomial functions
Fewer samples->high efficiency (60% reduction in the sample number)
Easier investigation on the nonlinearity (e.g., peak value, derivative)

## Slide 12: Design of RSM with polynomial functions
PM2.5
O3
NOx
1st
2nd
3rd
4th
NH3
1st
2nd
3rd
SO2
1st
2nd
POA
1st
VOC
1st
2nd
3rd

## Slide 13: Composition of O3 response to NOx (Beijing)
Term1-NOx5; Term2-NOx4; Term3-NOx3; Term4-NOx2; Term5-NOx
VOC-limited
VOC-limited
VOC-limited
NOx-limited
the change in the Term 4 and Term 5 from positive to negative largely contributes to the nonlinear behavior in O3 response to NOx

## Slide 14: Validation of pf-RSM prediction
CMAQ
pf-RSM
Baseline
ΔCase1 (moderate control)
ΔCase2 (strict control)
O3 (monthly averages of daily 1-hour maxima in July 2014, unit: ppb)

## Slide 15: Validation of pf-RSM prediction
CMAQ
pf-RSM
Baseline
ΔCase1 (moderate control)
ΔCase2 (strict control)
PM2.5 (monthly averages in January 2014, unit: µg m-3)
(Xing J. et al. ACP, 2018)

## Slide 16: Definition of Peak Ratio (PR)
NOx-limited
VOC-limited
95.00
90.00
85.00
80.00
75.00
70.00
65.00
60.00
55.00
1.2
1.0
0.8
0.6
0.4
0.2
0.0
0.0 0.2 0.4 0.6 0.8 1.0 1.2
2-D isopleths of O3 sensitivity to NOx and VOC emission changes
PR <1: VOC-limited PR>1: NOx-limited
PR can be directly calculated from the polynomial function

## Slide 17: Peak Ratio (PR) in the BTH region
2014/7
 | Jan | Jul
Beijing | 0.11 | 0.76
Tianjin | 0.1 | 0.45
HebeiN | 0.19 | >1.2
HebeiE | 0.15 | 0.74
HebeiS | 0.13 | 0.59
Smaller PRs (0.4–0.8) were evident in urban areas where NOx emissions are saturated, resulting in a strong VOC-limited condition
PR map

## Slide 18: Comparion between photochemical indicators and PR
Strong correlations, while some indicators fail to capture the O3 chemistry

## Slide 19: ABaCAS: a scientifically sound decision support system
  RSM
Emission
Air quality
Benefit
Cost
Target
  BenMAP
  CoST
  SMAT

## Slide 20: ABaCAS: a scientifically sound decision support system
Xing, J. et al. ABaCAS: an overview of the air pollution control cost-benefit and attainment assessment system and its application in China. The Magazine for Environmental Managers - Air & Waste Management Association 2017, April.

## Slide 21
Baseline
PM2.5 Response Surface Modeling
Control factor
RSM-VAT

## Slide 22
Control Scenario
PM2.5 Response Surface Modeling
RSM-VAT
Control factor

## Slide 23: Real-time prediction under various scenarios
Real time Pred. by RSM
NOx
Reduce 10%
Reduce 100%
SO2
Reduce 10%
Reduce 100%
…
…
Reduce 10%
VOC
Reduce 100%
Reduce 10%
…
NH3
…
Reduce 100%
10000 scenarios
√
√
√

## Slide 24: LECO: optimization of control pathway
S1: No NH3 control
S2: With NH3 control
NH3 emission controls can be a cost-efficient strategy to reduce PM2.5
Xing et al., in prep.
Optimal control pathway to achieve certain concentration:
S1: NOx(-35%), SO2(-75%), VOC(-65%), PM(-85%)
S2: NOx( -5%), SO2(-75%), VOC(-25%), PM(-85%), NH3(-65%)

## Slide 25: LECO: optimization of control pathway
S1: No NH3 control
S2: With NH3 control
Response of PM2.5 and O3
Large co-benefit for O3 reduction
Small co-benefit for O3 reduction

## Slide 26: Multi-regional scenario: Local vs Regional
5 × 10000 = 50000 scenarios
L:R = 1:1
L:R = 1:0.75
L:R = 1:0.5
L:R = 1:0
L:R = 0.5:1
Control ratio between Local and Regional
…
5 × = 50000
NOx
Reduce 10%
Reduce 100%
SO2
Reduce 10%
Reduce 100%
…
…
Reduce 10%
VOC
Reduce 100%
Reduce 10%
…
NH3
…
Reduce 100%
Real time Pred. by RSM

## Slide 27: Multi-regional scenario: Local vs Regional
(L:R = 1:1): the same reduction rate is applied in local and regional sources;
(L:R = 1:0.75): regional reduction rate is 75% of the local reduction rate;
(L:R = 1:0.5): regional reduction rate is half of the local reduction rate;
(L:R = 0.5:1): regional reduction rate is twice the local reduction rate;
(L:R = 1:0): only local reductions are considered)
PM2.5
O3
the same level of reductions should be conducted across the whole BTH region to achieve more aggressive targets
local reduction has priorities for attaining moderate targets
Xing et al., in prep.

## Slide 28: Sensibility of health outcomes
Beijing Tianjin N Hebei E Hebei S Hebei
Sensibility of chronic health outcomes
All
Other
LPS
Other
LPS
All
All
Transportation
Residential & Commercial
Industry
Power plant
All
Sensitivity of health outcomes to stepped control of individual air pollutants (left) and individual pollutant-sector combinations (right)
defined as the change ratio of health outcome divided by the reduction ratio of emissions

## Slide 29: 2018 ABACAS & CMAS-ASIA-PACIFIC
Please visit ABaCAS website for more information: http://www.abacas-dss.com/

## Slide 30
Thank you very much!
Jia Xing
Associate Professor
School of Environment, Tsinghua University
Beijing, China, 10084
Email: xingjia@tsinghua.edu.cn