## Slide 1
Year-long Simulation of PM2.5 in Pearl River Delta using WRF-SMOKE-CMAQ System
Xuguo ZHANG, Jimmy FUNG, Alexis LAU and Wayne Wei HUANG
Oct 23, 2018
17th annual CMAS conference, Chapel Hill, NC, USA

## Slide 2
Research Background
Air Quality Modelling System
Refining 2012 emission inventory
Model performance of PM2.5
Summary
Outline
1

## Slide 3: Research Background
Spatial 2D Plot for PM2.5 for the Whole China
(1522 Stations)
PRD
Spatial 2D Plot for PM2.5 for PRD
(70 Stations)
Complex Air Pollution has become a severe issue throughout the whole China.
  Causes: Meteorological Conditions and Emissions (Zhang Q. (2012) Nature; Guo S. (2014) PNAS )
Real time monitoring data have been released since Jan. 2013.
  Challenges: Large gradient & Too Sparse & Paucity.
Targeting: What is it? Where does it come from? Where does it go?
2

## Slide 4: Objectives of this study
Assessing 2012 emission inventory to provide a reliable model-ready hourly, gridded emission input.
Total comparison.
Spatial surrogates and temporal profiles.
Scenario analysis to refine the emission inventory.
Year-long simulation to analyze spatial distribution and seasonal variations.
Time series and spatial map for PM2.5 performance.
Seasonal changes of PM2.5 components.
3

## Slide 5
AIR QUALITY MODELLING SYSTEM
4
Meteorological Model
Create Physical Atmosphere
Solve full set of atmospheric equations for evolution of wind, temperature, pressure and moisture content, etc.
(WRF)
Atmospheric Chemistry Model
Chemical reactions of various chemical species
and solve the advection-diffusion equations
(CAMx, CMAQ)
Emissions Model
Anthropogenic, Natural
(SMOKE)
Analysis Model
Evaluation
Sensitivity
Display

## Slide 6
Targeting Domains
D3
D4
D1
D2
Larger WRF domain could minimize the boundary effects of meteorological parameters on CMAQ grid.
Parameter | Value
Projection | Lamber-Conformal
Alpha | 250 N
Beta | 40 N
X center | 114 E
Y center | 28.5 N
5

## Slide 7
6
Spatial distribution of WRF output for parameters: Tem., surface wind vector, sea level pressure.
Meteorological Field Validation

## Slide 8
Meteorological Field Validation
2012 Wind speed and wind direction
Note (1) Observed Wind; (2) Ratio Mean; (3) Mean Bias; (4) Mean Normalized Bias; (5) Norm Mean Bias; (6) Mean Fractionalized Bias; (7) Coefficient Determination; (8) Simulated Mean; (9) Root Mean Square Error; (10) Mean Absolute Gross Error; (11) Mean Normalized Gross Error; (12) Normalized Mean Err; (13) Mean Fractionalized Bias; (14) Index of Agreement. For wind direction: (15) Corr; (16) RMSE and (17) IOA.
Performance matrix for WRF field
7

## Slide 9: Raw Data Comparison: Total
Chart: Difference of Total PM10 for PRD
| Mobile | Dust | Biomass | Industry | Power_P | Marine | Total
2006 | 129339.717 | 302832.014 | 38818.63 | 314510.8701 | 127251.1511 | 20350.62 | 933103.0022
2012V1 | 58026.75 | 207724.602 | 42961.4 | 294804.7 | 82849.77 | 4477.5531 | 690844.7751
2012V2 | 58026.75 | 183272.192 | 42961.4 | 204900.4 | 77988.62 | 4551.3587 | 513673.9707
Chart: Difference of Total PM2.5 for PRD
| Mobile | Dust | Biomass | Industry | Power_P | Marine | Total
2006 | 107988.8264 | 144751.226 | 16819.17 | 117678.7688 | 27782.402 | 19397.67 | 434418.0632
2012V1 | 55120.56 | 50255.953 | 21480.701 | 155215.3 | 40012.05 | 4071.455 | 326156.019
2012V2 | 55120.56 | 20538.541 | 21480.701 | 92251.71 | 37490.86 | 4138.618 | 231020.99
Chart: Normalized Total PM2.5 for PRD
| Mobile | Dust | Biomass | Industry | Power Plant | Marine | Total
2006 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2012V1 | 0.51043 | 0.34719 | 1.2772 | 1.319 | 1.4402 | 0.20989 | 0.75079
2012V2 | 0.51043 | 0.14189 | 1.2772 | 0.78393 | 1.3494 | 0.21336 | 0.53179
Chart: Normalized Total PM10 for PRD
| Mobile | Dust | Biomass | Industry | Power Plant | Marine | Total
2006 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2012V1 | 0.44864 | 0.68594 | 1.1067 | 0.93734 | 0.65107 | 0.22002 | 0.74037
2012V2 | 0.44864 | 0.60519 | 1.1067 | 0.65149 | 0.61287 | 0.22365 | 0.5505
2012PM2.5 47%, due to Fugitive Dust 86%, Mobile 49%, Industry 22%，
But Power Plant 35% .
2012PM10 45%, due to Mobile 55%, Fugitive Dust 39%, Power Plant 39%，
Industry 35% .
8

## Slide 10: Spatial Surrogates Database
Road Network
9
Population
Year 2006
Year 2012
D3 (3km)

## Slide 11: Temporal Profiles Database
  Power plant: Continues Emission Monitoring system (CEM) data , monthly fuel consumption and electricity production.
  On-road mobile source: traffic flow, vehicle types, vehicle mileage , et al.
  None-road mobile source: Automatic Identification System (AIS) data, Port handling capacity
  ……
10
Monthly Profile
Weekly Profile
Diurnal Profile

## Slide 12: Comparison of the 2006EI and 2012EI
PM2.5 | Corr | MB | ME | IOA | RMSE
CMAQ06EI | 0.44 | -4.50 | 12.33 | 0.66 | 15.38
CMAQ12EI | 0.50 | -5.08 | 11.83 | 0.70 | 14.94
With new updated 2012 emission inventory, the overall model performance has been improved.
Peaks or valleys have been well captured in the new updated run.
UTC Time
11

## Slide 13: Comparison of the 2006EI and 2012EI
PM2.5 | Corr | MB | ME | IOA | RMSE
CMAQ06EI | 0.50 | 22.53 | 32.98 | 0.61 | 44.15
CMAQ12EI | 0.59 | -6.16 | 22.39 | 0.75 | 29.30
With new updated 2012 emission inventory, the overall model performance has been improved by over 10% in IOA.
Peaks or valleys have been well captured in the new updated run.
12

## Slide 14
 |  | Corr |  | MB |  | IOA |  | RMSE | 
No. | PM2.5 | New WRF 06EI | New WRF 2012EI | New WRF 06EI | New WRF 2012EI | New WRF 06EI | New WRF 2012EI | New WRF 06EI | New WRF 2012EI
1 | Central | 0.43 | 0.47 | -7.96 | -8.71 | 0.63 | 0.65 | 17.15 | 17.18
2 | Central/Western | 0.48 | 0.52 | -7.78 | -8.67 | 0.66 | 0.68 | 16.71 | 16.79
3 | Eastern | 0.44 | 0.50 | -4.50 | -5.08 | 0.66 | 0.70 | 15.38 | 14.94
4 | Kwai Chung | 0.48 | 0.52 | -7.30 | -8.54 | 0.66 | 0.67 | 17.11 | 17.35
5 | Kwun Tong | 0.45 | 0.49 | -4.15 | -4.78 | 0.67 | 0.69 | 14.93 | 14.74
6 | Sha Tin | 0.51 | 0.54 | -3.88 | -4.73 | 0.71 | 0.72 | 15.13 | 15.25
7 | Sham Shui Po | 0.43 | 0.48 | -1.21 | -2.10 | 0.66 | 0.69 | 15.50 | 15.48
8 | Tai Po | 0.37 | 0.42 | -9.02 | -10.98 | 0.60 | 0.61 | 20.39 | 20.78
9 | Tai Mun | 0.53 | 0.59 | -9.36 | -10.60 | 0.66 | 0.68 | 16.09 | 16.16
10 | Tsuen Wan | 0.44 | 0.47 | -3.06 | -4.24 | 0.66 | 0.67 | 15.99 | 16.26
11 | Ave | 0.46 | 0.50 | -5.82 | -6.84 | 0.66 | 0.68 | 16.44 | 16.49
HK
 | Corr |  | MB |  | IOA |  | RMSE | 
PM2.5 | New WRF 06EI | New WRF 2012EI | New WRF 06EI | New WRF 2012EI | New WRF 06EI | New WRF 2012EI | New WRF 06EI | New WRF 2012EI
Ave | 0.42 | 0.47 | 20.74 | -1.52 | 0.56 | 0.66 | 42.99 | 32.27
PRD
Average of around 31 monitor stations
With new updated 2012 emission inventory, the overall model performance has been improved.
The model performance in PRD has been improved larger comparing with that in HK.
Comparison of the 2006EI and 2012EI
13

## Slide 15
Model ready emission for different species
2006EI
2012EI
PM2.5
PM10
3km
14

## Slide 16
2006EI
2012EI
NOx
PEC
3km
15
Model ready emission for different species

## Slide 17
2006EI
2012EI
SO2
CO
3km
16
Model ready emission for different species

## Slide 18
Daily column composite plot for Domain 2 (Resolution: 9km)
The Guang Dong (GD) local information was dealt by SMOKE while outside GD was
adapt from MIX Asia Emission Inventory published by Tsinghua in 2016.
9km
PM2.5
NO
SO2
NO2
PM10
PEC
Propagate with GD information
17
Model ready emission for different species

## Slide 19
Daily column composite plot for Domain 1 (Resolution: 27km)
The Guang Dong (GD) local information was dealt by SMOKE3.7 while outside GD was adapt from the MIX Asia Emission Inventory published by Tsinghua in 2016.
27km
Propagate with GD information
PM2.5
NO
SO2
NO2
PM10
PEC
18
Model ready emission for different species

## Slide 20
Year-long simulation for HK: Kwun Tong
1st Quarter
2nd Quarter
3rd Quarter
4th Quarter
19
PM2.5

## Slide 21
Year-long simulation for HK: Sha Tin
1st Quarter
2nd Quarter
3rd Quarter
4th Quarter
PM2.5
20

## Slide 22
Year-long simulation for PRD: Guangzhou Luhu
1st Quarter
2nd Quarter
3rd Quarter
4th Quarter
21
PM2.5

## Slide 23
Year-long simulation for PRD: FS Jinjvzui
1st Quarter
2nd Quarter
3rd Quarter
4th Quarter
22
PM2.5

## Slide 24
Model performance on PM2.5 for HK and PRD stations in 2012
Performance matrix of model outputs
23

## Slide 25
C: 2nd Q
E: 4th Q
B: 1st Q
A: Annual Average
Annual and quarterly average spatial map for PM2.5 (A is the annual average while B is for the first quarter, C: 2nd quarter, D: 3rd quarter, E: 4th quarter.)
Spatial distribution of model outputs
Wet Season
Wet Season
Dry Season
Dry Season
D: 3nd Q
24

## Slide 26
Seasonal variations of PM2.5 components
Nitrate
EC
OC
Ammonium
Spring
Winter
Fall
Summer
25

## Slide 27
Summary
Research Findings
Successfully reproduce PM2.5 concentrations at most cities for most months of the year.
Shows the capability of the system integrating 2012-based emission inventory and MIX Asian emission data to reproduce severe air pollution.
Accurate surrogate database could improve model at a moderate level.
Seasonal variations for the PM2.5 components.
Significances
In-depth understanding of the new 2012 emission inventory.
Extensive model validation and sensitivity tests for different emission reduction scenarios.
High resolution concentration map for evidence-based air pollution control policy.
26