## Slide 1: Coupling Meteorology-sensitive Emissions with Air Quality Forecasting System in Korea
B. H. Baek
University of NC at Chapel Hill / CMAS
SoonTae Kim & Changhan Bae
Ajou Unversity

## Slide 2: Motivations

## Slide 3
SO4 Overestimate since 2015?
NO3: Overestimate: NOx or NH3 Emissions?
Long-term PM2.5 Performances
Obs. location b/n China & Korea
Obs location in Seoul

## Slide 4: Meteorological Adjustor (MetADJ)
Does not estimate but adjust meteorology-sensitive emissions based on hourly gridded meteorological factors
Agricultural Ammonia Sources (AGNH3)
  Meteorological Factors: Ambient Temperature and Wind Speed
  Russell and Cass (1986): Egrid,hour = [2.36(Temperature-273)/10] x Vgrid,hour (wind speed)
  Base : Temperature (TB=59 ℉) ; WS at 10 meter (VB=4 m/sec)
  Adjusted Emissions: = *
Residential Wood Combustion Sources (RWC)
  Meteorological Factors: Ambient Temperature
  Adelman and Baek (2010): Egrid,hour = 42.12–0.79* Temperaturethreshold by region
  Base : Temperature (TB=50 ℉) ; Zero emissions when Ti,h > 50℉

## Slide 5: Meteorological Adjustor (MetADJ)
Onroad Mobile Sources
  Meteorological Factors: Ambient Temperature and Relative Humidity
  Reconciliation between US EPA Mobile Source Category Codes (SCCs) vs Korea CAPSS SCCs Best Curve Fitted Polynomial Equations by ambient temperature based on U.S. EPA’s MOVES Emissions Factors by:
    Ambient temperature, operating patterns, fuel, pollutants and time
  Best Curve Fitting Algorithms (BCFA) Function : EFs vs Temperature
US EPA MOVES Emissions Factor Lookup Tables
BCFA
Polynomial Equations by SCC, Pollutants,Fuel,,,,

## Slide 6: Mobile Emissions by Temperature

## Slide 7: Meteorological Adjustor (MetADJ)
MetADJ
AG_NH3
RWC
Mobile 1
Mobiles 2
Mobile 4
Mobile 3
Others
CMAQ-ready Emissions
SMOKE
Meterology
Polynomial Eqs for Mobile Src
Emissions Inventory

## Slide 8: Met. Adjusted NH3 Emissions in China

## Slide 9: Seasonal Adjustment NH3 in China
Clear Seasonal and Regional Variations
South region shows the increase of NH3 during Winter
North region shows the decrease of NH3 due to temperature differences
Jul-Sep
Apr-Jun
Oct-Dec
Jan-Mar

## Slide 10: Seasonal [PM2.5] Variation in China
Clear Seasonal Variation overall
Lower PM2.5 Estimates during Winter
Higher PM2.5 Estimates during Summer
Jan-Mar
Jul-Sep
Apr-Jun
Oct-Dec

## Slide 11
Daily [NO3-] Evaluation @ Obs. b/n China & Korea
■ MetADJ case shows the overall improvements on [NO3-] estimates compared to the [PM2.5].
■ MetADJ case over-estimated high [NO3-] episode : Need further investigation!
~10 ㎍/㎥
Jan-Mar
Apr-Jun

## Slide 12
■ Daily [NH4+ ] Performance is better compared to [PM2.5]
  Winter Season: Under-Estimates ; Summer Season: Over-estimates
■ Improvement on estimating low concentrations during the Winter season
■ Trying to capture some high peak of Daily [NH4+ ] during the Summer season
Daily [NH4+] Evaluation @ Obs. b/n China & Korea

## Slide 13
Met. Adjustment of NH3 in Korea
High Agricultural Activity Regions ≅ High NH3 Emissions Variations over the seasons
Total NH3 Emissions:
15.6 % Increase

## Slide 14
PM2.5 Variation by NH3 Changes in Rural
South Region
North Region

## Slide 15
Monthly average PM2.5 shows under-estimates overall.
  Before: Annual average PM2.5 5.7 ㎍/㎥ underestimates
  After: Annual average PM2.5 7.9 ㎍/㎥ underestimates
No PM2.5 changes shown during the summer due to no NH3 increase in Seoul
  Due to no significant NH3 increase during Summer
  No agricultural NH3 sources near Seoul area
PM2.5 Evaluation in Seoul

## Slide 16
Increase of PM2.5 and NOx Emissions in Metropolitan Area during Winter Season
  Due to the dependency of Cold Engine Start PM2.5 and NOx Emissions and Evaporative NOx Emissions to local ambient temperature.
NOX Emissions  2.9% INcrease
PMFINE Emissions  25.6% Increase
Met. Adjustment to Mobile Emissions

## Slide 17
Regional Variation of PM2.5 by Mobile Emissions

## Slide 18
Cold Engine Start PM2.5 Emissions increase approximately 5 ㎍/㎥ in Seoul during Winter Season
No changes of PM2.5 during the Summer season : Due to no changes in PM2.5 emissions during Summer
Monthly PM2.5 Evaluation in Seoul

## Slide 19
SO2 Emissions Increase approximately 2.9%
Mostly Increased during the Winter season due to the increase of heating
Met. Adjustment for Residential Wood Combustion

## Slide 20
SOx Emissions Increases ≅ Increase of PM2.5 concentrations near Metropolitan Area
SO42- concentration increased surrounding of Metropolitan Area
Annual Average [PM2.5 ] Regional Variation

## Slide 21: Conclusion and Future Plans
AGNH3: Lower NH3 during Winter, Higher NH3 during Summer
Mobile: Higher PM2.5 emissions during Winter due to Cold Engine Start
RWC: Higher PM2.5 emissions during Winter due to Residential Heating
Future Detail Analysis are needed but we concluded that there are some improvements on forecasting of the peak of PM2.5 and Ozone concentrations.
Future Plans
Long-term Cumulative Sector-impact studies (AGNH3+Mobile+RWC)
Regional Analysis
Episodic Analysis

## Slide 22: Acknowledgement
Korea National Institute of Environmental Research (NIER)
National Strategic Project-Fine Particle:
(NRF-2017M3D8A1092022)
National Research Foundation of Korea (NRF)
Ministry of Science and ICT(MSIT)
Ministry of Environment(ME)
Ministry of Health and Welfare(MOHW)