## Slide 1
Reconstruction of surface NO2 concentrations using a conservative downscaling of OMI, GOME-2, and CMAQ
Hyun Cheol Kim1,2, Sang-Mi Lee3, Tianfeng Chai1,2, Barry Baker1,2, Fong Ngan1,2, Li Pan1,2, and Pius Lee1
1Air Resources Laboratory, National Oceanic and Atmospheric Administration, College Park, MD
2Cooperative Institute for Climate and Satellites, University of Maryland, College Park, MD
3South Coast Air Quality Management District, Diamond Bar, CA

## Slide 2: Motivation
Need for high-resolution and full coverage NO2 data
  For epidemiology,
    One of NAAQS pollutants
    Raised levels of nitrogen dioxide causes respiratory problems. Significant impacts on people with asthma.
  For emission estimation,
    Import precursor of ozone and particulate matter
    Detection of urban emission sources
    Fine-scale air quality simulations
Notes: 위성자료를 이용한 배출량의 보정은 우선 위성에서 관측된 VCD와 모델에서 계산된 VCD를 정확하게 비교하는 과정이 필요합니다.
위성 VCD에 맞추어 모델에서 특정 시간을 맞추어 추출해야 하며, 수직적인 민감도를 고려하기 위해 averaging kernel 기법을 도입합니다.
위성 VCD의 경우 격자 해상도가 위성에 비해 성기기 때문에 이를 보완하기 위해 최근에 개발된 Conservative Downscaling 기법을 이용합니다.
- 자세한 사항은 다음 슬라이드에 제시되어 있습니다.
VCD는 대기 중 가스상 오염물질의 분포로, 배출량과 보정을 하기 위해 장기런을 이용한 배출량 – 농도 전환율을 고려합니다.

## Slide 3: Topics to discuss
Fair comparison of model and satellite
  Temporal sampling (diurnal)
  Spatial resolution (downscaling)
  Vertical sensitivity (averaging kernel)
Reconstruction of surface NO2 concentration
  Data fusion
Conversion to emission
  Machine learning (See Kim et al. poster [#4] tomorrow)

## Slide 4: Top-down estimation of NOx emissions
Satellite
Model
sVCD
mVCD
AK
mVCD/AK
sVCD/DS
Local pass time
(Temporal match)
Conservative Downscaling
(Horizontal match)
Averaging Kernel
(Vertical match)
Comparison
Emission
Adjustment
Emission-to-VCD
Conversion
Notes: 위성자료를 이용한 배출량의 보정은 우선 위성에서 관측된 VCD와 모델에서 계산된 VCD를 정확하게 비교하는 과정이 필요합니다.
위성 VCD에 맞추어 모델에서 특정 시간을 맞추어 추출해야 하며, 수직적인 민감도를 고려하기 위해 averaging kernel 기법을 도입합니다.
위성 VCD의 경우 격자 해상도가 위성에 비해 성기기 때문에 이를 보완하기 위해 최근에 개발된 Conservative Downscaling 기법을 이용합니다.
- 자세한 사항은 다음 슬라이드에 제시되어 있습니다.
VCD는 대기 중 가스상 오염물질의 분포로, 배출량과 보정을 하기 위해 장기런을 이용한 배출량 – 농도 전환율을 고려합니다.

## Slide 5: Problems
Satellite
Model
sVCD
mVCD
AK
mVCD/AK
sVCD/DS
Local pass time
(Temporal match)
Conservative Downscaling
(Horizontal match)
Averaging Kernel
(Vertical match)
Comparison
Emission
Adjustment
Emission-to-VCD
Conversion
Retrieval uncertainties: Detection limit & Instrumental error
Model uncertainties: Chemical & Meteorological (e.g. PBL)
AK quality & spatial resolution
Footprint resolution
Diurnal profile
Conversion ratio
Transport
Notes: 위성자료를 이용한 배출량의 보정은 우선 위성에서 관측된 VCD와 모델에서 계산된 VCD를 정확하게 비교하는 과정이 필요합니다.
위성 VCD에 맞추어 모델에서 특정 시간을 맞추어 추출해야 하며, 수직적인 민감도를 고려하기 위해 averaging kernel 기법을 도입합니다.
위성 VCD의 경우 격자 해상도가 위성에 비해 성기기 때문에 이를 보완하기 위해 최근에 개발된 Conservative Downscaling 기법을 이용합니다.
- 자세한 사항은 다음 슬라이드에 제시되어 있습니다.
VCD는 대기 중 가스상 오염물질의 분포로, 배출량과 보정을 하기 위해 장기런을 이용한 배출량 – 농도 전환율을 고려합니다.

## Slide 6: How to compare?
(A) OMI
(B) CMAQ

## Slide 7
(A) OMI
(B) CMAQ
(C) OMI-downscaled
(D) CAMQ-upscaled
(Pseudo-OMI)
Downscaling
Upscaling
Fair comparison

## Slide 8: Conservative downscaling of NO2 column density
OMI
CMAQ
Spatial weighting kernel
Reconstructed OMI
Apply model’s spatial information to OMI pixels
Model’s emission inventory has high uncertainty in its intensity, but has reliable accuracy in the location of emission sources.
OMI’s original quantity is strictly preserved

## Slide 9: OMI & P3 NO2 column density (CALNEX2010)
(A)
(B)
[X10 15 #/cm2]
[X10 15 #/cm2]
Original
Downscaled

## Slide 10: Model and observations
4-km WRF-CMAQ simulations over Southern California (SCAQMD)
AQS surface observations
OMI and GOME-2 NO2 column densities (KNMI, TEMIS)

## Slide 11
Spatial distribution of OMI and CMAQ NO2 column densities. “DS” and “xDS” denote OMI NO2 column densities with and without the downscaling method, respectively, whereas “AK” and “xAK” denote CMAQ NO2 column densities with and without the averaging kernel, respectively.

## Slide 12
Scatter plot comparison of OMI and CMAQ NO2 column densities. “DS” and “xDS” denote OMI NO2 column densities with and without the downscaling method, respectively, whereas “AK” and “xAK” denote CMAQ NO2 column densities with and without the averaging kernel, respectively.
AK
DS+AK
DS

## Slide 13
Spatial distribution of GOME-2 and CMAQ NO2 column densities. “DS” and “xDS” denote GOME-2 NO2 column densities with and without the downscaling method, respectively, whereas “AK” and “xAK” denote CMAQ NO2 column densities with and without the averaging kernel, respectively.

## Slide 14
Scatter plot comparison of GOME-2 and CMAQ NO2 column densities. “DS” and “xDS” denote GOME-2 NO2 column densities with and without the downscaling method, respectively, whereas “AK” and “xAK” denote CMAQ NO2 column densities with and without the averaging kernel, respectively.
DS+AK
AK
DS
What’s wrong with GOME-2 AK?

## Slide 15: Averaging Kernel (bottom layer)
Daily snapshots
GOME-2
OMI

## Slide 16: Reconstruction of surface NO2 concentration
where α is an additional adjustment due to satellite and model uncertainties.
For perfect model and satellite, α=1.
Satellite inferred surface NO2 concentrations

## Slide 17: Reconstructed NO2 [OMI]
CMAQ
Bias = -3.73
RMSE=5.03
R=0.86
AK
Bias = -3.59
RMSE=5.56
R=0.76
DS
Bias = -3.03
RMSE=4.63
R=0.86
DS & AK
Bias = -2.59
RMSE=4.31
R=0.86

## Slide 18
Reconstructed surface NO2 concentrations using OMI column densities and CMAQ column-to-surface ratios at 13:30 local time in 2008.

## Slide 19: Reconstructed NO2 [GOME-2]
CMAQ
Bias = -3.66
RMSE=6.14
R=0.84
AK
Bias = 0.64
RMSE=7.18
R=0.82
DS
Bias = 1.84
RMSE=6.62
R=0.87
DS & AK
Bias = 11.38
RMSE=18.48
R=0.86

## Slide 20
Reconstructed surface NO2 concentrations using GOME-2 column densities and CMAQ column-to-surface ratios at 09:30 local time in 2008.

## Slide 21
OMI with α=1.37
Bias = 0, RMSE=4.31, R=0.86
GOME-2 with α=0.88
Bias = 0, RMSE=6.62, R=0.87

## Slide 22: Conclusion
A conservative downscaling was designed to enhance the spatial resolution of satellite measurements by applying the fine-scale spatial structure from the model, with strict mass conservation at each satellite footprint pixel level.
With the downscaling approach, NO2 column densities from the OMI (13×24 km) and the GOME-2 (40×80 km) show excellent agreement with the CMAQ (4×4 km) NO2 column densities, with R = 0.96 for OMI and R = 0.97 for GOME-2.
We further reconstructed surface NO2 concentrations by combining satellite column densities and simulated surface-to-column ratios from the model. Compared with AQS surface observations, the reconstructed surface concentrations show a good agreement; R = 0.86 for both OMI and GOME-2.
Limitation in using current GOME-2 AK is also discussed.