## Slide 1: Estimating smoke emission using GOES satellite observations and HYSPLIT model
Tianfeng Chai1,2,3, Hyuncheol Kim1,2,3, and Ariel Stein1
1: NOAA/OAR/Air Resources Laboratory (ARL)
2: Cooperative Institute for Climate & Satellites-Maryland (CICS-MD)
3: University of Maryland, College Park, MD

## Slide 2: Motivation
Smoke from wildfires has significant negative impacts on public health;
The air quality forecast quality is greatly hindered by the large uncertainties of the wildfire emission estimates;
We aim to objectively and optimally estimate the fire sources based on the satellite observations of the fire plumes and HYSPLIT model.
Thick smoke from wildfires fills the air as a motorist travels on Hwy. 27 between Vanderhoof and Fort St. James, B.C., on Wednesday, August 15, 2018. DARRYL DYCK / CP
https://vancouversun.com/news/local-news/b-c-wildfires-2018-air-quality-in-vanderhoof-double-hazardous-levels
Air quality in several B.C. communities is listed as ‘hazardous’ due to wildfire smoke. AirVisuals

## Slide 3: Smoke forecasts with HYSPLIT: Current status
Smoke column from the HYSPLIT model (blue) and NESDIS Hazardous Mapping System (orange)
NOAA NESDIS HMS Smoke and fire detection
Incorporates imagery from NOAA and NASA satellites (GOES-West, GOES-East, Terra/Aqua MODIS, AVHRR on NOAA-15/-18/-19)
Provides fire locations, starting time, durations
USFS’s BlueSky: Estimate PM2.5 emissions and plume rise
Emission aggregated and assumptions are made to for the forecasting period
Operational since March, 2007

## Slide 4: NOAA NESDIS GOES Aerosol/Smoke products (GASP)
The GASP product is a retrieval of the Aerosol Optical Depth (AOD) made from the current GOES West/East visible imagery. Satellite measured aerosol optical depth (AOD) is available at a 30-minute interval and 4 km X 4 km spatial resolution during the sunlit portion of the day. (http://www.ssd.noaa.gov/PS/FIRE/GASP/gasp.html)
Can we objectively and optimally estimate the fire sources based on the satellite observations of the fire plumes, instead of using BlueSky to estimate the emissions?

## Slide 5: Methodology
An independent HYSPLIT simulation starting at each HMS fire location with given starting time and duration is run with unit source, at several possible release height to generate a Transfer Coefficient Matrix (TCM).
Source terms are solved by minimizing a cost function built to mostly measure the differences between model predictions and observations, following a general data assimilation approach.
Hourly gridded GASP

## Slide 6: HYSPLIT inverse modeling
1. Fukushima source term estimation
2. Volcanic ash application-Kasatochi eruption
Ref: Source term estimation using air concentration measurements and a Lagrangian dispersion model–Experiments with pseudo and real cesium-137, T Chai, R Draxler, A Stein – Atmos. Environ., 2015
Ref: Imprvoving volcanic ash predictions with the HYSPLIT dispersion model by assimilating MODIS satellite retrievals
Chai, T., A Crawford, B Stunder, MJ Pavolonis, R Draxler, A Stein
Atmos. Chem. Phys. 17, 2865-2879

## Slide 7: Twin experiments
In twin experiments, known wildfire sources are released to generate smoke plumes. Then pseudo-observations (satellite mass loadings) are generated based on the HYSPLIT simulation results ;
With exact solutions available, the inverse algorithm can be fully evaluated.
Hourly, at 0.5ox0.5o resolution
9 fire locations, constant releases each day for 2 days from 6Z on 8/17/15, at 1500m or 2000m, MET: gdas1

## Slide 8: NASA WORLDVIEW – Corrected reflectance (true color) Aqua & Terra MODIS
8/17/2015
8/18/2015

## Slide 9: Case 1:
All 48 hourly non-zero mass loadings are assumed retrieved accurately;
ln(qik) as control variables to avoid negative emission results;
First guess is 105kg/hr at all location/height;
Background term effect is minimized with extremely large uncertainty given ;
Observations uncertainties at 10% M + 0.003kg/m2;
Minimization stops after cost function reduced to be 10-6Finit.
Case 1 result
Actual sources

## Slide 10: Source term error statistics
 | Source term | MAE (kg/hr) | Normalized MAE | RMSE (kg/hr) | Normalized RMSE
Case 1 | Day 1 | 534.9 | 0.77% | 841.4 | 1.21%
 | Day 2 | 1760.5 | 2.53% | 3332.5 | 4.78%
Case 2 | Day 1 | 1985.8 | 2.85% | 3310.2 | 4.75%
 | Day 2 | 1393.0 | 2.00% | 2943.2 | 4.22%
48 hr observations 24 hr observations
Case 2: Remove 1st day observations from Case 1

## Slide 11: Spatial coverage
 | Source term | MAE (kg/hr) | Normalized MAE | RMSE (kg/hr) | Normalized RMSE
Case 3 | Day 1 | 606.4 | 0.87% | 1156.3 | 1.66%
 | Day 2 | 301.2 | 0.43% | 573.4 | 0.82%
Case 4 | Day 1 | 23834.6 | 34.21% | 32157.9 | 46.16%
 | Day 2 | 66177.5 | 94.99% | 78653.3 | 112.90%
Case 5 | Day 1 | 3974.9 | 5.71% | 8803.3 | 12.64%
 | Day 2 | 3400.6 | 4.88% | 10663.2 | 15.31%
Case 3 | Day 2 observations, w/o Region A
Case 4 | Day 2 observations, w/o Region B
Case 5 | Day 2 observations, w/o Region C
Source term error statistics

## Slide 12: Observation errors
 | Source term | MAE (kg/hr) | Normalized MAE | RMSE (kg/hr) | Normalized RMSE
Case 6 10% | Day 1 | 1448.6 | 2.08% | 2259.7 | 3.24%
 | Day 2 | 4418.7 | 6.34% | 11121.8 | 15.96%
Case 7 | Day 1 | 2105.8 | 3.02% | 3954.7 | 5.68%
20% | Day 2 | 8567.9 | 12.30% | 22884.4 | 32.84%
Case 8 | Day 1 | 6227.6 | 8.94% | 12047.1 | 17.29%
50% | Day 2 | 22034.5 | 31.63% | 67298.2 | 96.60%
Case 9 | Day 1 | 10104.2 | 14.50% | 19759.9 | 28.36%
100% | Day 2 | 34560.9 | 49.61% | 131203.9 | 188.33%
Source term error statistics
2nd day observations only;
without spatial blocking;
Gaussian-distributed errors are added to pseudo observations.

## Slide 13: HYSPLIT-based Emission Inverse Modeling System
HYSPLIT
BlueSky
TCM
Cost Function
Minimization
NOAA ARL
NOAA NESDIS
USDA Forest Service
Adjusted
Fire Emissions
First guess
Constrain
HMS
GASP
ASDTA
Fire detection
(Location/Time)
AOD
Fuel-loading based fire emissions system

## Slide 14
Observed fire events in southeastern US on November 10, 2016. MODIS truecolor image is shown in left panel, and MODIS, GASP, ASDTA aerosol optical depths are shown in right panel. Red circles indicate locations of wildfires detected by HMS.
GASP: GOES Aerosol/Smoke Product
ASDTA: Automated Smoke Detection and Tracking Algorithm

## Slide 15
Observed wildfire events for the study during November 10-17, 2016. MODIS truecolor images, MODIS AOD, GASP AOD, and ASDTA AOD are shown.

## Slide 16
Scatter plot comparison between initial and assimilated particulate matter concentrations (10-10 kg/m3 ) using adjusted fire emissions during November 10-17, 2016

## Slide 17: Performance evaluation - Statistics of modeled smoke particulate concentration (10-10 kg/m3) using initial and top-down fire emissions
 |  | Nov. 10 | Nov. 11 | Nov. 12 | Nov. 13 | Nov. 14 | Nov. 15 | Nov. 16 | Nov. 17
 | Observation | 70.28 | 78.72 | 93.45 | 102.99 | 77.62 | 54.44 | 47.35 | 56.13
mean | Initial | 7.42 | 49.93 | 34.28 | 30.58 | 24.75 | 19.84 | 6.85 | 0.59
 | Top-down | 42.05 | 61.88 | 57.85 | 61.12 | 53.49 | 33.72 | 23.10 | 26.94
RMSE | Initial | 73.34 | 118.20 | 93.68 | 11.53 | 69.63 | 46.56 | 50.49 | 61.22
 | Top-down | 51.43 | 46.50 | 68.14 | 72.44 | 51.87 | 39.28 | 40.61 | 43.69
Slope | Initial | 0.41 | -2.81 | 1.22 | 1.54 | 0.82 | 1.04 | -0.45 | 0.04
 | Top-down | 1.16 | 1.08 | 1.15 | 1.30 | 1.14 | 1.24 | 1.06 | 1.32
R | Initial | 0.28 | -0.16 | 0.11 | 0.09 | 0.2 | 0.09 | -0.08 | 0.1
 | Top-down | 0.49 | 0.35 | 0.40 | 0.46 | 0.4 | 0.15 | 0.3 | 0.44

## Slide 18
Spatial distributions of reconstructed fire particulate matter column concentrations (10-10 kg/m3 ) using top-down estimated wildfire emissions.

## Slide 19: Summary and future direction
  Wildfire emission inversion has been built based on HYSPLIT model, its TCM, and a cost function;
  With pseudo observations generated using HYSPIT model simulations (twin experiments), true emissions (release height and emission rate) can be recovered;
  A case study using real GOES data has been performed;
  High resolution GOES-16 data will be tested;
  More evaluation will be performed using VIIRS AOD and surface PM2.5 observations;
  Model uncertainty will be included in the HYSPLIT inversion system.

## Slide 20
Thank you!
This work is funded by NOAA Award NA16OAR4590121

## Slide 21: Twin experiments