## Slide 1: CMAQ 5.2.1 PARALLEL PERFORMANCE WITH MPI AND OpenMP George Delic, Ph.D., HiPERiSM Consulting, LLC
Introduction
This presentation reports on implementation of the parallel sparse matrix solver, FSparse, in the Chemistry Transport Model (CTM) in CMAQ [1]. This release is v6.3 and is a major redesign. It is applicable in the CMAQ version that uses either the Rosenbrock (ROS3) or SMV Gear (GEAR) [2] algorithms in the CTM.
Test Bed Environment
The hardware systems chosen were the platforms at HiPERiSM Consulting, LLC. This heterogeneous cluster consists of 128 cores across two nodes with dual Intel E5v3 CPUs (16 cores each), and eight nodes on an HP blade server populated with dual E5640 CPUs (4 cores each). This report implemented the Intel Parallel Studio® suite (release 17.6) and Portland CDK (release 18.1).
Profile of CMAQ processes
For a profile of where time is consumed Fig.1 compares the fraction of total wall clock time expended in the dominant science processes in CMAQ for one MPI process. The CHEM process is the Gear (GEAR) version of the CTM. The EPA version is compared with the FSparse threaded version for 8, 12, and 16 OpenMP threads, as identified in the legend. As the fraction of time in CHEM decreases the fraction of time in the other science processes increases.
Results
[1] Delic, G., 2016: see presentation at the Annual CMAS meeting ( http://www.cmasecenter.org ).
[2] Jacobson, M. and Turco, R.P., (1994), Atmos. Environ. 28, 273-284.
Key Observations
MPI communication
MPI communication time tends to compete with, or exceed, computation time.
MPI scaling increases with process count
Corresponding to this MPI parallel efficiency decreases
Computation
CHEM is by far the dominant science process in CMAQ computation time (Fig. 1)
Scalar computation time dominates, or competes with, OpenMP computation time (Fig. 3)
The scalar computation fraction (of total time) dominates whenever the MPI communication fraction is greater than 12%
The OpenMP computation fraction dominates when the MPI communication fraction is less than 12%
Hybrid parallel algorithm
Thread speedup reaches 1.42 with 8 threads (Fig. 2)
Hybrid MPI+OpenMP algorithms that offer more on-node compute intensity as the number of available threads rises (in Fig. 4 note the 1.5 times performance boost with 16 vs 8 threads)
Fig. 4: Parallel thread speedup over the standard U.S. EPA model using the Intel compiler in 288 calls to CHEM with GEAR solver for 8, 12 and 16 threads, for NP=1 MPI process in the 24 hour episode.
References
Figure 1: Fraction of wall clock time (percent) by science process for the FSparse GEAR version of CMAQ for NP=1 and OpenMP thread counts of 8, 12, and 16.
Figure 2: This shows OpenMP speedup with 8 threads for the GEAR solver in the thread parallel version over the standard U.S. EPA model using the Intel compiler for various combinations of nodes.
Figure 3: For the 8 thread FSparse version of CMAQ this compares the fraction of total time (percent) spent in MPI message passing, OpenMP computation region, and scalar computation region with the Intel compiler for various combinations of nodes.
Conclusions
This report has described an analysis of CMAQ 5.2.1 behavior in the standard U.S. EPA release and a new thread parallel version of CMAQ suitable for the Rosenbrock and Gear solvers. In this version (v6.3) subroutines common to both algorithms have been successfully developed and tested in the Gear case.
The new FSparse version of CMAQ offers layers of parallelism not available in the standard U.S. EPA release and is portable across multi- and many-core hardware and compilers that support thread parallelism.
Fig. 1
Fig. 2
Fig. 3
FSparse CMAQ thread speedup
Fig. 2 shows the speedup of the OpenMP version over the EPA release which peaks at 1.42. The horizontal axis shows the number of MPI processes, and the multiple values are for differing combinations of participating nodes of the cluster. Variability for any fixed value of NP is determined by how many processes are resident on the two fastest nodes, versus the number on the eight blade nodes. Grid cells are partitioned into blocks of size 50 and these blocks are distributed to threads in a thread team in the OpenMP version (which is limited to 8 per MPI process).
Computation vs communication
Intel trace tools allow instrumentation that measures the fraction of run time expended in MPI message passing versus computation. In the latter case trace instrumentation also separates scalar and thread parallel computation fractions. Fig. 3 shows this summary for the FSparse version of CMAQ. More than 20% of the time is spent in MPI message passing at larger NP values. The exceptions are for cases when MPI processes reside on the fastest nodes where MPI communication is predominantly via on-node memory, and not the interconnect fabric.
Numerical issues
Concentration values for 11 selected species (O3, NOx, etc) were compared for the entire domain and all 24 time steps. Examples of such a comparison is the difference in predicted concentrations. To within the tolerances required in GEAR (ATOL=1.0e-09, RTOL=1.0E-03), agreement was observed.
Chart: 
| 4 | 4 | 4 | 4 | 8 | 8 | 8 | 8 | 8 | 8 | 16
OMP8 | 1.1601 | 1.3661 | 1.3514 | 1.4188 | 0.83687 | 1.3257 | 1.2803 | 1.2362 | 1.3541 | 1.2865 | 1.1443
Chart: 
| 4 | 4 | 4 | 4 | 4 | 8 | 8 | 8 | 8 | 8 | 8 | 16
MPI | 8.5 | 27.7 | 19.3 | 11.7 | 7.1 | 33 | 42.7 | 47 | 22.7 | 32.9 | 33.9
OpenMP | 50 | 31.7 | 34.6 | 37.7 | 60.3 | 30.6 | 25.4 | 22.1 | 31.8 | 26.8 | 32.9
Scalar | 41.5 | 40.6 | 46.1 | 50.6 | 32.6 | 36.4 | 31.9 | 30.9 | 45.5 | 40.3 | 33.2
Chart: 
| CHEM | AERO | VDIFF | HADV | ZADV | CLDPROC
EPA | 70.2655 | 16.8742 | 7.129 | 2.1844 | 1.783 | 1.1009
omp8 | 61.6145 | 17.5234 | 11.3824 | 4.1074 | 2.2886 | 1.5572
omp12 | 55.787 | 20.7116 | 12.2916 | 4.8589 | 2.7047 | 1.8404
omp16 | 50.6743 | 22.1514 | 14.4123 | 5.1997 | 3.2753 | 2.356
Chart: