## Slide 1: Updates and Improvements to 2023 and 2028 Emission Inventory Projections
Caroline Farkas, Alison Eyth, Jeff Vukovich
October 22, 2019
Notes: Projections are created from the emissions modeling platform base year to support policy and regulation research and evaluation

## Slide 2
The views expressed in this presentation are those of the author(s) and do not necessarily represent the views or policies of the Agency.
Disclaimer

## Slide 3: Outline
Why develop projected emission inventories?
How do we project emissions?
2016 Collaborative Emissions Modeling Platform
Pollutant-Sector Comparison
Projections for Various Sectors

## Slide 4: Why develop projected emission inventories?
To evaluate policy options and impacts of changing emissions and use the results in a relative sense
EPA develops Regulatory Impact Analyses (RIAs) for regulations
  Describe the potential social benefits and social costs
Interstate transport: The Clean Air Act’s "good neighbor" provision requires EPA and states to address interstate transport of air pollution that affects downwind states' ability to attain and maintain National Ambient Air Quality Standards (NAAQS)
Other types of analyses: regional haze, etc.

## Slide 5: How do we project emissions?
Models are used to project some sectors (e.g., electric generating units (EGUs), nonroad, onroad)
Projection factors are developed for many sectors based on the U.S. Energy Information Administration’s (EIA) Annual Energy Outlook (AEO)
  AEO is a rich data source with 30 year forecasts of U.S. energy markets
  Sectors: non-EGU point, nonpoint, onroad activity, oil and gas
Known federal, state, and local regulations and control technology requirements are implemented as “control factors”
Meteorology is kept the same as the base year
  Base year fire and biogenic emissions are used in future years

## Slide 6: 2016v1 Platform Projections
The projection of 2016v1 emissions was a collaborative process with heavy involvement from sector workgroups
  Includes data provided by Federal, State, and Local agencies and Regional Organizations
  Updated data were due by May 31, 2019
Projected inventories released early October
  https://www.epa.gov/air-emissions-modeling/2016v1-platform
  Future year scripts and air quality model-ready files coming soon
First public projections since 2011 platform

## Slide 7
Notes: Emissions of SO2 are predicted to decrease – especially from EGUs

## Slide 8
Notes: Emissions of NOx are predicted to decrease – especially for EGUs, onroad, and nonroad

## Slide 9
Notes: Emissions of VOCs are dominated by biogenic processes, but onroad VOC emissions are predicted to decrease

## Slide 10
Notes: Ammonia emissions are projected to increase – especially from agriculture

## Slide 11: Electric Generating Units (EGUs)
Two options are available for future year EGUs:
  Eastern Regional Technical Advisory Committee (ERTAC) EGU model v16.0
  EPA’s Integrated Planning Model (IPM) version 6, May 2019 case
New for 2016v1 platform projections
  Recent closures and committed units have been incorporated
  ERTAC
    New CAMD data
  IPM
    Adjustments to SO2 emission factors for coal units
    Updated methodology for PM post-processing that makes base and future year PM more consistent for units operating similarly

## Slide 12
2028 EGU SO2 Emissions and Changes from 2016
Notes: EGU county projection map

## Slide 13: Onroad Emissions
Projected by combining emission factors from the Motor Vehicle Emissions Simulator (MOVES) with year-specific activity data
New for 2016v1 platform projections
  Projections of vehicle age distributions now reflect the dip in vehicle counts that resulted from reduced car sales during the economic recession
  AEO 2019 to project vehicle miles traveled (VMT)
  Hoteling hours reduced based on new factors for combination long haul truck VMT on restricted highways
  State/local agencies provided updated inputs
California provided emissions for base and future years

## Slide 14
Example Base and Future Year Age Distributions for Passenger Cars
Notes: Notice the dip for the recession moving back in time as the year modeled is later

## Slide 15: Total Onroad NOx 202x-2016
2023 v1 Onroad total NOx
2028 v1 Onroad total NOx
2023 minus 2016 v1 NOx
2028 minus 2016 v1 NOx

## Slide 16: Nonroad Projections: 2016v1
Declines in emissions from 2016 to 2028 are the result of equipment turnover  newer, cleaner engines are projected to dominate the market in future years
Nonroad engine regulations driving emissions reductions include:
  Tier 4 standards for nonroad diesel engines (starting in 2008)
  Emission standards for new nonroad spark-ignition engines, equipment, and vessels (starting in 2010)
-61.6%
-61.9%
-10.5%
-25.8%
-9.2%
+21.5%
-13.6%
-70.6%
-68.8%
+5.0%
-30.2%
-37.9%
-30.4%
-59.2%

## Slide 17: Oil and Gas Projections
Point Oil and Gas sources
    Production-related sources: used State historical data and AEO 2019
    Exploration-related sources: used a four year average of 2014-2017 exploration activity (instead of 2 year average in beta version)
    Transmission-related sources: used factors based on AEO 2019
Nonpoint Oil and Gas sources
    Exploration-related sources: used 4-year average emission dataset
    Production-related sources: used State historical data and AEO 2019
Federal and state-level controls
  New source performance standards (NSPS) for oil and gas, reciprocating internal combustion engines (RICE), natural gas turbines, and process heaters
  Reasonably Available Control Technology (RACT) in Pennsylvania, and updates to natural gas transmission compressors in New Jersey
Western Regional Air Partnership (WRAP) Oil and Gas inventory has been provided and is being reviewed

## Slide 18
Texas Oklahoma Kansas Louisiana Arkansas Mississippi
Colorado New Mex. Wyoming N.Dakota Utah Montana California
Green: 2016v1
Orange: 2023v1
Red: 2028v1
Penn. W.Virginia Louisiana Kentucky Illinois Michigan Virginia
2028-2016 NOx nonpoint Oil and Gas percent difference
Nonpoint Oil & Gas NOx emissions comparison
Notes: O&G plot?

## Slide 19
Point Oil & Gas NOx emissions
Texas Oklahoma Louis. Kansas Arkansas Miss. Nebraska
CO NM WY ND CA UT AZ MT ID WA SD OR NV
Green: 2016v1
Orange: 2023v1
Red: 2028v1
Notes: O&G plot?

## Slide 20
Residential
Wood
Combustion difference maps
VT and NC submitted edits for v1
CA, OR, WA have no growth for future year scenarios
Largest decreases in projections are from indoor wood non-EPA certified furnaces

## Slide 21: Projections for Other Sectors
Area fugitive dust (afdust) projections
  Unpaved road dust emissions are held constant (instead of growing them in future years)
Nonroad emission projections
  Texas provided future-year nonroad emissions for v1
Rail projections updated
  2016v1 method uses emission factor trend derived from recent rail inventory efforts

## Slide 22: Questions?
Access 2016, 2023, and 2028 modeling platform and emission inventories: https://www.epa.gov/air-emissions-modeling/2016v1-platform
Thank you to our collaborators!

## Slide 23: Changes in future year emissions carried over from work on 2017NEI
Ag Livestock Waste Emissions
  2017 National Emissions Inventory (NEI) data used in 2016v1 corrected a past underprediction of animal counts for dairy cows, poultry
Airport Emissions
  2017 NEI estimates emissions using Aviation Environmental Design Tool (AEDT), but projections are still based on the Terminal Area Forecast (TAF)
Onroad Age Distributions
  CRCA-115 VIN decode project
Nonroad MOVES setup
  Month and spatial allocations of snowmobiles in UT
  Recreational marine allocations in WA
  Updated equipment pops. in AZ, UT, CT
Commercial Marine Vessel (CMV) Inventory

## Slide 24
2016
2023
2028
2016
2016
2016
2023
2023
2023
2028
2028
2028