## Slide 1: Mutual comparison of source sensitivities and apportionments obtained by BFM, DDM, and ISAM on PM2.5 and ozone concentrations over Japan
Satoru Chatani1, Hikari Shimadera2,
Syuichi Itahashi3, and Kazuyo Yamaji4
1 National Institute for Environmental Studies
2 Osaka University
3 Central Research Institute of Electric Power Industry
4 Kobe University
The 18th Annual CMAS Conference
Oct 23, 2019
Chapel Hill, North Carolina - United States

## Slide 2: Background
Ozone
  Little change
  0% attainment
PM2.5
  Gradually declining
  Non-attainment in some areas
  Mainly secondary components
Need effective strategies to reduce precursors

## Slide 3: J-STREAM
Japan's Study for Reference Air Quality Modeling
  (J-STREAM)
Regional model inter-comparison
  Evaluate ranges of results simulated by participating models
  Seek optimal model configurations for better model performance

## Slide 4: Influence of emission sources
Essential information to consider effective strategies
Source sensitivity
  Brute Force Method (BFM)
  High-order Decoupled Direct Method (HDDM)
Source apportionment
  Integrated Source Apportionment Method (ISAM)
Mutual comparison
  To appropriately understand implications

## Slide 5: Methodology
Regional meteorological model
  WRF-ARW version 3.7.1
Regional chemical transport model
  CMAQ version 5.0.2
Target period
  2 weeks in 4 seasons in FY2016
Target domains
d01 (45 x 45 km)
d02 (15 x 15 km)
BCON
Tokyo

## Slide 6: Input datasets
Boundary concentration
  CHASER (Sudo et al., 2001)
cb05tucl_ae6_aq
Emissions:
Area | Source | Data
Asia | Anthropogenic Ship | HTAP version 2.2 (Janssens-Maenhout et al. 2015) + Recent changes (Zheng et al., 2018)
 | Biogenic | MEGAN version 2.1 (Guenther et al., 2012)
 | Volcano | AeroCom (Diehl et al., 2012)
 | Biomass burning | GFED version 4.1s (van der Werf et al. 2017)
Japan | Transportation | MOEJ PM2.5EI
 | Ship | OPRF
 | Other anthropogenic | J-STREAM (Chatani et al., 2018)
 | Biogenic | MEGAN version 2.1 + Japanese vegetation (Chatani et al., 2017)
 | Volcano | JMA

## Slide 7: Target sectors
-20% perturbations in BFM (x 5 to show results)
Group | Sector
s01 | On-road vehicles
s02 | Ships
s03 | Non-road transport (machineries, railways, and airplanes)
s04 | Stationary combustion (power plants, industries, and commercial)
s05 | Biomass combustion (smoking, cooking, and agricultural residue burning)
s06 | Residential
s07 | Fugitive volatile organic compounds
s08 | Agriculture (except for residue burning) and fugitive ammonia
s09 | Natural (volcanoes, and biogenic)
s10 | Other countries in d02
s11 | Transport through boundaries of d02
s12 | Sea salt

## Slide 8: Mean O3 distributions
Spring
Summer
Autumn
Winter

## Slide 9: Mean PM2.5 distributions
Spring
Summer
Autumn
Winter

## Slide 10: Sensitivity and apportionment for O3
Overwhelming influence of transport through boundaries
Smaller or negative sensitivities of domestic sources
Similar sensitivities by BFM and HDDM
HDDM results obtained only for winter

## Slide 11: Maps of sensitivities and apportionments
O3 s04 ISAM Sum.
O3 s04 BFM Sum.

## Slide 12: Sensitivity and apportionment for PM2.5
Large influence of transport through boundaries
Higher sensitivities than apportionments

## Slide 13: Sensitivity and apportionment for EC and POA
Consistent sensitivities and apportionments for inert components

## Slide 14: Sensitivity and apportionment for SO42-
Different sectoral contributions to sensitivities and apportionments
  Origins of S obtained by ISAM
  Larger sensitivity of transport through boundaries

## Slide 15: Maps of sensitivities and apportionments
SO42- s11 ISAM Spr.
SO42- s11 BFM Spr.
SO2 s11 BFM Spr.
(equivalent to SO42-)

## Slide 16: Sensitivity and apportionment for NO3-
Significant nonlinearities in sensitivities
Large sensitivity of NH3 sources on NO3-
Large sensitivity of transport through boundaries due to oxidation and partitioning

## Slide 17: Sensitivity and apportionment for NH4+
Features similar to NO3-
Large sensitivity of NOX sources on NH4+

## Slide 18: Dependence of O3 on NOX and VOC
Similar dependences on VOC in apportionments by ISAM and sensitivities by BFM
Large differences of dependences on NOX
(for s01)

## Slide 19: Maps of dependences on NOX and VOC
O3 s01-NOx ISAM Sum.
O3 s01-VOC ISAM Sum.
O3 s01-NOx BFM Sum.
O3 s01-VOC BFM Sum.

## Slide 20: Summary
Sensitivities and apportionments are consistent for inert species.
Significant nonlinearities appear in sensitivities of secondary species.
  Smaller or negative sensitivities of domestic NOX sources on O3.
  Different attributions of SO42- in apportionments and sensitivities.
  Mutual dependences of NOX and NH3 sources in sensitivities on NO3- and NH4+.
It is important to evaluate sensitivities for considering effective strategies taking nonlinear changes in concentrations into account.

## Slide 21: Acknowledgement
The study was supported by the Environment Research and Technology Development Fund (5-1601) of the Environmental Restoration and Conservation Agency.
Thank you
for your attention

## Slide 23: Model performance on O3

## Slide 24: Model performance on PM2.5