## Slide 1: Impact of using detailed-level marine emissions on Canadian Air Quality
Air Quality Policy-Issue Response Section (REQA)
Rabab Mashayekhi
Mourad Sassi
Calin Zaganescu
Radenko Pavlovic
Integrated Transportation Policy Section
Navin Sundar
Environment and Climate Change Canada (ECCC)

## Slide 2: Motivations
13% of total NOX emissions in Canada are from Commercial Marine Vessels.
Improve SMOKE inputs for Canadian marine emissions:
  Emissions inventory files
  Spatial and temporal allocations files
Evaluate the impact of point sources marine emissions on air quality.

## Slide 3: Canada’s Marine Emissions Inventory Tool (MEIT 2015)
Developed by Transportation section of ECCC.
Bottom-up, activity-based inventory.
All marine vessels operating in Canadian waters. (15 ship classes; 69 sub-class)
High temporal, spatial resolution (1-km gridded, linked-based).
Allocated in 22 MEIT regions.

## Slide 4: SMOKE-Ready Inventory
1-km aggregated to 3-km.
69 ship types aggregated to 15 ship classes.
Mapped in SCCs (ship class, fuel type and operating mode).
Link-based hourly data aggregated to monthly emissions.
Assigned stack parameters (height: 20m, diameter: 1m, velocity: 20m/s, temperature:275C).
Two types of inventory files (point and area).
15 surrogates generated for each ship class (using annual fuel consumptions)

## Slide 5: Ship-class based Surrogates
Barge
Coast Guard
Cruise
DFO Fishing
Excursion passenger
Fishing
INNAV Test Vessels
Merchant Bulk
Merchant Container
Merchant Other
Merchant Passenger
Special Purpose
Tanker
Tug
War

## Slide 6: AQ-Model Ready Emissions (NO; g/s)
September 4 at 14 UTC
Point source
Area source

## Slide 7: GEM-MACH simulation Global Environmental Multi-scale Modeling Air Quality and Chemistry
ECCC’s operational regional air quality model.
In-line Chemistry Transport Model.
10-km grids, 80 vertical levels up to 0.1hPa.
Other anthropogenic emissions (2015 Canadian APEI; 2017 USA projected from NEI 2011, Mexico 2008)
Summer episode (June to September 2017).

## Slide 8: 2017 Summertime Average NO2 (ppb)
treating marine emissions as point sources reduces the surface NO2 concentration (up to 15%)
Point - Area

## Slide 9: Mean bias; NO2
Point - Area
Point - Area

## Slide 10: Mean bias; NO2
Point - Area
Point - Area

## Slide 11: East Canada
Per-hour average NO2 (ppb)
Observation
Marine as point
Marine as area

## Slide 12: East Canada
Per-hour average NO2 (ppb)
Observation
Marine as point
Marine as area

## Slide 13: East Canada; NO2 (ppm)
Halifax
St. John
Quebec
Observation
Marine as point
Marine as area

## Slide 14: West Canada
Observation
Marine as point
Marine as area
Per-hour average NO2 (ppb)

## Slide 15: West Canada
Observation
Marine as point
Marine as area
Victoria
Vancouver

## Slide 16: 2017 Summertime 8-h Average O3 (ppb)
Point - Area

## Slide 17: 2017 Summertime 8-h Average O3 (ppb)
Point - Area

## Slide 18: 2017 Summertime 8-h Average O3 (ppb)
Point - Area

## Slide 19: Hourly Score Statistics
Mean Bias | Canada |  | East-Canada |  | West-Canada | 
 | Point run | Area run | Point run | Area run | Point run | Area run
NO2 | 1.756 | 2.081 | 1.867 | 2.242 | 1.649 | 1.926
O3 | -1.479 | -1.731 | -0.330 | -0.560 | -3.249 | -3.534
RMSE | Canada |  | East-Canada |  | West-Canada | 
 | Point run | Area run | Point run | Area run | Point run | Area run
NO2 | 6.900 | 7.341 | 6.406 | 6.926 | 7.346 | 7.720
O3 | 10.646 | 10.695 | 10.101 | 10.182 | 11.457 | 11.44

## Slide 20: conclusion
Upgrading emission platform using MEIT 2015 is an improvement in marine emissions processing.
There is an overall improvement in NO2 and O3 by processing marine emissions as point sources.

## Slide 21
THANK YOU