## Slide 1: Application of Data Fusion for Improved Background Ozone Estimates
Nash Skipper, Talat Odman, Yongtao Hu, Petros Vasilakos, Armistead (Ted) Russell
School of Civil and Environmental Engineering, Georgia Institute of Technology, Atlanta, Georgia, USA
18th Annual CMAS Conference
October 2019
Chapel Hill, North Carolina

## Slide 2: Ozone in the United States
US ozone air quality standard set to 70 ppb in 2015
Background ozone (BGO) may take up a significant portion of the standard
  BGO – the hypothetical ozone concentration that would be observed with no anthropogenic emissions
    US BGO – Ozone concentration with no US anthropogenic emissions
    Of interest for regulatory purposes (see Draft Ozone ISA)
As anthropogenic emissions are reduced and as air quality standards are (potentially) strengthened, accurate BGO estimates will become increasingly important to informing ozone control strategies

## Slide 3: Background Ozone
Different types depending on the purpose
  Global background, North American background, US background, etc.
US BGO originates from non-controllable ozone sources such as stratosphere-troposphere exchange, wildfires, biogenic sources, and non-domestic pollution
US BGO typically estimated as 30-40 ppb, but may exceed 70 ppb in certain locations on some days
  Seasonally and geographically varying
Cannot be observed  use chemical transport models to estimate
Different CTMs provide different estimates, and models have biases  uncertainty
  Uncertainty of ±10 ppb for seasonal mean BGO; higher for individual days (Jaffe et al. 2018)

## Slide 4: Objective
Integrate modeled and observed ozone concentrations to develop improved estimates of background ozone
Run regional scale CTM (CMAQ) for base case (includes all emissions) and background case (zero US anthropogenic emissions) for 2017 at 36 km resolution
Use two estimates of boundary conditions for each case
  CMAQ default profile (static) BCs
  Dynamic BCs from Hemispheric CMAQ simulation
Separate base case ozone into background and US anthropogenic components
Apportion model error for each component using regression with observed ozone
Use results of regression to adjust modeled BGO to improve estimates

## Slide 5: Approach
US Anthropogenic Sources
International Sources
Chemical Transport Model
(CMAQ)
HCMAQ BCs
Static BCs
Natural Sources
Boundary Conditions
Emissions
Base Case O3
Background O3
Formed (US Anthropogenic) O3
= Base Case O3 – Background O3
Observed O3
Regression Model
Base Case
Background
Adjusted O3

## Slide 6: Boundary Conditions
More ozone at lower layers with static BC
  Still within about 10 ppb of one another
More ozone in upper layers with HCMAQ BC
  More accurate compared to ozone sonde data

## Slide 7: Model Results
Mean of 10 highest MDA8 ozone concentrations
Mean of same 10 days as Base Case
Formed = Base - Background
HCMAQ case results in greater concentrations for base and background for the highest ozone days
  Formed is fairly consistent
Ozone formed represents the enhancement of ozone above the background concentration due to US anthropogenic emissions

## Slide 8: Correlation of Ozone Components
O3 formed shows high agreement between the two BC cases (r=0.99)
BG O3 and O3 formed are negatively correlated
  O3 formed = base O3 – BG O3
  Correlation is stronger for Static BC
HCMAQ BG has stronger correlation with observations
Notes: Correlation coefficients

## Slide 9: Boundary Condition Effects
Plots show the comparison only at observation locations (N=379120)
Ozone formed is mostly consistent between the two BC cases
Most of the difference in the base cases is due to the background contribution

## Slide 10: Background and Formed Ozone
Difference in base case and difference in background case have a highly linear relationship
Difference in formed has a much weaker relationship with the difference in the base case
  Difference in formed is usually near zero
Notes: Red bar indicates one standard deviation from the mean.

## Slide 11: Ozone Regression Model
Develop a regression model for each BC case to estimate adjustment factors for background and formed ozone
    Let to calculate adjusted BGO
Variables included in regression for coefficients (αx):
  Longitude and latitude
  Elevation
  Day of year (transformed to sinusoidal function)
  Deviation of daily mean temperature from annual mean
  Daily mean cloud cover
  Daily mean RH

## Slide 12: Adjusted Base Case Ozone
Adjusted
CMAQ
Performance is improved compared to original CMAQ results
Fewer extreme high ozone outliers after adjusting
Improved performance  decreased uncertainty in background ozone prediction

## Slide 13: Adjusted Background Ozone
Mean of 10 highest MDA8 ozone days from Base Case
Improved agreement after applying adjustment factor
  CMAQ: R2 = 0.20
  Adjusted: R2 = 0.70
Information from the model is still retained after adjusting
  Fire impacts from HCMAQ southern boundary conditions
  Higher concentrations in western US with HCMAQ BC

## Slide 14: Regression Model Comparison – Background
Agreement of BGO estimates is greatly improved when adjustment factor is applied
Less variability in background ozone between BC cases  decreased uncertainty in background ozone prediction
Adjusted
Original CMAQ
Notes: Scatter plot shows comparison only at observation locations.

## Slide 15: Ozone Adjustment Ratios
O3 ratio = adjusted O3 / simulated O3
Adjustment to O3 formed is consistent for the two cases
Adjustment to BGO shows more differences
  More seasonal variation in HCMAQ case

## Slide 16: Ozone Adjustment Ratios – Annual Mean
Adjustment to O3 formed has a clear pattern
  High in the mountain west and southwest
  Low in the east
Adjustment to BGO has less spatial variation
Notes: Max/min refers to the maximum and minimum in US grid cells.

## Slide 17
BGO adjustment is higher in Winter and Spring
Spatial pattern of O3 formed adjustment is consistent across seasons

## Slide 18: Summary and Conclusions
Application of the adjustment factors resulted in improved agreement of background ozone estimates with different boundary conditions
  At observation sites, BGO correlation is improved from 0.58 to 0.92
  Across the entire model domain, BGO correlation is improved from 0.63 to 0.90
Adjustment of BGO follows a seasonal trend – higher in Winter/Spring
Adjustment of O3 formed shows a spatial pattern – higher in Southwest/Mountain West
Ozone adjustments resulted in decreased uncertainty in background ozone prediction due to:
  Improved performance in the base case
  Increased agreement of background ozone estimates

## Slide 19: Acknowledgements
Thanks to US EPA for providing Hemispheric CMAQ boundary conditions.

## Slide 20: Extra Slides

## Slide 21: Ozone Regression Model
Formulation of the model
  [O3] = [O3]bg*(αbg,0 + αbg,ΔT ΔT + αbg,X X + αbg,Y Y + αbg,Z Z + αbg,sin sin(ωd) + αbg,cos cos(ωd) + αbg,CLD CLD + αbg,RH RH)
  + [O3]formed*(αf,0 + αf, ΔT ΔT + αf,X X + αf,Y Y + αf,Z Z + αf,sin sin(ωd) + αf,cos cos(ωd) + αf,CLD CLD + αf,RH RH)
  + C
Let [O3]formed = 0 to calculate adjusted BGO
  Since [O3]formed represents the enhancement of ozone above the background level, it is neglected when calculating the adjusted BGO based on the regression model
ΔT = deviation from annual mean temperature
X = |longitude|/180
Y = |latitude|/90
Z = elevation in km
ω = 2π/365
d = day of year
CLD = cloud fraction (0-1)
RH = relative humidity (0-1)

## Slide 22: Regression Model Results
p > 0.05
Regression variables normalized to zero mean and unit variance
Term | HCMAQ BC |  | Static BC | 
 | αbg | αformed | αbg | αformed
constant (α0) | 0.4572 | 0.6633 | 0.4020 | 0.6974
αΔT | 0.0055 | 0.0410 | 0.0129 | 0.0845
αX | -0.0007 | 0.0135 | -0.0119 | 0.0337
αY | 0.0387 | -0.0383 | 0.0198 | -0.0294
αZ | 0.0058 | 0.0663 | 0.0139 | 0.0711
αsin | 0.1334 | -0.0621 | 0.0775 | -0.0112
αcos | -0.0082 | 0.0610 | -0.0313 | 0.0792
αCLD | -0.0238 | -0.5301 | -0.0195 | -0.5391
αRH | -0.0357 | -0.1456 | -0.0346 | -0.1445
Intercept | 19.1322 |  | 19.8428 | 
R2 | 0.58 |  | 0.57 | 
Term | HCMAQ BC |  | Static BC | 
 | αbg | αformed | αbg | αformed
constant (α0) | 0.4180 | 0.5769 | 0.3769 | 0.6283
αΔT | -0.0160 | 0.0848 | -0.0181 | 0.1495
αX | -0.0028 | 0.0336 | -0.0187 | 0.0708
αY | 0.0181 | -0.0078 | 0.0063 | -0.0030
αZ | 0.0457 | -0.0071 | 0.0537 | -0.0066
αsin | 0.1319 | -0.0571 | 0.0688 | 0.0048
αcos | -0.0250 | 0.0966 | -0.0580 | 0.1386
αCLD | -0.0497 | -0.1949 | -0.0369 | -0.2535
αRH | -0.0095 | -0.2575 | -0.0164 | -0.2423
Intercept | 22.2098 |  | 22.2458 | 
R2 | 0.64 |  | 0.64 | 
AQS + CASTNET monitors
CASTNET monitors only