## Slide 1: Estimation of Surface NO2 Using Airborne Remote Sensing Data and CMAQ Model Output from DISCOVER-AQ Campaigns
Kenneth Pickering1, Lok Lamsal2, Melanie Follette-Cook2, Dale Allen1, William Swartz3, Scott Janz4, Wyat Appel5, Gabriele Pfister6
1 Dept. of Atmospheric and Oceanic Science, University of Maryland
2 GESTAR, NASA Goddard Space Flight Center
3 Johns Hopkins University Applied Physics Laboratory
4 NASA Goddard Space Flight Center
5 EPA Center for Environmental Measurement and Modeling
6 ACOM, National Center for Atmospheric Research

## Slide 2: Motivation: Surface (“nose-level”) NO2 from airborne and satellite observations
There is strong interest in satellite-derived ground-level air pollutant products (NO2, PM2.5) for air pollution and health studies.
NO2 associated with mortality
(toxic gas at high concentrations; increases bronchitis and reduces lung function; a marker for combustion-related pollutants; major
precursor for tropospheric ozone)
Jaffe et al. [2003]
Insufficient NO2 monitoring by in situ sensors (heterogeneous coverage; some US states and many countries lack monitoring)
NO2 measurements from FRM in situ monitors are biased relative to true NO2 (biases (10-50%) vary diurnally/seasonally and are difficult to quantify)
Active NO2 Monitors – Oct. 2019
TEMPO geostationary satellite observations coming in 2022
(hourly fine horizontal resolution column NO2; need to prepare for
using these data to estimate surface NO2)
Relative
Risk
420 stations
Notes: NO2 is harmful to health.
It is important to know what the surface concentration is.
Surface measurement is challenging, due to insufficient surface network coverage, even in the US.
There are also known biases in in situ surface monitors.
This has led us to satellite and airborne remote sensing for better surface measurements.

## Slide 3: Satellites and ground-based monitors show similar* NO2 trends
OMI Trop NO2
EPA/AQS NO2
Lamsal et al. [2015]
*see Silvern et al. [2019] for recent trend (dis)agreement
Notes: We have been developing NO2 retrievals from OMI for a number of years.
Top row shows how trop VCDs have diminished over the US over Aura time period, with reductions in emissions.
A similar trend is seen in ground-based AQ monitors.
Although trend in the last few years has been more difficult to discern.

## Slide 4: Taking advantage of DISCOVER-AQ correlative observing strategy to enhance approach to inferring surface concentrations
Four deployments
  MD – Jul 2011
  CA – Jan/Feb 2013
  TX – Sep 2013
  CO – Jul/Aug 2014
Coordinated satellite, airborne column and in situ profile measurements, surface monitors, surface remote sensing, etc.
Multiple modeling simulations
Our goals:
  Develop science-quality NO2 data products from airborne and satellite sensors
  Assess and interpret various NO2 observations and simulations
  Improve approach to infer surface concentrations from remote sensing data
NASA Earth Venture mission intended to improve the interpretation of satellite observations to diagnose near-surface conditions related to air quality
Notes: Work today will utilize data and modeling simulations from the DISCOVER-AQ campaign.
D-AQ is an Earth Venture mission that took place over four intensive field campaigns, in MD, CA, TX, and CO.
D-AQ valuable because of its rich correlative data set, including satellite, airborne in situ and remote sensing, and surface monitors, etc.
Also multiple modeling simulations.
Our goals are to:
develop science-quality NO2 products from aircraft and satellites
assess and interpret various retrievals and simulations
improve approach to remote sensing of surface concentrations

## Slide 5: Aircraft remote sensing observations provide for retrieval of NO2 column densities
Slant column abundance retrievals based on the differential optical absorption spectroscopy (DOAS) method
NO2 vertical distributions from high-resolution Community Multiscale Air Quality (CMAQ) model simulations to account for the spatial/temporal variation in atmospheric NO2
Air mass factor (AMF) computations for conversion to vertical column density (VCD) using on-line VLIDORT, surface reflectivity from MODIS BRDFs, and CMAQ model profiles
VCDs validated with in situ airborne profiles and ground-based remote sensing observations
Lamsal et al. [2017]
ACAM NO2 VCD (below aircraft) from July 29, 2011 (MD)
 | Airborne Compact Atmospheric Mapper (ACAM) | GEO-CAPE Airborne Simulator (GCAS)
Campaign | MD, CA | TX, CO
Aircraft | UC-12 (MD), B200 (CA) | B200
Flight altitude | ~8 km | ~9 km
Ground spatial resolution | 1.5 x 1.1 km2 | ~250 x 250 m2
EDT
Notes: We are using airborne remote sensing from two instruments that flew during D-AQ (although today only focusing on ACAM during the MD campaign).
ACAM flew at ~8 km, observing scattered/reflected radiance from below.
Retrieval akin to OMI methodology, as stated in slide.
Example VCD retrieval in right plots, which have been validated with airborne in situ and ground-based remote sensing observations.

## Slide 6: WRF and CMAQ Model Simulations
 | Maryland | Texas | Colorado
Modeler | Wyat Appel - EPA | Dale Allen - UMD | Gabi Pfister - NCAR
Meteorological driver | WRF 3.8.1 | WRF 3.8.1 | WRF 3.8.1
WRF PBL scheme | ACM2 | ACM2 | YSU
Coupled WRF/CMAQ | yes | no | no
Nudging | FDDA, surface, obs. | FDDA, surface, obs. | FDDA, obs.
CMAQ version | 5.2 | 5.2 | 5.2 Beta
Chemical mechanism | CB6 | CB6r3 | CB6r3
Aerosol mechanism | AERO6 | AERO6 | AERO6
Horizontal resolution | 1 km (nested in 4 km) | 4 km (nested in 12 km) | 4 km (nested in 12 km)
Lightning NO emissions | no | yes | no
Anthropogenic emissions | NEI 2011 | CEMS; TCEQ | Colorado specific*
Meteorological IC/BC | NAM | NAM | ECMWF
Chemical IC/BC | GEOS-Chem | MOZART | RAQMS
* https://www.colorado.gov/airquality/tech_doc_repository.aspx?action=open&file=
FRAPPE-NCAR_Final_Report_July2017.pdf

## Slide 7: Surface concentration inferred from aircraft column retrievals and model vertical profile information
Model (blue)
Measurement (red)
Simple, intuitive case:
Accounting for spatial variability in the PBL:
Subscripts:
M, model
F, free troposphere
B, boundary layer
-
Results using mean
values of columns
for each site
Notes: The simplest approach to inferring surface concentration from ACAM VCDs is to scale them with the modeled ratio of surface concentration to VCD below aircraft.
The more complicated approach accounts for spatial variability in the PBL.
Thus, we use the more complicated formulation, which includes spatial inhomogeneity and model information on FT/PBL partitioning.

## Slide 8: Inferred surface concentrations correspond to aircraft VCDs
ACAM NO2 VCD from July 29, 2011 (MD)
ACAM-derived NO2 surface concentration
Lamsal et al. [2017]
July 29 was a very hot and high O3 day
EDT
EDT
Notes: Example of ACAM VCDs (from previous slide) and new surface concentration.
Correspondence over polluted regions shown.

## Slide 9: Aircraft VCDs, surface concentrations, and ground-based comparisons
Ground-based coincidence criteria: 5 km, 10 min
Essex
Fairhill
Edgewood
Padonia
CMAQ monthly mean
Time (h EDT)
Surface Concentration (ppbv)
Essex – urban Padonia - suburban
Fairhill – rural Edgewood – on the bay
July 29, 2011
Notes: These are line plots of the data from the same flight (as previous slide).
Top is ACAM VCD (below aircraft) compared with CMAQ. Generally good but with biases and differences in some peaks.
Bottom is surface concentration (will be more clear on next slide).
Added ground-based measurements coincident with aircraft overflights (based on coincidence criteria).
Essex, Padonia, and Fairhill represent urban/suburban/rural measurements. Edgewood is a hard case because it’s complicated dynamically and right on Bay.

## Slide 10: Scatterplots – Maryland
ACAM-Derived Surface NO2 vs. Surface Obs.
CMAQ Surface NO2 vs. Surface Obs.
Used average of CMAQ grid points within 1 km of
surface station
Used average of ACAM pixels within 2 km of
surface station
Data points are
for each ACAM over-
pass during MD
campaign
Less scatter in
ACAM estimates of
surface NO2

## Slide 11: Statistics for Maryland
Station | Essex Molybdenum converter | Padonia Photolytic | Fairhill Photolytic | Edgewood Photolytic
Median Ratio of ACAM Sfc estimate to Sfc Obs. | 0.63 | 1.04 | 1.01 | 1.53
Data from all 14 Maryland flight days
Station | Essex Molybdenum converter | Padonia Photolytic | Fairhill Photolytic | Edgewood Photolytic
Correlation of ACAM Sfc Estimate vs. Sfc Obs. | 0.67 | 0.43 | 0.65 | 0.67

## Slide 12: Texas – Time series for September 25, 2013
Surface Concentration (ppbv)
Time (h CDT)
Highest ozone day of Houston
campaign
Daily mean CMAQ NO2 and station locations
GCAS

## Slide 13: Texas – Scatter plots
Using all GCAS overpasses

## Slide 14: Texas 15-20 UT (10 – 15 CDT) Scatterplots
Only considering the
midday hours
improves the slope
for GCAS-derived sfc
concentrations
And, now the GCAS-
derived surface data
compare better with
observations than
those from CMAQ itself

## Slide 15: Texas Statistics
Station | Median GCAS/GB | GCAS–GB Correlation
Galveston | 1.34 | 0.02
La Porte | 1.30 | 0.80
Manvel Croix | 0.76 | 0.75
Seabrook Park | 1.70 | 0.43
Smith Point | 0.49 | 0.49
Texas Avenue | 0.75 | 0.78
Data from all 9 flight days.
Six ground sites with true NO2 obs.
Highest correlations of
GCAS-based surface NO2
with surface observations at
most polluted sites: LaPorte,
Manvel Croix, Texas Ave.
Lower correlations at sites
on Galveston Bay: Seabrook
Park and Smith Point
Lowest correlation at site
dominated by marine air:
Galveston
See talk by Dale Allen at 3 PM in Dogwood Room: more detail on CMAQ simulation
and NO2 results

## Slide 16: Colorado – Scatter plots
GCAS-based estimates provide
less scatter than model
estimates.
Daily mean CMAQ NO2 and station locations
8/2/14

## Slide 17: Colorado Statistics
Station | Median GCAS/GB | GCAS–GB Correlation
BAO Tower | 1.67 | 0.27
Chatfield Park | 1.14 | 0.42
Denver La Casa CAPS | 1.30 | 0.39
Denver La Casa Moly | 1.00 | 0.38
Ft Collins | 1.54 | 0.46
NREL Golden | 1.39 | 0.37
Platteville | 1.10 | 0.66
Data from all 17 flight days
All true NO2 except Denver La Casa
GCAS-derived surface
NO2 has a high bias at
all sites
Further investigation
needed to determine
cause.
Correlations only fair
to moderate; lower than
other campaigns

## Slide 18: Summary
Estimates of surface NO2 have been computed from a combination of airborne remotely
sensed data and CMAQ model output.
Maryland campaign - moderate correlations were found between ACAM-derived surface NO2
and ground-based in situ observations.
Median ACAM-derived and ground-based NO2 were similar at the suburban and rural sites with
true NO2 observations.
Texas campaign – correlations between GCAS-derived and observed mixing ratios were greater
for the more polluted sites and lower at coastal sites where strong NO2 gradients exist.
Better comparison with surface observations obtained for mid-day hours when the boundary
layer was better mixed in the vertical.
Colorado campaign – Agreement of GCAS-derived surface estimates with observations poorer
than in other campaigns. Further investigation necessary.
Future work – Investigate use of CMAQ PBL vertical gradient to filter times/locations to analyze