## Slide 1
18th Annual CMAS Conference October 23rd, 2019
M. J. Alvarado1, K. Cady-Pereira1, J. Mascio1, C. R. Lonsdale1, and M. Shephard2
1Atmospheric and Environmental Research (AER)
2Environment and Climate Change Canada
Acknowledgements: NASA Applied Science
Grant #80NSSC19K0190
A Retrieval Closure Study to Determine the Best Metrics for Evaluating the CMAQ Model with CrIS NH3 Retrievals

## Slide 2: Ammonia (NH3) is a PM2.5 precursor and reactive N species
NH3 + HNO3NH4NO3
2 NH3 + H2SO4(NH4)2SO4
Increase incidence of cardiovascular and respiratory diseases
Increase number of CCN
NH3 is also one of the most important reactive nitrogen species
  Leads to soil acidification, water eutrophication (e.g. algal blooms)
  Ammonia is the least well understood part of the nitrogen cycle
SO2, NOx emissions decreasing due to controls, but NH3 increasing!

## Slide 3: NH3 sources are not well known
Bi-directional
Flux
AGRICULTURE
Animal waste (temperature dependent)
Fertilizer application
Industry
Fertilizer
Coal Mining
Power generation
Biomass burning
Automobiles (catalytic converters)
Large urban centers
  50% of NH3 in LA area (Nowak et al., GRL, 2012)

## Slide 4: CrIS can identify NH3 sources
CrIS Satellite NH3 warm season (Apr. – Sept., 2013) average surface map, with corresponding AMoN surface network measurements overlaid.
AMoN Surf. Site
Notes: AMoN: Ammonia Monitoring Network (surface observations in the USA)
NAPS: National Air Pollution Surveillance Program (NAPS) (Canada)

## Slide 5: CrIS Satellite Ammonia Monitoring and Evaluation
Multi-year monthly comparisons of CrIS surface NH3 with AMoN obs.
Initial assessment shows that the satellite and AMoN surface observations agree well despite sampling differences
Stockton, Illinois
Fort Collins, Colorado
Notes: AMoN: Ammonia Monitoring Network (surface observations in the USA)
NAPS: National Air Pollution Surveillance Program (NAPS) (Canada)

## Slide 6: Validation in DAQ Colorado: CrIS vs PTR
Jul/Aug 2014
Jul 17, 2014
Aircraft measurements often start higher up
Few inversion cases
CrIS is unbiased in direct comparisons
Bias when operator is applied may be due to non-optimal choice of a priori

## Slide 7: Technical Approach For This Project
Schematic of the AQcast processing set up for this project on the Amazon cloud. The steps on the left outline include monthly iterations of the CrIS data record. The steps on the right outline each user output request.

## Slide 8: AQcast CMAQ System for Continental US
EPA Emission Modeling Platform
SMOKE
Emission Inventory
NEI
Air Quality Analyses
Sensitivity Studies
Air Quality Forecasts
nCast WRF
WRF
MCIP
Met Inputs
Reanalysis Data
Real-Time
Forecasts
Other Inputs and Preprocessors
ICON/BCON
OMI O3
Lightning
NormBEIS
FEST-C
CTM
CMAQ
Global CTMs
NCAR
Forecasts
EPA Modeling Platform Scripts

## Slide 9
AQcast Production Architecture

## Slide 10: Proof-of-Concept Inversion Method
Finite-difference mass balance (Lamsal et al., GRL, 2011).
Requires two model runs per iteration to estimate sensitivity to emissions.
Calculate emission scaling factors and apply to next iteration.

## Slide 11: How best to evaluate CMAQ with CrIS?
Selected ~850 CMAQ NH3 profiles from SENEX period/region
The average CMAQ resembles the CrIS moderate a priori profile
But individual CMAQ profiles have very different shapes from the CrIS polluted and moderate a priori profiles
  Well mixed BL
  Elevated amounts above BL
Key Question: What is the best metric for comparing CrIS and CMAQ?

## Slide 12: Simulated CrIS retrievals
Used the CMAQ profiles as input to our forward model (OSS) and added typical CrIS noise to the output radiances
Ran the simulations with and without NH3 to determine NH3 signal
Since the NH3 signal is very dependent on the thermal contrast (TCON) ran sets of simulations with different TCON values: 15K and 5K
Selected TCON values are high but not unusual over many source regions
NH3 on - off
BT Diff [K]

## Slide 13: NH3 Signal Drivers
CMAQ Surface NH3
CMAQ Total Column NH3
ppbv
molec/cm2
Peak BT Diff [K]
Since NH3 is concentrated in the boundary layer, surface NH3 is a strong driver of the NH3 signal
Kharol et al. (2019) have shown similar correlation between AMoN and CrIS surface data
In this simulation total column and the NH3 signal are almost perfectly correlated
Could total column be the most robust retrieval metric?

## Slide 14: Surface NH3: Retrieved vs CMAQ
Straight comparisons (no AK)
CrIS biased high for polluted and low for moderate
Applying the operator improves correlation and reduce bias
Retrieval is performing as well as possible
TCON: 15K
CMAQ no AK
CMAQ+AK log
CMAQ +AK linear
TCON: 5K
Similar results for weaker signal, but:
Selection of a priori has larger impact on the spread of the retrieved surface amounts

## Slide 15: Retrieved Total Column: CrIS vs CMAQ
CMAQ+AK log
CMAQ +AK linear
CMAQ no AK
TCON: 15K
TCON: 5K
Correlations
Very high and better than surface correlations
Smooth transition between a priori choices
Applying the AK also has little impact
Correlations
Higher and better than surface correlations
But a priori selection does create a gap

## Slide 16: Summary
We performed a model-retrieval closure study to determine the best metrics to use in the CMAQ inverse modeling, concluding that the total column of NH3 from CrIS should be compared with the total column from CMAQ after an observation operator with a linear averaging kernel (instead of a log AK) is applied.
The current set up for our NASA Applied Science project includes:
  WRF, SMOKE, EPA Emission Platform, and CMAQ along with its pre-processors
  A North American WRF/CMAQ domain
  Using AWS batch which saves the infrastructure as software and allows you to create identical machines and easily maintain them
This work will provide improved emission inventories of NH3 to air quality (AQ) forecasters, AQ managers, and other stakeholders.

## Slide 17: Additional Slides

## Slide 18: NASA Applied Science Project Expanded North American Domain
WRF version 3.8.1 with the YonSie University (YSU, Hong et al., 2006) non-local turbulent PBL scheme and the Noah land surface scheme (Chen and Dudhia, 2001) were used. Initial and boundary conditions for WRF were provided by the North American Regional Reanalysis (NARR, Mesinger et al., 2006),

## Slide 19: Using Satellites to Investigate NH3 in California
TES NH3 transects over Bakersfield in CalNex suggested a x2 underestimate in afternoon due to diurnal cycle errors (Lonsdale et al., ACP, 2017)
2012 CrIS NH3 is consistent with CalNex TES results.

## Slide 20: Monitoring NH3 is difficult
NH3 is highly reactive
 highly variable in space and time
NH3 from an Open path Quantum Cascade Laser (QCL) on a moving platform in the San Joaquin Valley during DISCOVER-AQ 2013.
Miller et al., AMT 2013

## Slide 21: Cross-track Infrared Sounder (CrIS)
 | TES | CrIS
Satellite | AURA | NPP and JPSS-1
Available Data | July 2004 - Jan. 2019 | October 2011-present
Resolution | 0.06 cm-1 | 0.625 cm-1
Footprint | 5x8 km rectangle | 14 km diameter circle
Repeat cycle | Once every 16 days | Daily
Equatorial crossing | 1:30 am and 1:30 pm | 1:30 am and 1:30 pm
Noise in NH3 window | 0.09 – 0.12 K | 0.03 – 0.06 K
CrIS can monitor global NH3 with high spatial coverage from 2011 and over the next decade or more

## Slide 22: Project Goal
To use CrIS NH3 retrievals to provide improved emission inventories of NH3 to air quality (AQ) forecasters, AQ managers, and other stakeholders.
  Integrate the NASA CrIS NH3 retrieved product and our CMAQ-based inversion methodology into a prototype application system on the Amazon cloud (ARL 4)
  Develop model-ready updated NH3 emission files for CMAQ, CAMx, and GEM- MACH and beta-test them in the end-user applications (ARL 5)
  Demonstrate that the prototype application improves the simulation of NH3 and inorganic PM2.5 in end-user modeling and leads to better decision making (ARL 6)
  Fully integrate the prototype application into end-user decision-making (ARL 7)
Project Objectives

## Slide 23: Application Work Flow
Modeling work flow currently includes:
  North American met configuration
  AMET evaluation
  Spatial allocator shapefiles
  Multiple emission configuration options
  Pre-processor configuration
  Multiple CCTM configuration options
nCast WRF + MCIP
Container
Original Emissions
AMET
Updated Emissions
Report and Review
Pre-processors
CMAQ
CAMx Emissions
GEM-Mach Emissions
Spatial Allocator Tool

## Slide 24: Simulated Retrievals - examples
Polluted
Moderate
Notes: Comme

## Slide 25: CrIS NH3: Example of Daily Spatial Variability of Surface NH3 over North America on August 10, 2013
MODIS
Infrared:
Fire Detection
(red)
Visible:
Cloud (White)
Smoke (blue/gray)
CrIS
Infrared NH3

## Slide 26: Linear AKs Have Less Bias for Moderately Polluted Cases
Mean Bias for +15K
CMAQ No AK CMAQ AK linear – vmr limit xa
CMAQ AK log CMAQ AK linear – vmr max
Mean Bias for +5K