## Slide 1: Traffic-Related PM2.5 and NO2 Health Risk Assessment in the United States A Fine-Scale Hybrid Modeling Approach
Alejandro Valencia1, Marc Serre1, Dongmei Yang 2, Sarav Arunachalam 1,2
1University of North Carolina at Chapel Hill – Environmental Sciences and Engineering Dept.
2University of North Carolina at Chapel Hill – Institute for the Environment – Center for Environmental Modeling and Policy Development
Notes: Date and Where

## Slide 2: Background
TRAP concentrations are highest near roads and dramatically decrease to background levels within 150m from roads. 1
In United States, around 19% of the population resides in the vicinity of a heavily trafficked road. 2
Traffic related air pollutants (TRAPs) have been associated with a range of adverse health effects.
1 Barzyk et al., 2009; Hagler et al., 2009
2 Rowangould, 2013
Notes: California, up to 40% of the population live close to TRAPs

## Slide 3: Previous Traffic Related PM2.5 Premature Mortality Studies
36% ﻿of U.S. premature mortality is associated to traffic related PM2.5 1
U.S. traffic related PM2.5 causes between 29,000 and 53,000 premature deaths per year2
  Top largest contributor to premature mortality
1 Lelieveld et al., 2015
2 Caiazzo et al., 2013; Fann et al., 2013
Notes: Impact of on-road PM2.5:
Coarse resolution CTMs were used in these study. And this is a problem beacuse

## Slide 4: Motivation
Chemical transport models (CTMs) lack the spatial gradients necessary to assess the relationship between TRAP population exposure and health.
Land use regression (LUR) models ignore chemical/transport processes that can better quantify road source contributions.
A hybrid modeling approach in Central North Carolina estimated 24% more on-road PM2.5-related premature mortality than only a CTM.1
1 Chang et al., 2017
12km
Notes: Census block is the smallest geographic unit in the US

## Slide 5: Objectives
Estimate mortality due to traffic-related emissions at fine scales in the U.S.
  Use dispersion modeling to estimate primary PM2.5 at Census-block scales
  Combine CMAQ at 12 x 12-km resolution to estimate both secondary PM2.5 and background sources
  Apply Bayesian Maximum Entropy (BME) Methods to correct model bias
Compare with prior studies that used only coarse resolution grid-based modeling

## Slide 6: Study design flowchart
CMAQ
Concentrations at 12km Grid Resolution
Hybrid
Concentrations at Census Block
Resolution
Health Impact Function (HIF)
Grid-Based Mortality
Census Block-Based Mortality
HIF

## Slide 7: CMAQ-RLINE Hybrid
+
=
=
-
RLINE
Major Roads
CMAQ
All Emissions
RLINE
Major Roads
Average
CMAQ without
Major Roads
Interpolated
CMAQ w/o Major Roads
RLINE
Major Roads
CMAQ-RLINE Hybrid
Low
High
Concentration
Removes the need to run multiple CTMs to obtain background emissions
Includes chemistry formation or loss from local sources that CTMs cannot simulate if emissions were zeroed out
Notes: Explain RLINE and CMAQ
Different from Chang because it requires only one CMAQ run
Used by Lefebvre, 2011 Scheffe, 2016 and Bates, 2018

## Slide 8: Bayesian Maximum Entropy (BME) Biased Corrected Hybrid
Run Hybrid at AQS measurement locations
Constant Air quality Model Performance (CAMP)
  Performs a model performance analysis that accounts for the non-linearity and non-homoscedastic behavior of model performance with respect to the modeled value 𝑥̃𝑘.
  Models the mean 𝜆1 (𝑥̃𝑘; 𝒟) and variance 𝜆2 (𝑥̃𝑘; 𝒟) of the observed value
    where
BME kriging →
  Covariance model: Cx(𝑟,𝜏) for PM2.5 across the US
=
Reyes et al., 2017
Notes: ### Work in progress
Different from Chang
The experimental covariance and covariance models for the posterior mean estimates for kriging
The CAMP method does not investigate how λ1 (x˜k; 𝒟) and λ2 (x˜k; 𝒟) change across the domain 𝒟.
Plot (j) shows the RAMP analysis of an arbitrary CMAQ grid location on 07/01/2001 for daily PM2.5. The black dots are all the paired modeled and observed daily PM2.5 concentrations within a space/time region ℛ(𝒑) consisting of the 3 closest stations to the CMAQ grid location of interest within 180 days of 07/01/2001, with modeled data on the independent axis and observed data on the dependent axis. The vertical black lines identify the 10 bins used to stratify all the paired data in which each bin contains one decile of all the paired points. The dotted black line is the one-to-one line between the modeled and observed data. The red + marker in each bin denotes 𝜆1,𝑙(𝑥̃𝑙 , ℛ(𝒑)), the average of paired observed values within the 𝑙-th decile bin. The blue x marker in each bin denotes the square root of 𝜆2,𝑙(𝑥̃𝑙 ; ℛ(𝒑)), the standard deviation of paired observed values within that bin. As shown in the figure, the + and x markers are linearly interpolated to obtain the 𝜆1(𝒑) and √𝜆2(𝒑) values, respectively, corresponding to the CMAQ modeled data 𝑥̃(𝒑) within ℛ(𝒑).

## Slide 9: Health Impact Function (HIF)
Relative Risk (RR)
Integrated exposure-response (IER)1
Population Attributable Factor (PAF)
Mortality (Mort)
Chronic obstructive pulmonary disease (COPD), Lung Cancer (LC), Stroke, Ischemic heart disease (IHD)
𝛾0: baseline mortality rate
pop: population
1Burnett et al., 2014
C: annual average ambient PM2.5
C0: PM2.5 threshold concentration (below which no additional risk is assumed)
Notes: Alpha gamma delta
extensively used by recent studies, Liu et al. (2017), Silva et al. (2016a, b), Wang et al. (2017), and the World Health Organization (2016), Zhang et al. (2018).
The baseline mortalities for IHD, COPD, stroke, and lung cancer were collected from the CDC-WONDER database, where county-level age-stratified baseline mortality for 2016 is available.(3)

## Slide 10: Modeling Domain
~7.5 million major road sources
~11 million census blocks
~130,000 CMAQ grid cells
Study period: 2016
Each hybrid run is divided into
  CMAQ run
    12x12km CMAQ grid
  RLINE run
    Major road segments with emission
    Census Blocks Centroid (CBC) Receptors
    1x1km RLINE Grid of Receptors
    Hourly Met at each CMAQ Grid
Hybrid Stats
  ~55,500 Hybrid calculations
    Only grid cells that contain both major roads and CBC
    ~2 weeks with 800 processors for one pollutant
Notes: Different from Chang not MetARE

## Slide 11: Inputs
CMAQv5.2.1
Meteorology
2016 MCIPv4.3 (Meteorology-Chemistry Interface Processor) from WRF﻿v3.8
Emissions
2016v7.2 (beta) Platform
Chemical Mechanism
CB6R3_AE6_AQ
RLINEv1.2
Meteorology
2016 ﻿Mesoscale Model Interface Program (MMIF) extracted from ﻿WRFv3.8 grid cells
Emissions
2016v7.2 (beta) Platform
Emission Factors, Fleet mix, and Temporal allocation
Highway Performance Monitoring System (HPMS) 2016
Census Blocks Centroid Locations
Annual Average Daily Traffic (AADT )
Health Impact Function (HIF)
2016 County-based Baseline Mortality (CDC-WONDER)
For COPD, LC, Stroke, and IHD
Population at Census Blocks
Constant Air quality Model Performance (CAMP) with BME
2016 hourly AQS Observations
Notes: Using Meteorology from MMIF at each grid cell.
Weather Research and Forecasting Model (WRF). continental U.S. at a 12km resolution with 35 vertical layers.
Census Block Population needs to be projected to 2016

## Slide 12: Annual PM2.5 Results - Durham, NC
CMAQ
Interpolated
Hybrid
CMAQ
Allocated CMAQ gridded concentrations to each Census Block Centroid (~1900)
Used bilinear interpolation to allocate each Census Block Centroid
Hybrid estimates peaks that are ignored in CMAQ

## Slide 13: Annual PM2.5 Results - Central North Carolina
~150,000 census blocks centroids in 320 grid cells
Hybrid shows better distribution of high and low concentrations
CMAQ
Interpolated
Hybrid

## Slide 14: Annual PM2.5 Results - Central North Carolina
PM2.5 (μg/m3)
■ CMAQ Interpolated
■ Hybrid
Distance From Road (m)
RLINE CMAQ Hybrid
Interpolated
Hybrid shows a marked decrease as CBCs are farther away from road
RLINE adds concentration spikes to Hybrid with marginal changes to the CMAQ distribution
PM2.5 (μg/m3)

## Slide 15: Discussion
Successfully implemented the Hybrid approach
Hybrid improves on our previous approach
  Requires only 1 CMAQ run
  Includes secondary from local sources by not using a zero out run
  Uses actual hourly meteorology
Hybrid model captures PM2.5 fine resolution spatial gradient

## Slide 16: Future Work
Expand analysis nationwide
Apply bias adjustment to CMAQ and RLINE before hybrid
Calculate mortality
Evaluate against other exposure-response functions
Compare mortality against CMAQ using Berrocal et al. downscaler
Add NO2 Analysis

## Slide 17: Acknowledgment
UNC
  Calvin Arter
  Brian Naess
  Catherine Seppanen
Sonoma Technology
  Shih Ying Chang (Changsy)
U.S. EPA
  Allison Eyth
  Chris Misenis
  James Thurman
  David Heist
  Vlad Isakov
  Michael Breen
This work was supported by the National Center for Advancing Translational Sciences, National Institutes of Health [grant number OT3TR002020].
The U.S. EPA, through its Office of Research and Development, also partially funded and collaborated in the research described here under Contract EP-W-16-014 to the University of North Carolina at Chapel Hill.

## Slide 18: References
Barzyk TM, George BJ, Vette AF, Williams RW, Croghan CW, Stevens CD. 2009. Development of a distance-to-roadway proximity metric to compare near-road pollutant levels to a central site monitor. Atmos Environ 43:787–797; doi:10.1016/j.atmosenv.2008.11.002.
Berrocal, V.J., Gelfand, A.E. and Holland, D.M., 2012. Space‐time data fusion under error in computer model output: an application to modeling air quality. Biometrics, 68(3), pp.837-848
Burnett RT, Pope CA, Ezzati M, Olives C, Lim SS, Mehta S et al. An integrated risk function for estimating the global burden of disease attributable to ambient fine particulate matter exposure. Environ Health Perspect 2014; 122: 397–403.
Caiazzo, F., Ashok, A., Waitz, I.A., Yim, S.H.L., Barrett, S.R.H., 2013. Air pollution and early deaths in the United States. Part I: Quantifying the impact of major sectors in 2005. Atmos. Environ. 79, 198–208. doi:10.1016/j.atmosenv.2013.05.081
Chang SY, Vizuete W, Serre M, Vennam LP, Omary M, Isakov V, et al. 2017. Finely Resolved On-Road PM2.5and Estimated Premature Mortality in Central North Carolina. Risk Anal 37:2420–2434; doi:10.1111/risa.12775.
Fann, N., Lamson, A.D., Anenberg, S.C., Wesson, K., Risley, D., Hubbell, B.J., 2012. Estimating the national public health burden associated with exposure to ambient PM2.5 and ozone. Risk Anal. 32, 81–95. doi:10.1111/j.1539-6924.2011.01630.x
Hagler GSW, Baldauf RW, Thoma ED, Long TR, Snow RF, Kinsey JS, et al. 2009. Ultrafine particles near a major roadway in Raleigh, North Carolina: Downwind attenuation and correlation with traffic-related pollutants. Atmos Environ 43:1229–1234; doi:10.1016/j.atmosenv.2008.11.024.
Lefebvre W, Vercauteren J, Schrooten L, Janssen S, Degraeuwe B, Maenhaut W, et al. 2011. Validation of the MIMOSA-AURORA-IFDM model chain for policy support: Modeling concentrations of elemental carbon in Flanders. Atmos Environ 45:6705–6713; doi:10.1016/j.atmosenv.2011.08.033.
Lelieveld J, Evans JS, Fnais M, Giannadaki D, Pozzer A. 2015. The contribution of outdoor air pollution sources to premature mortality on a global scale. Nature 525:367–371; doi:10.1038/nature15371.
Reyes, J. M., Xu, Y., Vizuete, W., & Serre, M. L. (2017). Regionalized PM2.5 Community Multiscale Air Quality model performance evaluation across a continuous spatiotemporal domain. Atmospheric environment (Oxford, England : 1994), 148, 258–265. doi:10.1016/j.atmosenv.2016.10.048
Rowangould, G.M., 2013. A census of the US near-roadway population: Public health and environmental justice considerations. Transp. Res. Part D Transp. Environ. 25, 59–67. doi:10.1016/j.trd.2013.08.003

## Slide 19: Extra Slides

## Slide 20: Annual PM2.5 Results - New York City
CMAQ
Interpolated
Hybrid
20,000 census block centroids in 4 CMAQ grid cells
Hybrid shows better distribution of high and low concentrations
Notes: Change to CNC

## Slide 21
Annual National PM2.5 Results
■ CMAQ Interpolated
■ Hybrid
PM2.5 (μg/m3)
Distance From Road (m)
Hybrid shows a marked decrease as CBCs are farther away from road
RLINE adds concentration spikes to Hybrid with marginal changes to the CMAQ distribution
RLINE CMAQ Hybrid
Interpolated
PM2.5 (μg/m3)