## Slide 1: Using mobile phone data to quantify the impact of spatiotemporal human mobility on air pollution exposure estimation
Haofei Yu1,*, Cesunica E. Ivey2, Xiaonan Yu1,
Lucas Henneman3, Zhijiong Huang4
1Department of Civil, Environmental, and Construction Engineering. University of Central Florida. Orlando, FL. USA
2Department of Chemical and Environmental Engineering, University of California Riverside. Riverside, CA. USA
3T.H. Chan School of Public Health, Harvard University. Cambridge, MA. USA
4Inisitute for Environmental and Climate Research, Jinan University, Guangzhou, China.
+
=

## Slide 2
Rutgers University: Desheng Zhang
UC Riverside: Cesunica (Sunni) Ivey
Jinan University: Zhijiong Huang, Junyu Zheng
AirSage: Sashi Gurram, Vijay Sivaraman
Georgia Tech: Huizhong Shen, Armistead Russell
Harvard University : Lucas Henneman
Nankai University: Guoliang Shi
University of Central Florida: Naveen Eluru, Samiul Hasan
Acknowledgements
Notes: Historical and forecast simulations for human health and welfare protection

## Slide 3
Motivation and Background
Home address often used in air pollution exposure estimation
  Lack data on individual mobility
  Potential exposure misclassification
Most people own a cell phone, Call detail record (CDR) is collected when cellphone connected to nearby tower
  Tower location known
  An individual’s CDR data (>300 records)
Home

## Slide 4
Shenzhen, Guangdong Province, China
Study Region

## Slide 5
Location Data, Pollution Field, and Exposure
CDR data collected from Shenzhen, China (One mid-week day in Oct 2013)
35 million records, 310,989 subjects
Two pollution concentration fields
  CMAQ: 3 km, adjusted using measurement data from 12 stations
  IDW: Inverse Distance Weighting
Six pollutants: PM2.5, EC, CO, NO2, SO2, O3
Two exposure estimates:
  CDR-based exposure (CDRE): Detailed CDR data + CMAQ data
  Home-based exposure (HBE): CMAQ average at home location, determined as the most frequent place at night (8:00 PM - 7:00 AM)
Exposure also estimated for 10 groups with different mobility levels
  # unique CMAQ grid cells visited

## Slide 6
Pollution fields
Yu et al., Under review

## Slide 7
Results: CDRE vs. HBE with CMAQ field
Yu et al., Under review

## Slide 8
Results: CDRE vs. HBE with IDW field
Yu et al., Under review

## Slide 9
Results: CDRE vs. HBE
While mean exposures were similar, correlations worsened with increasing mobility
Exposure Estimates for NO2
Yu et al., Under review
Notes: lower R2 and mean normalized error (MNE) between HBE and CDRE

## Slide 10
Results: CDRE vs. HBE
This difference is less apparent when using IDW
Exposure Estimates for NO2
Yu et al., Under review
Notes: lower R2 and mean normalized error (MNE) between HBE and CDRE

## Slide 11
Results: Temporal Analysis
Temporal bias varies by pollutant and individual mobility
CO, NO2 and PM2.5: largest error at afternoon rush hour, and HBE underestimates exposure
O3: biggest error at around 4 pm, and HBE overestimates exposure
Notes: lower R2 and mean normalized error (MNE) between HBE and CDRE

## Slide 12
Results: Exposure Misclassification
Misclassification is likely when individuals are highly mobile
Exposure Estimates for CO
Notes: lower R2 and mean normalized error (MNE) between HBE and CDRE

## Slide 13
Key Takeaways
Population level:
No considerable differences between HBE and CDRE mean exposures
HBE method still informative when only averaged exposures on a large population is needed
Individual level:
Higher mobility = higher exposure misclassification
HBE under-estimated exposure to TRAPs at afternoon rush hour, and over-estimated O3 exposure at mid-afternoon