## Slide 1
Quantifying the Air Quality and Human Health Benefits of GHG Mitigation Pathways in California
a Advanced Power and Energy Program
b Computational Environmental Sciences Lab
University of California, Irvine
Michael Mac Kinnona, Shupeng Zhua,b, Brendan Shaffera, Owen Yanga, Donald Dabduba,b, G.S. Samuelsena

## Slide 2: AQ Assessment Methodology
Assess impacts on emissions, air quality, and human health from low carbon mitigation scenarios from the PATHWAYS model (E3)
  Provide insight into the air quality co-benefits of technological shifts within cases
Resolve Emissions (SMOKE 4.0)
Simulate Air Quality
(CMAQ 5.2
SAPRC 07)
Pathways Scenarios
  ~15 different scenarios considered
  Scenarios not designed from an AQ impact perspective, i.e., targeting criteria pollutant emission reductions
80% below 1990
Health Impact Assessment
  (BenMAP 1.4)
Notes: E3=Energy + Environmental Economics What is pathway model? PATHWAYS model helps clients plan for and achieve economy-wide decarbonization. It identifies GHG reduction measures from transportation, buildings, industry, electricity, and other sectors, and captures interactions among measures to create a detailed picture of emissions reductions and costs through 2050.

## Slide 3: California 2035 NOx
Source: CARB CEPAM 2016 SIP

## Slide 4: Scenario Development
Scenarios encompass shifts in energy consumption, technologies and fuels from Current Policy Reference Scenario
  All assume measures in LDV, Off-road, Rail, Aircraft, Ships, Refining, Industry, etc. (Constant)
  Three scenarios presented here have differences in:
    MDV and HDV, Residential and Commercial Buildings, Electricity Generation
*Includes the use of battery electric and low NOx CNG

## Slide 5: Commercial Energy Consumption (Pathway Model)
High Building Electrification
No Building Electrification

## Slide 6
Emissions Projection Results
**Scale does not start at 0**

## Slide 7
Emissions Projection Results
**Scale does not start at 0**

## Slide 8: AQ for Current Policy Reference Scenario
Serves as baseline for comparison with alternative cases in 2050
  Particular concerns for summer ozone in SoCAB and winter PM2.5 in Central Valley
Peak Summer MD8H Ozone: 137.7 ppb
Peak Winter 24-h PM2.5: 74.2 µg/m3

## Slide 9: AQ Impacts: HBE+ VS. Current Policy
Significant improvements in key locations (high population + base line levels) from CPR reference scenario in 2050
  Ozone benefits in SoCAB and Central Valley, PM2.5 in Central Valley
Δ Peak Summer MD8H Ozone : -25.1 ppb
Δ Peak Winter 24-hr PM2.5: - 13.3 µg/m3

## Slide 10: AQ impacts of the Electrification of Buildings
Largest impacts correlated with locations of urban population centers
  Difference between the HBE+ and NBE+ scenarios (13% vs. 88%)
  Secondary PM2.5 reductions in Central Valley/Bay Area from NOx reductions
Δ Peak Summer MD8H Ozone : -6.9 ppb
Δ Peak Winter 24-hr PM2.5: - 4.93 µg/m3

## Slide 11: AQ impacts of the Electrification of Trucks
Benefits to ozone widespread throughout the State, peak in SoCAB
  Should be noted this is in the context of significant MDV/HDV reductions for all cases (53% vs. 86%)
  Difference between the HBE+ and HBE scenarios
Δ Peak Summer MD8H Ozone : -5.6 ppb
Δ Peak Winter 24-hr PM2.5: - 3.0 µg/m3

## Slide 12: Value of Health Savings: Summer Episode
Health savings of 202 to 261 million $ for the modeled episode
  Impacts of MDV/HDV NOx mitigation on ozone and PM2.5 in the South Coast Air Basin
  Impacts of building NOx reductions in the South Coast Air Basin
*Mean values estimated from the BenMAP-CE Model
Chart: Health Savings - Summer Episode
| HBE | NBEwSNG | HBEwT
Total | 202.063 | 202.3523 | 261.22
High Building Electrification w/ Trucks
High Building Electrification
No Building Electrification

## Slide 13: Value of Health Savings: Winter Episode
Chart: Health Savings - Winter Episode*
| HBE | NBEwSNG | HBEwTruck
Total | 190.5687 | 166.84 | 249.595
Health savings of 166 to 249 million $ for the modeled episode
  Impacts on secondary PM2.5 in the Bay Area/Central Valley from NOx reductions from NG appliances have a major impact
  Impacts from trucks achieve health savings from the same mechanism
*Mean values estimated from the BenMAP-CE Model
High Building Electrification w/ Trucks
High Building Electrification
No Building Electrification

## Slide 14: Benefits for disadvantage communities
$/Census Tract
Disadvantaged communities from CalEnviroScreen 3.0 are highlighted
Health Savings for the HBE+ Scenario in winter allocated to census tracts in California
  In winter 39% of the total health savings goes to disadvantage communities (25% of total population), in summer the number is 31%.
Disadvantaged communities:
Poverty
High unemployment
Air and Water pollution
Presence of hazardous wastes
High incidence of asthma and heart disease.

## Slide 15: Conclusions
Technological strategies to reach 2050 carbon goals attain notable co-benefits to air quality and human health
  Impacts vary by season, source, and region
Reductions from MDV/HDV attain important benefits
  Widespread benefits to ozone and secondary PM2.5 in summer from NOx reductions
Building electrification has important impacts in densely populated urban areas
  Impacts on secondary PM2.5 in winter from NOx reductions from NG appliances
Disadvantage communities could benefit above average with both high building electrification and truck electrification.

## Slide 16: Thank you!
Integrate and assess the potential impacts of bio-refineries
  Results presented here do not account for emission impacts of renewable fuel production
Develop and assess scenario considering potential emission impacts from hydrogen/NG blending
  End-use impacts could be positive or negative
Next Steps

## Slide 17: Back Up Slides

## Slide 18: Task 4 – Emissions Projection Methodology
Emissions projection based on CARB 2035 emissions projected to 2050 via Pathways Output
  Projection of 2012 to 2050 yielded unrealistic concentrations
  CEPAM 2016 is ARB projected emissions to 2035 accounting for current policy
Baseline Emissions
CARB 2012
Baseline Emissions
CARB 2035
Baseline and Alternative Case Emissions
E3 FONG 2050
ARB Projection (CEPAM Tool)
Pathways Output for 2035 to 2050
Pathways Output for 2012 to 2050

## Slide 19: AQ impacts of Buildings and Trucks
-0.74 ug/m3 ppb peak difference in SoCAB
Impacts on Summer PM2.5
  Difference between the HBE with Truck Measures and NBE scenarios
  Secondary PM2.5 reductions in Central Valley/Bay Area from NOx reductions
-1.2 ug/m3 peak difference in SJV
Buildings
Trucks

## Slide 20: South Coast Air Basin 2035 NOx
Chart: 2035 NOx Emissions in the South Coast Air Basin
| HDV | Offroad | Ships | Aircraft | Residential and Commercial Buildings | LDV | MDV | Manufacturing and Industrial | Trains | Refining | Electricity Generation | Waste | Other
 | 34.1134 | 29.8543 | 22.7838 | 20.7713 | 20.1841 | 15.748 | 14.4553 | 13.7632 | 10.6514 | 5.09 | 3.5198 | 2.9042 | 2.6163
Source: CARB CEPAM 2016 SIP

## Slide 21: Task 4 –AQ Results
Summer MD8H
  Average difference: -2.7 ppb to -3.41 ppb
  Peak difference: -13 ppb to -18 ppb
Summer 24-h PM2.5
  Average difference: -0.89 ug/m3 to -1.37 ug/m3
  Peak difference: -2.0 ug/m3 to -2.91 ug/m3
Winter 24-h PM2.5
  Average difference: -4.01 ug/m3 to -6.03 ug/m3
  Peak difference: -8.41 ug/m3 to -12.72 ug/m3

## Slide 22: Task 4 – Emissions Projection Results
Total NOx is reduced by 15-25%
Chart: 2050 Total NOx Emissions
| CPR | HBE | NBEwSNG | HBEwTruck | NBEwITM
 | 48.1 | 40.41 | 41 | 37.5 | 36.3
 | 0 | 7.69 | 7.1 | 10.6 | 11.8
-15%
-22%
-25%
-16%
Current Policy Reference
High Building Electrification
No Building Electrification with SNG
High Building Electrification with Truck
No Building Electrification with Industry and Truck

## Slide 23: Task 4 – Downscaling
Constant Across Cases | Differences Between Cases
On-road Vehicles LDV, Bus | On-road Vehicles MDV, HDV
Off-road Equipment | Residential and Commercial Buildings
OGV, Harbor Craft | Industrial Sector (non-petroleum)
Rail | Electricity Sector
Aircraft | Bio refineries
Petroleum Refineries | 
Differences between cases driven by MDV, HDV and industry
  Electricity sector emissions contribute to a lesser degree
Chart: Total NOx
| Variable | Constant
 | 410.5364 | 484.0384

## Slide 24: Pathways Downscaling
Chart: HDV Fuel Share in 2050
| CPR | HBE | HBEwT | NBEwSNG | NBEwITM
CNG | 0.1321 | 0.31426 | 0.37618 | 0.37618 | 0.017686
Diesel | 0.82147 | 0.45205 | 0.13097 | 0.13097 | 0.016195
Electricity | 0.021715 | 0.23369 | 0.45435 | 0.45435 | 0.41631
Hydrogen | 0.024708 | 0 | 0.038497 | 0.038497 | 0.54981
Downscale Pathways model results to an ARB criteria pollutant emission inventory in 2050
  Energy consumption from various combinations of conventional and alternative fuels used to determine emission changes
High Building Electrification
No Building Electrification w/ Industry and Truck Measures
No Building Electrification w/ SNG
Current Policy Reference
High Building Electrification w/ Truck Measures

## Slide 25: Scenario Development
Chart: 2035/2050 NOx Growth Factors
| Residential and Commercial Buildings* | Trucks | Industry | Electricity Generation
High Building Electrification | 0.28356 | 0.69649 | 1.0229 | 0.43953
No Building Electrification w/ SNG | 1.1354 | 0.27338 | 1.0229 | 0.29949
High Building Electrification w/ Trucks | 0.28356 | 0.27338 | 1.0229 | 0.43953
No Building Electrification w/ Industry and Trucks | 1.4232 | 0.017058 | 0.5785 | 0.20023
Differences between cases driven by MDV, HDV and industry
  Electricity sector emissions contribute to a lesser degree
*Representative, commercial NG other sources