## Slide 1: Estimation of nose-level NO2 in the Houston-Galveston area using airborne remote sensing data from DISCOVER-AQ and output from a 4-km resolution simulation with CMAQ
Dale J. Allen1, Lok N. Lamsal2,3, Melanie B. Follette-Cook2,3, Kenneth E. Pickering1, William H. Swartz4, and Scott J. Janz2
1University of Maryland, College Park, MD
2NASA Goddard Space Flight Center, Greenbelt, MD
3Goddard Earth Sciences Technology and Research (GESTAR), Columbia, MD
4Johns Hopkins University Applied Physics Laboratory, Laurel, MD

## Slide 2
NO2 is criteria pollutant
Exposure to high-levels of NO2
(~20 ppbv in Naess et al. study) increases chances of dying from heart or lung diseases
O3 is an air pollutant and GHG
NOx is an O3 precursor
[Dodge, 1977]
[Naess et al., 2007; American Jl. of Epidemiology]
Why we are interested in inferring nose-level NO2 from space

## Slide 3
NO2 is excellent marker of combustion-related pollutants
NO2 columns are dominated by PBL
Thus NO2 columns provide more info on nose-level concentrations than do columns from other trace gases
R. Burnett et al. (2004)
R. Martin et al. (2008)
Normalized
vertical
profiles of
trace gases
[30-50N,
125-70W)
for 2004
from
GEOS-Chem
Correlations
between
PM2.5 (NO2)
and combustion
related
pollutants
Why we are interested in inferring nose-level NO2 from space?

## Slide 4
Why we are interested in inferring nose-level NO2 from space
Surface measurements of NO2, especially true NO2, are relatively sparse
Remotely sensed columns for a set of days are available from aircraft in DISCOVER-AQ and other field campaigns
and soon hourly columns will be available from TEMPO

## Slide 5
Nominal Flight Plan over Houston-Galveston during DISCOVER-AQ TX campaign (Sep 2013)
DISCOVER-AQ: NASA Earth Venture mission
designed to determine the extent to which column observations
can be used to diagnose surface air quality

## Slide 6: Daily 1-Hour Max Ozone (ppbv) – All Stations
Relatively clean 3 flight days
Moderate pollution 4
Strongly polluted 2
Chart: Daily 1-Hour Max Ozone (ppbv)
 | 58 | 50 | 77 | 87 | 67 | 56 | 48 | 55 | 78 | 55 | 61 | 79 | 80 | 77 | 38 | 55 | 50 | 59 | 34 | 27 | 39 | 50 | 89 | 58 | 151 | 101 | 77 | 52 | 34 | 50
#1
#2
#3
#4
#5
#6
#7
#8
#9
clouds, heavy
rains, marine air
bay, sea breezes
following cold front
September 1st – 30th

## Slide 7: Nose-level NO2 is inferred using NO2 vertical columns derived from NASA Geo-CAPE Airborne Simulator (GCAS) and surface-layer tropospheric column relationship from CMAQ
GCAS measures differential slant column density (SCD) at 250 x 250 m resolution using
UV/VIS spectrometer
(Kowalewski and Janz, 2014)
Absolute SCD is converted to vertical column density (VCD) by dividing by an air mass factor (AMF) computed with VLIDORT (Lamsal et al., 2017).
Differential SCD is converted to an absolute SCD by subtracting off NO2 SCD from PANDORA instrument at a “clean” reference location.
AMFs assume Lambertian surfaces, use surface reflectivity information from MODIS, and NO2 profile information from CMAQ.
GCAS instrument being serviced at Warner Robins AFB
during GOES-R Validation Campaign

## Slide 8
GCAS NO2 columns over D-AQ Texas Region on September 25
9 AM LT 1 PM LT 3 PM LT

## Slide 9
GCAS NO2 columns over D-AQ Texas Region on September 26
9 AM LT 1 PM LT 3 PM LT

## Slide 10: CMAQ is run off-line using MCIP-processed meteorological fields from WRF
WRFv3.8.1 |  |  | CMAQv5.2 | 
Resolution | 36, 12, & 4 km |  | Resolution | 36, 12, & 4 km
Time Period | Aug 17 – Oct 2, 2013 |  | Time Period | Aug 19 – Oct 1, 2013
BC & IC | NAM |  | BC & IC | MOZART
Nudging | grid_fdda=1,1,1 grid_sfdda=1,1,1 Obs_nudge=1,1,1 |  | Mechanism | cb6r3_ae6_aq (No halogen chemistry)
Longwave radiation Shortwave radiation | RRTM Goddard |  | Emissions | Ramboll ENVIRON and TCEQ
Surface layer physics | Pleim-Xu |  | Point Source Emissions | CEMS2013 2013 Oil & Gas
Cumulus Physics | KF (all domains) |  | Area | TCEQ 2012 SIP base (projected to 2013)
Other | Daily varying SST Soil Moisture & Temperature passed between 3 day segments |  | Other Emissions | MEGAN, FINNv1, Lightning (Y), Dust (Y)

## Slide 11: Inferred nose-level NO2 (S) is f(GCAS NO2 column) and S / from CMAQ Refined estimate utilizes sub-grid scale (PBL) variability from GCAS
Initial (Intuitive) Estimate Refined estimate includes sub-grid scale GCAS info
Texas D-AQ deployment provided data needed to apply this approach and evaluate its performance.

## Slide 12
Sep 24-26 time series showing biases between CMAQ- and-HSRL PBL heights
CMAQ PBL Height minus
NASA Langley
High Spectral Resolution Lidar (HSRL) PBL Height
Biases in modeled PBL heights can lead to biases in modeled- and inferred
NO2 concentrations.
Modeled biases were minimal during the morning; however, the modeled afternoon PBL height over water had a low-bias of up to 2 km
Water Land

## Slide 13
Sep24-26 AQ poor

## Slide 14
25 September

## Slide 15
(10 AM)

## Slide 16
Sea breeze
develops
between
17 and 20 UT
(12-15 CDT)

## Slide 21
Pollution front
advances
inland with
sea breeze
17-20 UT
(12-15 CDT)

## Slide 25
Correlation between modeled nose-level and column NO2 for 12-23 UT

## Slide 26
Correlation between modeled nose-level and column NO2 for 15-20 UT
Correlations
are higher
during mid-day period when PBL heights are large

## Slide 27
Well mixed
Poorly mixed
Urban (Polluted Site)

## Slide 28: GCAS-Inferred Nose-level NO2 as a f(LT) on 25 September

## Slide 29
September 25
1440 LT 4 x 4 km CMAQ NO2 250 x 250 m GCAS-Inferred NO2
Notes: TX – 20130925
CMAQ 14:40 CDT
Red box in left map shows zoom region
GCAS overflight, same scale
(cf. time series plot for this day, slide 12)

## Slide 30
Station | Median GCAS/GB | GCAS–GB Correlation | Location
La Porte | 1.30 | 0.80 | Polluted
Manvel Croix | 0.76 | 0.75 | Polluted
Texas Avenue | 0.75 | 0.78 | Polluted
Seabrook Park | 1.70 | 0.43 | Coastal
Smith Point | 0.49 | 0.49 | Coastal
Galveston | 1.34 | 0.02 | Marine
Summary statistics at true NO2 sites for all 9 flight days
CMAQ Mean surface NO2 during
Period of airborne remote sensing for
September 25

## Slide 31: Scatterplots for all overpasses comparing ground-based NO2 measurements (x-axis) with CMAQ NO2 (y-axis) Inferred GCAS-based NO2 (y-axis)
Notes: Same slope and r for both, coincidentally.

## Slide 32: 15-20 UT Scatterplots comparing ground-based NO2 measurements (x-axis) with CMAQ NO2 (y-axis) Inferred GCAS-based NO2 (y-axis)
Inferred GCAS/CMAQ NO2 agrees better with obs than CMAQ NO2, esp during mid-day

## Slide 33: Conclusions
GCAS provides high-resolution info (250 x 250 m) on spatial distribution of NO2 over Houston-Galveston Bay area during D-AQ campaign
CMAQ captures inland advance of pollutants associated with bay/sea breeze
Nose-level NO2 over Houston-Galveston Bay area has been inferred using GCAS and surface to column relationship from CMAQ
Inferred NO2 concentrations are biased high when PBL is poorly mixed. This information can be used to refine surface estimates
Correlations between inferred and measured surface concentrations are highest at polluted sites and during mid-day hours