## Slide 1: Development of JEDI Based AIRNow and AOD Assimilation Capabilities to Improve RRFS-CMAQ Predictions
Youhua Tang1,2, Cory Martin3, Min Huang2,3, Tianfeng Chai1,4, Mariusz Pagowski5,6, Hongli Wang5,6, Daryl Kleist3, Barry Baker1,2, Patrick Campbell1,2, Jianping Huang3,7, Jeff McQueen3, Raffaele Montuoro3,6, Rick Saylor1, Daniel Tong1,2, Catherine Thomas3, Ivanka Stajner3, Youngsun Jung8
1. NOAA Air Resources Laboratory (ARL), College Park, MD.
2. Center for Spatial Information Science and Systems, George Mason University, Fairfax, VA.
3. NOAA National Centers for Environmental Prediction (NCEP), College Park, MD
4. CISESS, University of Maryland, College Park
5. NOAA Global Systems Laboratory 6. CIRES, University of Colorado, Boulder
7. I.M. Systems Group Inc., Rockville, MD 8. NOAA NWS/STI
Acknowledgement: This work is sponsored by the NOAA JTTI FY20 Funding #NA20OAR4590352.

## Slide 2: Background
An inline air quality model, FV3-Based Unified Forecast System (UFS) with CMAQ chemical mechanism (UFS-AQM), is under development in NOAA. The corresponding chemical data assimilation (DA) capabilities are needed for the atmospheric composition prediction.
The new DA platform, Joint Effort for Data-Assimilation Integration (JEDI), starts to replace the old GSI platform. We are working on assimilating for both in-situ measurements and remote sensing data on the JEDI.

## Slide 3
JEDI Interface to various models

## Slide 4: JEDI’s Major Components
Object-Oriented Prediction System (OOPS): the generic data assimilation algorithms that can be used with different models and different observations
Interface for Observational Data Access (IODA): ingests and processes observational data
System Agnostic Background Error Representation (SABER): computing and working with the background error covariance matrix, often referred to as the B matrix
  BUMP: Background error on an Unstructured Mesh Package
  GSI: interface to the GSI covariance
  ID: identity operator
  SPECTRALB: spectral covariance/correlation
  StdDev: standard-deviation application
Unified Forward Operator (UFO): it enables the comparison between model forecasts and observations
FV3-JEDI: interface between the generic components of the JEDI system and FV3-based models
(NOAA GFDL, NOAA GFS, NASA GEOS)
MPAS-JEDI: interface between the generic components of the JEDI system and the MPAS model

## Slide 5: JEDI compared to old DA system, e.g. GSI
Cons
Longer learning curve (C++/FORTRAN mixed coding)
Sometimes it is hard to debug.
Could be sensitive to the compiler versions and bugs.
Pros
Rich community resources with various existing DA algorithms (3D-Var, 4D-Var, EnKF, LTEKF), observations and filters.
In most times, user only needs to change the yaml control file for the data assimilation.

## Slide 6: Current Status of Chemical DA in JEDI
So far, the existing methods only adjust concentration fields, e.g. chemical initial conditions. No emission assimilation yet.
It can handle the in-situ measurements, satellite/AERONET AOD, other column total retrievals (TROPOMI NO2, for example).
Most existing users are in the FV3-JEDI community.

## Slide 7
FV3-based online CMAQ
Regional Chemical Model
Emissions
Chemical Lateral Boundary Condition
GEFS
Met Lateral Boundary Condition
GFS
FV3-JEDI Regional
Chemical DA (both AIRNow and AOD)
FV3-JEDI Global
AOD DA
GDAS

## Slide 8: PM2.5 forward operator for online CMAQ (Aero6)
aso4i, ano3i, anh4i, anai , acli , aeci , aothri , alvpo1i , asvpo1i , asvpo2i , alvoo1i ,
alvoo2i , asvoo1i , asvoo2i
aso4j, ano3j , anh4j , anaj , aclj , aecj , aothrj , afej , asij, …. …… ……….
alvoo2j , asvoo1j , asvoo2j
aso4k, asoil , acors , aseacat , aclk , ano3k , anh4k
ATOTI
ATOTJ
ATOTK
PM2.5
PM25AT
(Aitkin mode portion in D< 2.5μm)
PM25AC
PM25CO

## Slide 9: AOD CMAQ Reconstruction method
Sulfate, Nitrate, Ammonium Aerosols (RH Dependence)
Elemental Carbon
Fine minerals (I,J mode)
Organic Carbon
Sea Salt (RH dependence)
Coarse minerals (K mode)
AOD Mapping to GOCART method (Tang et al., 2017)
Sulfate Aerosol
Black carbon (hydrophilic)
Organic carbon (hydrophilic)
Sea Salt
Dust

## Slide 10
AIRNow DA B-matrix Tuning. To reduce the noisy incremental result, AIRNow data is thinned/averaged to the model grid and corresponding observation standard deviation is used as observation error (DA1A).
DA3C: same as DA1A but limit the ObsError < 2 μg/m3 and each model aerosol error > 0.1 μg/m3.
DA3E: same as DA1A but limit the ObsError < 1 μg/m3 and each model aerosol error > 1 μg/m3.
DA3G: same as DA1A but limit the ObsError < 1 μg/m3 and each model aerosol error > 0.1 μg/m3. with varied horizontal length scales (75km in western U.S. and 150km in the eastern U.S).

## Slide 11: An example of AOD forward operator turning compared AIRNow DA. CMAQ reconstruction method (RM) (Binkowski and Roselle, 2003) allow users to define aerosol extinction coefficients.
DA

## Slide 12
Elevated biomass burning plume not captured by the model

## Slide 15
Surface PM2.5 Prediction without and with DA for summer 2019

## Slide 16
Surface Ozone Prediction without and with DA for Summer 2019

## Slide 17: Summary
We developed and tested the 3D-Var method in JEDI to assimilated the AIRNow surface in-situ observation. The AIRNow data assimilation in 4 cycles per day always improve the predictions
The VIIRS AOD DA (18Z) could have mixed results, and its aerosol increment could have inconsistency with the AIRNow DA. The issue could be related to retrieval quality, aerosol type/size and vertical distribution etc.
DA results highly depend on B-Matrix, and operators (for AOD DA) etc. Further tune are needed to improve the assimilation.
Acknowledgement: This work is sponsored by the NOAA JTTI FY20 Funding #NA20OAR4590352.