## Slide 1: Development and Application of Shipping Emissions Estimation Program
Fiona Jiang1, Beata Czader2, Christian Lindhjem1, Marco Rodriguez1
1Ramboll
2Texas Commission on Environmental Quality

## Slide 2: Ramboll’s MARINER tool

## Slide 3: What is MARINER?
Photo by Vidar Nordli-Mathisen on Unsplash
Photo by Lynda Hinton on Unsplash
A Python tool that automates
  the estimation of commercial marine vessel (CMV) emission inventories
  the generation of air quality modeling inputs
Development started in 2015, and its functionality has been continually expanded
Follows the 2020 EPA Ports Emissions Inventory Guidance explicitly

## Slide 4: Automatic Identification System (AIS)
Real-time tracking system
Collects vessel traffic data, such as location, time, speed, etc.
Available in U.S. and international waters
Required on all commercially active (small and large) vessels since late 2016
Quality assured data on the Marine Cadastre (a joint U.S. BOEM and NOAA initiative)
Notes: The AIS records provide a variety of attributes associated with vessel movements, including position, date and time, speed over ground, course over ground, instantaneous draft, vessel identification codes, and vessel type.
Starting in March 2016, all commercially active vessels were required to install AIS transponders; includes tug and other small craft used usually on inland waterways. Though data might not be completed until 2017.
Marine Cadastre is a publicly-available US government database. Quality assured via the Authoritative Vessel Identification System.

## Slide 5: Sea-Web IHS Markit Ships Database
Vessel size, age, type of cargo, and total capacity
Main engine, auxiliary engine, and boiler specifications
Fuel and exhaust scrubber types
Over 200,000 vessels characterized
Limited for domestically owned smaller vessels
Notes: IHS is very limited for domestically owned smaller vessels. IHS is useful primarily for large ocean-going vessel.

## Slide 6: MARINER Flowchart
Filter & Process AIS Data
Identify vessel types
Determine trips
Activity calculation
Match with IHS Database
Identify engine tier
Emission & Load Factors
Calculate Emissions
Combine AIS and IHS data to calculate emissions
Spatial Processing
Assign emissions to model grid, county, etc.
Fill missing data
Inputs for MARINER
AIS data
IHS data
User’s input (time period, domain, etc.)
Subset AIS data
Final Products
Emission Inventory for regulatory reporting
EPS3 PRESHP input files for photochemical modeling
Determine engine category
Temporal Profiles
Activity Report

## Slide 7: Emissions
Date Time | Latitude | Longitude | MMSI | IMO | AIS Vessel Type | Operating Mode | EPA Ship Type | Vessel Class | Propulsion NOx (g) | Auxiliary NOx (g) | Boiler NOx (g)
7/24/2019 20:11 | 31.78273 | -93.0199 | xxx | xxx | 00 | Transit | Miscellaneous (C3) | C3 | 269 | 4.0 | 3.3
7/24/2019 20:14 | 31.78497 | -93.0226 | xxx | xxx | 00 | Maneuvering | Miscellaneous (C3) | C3 | 160 | 2.5 | 2.2
7/24/2019 20:16 | 31.78702 | -93.0245 | xxx | xxx | 00 | Hotelling | Miscellaneous (C3) | C3 | 127 | 1.8 | 1.7
Highly resolved by vessel, vessel type, spatial region or temporal period
Can be aggregated over desired resolution by modeling grid scale and temporal event for air quality modeling
Example of calculated emissions for a vessel

## Slide 8: Application to Shipping Emissions in Texas

## Slide 9: Importance of Shipping Emissions in Texas
Texas and Gulf Coast – home to very active shipping lanes and some of nation's busiest ports
The Houston-Galveston-Brazoria (HGB) ozone nonattainment area impacted by shipping activity
CMV emit NOx and VOC impacting air quality
Chart: Tonnage of Top U.S. Water Ports
| Houston, TX | South Louisiana, LA | Corpus Christi, TX | New York, NY and NJ | New Orleans, LA | Long Beach, CA | Baton Rouge, LA
Total tons (millions) | 275.9403 | 225.0867 | 150.7555 | 123.6974 | 81.0674 | 79.1781 | 71.6869
Data Source: Bureau of Transportation Statistics
Notes: CMV emit NOx and VOC impacting ozone formation and air quality in the area.
It is essential to understand and quantify CMV emissions to be able to project in future years.
Couple of ports along the Gulf, the Houston port is the largest.
The bar chart shows top US water ports. Port of Houston is the largest. Other ports in the area: Freeport, Texas City, and Galveston add about 30% to the Houston tonnage. All of these port operations impact the HGB air quality.”

## Slide 10: Tracking Emissions by Vessel Activity
Custom SCC codes
distinguish and allow tracking emissions from different vessel activities
Transit Emissions
Maneuvering Emissions
Hoteling Emissions
Notes: Custom SCC codes allow tracking emissions from different activity types
Spatial pattern of emissions varies with activity type
Transit – Emissions in the Houston Ship Channel and along the coastline
Maneuvering – Emissions mainly in the Houston Ship Channel, lower values along coastline
Hoteling – Emissions at the entrance to the Houston Ship Channel and at the end of it. Also, on the left from the Houston Ship Channel, emissions from port Freeport, located about 60 miles south of Houston, near industrial businesses

## Slide 11: Tracking Emissions by Vessel Type
Custom SCC codes
Distinguish and allow tracking emissions from different vessel types
Chart: 2019 emissions by vessel type in HGB
| Offshore Support/Drillship | Government | Work Boat | Refrigerated (REEFER) Cargo | Dredging | Pilot Boat | Crew and Supply | Other Tanker | Roll-On/Roll-Off (RORO) | Fishing (C1/C2) | Harbor Ferry (C1/C2) | Cruise Ship | LNG Tanker | Bulk Carrier | General Cargo | Miscellaneous | Container Ship | Tug Boat | Crude Oil Tanker | Chemical Tanker | Towboat/Pushboat
NOx (tons per day) | 0.0009991 | 0.015926 | 0.0501 | 0.0699 | 0.13541 | 0.23591 | 0.32611 | 0.4281 | 0.6039 | 0.6443 | 0.7615 | 0.8591 | 1.3895 | 1.7916 | 2.3241 | 2.3589 | 2.4249 | 3.4915 | 3.735 | 7.7004 | 19.9334
Total 63 custom SCC codes represent
21 vessel types and
3 activity types

## Slide 12: Houston Ship Channel Sensitivity
Houston Ship Channel expected emissions reductions due to its expansion plans
  fewer large ships
  reduced hoteling
MARINER estimated emissions
  2026 future year
  Harris, Chambers, Galveston Counties
  Category 3 vessels: 9 vessel types
  Hoteling only
Image source: www.expandthehoustonshipchannel.com
Period​ | NOx​ | VOC​
Annual Reductions (tpy)​ | 147.20​ | 3.35​
Daily Reductions (tpd)​ | 0.40​ | 0.01​
Daily Unadjusted Emissions (tpd)​ | 16.71​ | 2.18​
Daily Adjusted Emissions​ (tpd) | 16.31 | 2.17
Daily Adjustment Factor​ | 0.9759​ | 0.9958
Notes: Expected reductions only for 9 categories of ocean-going vehicles, not harbor craft, and only for Hoteling
Current emissions Nox = 19.4 tpd, expected reductions Nox = 0.4 tpd, percent of expected reductions = 2%
Daily unadjusted emissions = current emissions – expected daily reductions

## Slide 13: MARINER and EPA 2016v2 Platform Emissions
Emission decreases between 2023 and 2026
NOx emission estimates slightly higher from MARINER
VOC emission estimates slightly lower from MARINER
Chart: CMV Emissions
| NOx (TPY) | VOC (TPY) | CO (TPY)
2023 EPA | 30286 | 2526 | 5673
2023 TCEQ | 32347.9 | 2217.8 | 6167.2
2026 EPA | 27912 | 2601 | 5929
2026 TCEQ | 28896.4 | 2267.2 | 6463.6
Notes: Blue colors – EPA estimates
Orange colors – MARINER estimates

## Slide 14: Potential Future Development Ideas
Expand estimates to waters outside Texas
Reduce memory requirement
Minimize mismatched vessels
Prepare CAMx or CMAQ-ready emission files
Notes: Added CMAQ since it’s a modeling conference; Conduct a formal uncertainty analysis to determine which data strongly influence emission magnitude

## Slide 15: Questions?
Contacts:
Fiona Jiang fjiang@ramboll.com
Beata Czader beata.czader@tceq.texas.gov