## Slide 1: Resolving the effect of roadside green infrastructure on near-road air quality in a multi-regime modeling framework
Richard Baldauf, U.S. Environmental Protection Agency
CMAS Annual Meeting
October 19, 2022

## Slide 2: Introduction
Interest in planting more trees and providing more urban green space has grown in recent years
  Global planting programs such as the Trillion Trees Initiative
  Climate adaptation and mitigation projects for stormwater management, urban cooling, and CO2 sequestration
Recent research shows that urban green infrastructure can also impact local air pollution and mitigate select SLCPs, notably black carbon
  Promoting urban vegetation can have multiple benefits on climate change mitigation, air quality, and overall improved public health
  Care is needed on the design and implementation of urban green infrastructure development, especially when sited near large roadways and other air pollution sources
SLCPs = short-lived climate pollutants

## Slide 3: Presentation Overview
Background
  Air pollution health concerns
  SLCP climate concerns
  Air quality and SLCPs mitigation opportunities
Urban green infrastructure and air pollution
  Mechanism of air pollution mitigation by vegetation
  Research on vegetation air pollution mitigation
Dispersion modeling framework
Relevant resources
Conclusions

## Slide 4: Air Pollution Health Effects

## Slide 5
People living, working and going to school near highways and large transportation facilities face increased health risks
Other studies have also linked other adverse effects including:
Childhood leukemia
Cognitive development
Neurological disorders including autism
Health Concerns from Transport
Notes: Reference:
Health Effects Institute, 2010: Traffic-Related Air Pollution: A Critical Review of the Literature on Emissions, Exposure, and Health Effects, p. xv.
See: http://www.sonomatech.com/project.cfm?uprojectid=1163
https://www.healtheffects.org/publication/traffic-related-air-pollution-critical-review-literature-emissions-exposure-and-health
Perez L., Lurmann F., Wilson J., Pastor M., Brandt S., Kunzli N., and McConnell R. (2012) Near-roadway pollution and childhood asthma: implications for developing "win-win" compact urban development and clean vehicle strategies. Environ. Health Persp., (Published online), ed. doi: 10.1289/ehp.1104785. Available on the Internet at http://ehp.niehs.nih.gov/wp-content/uploads/2012/10/ehp.1104785.pdf (found about 8% of childhood asthma was partly due to living within 75 m of a major road).
Right:
References:
Effect of exposure to traffic on lung development from 10 to 18 years of age: a cohort study
By: Gauderman, W. James; Vora, Hita; McConnell, Rob; et al.
LANCET Volume: 369 Issue: 9561 Pages: 571-577 Published: FEB 17 2007

## Slide 6: Short-Lived Climate Pollutants (SLCPs)

## Slide 7
Mitigating transport emissions, exposures, and health effects can be achieved by:
  Reducing vehicle direct emissions
  Reducing vehicle use and activity
  Reducing ambient air concentrations through urban and transportation development
    Increasing urban green infrastructure and green space
Transport Mitigation Options

## Slide 8: How Urban Vegetation Mitigates Air Pollution and SLCPs

## Slide 9: Research Example
Particulate matter including black carbon was reduced downwind of the vegetation
Higher reductions occurred closer to ground-level with winds from the road
Reductions in particle number could be 50% or greater
Steffans et al. (2012)
Steffens et al 2012, Atmospheric Environment, 50, pp.120-128

## Slide 10: Research Example
1
2
3
4
5
6
Baldauf et al., in press
Plant conditions can affect the levels of downwind pollution
    Thick, tall and full coverage reduced pollution downwind of the road
    Gaps and porous vegetation led to no reductions or even higher levels downwind of the road

## Slide 11: Review Articles
Janhäll, 2015. Atmospheric Environment, 105, pp.130-137
Gallagher et al, 2015. Atmospheric Environment, 120, pp.61-70
Baldauf, 2017. Transport Res Part D: Transport & Environ, 52, pp.354-361
Abhijith et al, 2017. Atmospheric Environment, 162, pp.71-86

## Slide 12: Modeling Framework
Parameterization framework: the multi-regime approach
Four regimes:
I: Vegetation
II: Wake
III: Transition
IV: Recovery
Goal for parameterization:
Describe the Gaussian parameters for each regime

## Slide 13: Modeling Framework
TKE ()
Inputs
Vegetation width (W)
Vegetation height (H)
Vegetation LAD
Vegetation LAI
Local wind speed @10m (U)
Concentration (Output)
Key Parameters
LAD/LAI
W
H
U (10 m)
U
Overall parameterization procedure

## Slide 14: Modeling Framework
CFD-assisted parameterization
x
Wind speed ()
1
2
3
4
5
1
2
3
4
5
= 75 LES cases
x
H: 2 m
H: 10 m
Height (m) | Width (m)
2 | 2.5
4 | 6
6 | 8
8 | 10
10 | 12
LAI: 4
LAI: 11
LAI
4
7
11
60 train cases
15 test cases
5 wind speeds
5 dimensions
3 LAI values
Notes: LES: Large Eddy Simulation, a type of turbulence solver that tends to be more accurate but computationally intensive.

## Slide 15: General parameterization procedure
Modeling Framework

## Slide 16
Modeling Framework
Accounting for size-dependent particle deposition
To account for deposition the emission rate A should be modified (Regime I):
Deposition velocity strongly correlates with mass reduction!

## Slide 17
CTAG CFD versus the parameterized Gaussian-based model
NME: 0.18 - 0.3
FB: -0.12 - 0.09
FAC2: 0.93 - 0.98
R2: 0.47 - 0.75
Modeling Framework

## Slide 18: Size-resolved evaluation results
For most particle sizes and the tracer gas, the 0.76, but the value is lower for particles 15 and 22 nm.
The FB was negative across all particle sizes and tracer gas, indicating that the parameterized Gaussian-based model tended to slightly underestimate the vertical concentrations.
Modeling Framework

## Slide 19
The U.S. EPA developed recommendations for planting and maintaining roadside vegetation
18
Urban Vegetation Recommendations
  Used to design and implement planting projects in the U.S. and Europe
  Includes vegetation alone and combined with solid barriers
  Provides designs intended to:
    maximize the potential for air pollution mitigation, and
    avoid unintended consequences and designs that may increase downwind concentrations and exposures
https://www.epa.gov/sites/production/files/2016-08/documents/recommendations_for_constructing_roadside_vegetation_barriers_to_improve_near-road_air_quality.pdf

## Slide 20
Urban vegetation, including roadside barriers, can have many other benefits, including:
  Increased CO2 sequestration
  Methane removal in vegetation soils
  Improved urban cooling
  Reduced stormwater runoff/flooding
  Improved water quality
  Reduced noise levels
  Improved aesthetics/property values
  Enhanced community livability
  Improved general public health
“Exposure to green space has been associated with better physical and mental health”
Urban Green Infrastructure Benefits
Dadvand et al. 2015, Proc. Nat Acad Sciences,
112(26), pp.7937-7942

## Slide 21: Conclusions
20
Climate and health concerns from transportation emissions have raised the importance of understanding how urban infrastructure can be used for mitigation.
Urban and roadside green and built infrastructure can provide important air pollution and SLCP reduction benefits when designed properly.
For More Information:
Richard Baldauf, PhD, P.E.
U.S. Environmental Protection Agency
919-541-4386
Baldauf.Richard@epa.gov
Authors: Khaled Hashad, Bo Yang, Jon Steffens, K. Max Zhang (Cornell Univ.), David Heist (EPA), Parik Deshmukh (ERG)
This presentation has been subjected to the Agency’s review process and has been approved for publication. These are the views of the authors and do not necessarily reflect official policy of the EPA.
Mention of trade names or commercial products does not constitute endorsement or recommendation for use.
Notes: 20