## Slide 1: Public health effects from the adoption of California’s Advanced Clean Cars II regulation in Oregon and Connecticut in 2040
By Jiaoyan (Joey) Huang, Eric Sussman, Jeff Houk, Shih-Ying Chang
Sonoma Technology, Petaluma, CA, USA
For 21st Annual CMAS Conference
October 17 - 19, 2022
STI-7615

## Slide 2: Outline
  California zero emission vehicle regulations
    Advanced Clean Trucks and Fleets: STI and ICCT previous work
    GHG phase 2
    Advanced Clean Cars II
  Motivations for this project
  Methods
    MOtor Vehicle Emission Simulator (MOVES)
    CO-Benefits Risk Assessment (COBRA)
  Results
    Electric vehicle penetration
    Emission reductions
    Co-benefits
  Conclusions
Notes: Add GHG phase 2 ?

## Slide 3: California Governor’s Executive Order N-79-20
Advanced Clean Cars (ACC)
Advanced Clean Fleets (ACF)
Advanced Clean Trucks (ACT)
Source: The Office of the California Governor

## Slide 4: STI and ICCT’s Heavy-Duty Vehicle Analysis (ACT and Low-NOx Omnibus adoption)
https://theicct.org/benefits-ca-multi-state-reg-data/
https://www.youtube.com/watch?v=Qmwm4-zdGfw&t=1s

## Slide 5: California Regulation – Advanced Clean Cars II (ACC II)
Zero emission vehicle (ZEVs) and Plug-in Electric Vehicles (PHEVs) will be 35% of light-duty vehicle (LDV) sales in 2026.
ZEVs and PHEVs will be 100% of LDV sales in 2035.
Low-emission Vehicle Regulations to include increasingly stringent standards for gasoline cars and heavier passenger trucks
ACC II ZEV and PHEV % of new sale in California

## Slide 6: Motivation for this Project
Understand how California ACC II regulation impacts EV penetration and on-road emission reduction in OR and CT in 2030 and 2040
Investigate the health benefits from on-road emission reduction due to adoption of ACC II regulation in OR and CT

## Slide 7: Methods – Scenarios and States
Scenarios | Description
BAU | Business as Usual
ACC II | ZEVs and PHEVs: 100% of light duty vehicles in 2035
 | Oregon | Connecticut
State total VMT | 3.68 x 1010 [Rank 29] | 2.97 x 1010 [Rank 34]
State total VPOP | 3.93 x 106 | 3.04 x 106
State LDV VMT | 3.10 x 1010 | 2.88 x 1010
State LDV VPOP | 3.33 x 106 | 2.85 x 106
Population | 4.24 x 106 [Rank 27] | 3.61 x 106 [Rank 29]
Population density | 44/mi2 | 745/mi2

## Slide 8: Methods – Modeling Workflow
MOVES
MOVES default data
State data
EQUATES 2017 data
Post Process
Well-to-Wheel
GREET emission factors by region
State renewable energy projections
COBRA
County level emission changes
CARB ACC II EV table
CARB ACC II emission reduction table
Downwind state impacts
Social cost (dollar)
MOVES 3.0.3
COBRA 4.1

## Slide 9: Methods – MOVES3 Input Data
MOVES3 Input | Oregon | Connecticut
VMT, VPOP | EQUATES 2017, grown to future years (2030 and 2040) using growth rates developed by OR | EQUATES 2017, grown to future years (2030 and 2040) using growth rates developed by CT
Fuel supply, fuel usage fractions, inspection/maintenance program parameters, VMT month, day, hour fractions | OR state data in 2020 | CT state data in 2020
Road type VMT distribution, vehicle age distribution | OR state data in 2020 | CT state data in 2020
Vehicle technology distribution, speed distribution | OR state data in 2020 | CT state data in 2020
Meteorology, retrofit program data | OR state data in 2020 | CT state data in 2020
LEV | EQUATES 2017 | EQUATES 2017
NLEV | - | EQUATES 2017
County-Level Run | EQUATES 2017 Representative Counties in Each State

## Slide 10: Results – EV penetration
Chart: ZEV population fraction
| 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
BAU | 0.026785 | 0.031213 | 0.036103 | 0.041662 | 0.047204 | 0.053456 | 0.059709 | 0.065969 | 0.072667 | 0.078463 | 0.084747 | 0.091033 | 0.097306 | 0.10357 | 0.10982 | 0.11606
ACC2 started from 2026 | 0.026785 | 0.037619 | 0.05203 | 0.070276 | 0.091333 | 0.11633 | 0.14835 | 0.18297 | 0.22136 | 0.25974 | 0.30221 | 0.34465 | 0.387 | 0.42928 | 0.47148 | 0.5136
ACC2 started from 2027 | 0.026785 | 0.031213 | 0.045637 | 0.063857 | 0.084966 | 0.10998 | 0.14201 | 0.17664 | 0.215 | 0.25344 | 0.29593 | 0.33838 | 0.38074 | 0.42303 | 0.46524 | 0.50738
ZEV fraction in light duty vehicle fleet is 40% higher than BAU scenario due to the ACC II.
Notes: Should we only show 2030 and 2050 Tank to wheel

## Slide 11: Results – NOx Emissions Reductions
NOx Emissions Reductions (tons) |  | 
Year | Connecticut | Oregon
2020 | 0 | 0
2025 | 0 | 0
2030 | 56 | 237
2035 | 167 | 505
2040 | 523 | 835
Total | 2,619 | 6,341
NOx emission reduction is approximately 42% due to ACC II adoption in 2040
Larger reductions are seen in OR than in CT because of the EGU mix
Chart: Well-to-Wheel + grid NOx emission reduction
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
CT reduction | 0.0024913 | 0.00098577 | 0.0039303 | 0.0072234 | 0.0088668 | 0.017953 | 0.030642 | 0.046603 | 0.069111 | 0.09565 | 0.14275 | 0.19848 | 0.26271 | 0.33575 | 0.41662
OR reduction | 0.0021561 | -0.0023518 | 0.0029392 | 0.01147 | 0.024142 | 0.037813 | 0.055 | 0.075672 | 0.10116 | 0.13034 | 0.17141 | 0.21924 | 0.27472 | 0.3399 | 0.41662

## Slide 12: Results – PM2.5 Emissions Reductions
PM2.5 Emissions Reductions (tons) |  | 
Year | Connecticut | Oregon
2020 | 0 | 0
2025 | 0 | 0
2030 | 2 | 3
2035 | 13 | 18
2040 | 40 | 52
Total | 187 | 242
PM2.5 emission reduction is 17% due to ACC II adoption in 2040
Chart: Well-to-Wheel + grid PM2.5 emission reduction
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
CT reduction | 0.00077897 | 0.0023752 | 0.004184 | 0.0063159 | 0.0086371 | 0.012751 | 0.018719 | 0.026505 | 0.037613 | 0.050774 | 0.068459 | 0.088633 | 0.11188 | 0.13736 | 0.16555
OR reduction | -0.0012827 | -0.0016303 | -0.00078866 | 0.00227 | 0.0087498 | 0.012959 | 0.019107 | 0.027409 | 0.038876 | 0.052957 | 0.070275 | 0.089984 | 0.11272 | 0.13774 | 0.16555

## Slide 13: CO-Benefits Risk Assessment (COBRA) Screening Model
EPA screening model used to quantify how changes in air emissions from policy decisions affect human health
User inputs emissions estimates from various industries/sectors for a baseline scenario and a sensitivity case study for the following pollutants:
  PM2.5, NOx, NH3, SO2, VOC, SOA
Model outputs the change in various air pollution related health incidence rates, as well as their associated economic costs
https://www.epa.gov/sites/default/files/2017-10/documents/cobra_training_eic_2017.pdf

## Slide 14: Methods – COBRA Input Data
COBRA Input | Data | Scaling Factor (2040/2028)
Baseline Incidence File | Default | --
Modeled Year | 2028 | --
Population File | 2028 default data scaled to 2040 | U.S. Census projection data
Baseline Emission | 2028 default data with scaled electricity generation and highway vehicle emissions to 2040 levels | Electricity generation: Energy Information Administration (EIA) projection data Highway Vehicles: MOVES3 national scale default data
Sensitivity Emission File | 2028 default data with replacement electricity generation (from GREET) and highway vehicle (from MOVES3) emissions | --
Discount Rate | Both 3 and 7% | --

## Slide 15: Results – COBRA, Modeled PM2.5 Concentration Decrease (µg/m3) from EV penetration from BAU in 2040
Connecticut
Oregon
Notes: Only 7% interest shown
Dollars are 2017 dollars

## Slide 16: Results – COBRA, Connecticut 2040
Analysis Year | In-State Benefit | Out-Of-State Benefit | In-State Burden | Out-Of-State Burden | Net Benefit
2040 | 15.58 | 10.01 | 0 | 0 | 25.60
Annual COBRA-estimated economic values of CT adopting ACC II, in millions of US dollars
Top five states that are most impacted by CT’s adoption of ACC II: New York, Massachusetts, Rhode Island, New Jersey, New Hampshire
Notes: Only 7% interest shown
Dollars are 2017 dollars

## Slide 17: Results – COBRA, Oregon 2040
Annual COBRA-estimated economic values of OR adopting ACC II, in millions of US dollars
Top five states that are most impacted by OR’s adoption of ACC II: Washington, California, Idaho, Nevada, Montana
Analysis Year | In-State Benefit | Out-Of-State Benefit | In-State Burden | Out-Of-State Burden | Net Benefit
2040 | 8.60 | 4.21 | 0 | 0 | 12.81

## Slide 18: Conclusions
NOx emission reduction (for RegClass 20, 30, 41) is approximately 42% and PM2.5 emission reduction (for RegClass 20, 30, 41) is 17% due to ACC II adoption in 2040
ZEV fraction in light duty vehicle fleet is slightly higher than 50% in 2040 which is 40% higher than BAU scenario.
Significant economic benefit for adopting ACC II for both the state (CT: $16M, OR: $9M) and their neighbors (CT: $10M, OR: $4M).

## Slide 19
Joey Huang
Air Quality Scientist
jhuang@sonomatech.com
Shih-Ying Chang
Air Quality Scientist
cchang@sonomatech.com
SonomaTech.com 707-665-9900
Jeff Houk
Transportation / Air Quality Analyst and Emissions Modeler
jhouk@sonomatech.com
Eric Sussman Air Quality Engineer
esussman@sonomatech.com

## Slide 20: Methods –
 | NPCC Mix (CT, MA, ME, NY, RI, VT) | RFC Mix (DC, MD, NJ, PA) | SERC Mix (NC) | WECC Mix (CO, OR, WA)
NOx | 19.370 | 45.157 | 50.017 | 39.549
PM2.5 | 2.180 | 5.985 | 5.147 | 3.988
CH4 | 3.787 | 9.491 | 8.497 | 6.273
N2O | 0.177 | 1.510 | 1.325 | 0.936
CO2 | 51,233 | 106,161 | 94,078 | 68,252
These 2020 values used as a baseline for all calendar years, and state-provided grid renewable energy projections were used to adjust the rates for future years.

## Slide 21: Results – COBRA, Population Map
Connecticut
Oregon
Notes: Only 7% interest shown
Dollars are 2017 dollars