## Slide 1: GPU Accelerated CMAQ Simulation
Khanh Do, George Delic, Bryan Wong, Cesunica Ivey
2022 CMAS Conference

## Slide 2: Motivation
Traditional CMAQ
  CPU Intensive processes and long simulation time
  Require lots of computing power
  8 to 32 threads per each run
Graphics processing unit (GPU)
  More than 10,000 CUDA cores (NVIDIA RTX 3090)
  Compute Unified Device Architecture (CUDA) released in 2007
  World’s first solution for general computing on GPUs (GPGPU)
GPU is used to accelerate the Community Multiscale Air Quality (CMAQ) model
  Parallelize and vectorize independent loops
  Target numerically intensive routines (horizontal advection, gas chem)
  Increase efficiency and reduce simulation time
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method

## Slide 3
Chart: Processor Cores
| 1 | 2 | 4 | 6 | 9 | 12 | 16
time | 9 | 4.5 | 2.2 | 1.5 | 0.75 | 0.45 | 0.35
Expectation: Double CPU cores, computational time decreases by half.
CMAQ configurations
  Parallelization with OpenMPI
  SAPRC-07 mechanism
  4x4 km resolution
  11 vertical layers
  156x102 grids
  Southern California
Computer configurations
  Ryzen R9 5950x with 16 cores
  16 GB of memory DDR4
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method
Figure 1: CMAQ Module Timing for one day simulation period.
Figure 2: Timing for one iteration step.
The Slowest Science Module in CMAQ

## Slide 4: CMAQ CHEM Solver
EBI (1993)
  EBI is the fastest but less accurate, convergence errors (stiff ODEs)
Rosenbrock (1997)
SMVgear (1994)
  Gear solver used to obtain accurate solutions to stiff ODE problems
  Highly vectorized and incorporated with sparse matrix to improve computational performance
  Slowest solver due to computing partial derivative, matrix decomposition, and backsub
CMAQ spends about 20% on EBI, 30% on Rosenbrock, and 50% on smvgear solver (George Delic)
Gear Solver
CMAQ Performance
Background/Objective
hrsolver
Future Work
Method
Timing
Figure 3: Time for one hour simulation with EBI and GEAR solver.

## Slide 5: Why GPU?
Central processing unit (CPU)
  Very fast, smart, and low latency
  Handle complex program
  Have very few cores and limitations in parallelization
Graphics processing unit (GPU)
  Thousands of cores
  Made up of many smaller and more specialized cores
  Speed up the massive workload by divided into many processes
  Traditionally known for rendering which GPU drawing millions of polygons each second (output billion pixels per second)
  Handle independent repetitive tasks
Intel Core i9 CPU
NVIDIA RTX 3090
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method

## Slide 6: Methods
Determine the CMAQ slowest process
  CHEM solver, advection, diffusion process
Create GPU-friendly data structure and algorithms (matrix operations)
  Scalable
  EBI, ROS, and GEAR solver
Design compilation compatibility with the CUDA platform
Perform code independent analysis
  Parallelizing can intentionally alter the results
  Only work with independent loops
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method

## Slide 7: Compilation with CUDA Platform
Traditional CMAQ is compiled with Intel/GNU Fortran compiler
  OpenMPI (GCC or ICC)
    All current CMAQ modules/subroutines
    Execute by the CPU
nvfortran
  Codes execute by the GPU
  Codes transfer data between CPU and GPU
One step compilation for CCTM
  by integrating CUDA platform to the makefile
  Simplify compilation process and make it easy for future improvements.
Figure 4: Ozone outputs from CMAQ compiled using MPICH/OpenMPI and MPICH/OpenMPI + nvfortran are the same over 14 days simulated period. Outputs must be the same cross different compilation methods.
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method

## Slide 8
sciproc.F
pa_output.F
pa_update.F
chksummer.F
hadv.F
zadv.F
couple_wrf.F
decouple_wrf.F
hdiff.F
vdiff.F
cldproc.F
chem.F
phot.F
grsmvgear.F
The driver.F calls all the subroutines and modules to perform simulation. The science processes (sciproc.F) contains all of our interest subroutines that we want to modify.
Showing on the diagram is the simplified version of CMAQ program.
CMAQ Flowchart
driver.F
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method
Figure 5: Visualization of GEAR solver location.

## Slide 9: GPU EBI Solver
EBI is very efficient
  CPU version takes 7x10-2 ms to solve for 1 grid cell
  GPU version takes 5x10-2 ms for data transfer between memory for 1 iteration (15 iteration to converge)
  If we only need 1 time data transfer per grid cell, still slower than CPU
Gear solver
  BLKSIZE
  Scalable
Chem Solver for One Iteration
Figure 6: Timing the EBI solver for one iteration step per grid cell. CPU + GPU version is significantly slower than the traditional CMAQ.
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method

## Slide 10: Timing Gear Solver Module (BLKSIZE = 50)
GEAR_DRIVER
FIND_DEGRADE
5X10-5 s
BACKSUB
0.6x10-4 s
SVMGEAR
2x10-2 s
FINAL_DEGRADE
10-5 s
DECOMP
0.8x10-3 s
SUBFUN
10-4 s
PDERIVE
0.2x10-3 s
Gear for gas phase subroutine
CPU only
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method

## Slide 11: GPU GEAR Solver Flowchart
grpderiv.F
pdkernel.cuf
intermediate.F
grpdecomp.F
dckernel.cuf
intermediate.F
grsubfun.F
sfkernel.cuf
intermediate.F
grbacksub.F
bskernel.cuf
intermediate.F
GEAR driver
Convergence check
Some updates to the GEAR driver
Repeat until converged
On device
On host
data transfer
host <-> device
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method
Gear Solver
data transfer
host <-> device
data transfer
host <-> device
data transfer
host <-> device
Some updates to the GEAR driver
Some updates to the GEAR driver

## Slide 12: Performance of the CMAQ-GPU
BLKSIZE 7000 | grpderiv.F (second) | grdecomp.F (second) | grsubfun.F (second) | grbacksub.F (second)
GPU Time | 0.07 | 0.11 | 0.037 | 0.05
CPU Time | 0.04 | 0.13 | 0.017 | 0.013
GPU Kernels perform the same operations as the CPU subroutines, but it is much faster (several order of magnitudes)
GPU Time = copy data to device + kernel time + copy results to host
It spends about 99% of the time for data transferring
Table 1: CMAQ simulation was in series (1 CPU core) with BLKSIZE of 7000. The time was for one each iteration
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method

## Slide 13: Error
Max difference is 9.1%
0.24% of the simulation results have a difference greater than 1%
Errors from parallelizing dependent loops, conversion check
Gear Solver
Background/Objective
Timing
hrsolver
Future Work
Method
CMAQ Performance
Figure 7: Percentage difference between traditional CMAQ and CMAQ-GPU.

## Slide 14: GPU GEAR Solver Flowchart
pderiv
decomp
subfun
backsub
GEAR driver
On device
On host
convergence check
Init and Update
reduce time-step
finish
intermediate
Gear Solver
Background/Objective
Timing
hrsolver
Future Work
Method
CMAQ Performance

## Slide 15: Preliminary Results of a Fully Ported Gear Solver
With only 1 GPU, CMAQ-GPU for GEAR is comparable with EBI.
Simulation time can be greatly reduced for systems with multiple GPUs.
The errors between CPU and CPU + CPU versions are huge
  Feedback loop to check for conversion
  Parallelize dependent loops
Gear Solver
Background/Objective
Timing
hrsolver
Future Work
Method
CMAQ Performance
Figure 9: Difference between traditional CMAQ and CMAQ-GPU
Figure 8: CMAQ-GPU benchmark

## Slide 16: Hardware Optimization
Data transfer rates and bandwidths are double in a couple of years
DDR6 is twice times as fast as DDR5
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Method
Future Work
Can We Further Improve CMAQ Simulation Time?
  Kernel optimization
  Hardware optimization
    Modern hardware
    Multiple GPUs
  Port more CMAQ modules/subroutines onto the GPU (HAVD, CLDPROC)

## Slide 17: Future Work
Complete porting GEAR to the GPU
Compare results with the CPU version
Simplify and optimize GPU kernels
Simplify the process of CMAQ compilation with GPU assisted CMAQ
Effect of GPU on integrated process and reaction rate analyses
Perform long-period simulations (2017-2024 and 2047-2054) to investigate meteorological drivers of ozone levels in SoCAB
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Method
Future Work

## Slide 18: Summary
Chem solvers are the slowest module of CMAQ
We can compile CMAQ GPU by combining the GCC compiler (for CPU codes) and nvfortran (for GPU codes). The outputs of the program are not different compared to traditional CMAQ
We ported the EBI solver on the GPU, but the computation time was much slower than the traditional CMAQ
  Cost of transferring data between the host (system) to the device (GPU)
  Small loop computation which did not take advantage of GPU
We replaced EBI solver on CMAQ with SMVGear
  Variable block size (larger block size, bigger data array)
  Large sparse vectorized matrices fully utilize the GPU
  Significant improvement even with a system with only one GPU
  Simulation results show errors
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method

## Slide 19: Thank you and Acknowledgments
Cesunica Ivey
Air Quality Modeling and Exposure Lab (AQMEL)
Nanoscale & Mesoscale Energy Materials Research Group
  Bryan Wong
  Prithviraj Yuvaraj
  Jose Rodriguez Borbon
George Delic from Hiperism Consulting LLC
This material is based upon work supported by the National Science Foundation under Grant No. 2053560. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.

## Slide 20: Back-up Slides

## Slide 21
grpderiv.F
pdkernel.cuf
intermediate.F
grpdecomp.F
dckernel.cuf
intermediate.F
grsubfun.F
sfkernel.cuf
intermediate.F
grbacksub.F
bskernel.cuf
intermediate.F
GEAR driver
Convergence check
Some updates to the GEAR driver
Repeat until converged
Some updates to the GEAR driver
Some updates to the GEAR driver
data transfer
host <-> device
data transfer
host <-> device
data transfer
host <-> device
data transfer
host <-> device
pderiv
decomp
subfun
backsub
GEAR driver
On device
On host
convergence check
Init and Update
reduce time-step
finish
intermediate
First ported GEAR version
Second ported GEAR version

## Slide 22: Simple Computer Architecture
(Keyboard, mouse)
(Monitor, printer)
100 MB/s
20,000 MB/s
20,000 MB/s
Program and data are loaded from storage and stored in system memory
Outputs are temporarily stored in memory and written to a hard drive for long term storage
All processes are executed by the CPU
  Modern CPUs have 2-16 cores per CPU
Most of today’s programs are written for the CPU
Figure: Simple computer architecture

## Slide 23: Simple Computer Architecture with a GPU
GPUs
Figure: GPU server
Figure: Computer with a GPU
Figure: Memory space on host and device (Seo at al., 2011)
Device/Host Memory Allocation

## Slide 24: Launching GPU Kernel
Figure: CUDA programing model (Gulati et al., 2009)

## Slide 25: Hardware Optimization
Current hardware
  DDR4 2666MHz
  PCIe 3.0
  CPU with 9 MB cache
  Double channel memory
DDR4 21GB/s
Limited by DDR4 Transfer Speed
Limited by PCIe 3.0 bandwidth
PCEe 3.0
16GB/s
< 9 MB
4GB
Gear Solver
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method
Figure 12: Transfer bandwidth limitation

## Slide 26: The effects of BLKSIZE on CMAQ Performance
CMAQ needs to solve the chem concentrations in all the grid cells
If the BLKSIZE is 1, the times that CMAQ calls the GEAR solver are equal to the number of total grid cells (row x column x height)
If the BLKSIZE is 1000, CMAQ calls the GEAR solver less than 1000 times (row x column x height/BLKSIZE)
Advantages
  More independent computation per one function call
  Optimized for GPU computation
Disadvantages
  Resulting in large arrays. Arrays with 1000 x 5400 dimensions are more than 40 megabytes
  CPU caches are small (30MB for high-end CPU). If an array is larger than CPU caches, the CPU must grab the extra data from system memory (RAM) which decreases the overall efficiency
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method
Gear Solver

## Slide 27
SMVGEAR(CPU only) with Different BLKSIZE
Effects of BLKSIZE on CMAQ performance
  Increase in BLKSIZE has negative effects on CMAQ performance
  CHEM process (GEAR solver) is largely affected. The change of other processes, such as vdiff is negligible with BLKSIZE
CMAQ Performance
Background/Objective
Timing
hrsolver
Future Work
Method
Gear Solver
Linearly increase computation time with increased block size
Total computation time for CMAQ remained the same
The default CMAQ BLKSIZE is 50
Linearly system memory
Figure 7: Effect of BLKSIZE on computational time and system memory.
Figure 8: Effect of BLKSIZE on simulation time for different processes.