## Slide 1: Potential Impact of Future Climate on Winter Time Particulate Matter in the Western U.S
Abiola S. Lawal, Cam Phelan, Heather Holmes, Cesunica Ivey
CMAS 2022
October 17th 2022

## Slide 2: Why is it important to look at Wintertime Particulate: Connection to PCAP/CAP
An event where elevated levels of particulate matter are caused due to an inversion layer (cold layer) below a warm layer (above)
Prevents mixing and leads to higher levels particulate matter.
CAP: Cold Air Pool
PCAP: Persistent Cold Air Pool (Lasting a couple of days)

## Slide 3: An Illustration of Winter Time Particulate Matter
1
2
Results in elevated particulate matter
Cooled Air pool
Pollutants are trapped
Build up over time
More reaction chemistry
Mountainous terrain allows for a pool of cold air to gather
Health implications
Visibility
Persistent Cold Air Pool (PCAP)
3

## Slide 4
PCAPs are characterized by episodes of elevated particulate matter and pollutant trapping
Geography matters
  Tends to persist in the western mountainous regions due “trapping” between ridges
  Loss of horizontal transport
Physical Dynamics created by meteorological conditions
  A loss of heat leading to a cooled air and inversion layer.
  Cold conditions: Winter Time PM
  Heat loss: Heat valley deficit (VHD)
Chemical Dynamics
  Atmospheric chemistry (PM largely comprised of nitrate)
  Daytime and night time chemistry can affect it.
  Winter time chemistry
Emissions
  Source profiles: different sectors have different impact
Temporal
  Definition: Anything lasting from 2 days to 3 days
Conditions that favor formation of a PCAP
Notes: https://www.valleyair.org/newsed/ca_primer/bigpicture/IIIA4a.html

## Slide 5
Project falls under umbrella of NIH funded project
To improve our understanding of winter time particulate matter.
  Particulate matter that is trapped primarily consists of secondary aerosol (80%)
  Goal: Through novel air quality modeling techniques, improve our understanding of sources and chemical formation mechanics in regards to aerosol formation. Will help with mitigation strategies.
  Will collect health data for 12 “mountainous cities”
Dr. Cesunica Ivey (PI)
Air Quality modeling
Dr. Heather Holmes (PI)
WRF Modeling/Meterology
Dr. Jenna Krall
Biostatistics
Dr. Calvin Riss
Epidemiology
Notes: Limitation with source apportionment models as typically used for primary aerosol

## Slide 6: Air Quality Modeling: AQMEL Group at UCB
Emissions
  Source Apportionment
    ISAM/DDM
  Develop new speciation profiles
Meteorology
  Levels: 41 vs 35
  Short wave and long wave radiation parameters
  Microphysics
Aerosol Reaction chemistry
  Evaluate differences between AE7 and AE6 (Cam Phelan’s poster please check it out)
  Chemical kinetics and process
  kinetics/emissions/meteorology.

## Slide 7: Objective
Improve prediction of PCAP episodes (mitigation)
  Modeling
    Emissions
    Meteorology
    Reaction chemistry
Part of prediction is to also see what will happen in the future

## Slide 8: Focus on 12 Western Sites
State | Site
Utah | Utah
Utah | Salt Lake
Utah | Davis
Colorado | Denver
Nevada | Washoe
Nevada | Clark
California | Sacramento
California | Fresno
California | Stanislaus
California | Kern
California | Tulare

## Slide 9
cp : Specific heat of air (1005 J kg-1 K-1)
𝜌(𝑧): Density of layer
𝜃(ℎ): Potential temperature at height h
𝜃(z): Potential temperature of layer
sfc: surface height
h: mean ridge height
VHD: MJ/m2
Changes to VHD:
h: height of the top of the temperature inversion
To find h, a PBLH is found using the bulk Richardson number (RB) and finding the point below the PBLH where a temperature inversion exists.
If PBLH determination fails, set h to 4000 m.
This typically takes a trained meteorologist, and examination of sounding data
First Step is to identify a PCAP: Group at Univ Utah
(original version)
.
Need to first get a measure of bulk atmospheric stability: Valley Heat Deficit
Notes: I will add more – from Colgan

## Slide 10: After PCAP episode is identified……. What trends are we looking for?
Identify the episode (PCAP)
Correlation between modeled/observed PM and PCAP
Correlation between (mod/obs) PM/PCAP and meteorology variables
CMAQ and WRF
SMOKE-2016 NEI platform
2016 National Emissions Inventory (NEI) was used as base case and to scale future emissions.
Sparse Matrix Operator Kerner Emissions (SMOKE) modeling system
Air Quality Modeling
The Community Multiscale Air Quality (CMAQ) system
CMAQv 5.3.2
12km by 12km grid size

## Slide 11
2016 JAN Base Case: Focused on WRF Differences

## Slide 12: Jan 2016 Salt Lake
Shaded areas are PCAP episodes
%
(m)
PBLH
RH
Correlation between RH and PCAP

## Slide 13: Jan 2016 Reno
Shaded areas are PCAP episodes
PBLH
RH
%
(m)
Correlation between PBLH/RH and PCAP

## Slide 14: Taking these preliminary trends as a way to determine important PCAP predictors. We use this, to try to predict episodes in the future 2050?

## Slide 15
State | Site
Utah | Salt Lake
Colorado | Denver
Nevada | Washoe

## Slide 16: SMOKE-WRF-CMAQ
SMOKE-2016 NEI platform GT NEMS
2016 National Emissions Inventory (NEI) was used as base case and to scale future emissions.
Sparse Matrix Operator Kerner Emissions (SMOKE) modeling system
Meteorology
Community Earth System Model Version 1 (CEMSI)
  Global model developed by the National Center for Atmospheric Research (NCAR)
Weather Research Forecasting (WRF) Model v4.1
  Used to downscale the global model
  Two climate scenarios: RCP4.5/RCP8.5
Air Quality Modeling
The Community Multiscale Air Quality (CMAQ) system
CMAQv 5.3.2
12km by 12km grid size

## Slide 17: Emissions Other Sectors
2050 emissions for other sectors were estimated using the GT-NEMS forecast model which assesses energy distribution, with demand in combination with technology changes and regulations.
Electricity Power Generation Power Units
Area Source and Non Point (Residential, Commercial, Agriculture and Industrial sectors)
Biogenic emissions: Biogenic Emissions Inventory System (BEIS) version 3.61
Details of the methods can be found in recently published article by Shen et al.
Relaxed Energy Policies Coupled with Climate Change Will Significantly Undermine Efforts to Attain US Ozone Standards (2019). Published in One Earth. DOI:https://doi.org/10.1016/j.oneear.2019.09.006

## Slide 18: Results

## Slide 19: Salt Lake Utah
Estimated PCAP

## Slide 20: Denver, Colorado
Estimated PCAP

## Slide 21: Reno, Nevada
Estimated PCAP
Notes: Add a map from arcgis to highlight the state

## Slide 22: Salt Lake UT: 2016 Observations match with PCAP
Shaded areas are PCAP episodes

## Slide 23: Salt Lake UT: RCP4.5 and RCP8.5 (VHD calc)
Shaded areas are PCAP episodes
Notes: Modeled are typically lower than observations
This points to the variability in meteorology from global climate models
Reduced emissions in the future, likely reason for lower PM
Very hard to make predictions and capture
But meteorology predicts more PCAP episodes and longer durations

## Slide 24: Denver CO: 2016 observations match with PCAP
Shaded areas are PCAP episodes
Notes: This points to the variability in meteorology from global climate models
Reduced emissions in the future, likely reason for lower PM
But meteorology predicts more PCAP episodes and longer durations

## Slide 25: Denver CO: RCP4.5 and RCP8.5 (VHD calc)
Shaded areas are PCAP episodes

## Slide 26: Reno NV: 2016 Observations match with PCAP
Shaded areas are PCAP episodes

## Slide 27: Reno NV: RCP4.5 and RCP8.5 (VHD calc)
Shaded areas are PCAP episodes

## Slide 28: PCAP Overall Metrics

## Slide 29: Effects analysis (Meteorology vs PM)
PM2.5
PM2.5
PM2.5

## Slide 30: Conclusions
Uncertainty in future emissions and meteorology makes it hard to predict potential PCAP events.
However, if meteorological variables (PBLH, RH) are important, then data from this preliminary investigations, means there are likely to be atmospheric conditions that favor PCAP events.
  In the case of increased wild fires, this can have health implications.
Automation of formula for calculation of Valley Heat Deficit to identify PCAP events shows promise.
More work (through the NIH project), is ongoing to quantify areas of uncertainty in CMAQ
  Aerosol chemistry (CMAQ)
  Emissions modeling (DDM)

## Slide 31: Acknowledgements: Collaborators
Research reported in this presentation was supported in whole by National Institute of Environmental Health Sciences of the National Institutes of Health under award number R01 ES032910-01. The content is solely the responsibility of the authors and does not necessarily represent the official views of the National Institutes of Health.

## Slide 32: Thank you for listening

## Slide 33: 2050 WRF Differences: RCP45 – RCP85
RH %
PBLH (m)
SOLAR RAD w/m2
TEMP oC
WSPD10 (m/S)
Notes: Will add setup in a neat table