## Slide 1: Modeling Agricultural Reactive Nitrogen Emissions with Soil Carbon Amendments using an Enhanced Version of Fertilizer Emissions Scenario Tool for CMAQ (FEST-C)
Lina Luo1, Daniel Cohan1, Caroline Masiello1, and Taras Lychuk2
1Rice University, 2Agriculture and Agri-Food Canada
Presentation to 21st Annual CMAS Conference
October 18, 2022

## Slide 2
N2O: Potent greenhouse gas (climate)
  ~100 year lifetime
  273x as potent as CO2
NH3: Forms particulate matter (health)
  Impacts depend on NOx, SO2, meteorology & population downwind
NOx: Forms particulate matter and ozone (health)
  Impacts depend on NH3, VOCs, meteorology & population downwind
Why we care about reactive N emissions

## Slide 3: How is reactive N released from soils
Agriculture is the largest source of reactive nitrogen emissions
& leading contributor to PM health effects in US

## Slide 4
Enhanced Fertilizer Emissions Scenario Tool for CMAQ (FEST-C*)

## Slide 5: Agricultural Emissions of Reactive Nitrogen Simulated by FEST-C*
NOx
NH3
N2O
Emissions are highest in intensely fertilized regions and vary with meteorology and soil conditions
Emissions
Luo et al., Environmental Science & Technology, 2022

## Slide 6: Potential Impacts of Soil Amendments
Impacts on nitrogen emissions
Methane
Miscanthus
straw
Sewage
sludge
Rice
husk
Zero-
valent carbon
Feedstocks
pH
Bulk density
CEC
Carbon
Soil mixtures
Pyrolysis
Soil Amendments
Water
pH
Cation exchange capacity (CEC)
Bulk density (BD)
C & N dynamics
Stimulation
Mitigation
Zhang et al., GCB Bioenergy, 2021
NH3
NOx
N2O

## Slide 7: Modeling of Biochar with FEST-C*
Year : 2011
Domain: U.S. fertilized soils
Biochar application
  Type: hardwood biochar
  Timing: 1st fertilizer application day
  Tillage depth: 15cm
  Rate: 5 ton/ha or 20 ton/ha
  CEC: 185 cmolC/kg
  Carbon content: 72.9%
  Bulk density: 0.64 ton/m3
Cation exchange capacity (CEC): ↑
pH: ↑ (less acidic)
Carbon pool allocation
  2% for active pool
  60% to slow pool
  38% to passive pool
Bulk density: ↓
Biochar impacts on soils
Simulation configurations
Lychuk et al., Mitig Adapt Strateg Glob Change, 2014

## Slide 8: Comparisons of Modeled and Observed Impacts of Biochar on N2O and NH3 Emissions
FEST-C* biochar model tends to capture the observed sign of emissions variations but predict smaller changes than are observed
●N2O: 9 sites
▲NH3: 2 sites
Simulated Impact (%)
Observed Impact (%)
Edwards et al., Soil Bio. Biochem, 2018
Deng et al., PloS ONE, 2015
Gao et al., Soil Use Manage, 2021
Verhoeven et al., Agric. Ecosyst. Environ, 2014

## Slide 9
Impact of Biochar on N2O Emissions
High-dose (20 ton/ha) biochar application showed more favorable impacts
Increase
Decrease
> 20
15
10
5
0
-5
-10
-15
< -20
Relative variation (%)
Biochar 5 ton/ha
Biochar 20 ton/ha
NH3 and NOx had similar spatial patterns
Mitigation of emissions occurred most in the Southeast and under high-dose application.

## Slide 10
Driving Factors for Variations of Nitrogen Emissions
under Biochar Applications
Nitrification is the primary process (~ 80%) for N2O emissions from fertilized soils, influenced mainly by NH4+ level
Base case
Biochar case
Direct changes
Indirect changes

## Slide 11
Why 20ton/ha case generates more favorable impacts
Biochar 5 ton/ha
Mineralization > Immobilization
N2O
Biochar 20 ton/ha
N2O
Mineralization < Immobilization

## Slide 12
Impact of Biochar on Inorganic Nitrogen Budget Pathways
Biochar 20 ton/ha vs. Base case
% Change
Other benefits : ↓ N loss via runoff & percolation
Trade-offs effects: ~5% ↓ N in crop yield due to N input from net mineralization
N2O
N2
NH3
N2O
NO

## Slide 13: Conclusions
Incorporated biochar algorithms to FEST-C* to simulate soil C amendments and their influence on reactive N emissions
High-dose application of biochar amendments mitigated nitrogen emissions across most agricultural regions
Net effects depend most on how nitrification is affected
Need more field measurements to assess model performance
Notes: In summary, we develop

## Slide 14: Acknowledgements
Funding:
Dr. Kristen Foley (EPA): Meteorology data
Dr. Stephen Del Grosso (USDA): Soil N2O data
Dr. Jesse Bash, (EPA): NH3 estimation
Dr. Dongmei Yang (UNC) and Dr. Limei Ran (USDA): FEST-C model
Dr. Luca Doro and Dr. R. César Izaurralde (Texas A&M AgriLife Research) and Dr. Curtis Jones (UMD): EPIC model
Dr. Quazi Z. Rasool (PNNL): N cycling scheme
Dr. Nick Muller and Peter Tschofen (CMU): APEEP model
Dr. Taras Lychuk, Biochar algorithms

## Slide 16: Spatially Variable Impacts of Agricultural Soil Emissions Linking FEST-C* with Reduced Form Air Quality Health Model APEEP
NOx
NH3
N2O
Total damage
($)
In most counties, NH3 emissions have largest impact
Luo et al., Environmental Science & Technology, 2022
Emissions
APEEP
APEEP
Social cost of N2O

## Slide 17
Driving Factors for Variations of Nitrogen Emissions
under Biochar Applications
Changes upon biochar applied | C | CEC | pH | BD | Water content | T (oC) | Respiration | NH4+ | NO3-
Influencing variables | ↑ | ↑ | ↑ | ↓ | ↑ | ↑ | ↑↓ | ↑↓ | ↑↓
N2O emissions | ↑↓ | ↓/− | ↑/−/↓ | ↓ | ↑ | ↑ | ↑↓ | ↑↓ | ↑↓
Except for nitrogen availability, the more biochar applied, the greater changes in soil properties
Net changes of N2O largely depends on nitrification processes
↑ increase ↓ decrease ⎯ no change
Changes of influencing variables and their impacts on N2O emissions
Biochar case
Notes: cmol kg moles of charge per kilogram soil