## Slide 1: Comparing Emissions and OH Reactivity of VOCs in three chemical mechanisms (CB6, SAPRC07, RACM2)
Siqi Ma1, Daniel Tong1,2, Havala Pye3, Yang Zhang4, Chi-tsan Wang2, Xiaoyang Chen4, Daiwen Kang3, Benjamin Murphy3, Bok Haeng Baek2
1. Department of Atmospheric, Oceanic and Earth Sciences, George Mason University, Fairfax, VA 22030 USA
2. Center for Spatial Information Science and Systems, George Mason University, Fairfax, VA 22030 USA
3. US Environmental Protection Agency, Research Triangle Park, NC, 27709 USA
4. Department of Civil and Environmental Engineering, Northeastern University, Boston, MA 02115 USA
CMAS 2022
October 17-19, 2022

## Slide 2
VOCs are key precursors to tropospheric ozone and secondary organic aerosols.
Chemical mechanisms differ in VOC grouping methods.
During the grouping process, the chemical reactivity of VOCs may be altered, causing unknown effects on air quality modeling results.
VOC Chemistry and Influence on Air Quality Prediction
Objectives:
1) Comparing the VOC emissions and OH reactivity of different chemical mechanisms;
2) Investigating their impacts on the O3 and NO2 prediction.
VOC cycle in the atmosphere
https://www.dwd.de/EN/research/observing_atmosphere/composition_atmosphere/trace_gases/cont_nav/voc_node.html

## Slide 3
Model Configuration
Emission model and tool
Models/Tools: Speciation Tool v5 for chemical speciation
SMOKEv4.7
Emission Inventory: US EPA National Emissions Inventory 2016v1
Anthropogenic: 8 area source sectors, 4 mobile source sectors and 8 point source sectors
Biogenic: BEIS 3.61 as in SMOKEv4.7
Chemical Mechanisms: CB6r3, SAPRC07, RACM2 with AE6 aerosol mechanism
Air quality model setup
Model: WRFv4.0 for meteorological simulations
CMAQv5.3.1 for air quality simulations
Date: Four representative months (January, April, July, October) in 2019
Domain: Contiguous United States (CONUS) 12 km
Meteorological: ECMWF ERA5, 0.25° × 0.25°, 4/day
Initial Conditions: CMAQ profile IC
Boundary Conditions: GEOS-Chem monthly data

## Slide 4
Reactive Anthropogenic VOC Emissions from CB6, SAPRC07, and RACM2
VOC emissions mainly in urban areas and oil/gas well locations; So are their differences.
CB6 emissions are the highest among three mechanisms.
Tons/mon
Distributions in January and July
VOC (CB6-SAPRC07)
VOC (CB6-RACM2)
CB6 VOC
January
July

## Slide 5
Emissions by Time Zone
Higher transportation emissions appear in EST, oil and gas emissions are mainly in CST and MST.
CST contributes the largest NMVOCs (45%), while MST emits highest CH4 (56%).
VOCs from CB6 are the highest in each sector.
EST shows the largest differences in four months.
Anthropogenic VOC Emissions from CB6, SAPRC07, and RACM2
Eastern time zone (EST)
Central time zone (CST)
Mountain time zone (MST)
Pacific time zone (PST)

## Slide 6
OH Reactivity of VOCs
Process analysis:
Jan 6~20, 2019
Jul 6~20, 2019
CB6
SAPRC07
RACM2
Accumulated VOC-OH reaction rate: RACM2>CB6>SAPRC07
More reactivity over the southeast, Rocky Mountains and Central Valley
January
July
CB6-SAPRC07
CB6-RACM2

## Slide 7
Effects on Surface Ozone (8-Hour Max)
CB6
October
ppb
ppb
April
July
CB6-SAPRC07
CB6-RACM2
January

## Slide 8
Effects on Surface NO2
SAPRC07 produce more NO2 in January while RACM2 is higher in July.
Differences appear high in the northeast (January) and southeast (July).
ppb
January
July
CB6-SAPRC07
CB6-RACM2
CB6 NO2
PNO3 (CB6-RACM2)
-
+
+
-

## Slide 9
Which Mechanism Produces Better O3 Prediction?
Simulations are usually biased low in January and April while higher in July and October.
RACM2 has lower discrepancies when the simulations are underestimated while CB6 shows opposite results.
On average, CB6 performs better in most time.
Normalized Mean Bias

## Slide 10
All mechanisms underestimate the NO2 concentration.
NMB in SAPRC07 are slightly lower.
Normalized Mean Bias
How about NO2 Prediction?

## Slide 11
High Ozone Prediction over Major Cities
 | CB6 | SPARC07 | RACM2
CORR | 0.97 | 0.98 | 0.98
RMSE | 10.29 | 7.81 | 7.46
 | CB6 | SPARC07 | RACM2
CORR | 0.97 | 0.97 | 0.96
RMSE | 10.46 | 10.09 | 10.40
 | CB6 | SPARC07 | RACM2
CORR | 0.96 | 0.97 | 0.97
RMSE | 9.35 | 8.38 | 8.38
Simulations with 3 mechanisms underestimate the O3 peaks while overestimate valleys.
The correlations are comparable, RACM2 usually has lower RMSEs.
 | CB6 | SPARC07 | RACM2
CORR | 0.93 | 0.94 | 0.94
RMSE | 16.92 | 14.66 | 12.75
CORR: Correlation RMSE: Root Mean Square Error
New York City
Houston
Los Angeles
Phoenix

## Slide 12
Conclusions
Reactive VOC mass emissions in CB6 are higher than in SAPRC07 and RACM2.
VOC-OH reactivity in RACM2 is the highest.
Differences of predicted O3 primarily appear in July. CB6 performs better during low/median O3 days but SAPRC07 and RACM2 perform better on high O3 days.
The effect on NO2 simulations is small compared to that for O3.
DISCLAIMER
The views expressed in this presentation are those of the authors and do not necessarily represent the views or policies of the U.S. EPA.