## Slide 1: Investigation of Impacts of Flaring and Venting from Onshore Oil and Gas Production in the United States on Air Quality using CMAQ
Huy Tran1, Jonathan Buonocore2, Erin Polka2, Ananya Roy3, Beth Trask3, Hillary Hull3 , Saravanan Arunachalam1
1Institute for the Environment, The University of North Carolina at Chapel Hill, NC, USA
2Department of Environmental Health, Boston University School of Public Health
3Environmental Defense Fund, Washington DC, USA
Presented at
The CMAS 2022 Conference, Chapel Hill, NC
Acknowledgments:
Environmental Defense Fund (EDF)
CDPHE, UDEQ, TCEQ, WDEQ, and NOAA

## Slide 2: Introduction
Background:
Flaring is widely used to dispose of natural gas produced at Oil and Gas (O&G) facilities that lack sufficient infrastructure to capture all of the gas that is produced for operational, safety and economic reasons
Objectives:
Estimate emissions from flaring (and venting) and compare to NEI
Assess air quality impacts due to O&G flaring (and venting) activities and other O&G source types in the U.S. using CMAQ brute-force and CMAQ-DDM modeling techniques
  Flared gas volumes are often self-reported and inaccurate Therefore, emissions from flaring could be underestimated
Flaring is performed during various O&G production (upstream), transporting (midstream) and processing (downstream) activities in which upstream activities have the largest flared volume
  O&G well drilling and completion
  Well casing venting
  Crude oil and condensate storage tanks
  Dehydrators
  Loading of oil and condensates
  Oil refinery, gas plants and compressor stations
Gas flare from well testing
Associated gas flare at a well
Ref: U.S. DOE, 2019
Ref: U.S. DOE, 2019
Notes: U.S. DOE 2019 Report: “Natural Gas Flaring and Venting: State and Federal Regulatory Overview, Trends, and Impacts”

## Slide 3: Emissions from O&G flaring is not well estimated in the current National Emission Inventory (NEI)
Emissions from flaring are not estimated separately but lumped in emissions from associated sources: crude oil and condensate tanks, well heads, storage tank loading, gas venting, dehydrators
Many states apply different Source Classification Code (SCC) to characterize same O&G source types making if difficult to track flaring emissions from the NEI
1Rystad Energy, 2022
2Francoeur et al, 2021. DOI: 10.1021/acs.est.0c07352
State | Rystad1 | FOG2 | NEI 2017
TX | 5,085 | 5,029 | 4,791
ND | 5,079 | 3,151 | 2,112
NM | 913 | 643 | 132
WY | 212 | 116 | 2,691
CO | 119 | 48 | 868
NOX emissions (tpy)
Inconsistent in “flaring” emissions between NEI 2017 and other emission inventories
Rystad: contains county-level flared gas volume based on state/local agencies’ reports
FOG: Fuel-based Oil & Gas emission inventory
Notes: 1Rystad Energy. Cost of Flaring Abatement Final Report. Accessed February 2022. URL: https://blogs.edf.org/energyexchange/files/2022/02/Attachment-W-Rystad-Energy-Report_-Cost-of-Flaring-Abatement.pdf
2Colby B. Francoeur, Brian C. McDonald, Jessica B. Gilman, Kyle J. Zarzana, Barbara Dix, Steven S. Brown, Joost A. de Gouw, Gregory J. Frost, Meng Li, Stuart A. McKeen, Jeff Peischl, Ilana B. Pollack, Thomas B. Ryerson, Chelsea Thompson, Carsten Warneke, and Michael Trainer. Quantifying Methane and Ozone Precursor Emissions from Oil and Gas Production Regions across the Contiguous US. Environmental Science & Technology 2021 55 (13), 9129-9139. DOI: 10.1021/acs.est.0c07352
Most of Flare NOx in Wyoming is from SCC 2310011020 - On shore oil production crude tanks including flash (1,656 tons/yr).

## Slide 4: Estimations of flaring emissions from VIIRS
https://daac.ornl.gov/CMS/guides/Methane_Flaring_Sites_VIIRS.html
Flared Volume: VIIRS vs RYSTAD
NOx = (m3 /y) * (26700±14000 BTU/m3)* (0.065±0.038 lb NOx/106 BTU)
(Monte Carlo simulations)
Empirical algorithms for estimating stack parameters
Emissions factors for NOx, CO, PM2.5 and SO2 taken from literature reviews
Nonpoint Flaring and Venting: for 19 nonpoint O&G SCC that associated with flaring:
Emissions of NOX, CO, PM2.5 and SO2 are removed and replaced with corresponding VIIRS estimates (as point sources)
Emissions of VOC are taken “as is” from the 19 SCCs in counties where VIIRS are detected. This treatment consider that emissions from Flaring and Venting should be combined if they are to be controlled
Point Flaring: including flaring from major point O&G sources (22 SCCs) including compressor stations, gas plant, refinery, tank batteries, etc. Emissions are extracted from point O&G sector in the NEI 2017; co-located VIIRS removed
State | VIIRS17 | VIIRS19 | Rystad | FOG | NEI 2017
TX | 4,208 | 7,774 | 5,085 | 5,029 | 4,791
ND | 2,804 | 5,291 | 5,079 | 3,151 | 2,112
NM | 559 | 1,209 | 913 | 643 | 132
WY | 111 | 111 | 212 | 116 | 2,691
CO | 36 | 19 | 119 | 48 | 868
NOX emissions (tpy)
Good agreement between VIIRS-based and FOG’s emission estimates
In 2019: US = 17.7 BCM; Top 5 States = 16.6 BCM
Notes: Visible Infrared Imaging Radiometer Suite (VIIRS)
US Sum VIIRS-BCM 2019: 17.7 BCM
5 State Sum VIIRS-BCM 2019: 16.6 BCM

## Slide 5: Challenges in applying VIIRS-based Flaring
Not all flares are detected by VIIRS
Uinta Basin, Utah
Use “hybrid” VIIRS & Rystad & NEI 2017 to capture all possible ranges of flare emissions.
Flare NOX emissions from VIIRS-based only
Additional flare NOX emissions from fusing VIIRS with Rystad and NEI

## Slide 6: CMAQ Model Configurations
CONUS 12US1 domain; Base year 2016 (January, April, July, October)
Three modeling scenarios (brute-force):
Zero-out case (woFlare): including emissions from NEI 2016 for non-O&G and NEI 2017 O&G with flaring and venting emission excluded
Base case (wFlare1): including emissions from woFlare and VIIRS-based combined with NEI 2017 based point O&G flaring and venting
Alternative base case (wFlare2): including emissions from wFlare1 augmented with Rystad and NEI 2017 estimations in counties where VIIRS-based emissions are smaller or missing
Notes: Contributions from flaring and venting: VOC = 50%, NOx = 2.5%, PM2.5 = 18%, SO2 = 81%

## Slide 7: Results: Flaring and Venting Impact on O3
Jan
Jul
Average Difference of MDA8O3 (ppbV)
wFlare1 - woFlare
wFlare2 - woFlare
Impact on O3 is significant (up to 5 ppbV) and is four times higher in winter than in summer months
Denver Basin observes the highest impact in comparison to other O&G basins
Marginal differences between wFlare2 and wFlare1
Large NOX emission over Pennsylvania in wFlare2 led to O3 disbenefit in winter but benefit in summer months
wFlare2 – wFlare1
Notes: Impact on O3 is more significant in winter than in summer months: Up to 16 ppbV (47%) in wFlare1 in January and at Denver Basin. Same values for wFlare2.
On average, flaring and venting contribute 0.05 ppbV (0.15%) to O3 MDA8 over CONUS with Denver Basin observes the highest impact (2.2 ppbV, 6.4%) in wFlare2 and wFlare1.
“Augmented” flaring and venting emissions in wFlare2 increase O3 MDA8 impact up to 6 ppb in January over wFlare1. Excess NOX emission over Pennsylvania in wFlare2 lead to O3 disbenefit in winter but benefit in summer months.

## Slide 8: Results: Flaring and Venting Impact on PM2.5
Jan
Jul
Average Difference of PM2.5 (µg/m3)
wFlare1 - woFlare
wFlare2 - woFlare
wFlare1 - woFlare
wFlare2 - woFlare
Similarly impact on MDA8O3, impact on PM2.5 is stronger in winter than in summer (~ 2 times), and up to 1.4 µg/m3
Highest impact occurs in Denver Basin in January and in Bakken basin in July
Small disbenefit of PM2.5 in the Northeast regions due to decrease in NO3 aerosol in wFlare1 and wFlare2 over woFlare
Annual
wFlare2 – wFlare1
Notes: On any day, flaring and venting contribute up to 5.2 (5.1) ug/m3, or 19% (18%) to total PM2.5 concentration in wFlare2 (wFlare1)
On average, flaring and venting contribute 0.01 ug/m3 (0.39%) and up to 1.4 ug/m3 to PM2.5 over CONUS with Bakken Basin observes the highest impact (0.57 ug/m3, 17%) in wFlare1. There are insignificant differences in wFlare2.
Small disbenefit of PM2.5 in the North East regions (Minnesota) due to decrease in NO3 aerosol in wFlare1 and wFlare2 over woFlare.

## Slide 9: Results: Flaring and Venting Impact on NO2
Jan
Jul
Average Difference of Daily Maximum NO2 (ppb)
wFlare1 - woFlare
wFlare2 - woFlare
Impact on NO2 is stronger in summer than in winter (unlike MDA8O3 and PM2.5)
NO2 disbenefit observed at downwind area of oil and gas production basins
Marcellus basin observes highest NO2 impact in wFlare2 due to high NOX emissions in Pennsylvania
wFlare2 – wFlare1

## Slide 10: Impacts on Air Quality Standard Exceedances
 | MDA8O3 > 70 ppbV |  |  | PM2.5 > 35 µg/m3 |  |  | NO2 Daily Max > 100 ppbV |  | 
 | woFlare | wFlare1+ | wFlare2+ | woFlare | wFlare1+ | wFlare2+ | woFlare | wFlare1+ | wFlare2+
Texas | 6,884 | 802 | 953 | 7,653 | 0 | 0 | 0 | 0 | 0
North Dakota | 62 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
New Mexico | 1,178 | 62 | 155 | 0 | 0 | 0 | 0 | 0 | 0
Colorado | 2,790 | 2,015 | 2,015 | 0 | 0 | 0 | 0 | 0 | 0
Wyoming | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Pennsylvania | 9,517 | 62 | 527 | 6,045 | 62 | 31 | 0 | 0 | 0
CONUS | 420,474 | 3,932 | 6,496 | 34,925 | 62 | 0 | 62 | 0 | 0
Count of exceedances
MDA8O3:
  Exceedances largest in Colorado (Denver Basin). No MDA8O3 exceedances due to flaring and venting emissions in January in both wFlare1 and wFlare2
  Largest additional exceedances occurred in July
PM2.5 :
  Exceedance is marginal and additional exceedances occur in January only
  Decreases in nitrate and OC aerosols led to decrease in exceedances in some areas
  If PM2.5 daily NAAQS were lowered to 30 ug/m3, flaring and venting emission would contribute 240 and 300 exceedances in wFlare1 and wFalre2, respectively
  NO2:
    Flaring and venting cause no additional NO2 exceedances until the 1-hour NO2 standard were lowered to 60 ppbV at which wFlare1 and wFlares would add 279 and 310, respectively, to 8,726 exceedances in woFlare.
(Simple count of exceedances over 53,852,518 grid-cells x 123 days)

## Slide 11: CMAQ-DDM to identify key segments that contribute to O3, PM2.5
DDM sensitivities based on wFlare2 for 4 source groups: (1) Flaring and Venting; (2) Fugitives and Pneumatics; (3) Compressor Engines; (4) Pumpjack, Well Drilling and Completions
Assess O3 and PM2.5 sensitivity to NOX and VOC emissions from 4 sources groups, and to SO2 and PM2.5 emissions from group 1 (flaring and venting).
Oil & Gas sector
50%
36%
73%
18%
Compressors Engines
Flaring and Venting
Pumpjack, Drilling & Completion
O3_EVOC
O3_ENOx
O3_ENOx
O3_ENOx
Flaring and Venting
Strong O3 sensitivities to NOX emissions from Compressor Engines and Pumpjack/Drilling/Completion
O3 (ppbV)
Notes: NOX emissions from Compressor Engines and Pumpjack/Drilling/Completion
have strongest impact on O3 in area outside Oil & Gas production basin.
However, over major Oil & Gas production basins, O3 negatively responses to NOX emissions.

## Slide 12: Summary
Impact of flaring and venting on O3 concentration is significant and is stronger in winter (up to 5 ppb; 18% in MDA8O3) than in summer months (up to 2 ppb; 5%)
Highest impacts often mostly occurred over O&G production basin where VIIRS flares were detected not captured in NEI). Denver Basin observed the highest impact on O3 and PM2.5
O3 is more sensitive to VOC than to NOX emissions from flaring and venting. O3 has strongest sensitivity to NOX from compressor engines, pumpjack engines and well drilling and completions
Strongest impact on NO2 in Appalachian basin is subject to uncertainty in NOX emissions in Pennsylvania. Denver Basin observes the second highest impact on NO2
Large uncertainties exist in current estimations of flaring and venting emissions. We have developed an approach that augments flaring emissions estimates from VIIRS-based satellite retrievals to identify flare locations
Additional improvements in emission inventory are needed for better quantification of air quality and health impacts
Next Steps
  Continue perform CMAQ-DDM analysis for summer and winter months
  Perform health-risk assessment due to O3, PM2.5 and NO2 based on DDM results

## Slide 13
Thank you
Ted Wood/Photo Group
Frans Lanting/Getty Images

## Slide 14: Annual Average (wFlare1 – woFlare)
Annual Average Difference (ppb)
O3 MDA8
PM2.5
O3
NO2

## Slide 15: Highest Impact Analyses (wFlare1 – woFlare)
Annual Maximum Difference (ppb)
O3 MDA8
PM2.5
O3
NO2

## Slide 16: Annual Average (wFlare2 – woFlare)
Annual Average Difference (ppb)
O3 MDA8
PM2.5
O3
NO2

## Slide 17: Highest Impact Analyses (wFlare2 – woFlare)
Annual Maximum Difference (ppb)
O3 MDA8
PM2.5
O3
NO2

## Slide 18: PM2.5 components (wFlare2 – woFlare) January
SO4
NH4
NO3
OC
EC

## Slide 19: PM2.5 components (wFlare2 – woFlare) July
SO4
NH4
NO3
OC
EC

## Slide 20: Emissions (wFlare1)
VOC wFlare1
VOC (wFlare1 – woFlare)
NOX wFlare1
NOX (wFlare1 – woFlare)

## Slide 21: Emissions (wFlare2)
VOC (wFlare2 – woFlare)
VOC (wFlare2 – wFlare1)
NOX (wFlare2 – woFlare)
NOX (wFlare2 – wFlare1)

## Slide 22: Emission Contributions of Flaring and Venting
wFlare2
NEI 2016
NEI 2017
wFlare1
44%
50%
1.4%
2.3%
Notes: SA: nice work

## Slide 23: O3 sensitivity to NOX and VOC emissions from Flaring and Venting
July
O3_EVOC
O3_ENOx
Strong O3 sensitivities to NOX emissions from Compressor Engines and Pumpjack/Drilling/Completion
O3 (ppbV)
January
O3_ENOx
O3_EVOC
Notes: NOX emissions from Compressor Engines and Pumpjack/Drilling/Completion
have strongest impact on O3 in area outside Oil & Gas production basin.
However, over major Oil & Gas production basins, O3 negatively responses to NOX emissions.

## Slide 24: Brute Force vs. DDM for O3 from Key Oil & Gas Source Types – July wFlare2)
Compressors Engines
Flaring and Venting
Fugitives and Pneumatics
Pumpjack, Drilling & Completion
O3_EVOC
O3_ENOx
O3_ENOx
O3_EVOC
O3_ENOx
O3 (ppbV)
Brute-force Average Difference (ppb)
Within Flaring and Venting group, ozone is more sensitive to VOC (positive) than to NOX (positive/negative) emissions.
Flaring and Venting
NOX emissions from Compressor Engines and Pumpjack/Drilling/Completion
have strongest impact on O3 in area outside Oil & Gas production basin.
However, over major Oil & Gas production basins, O3 negatively responses to NOX emissions.
(Brute-force is comparable to DDM analyses for group 1 only)
Notes: Discuss Bakken basin in color circle: We have positive ozone contribution from flaring and venting. However, ozone is negative to NOx but positive sensitive to VOC. If flare NOx is excluded, Ozone may increase in the Bakken.

## Slide 25: Brute Force vs. DDM for PM2.5 – July
PM2.5_ESO2
O3_EVOC
PM2.5 (ug/m3)
Average Difference (ug/m3)
PM2.5 is more sensitive to SO2 emission from flaring and venting on average over the model domain
At some hot spot, however, PM2.5 is more sensitive to primary PM2.5 emission, of which 100% is EC.
Flaring and Venting
PM2.5_EPM2.5
EC_EPM2.5
SO4_ESO2
NH4_ESO2
Notes: On average: 88% is to SO2 emission
At hot spot: 64% of PM2.5 contributed from flaring is from primary PM2.5 emission (of which 100% is EC)., the remaining contributed PM2.5 is from SO2 emission from which 86% is in form of SO4 and 14% is in form of NH4 aerosols.
Less than 2% of PM2.5 is contributed by NOX (positive contribution) and VOC (negative contribution) emissions.

## Slide 26: Brute Force vs. DDM for NO2 – July
Compressors Engines
Flaring and Venting
Pumpjack, Drilling & Completion
NO2_EVOC
NO2_ENOx
NO2 (ppbV)
Average Difference (ppb)
Monthly Average NO2 (ppb)
Flaring and Venting
wFlare2
Highest NO2 impact over Pennsylvania (up to 8 ppb). Second highest impact over Denver Basin (5 ppbV).
NO2_ENOx
NO2_ENOx
On average less than 1 ppb of NO2 contributed by NOX emissions from flaring and venting (with exceptions for Pennsylvania).
Notes: Discuss Bakken basin in color circle: We have positive ozone contribution from flaring and venting. However, ozone is negative to NOx but positive sensitive to VOC. If flare NOx is excluded, Ozone may increase in the Bakken.

## Slide 27
Abmormal high NOx emissions in Pennsylvania and Wyoming in Flare-SCCs class in NEI2017
States |  | VOC | NOX | CO | PM10 | PM2.5 | NH3 | SO2
Texas | non-point | 578,302 | 4,580 | 20,597 | 0 | 0 | 0 | 23,325
 | point | 604 | 1,013 | 2,780 | 10 | 9 | 0 | 7,037
North Dakota | non-point | 307,738 | 2,112 | 11,162 | 0 | 0 | 0 | 2,486
 | point | 17 | 27 | 115 | 2 | 2 | 0 | 532
New Mexico | non-point | 83,867 | 137 | 705 | 1 | 1 | 0 | 2,166
 | point | 311 | 109 | 425 | 1 | 1 | 0 | 2,424
Wyoming | non-point | 55,579 | 2,691 | 672 | 0 | 0 | 0 | 56
 | point | 385 | 264 | 338 | 4 | 4 | 0 | 2,129
Colorado | non-point | 81,867 | 868 | 0 | 0 | 0 | 0 | 0
 | point | 1,804 | 348 | 1,149 | 1 | 1 | 0 | 23
Pennsylvania | non-point | 6,608 | 7,465 | 2,631 | 195 | 192 | 0 | 1,602
 | point | 0 | 0 | 0 | 0 | 0 | 0 | 0
Most of Flare NOx in Pennsylvania is from SCC 2310021500 - On-Shore Gas Production; Gas Well Completion – Flaring (7,424 tons/yr).
Most of Flare NOx in Wyoming is from SCC 2310011020 - On shore oil production crude tanks including flash (1,656 tons/yr).

## Slide 28
CMAQ overestimates MDA8O3 over eastern U.S. in summer months

## Slide 29
CMAQ well approximates observed PM2.5