## Slide 1: COVID and beyond: COVID -19 interventions and power plant emissions in the United States
21st Annual CMAS Conference
Chapel Hill, NC October 17 – October 19, 2022
Munshi Md Rasel1*, Kevin L. Chen2, Rachel C. Nethery2, and Lucas R.F. Henneman1
1Department of Civil, Environmental, and Infrastructure Engineering, George Mason University, Fairfax, VA, USA
2Department of Biostatistics, Harvard T.H. Chan School of Public Health, Boston, MA, USA
*Corresponding Author:
Munshi Md Rasel
mrasel@gmu.edu
4400 University Drive,
Fairfax, VA 22030

## Slide 2: Background
U.S. power plants have historically contributed a big role in terms of air pollution and climate impact in the country
Health Effects Institute. 2020. State of Global Air 2020. Special Report. Boston, MA
Power plant facilities in the U.S.

## Slide 3: Emissions of many sources decreased during COVID-19 lockdown period—what was the impact on power plant emissions?
COVID-19
Lockdown (March-April, 2020)
Mobile Emissions
Stationary power plant emissions??
Refs: https://www.who.int/health-topics/coronavirus

## Slide 4: Objectives
Quantify impact of COVID-19 intervention on power plant emissions
Identify facility characteristics that drives changes in emissions
Estimate PM2.5 exposure changes associated with SO2 emissions changes

## Slide 5: Steps followed
Power plant emissions data
Meteorological data
GSYNTH
Facility characteristics associated with emissions changes
Exposure change
Model evaluation
GSYNTH: Generalized Synthetic Control Model

## Slide 6: Generalized synthetic control (GSYNTH) model
Computes counterfactual values using the control period’s time-varying information
Intervention
Actual
B
Intervention period
Control period
BAU: Business As Usual
Emissions

## Slide 7: Generalized synthetic control (GSYNTH) model
Control period: Jan 2010- Feb 2020
Intervention period: March-Dec 2020
  Lockdown period: Mar-Apr
  Longterm period: Mar-Dec
Analysis elements:
  Electricity generating unit facilities
  Weekly emissions
Covariates:
  Meteorology
    Precipitation, temperature, humidity, wind speed
Intervention
Actual
B
Intervention period
Control period
BAU: Business As Usual

## Slide 8
Operational EGUs
N=1654
EGUs operating at least >2015 year
N=1310 remained
Peaker Plants
N=1205 remained
EGUs operating in 2020
N=1403 remained
EGUs>15% operation 2010-2020
N=937 remained
EGU: Electricity Generating Units
Exclusions Criteria
937 EGUs across the U.S. (covering >80% of original emissions) are used for this study of which 238 EGUs are coal fueled facilities
937 EGU facilities
Peaker plants: EGUs that come online only when there is a high demand in the area

## Slide 9
Significant reduction of emissions from EGUs
64% reduction
85% reduction
46% reduction

## Slide 10: GSYNTH is better able to reproduce 2019 emissions than simple mean models
lockdown
longterm

## Slide 11: Emissions were greater than expected after the lockdowns began
>40% increase
>20% increase
>15% increase
BAU: Business As Usual

## Slide 12
Long-term effect of COVID-19 Intervention
Most of the states has observed increased power plants emissions during COVID intervention
: Total weekly emissions change
NOx emissions change
CO2 emissions change
SO2 emissions change

## Slide 13: Coal facilities across the US drove emissions increases over business as usual
Coal EGU drives the emission increase
Increased SO2 from facilities without scrubbers in Regions 5 & 6
EPA Regions
EPA Regions

## Slide 14: Coal facilities operated more time during intervention period
EPA Regions
EGU facility characteristics driven emissions change

## Slide 15: HYSPLIT Average Dispersion model (HyADS) Exposure Model
Reduced complexity model
Tracks air parcels based on wind speed and directions
Estimates unitless exposure, which is converted to “coal PM2.5” with statistical model

## Slide 16: Coal SO2 contributions to ambient PM2.5 increased relative from BAU
March-December, 2020
0.01µg m-3 (26%) increase

## Slide 17: Summary
EGU SO2, NOx and CO2 emissions increased after the COVID-19 lockdowns compared to BAU
  Pronounced increases in the East
  Increases driven by increased operations at coal facilities
Coal emissions drove higher exposure associated with SO2 relative to BAU

## Slide 18: Acknowledgement
This work was supported by research funding from EPA 835872 and George Mason University

## Slide 19: Recommending
US coal power plant emissions changes and inequities since 1999
Presented by: Lucas Henneman
Authors: Lucas Henneman, Munshi Md Rasel, Christine Choirat, Susan Anenberg, Corwin Zigler
Time: October 18, 2022, 9am @ Grumman Auditorium

## Slide 20: Thank you
Questions?
mrasel@gmu.edu