## Slide 1: The Pandemic Bottom-up Emission Inventory Development using human Activity, Satellite Retrieval, and Chemical Transport Model
NOAA Atmospheric Chemistry, Carbon Cycle, Climate (AC4) project
Chis-Tsan Wang, B.H. Baek, Jia Xing, Siqi Ma, Kai Yang, and Daniel Tong
George Mason University

## Slide 2: Motivations
The ambient measurement and satellite observational data indicated that some air pollutants (NOx and PM) largely decreased during the COVID pandemic. (Venter et. al., 2020; Tanzer-Gruener et. Al., 2020; Liu et. al., 2020; Kroll et. al. 2020)
Some studies did the CTM model sensitivity study or used simple scale method based on ambient observational data to represent the decline of emissions and reflected the air quality changes in CTM model simulation. (Liu et. al., 2021, Kang et.al., 2020)
The sensitivity study or emission adjustment by observational data can be processed fast, but those method did not consider the details of human activity changes in different emission sources.

## Slide 3: Research Outline
Phase I: Developed a rapid refresh method for fast projecting the future emission by human activity data.
Phase II: Run the CMAQ model for 2019 and 2020 year and apply the model result with deep-mechanism learning method (DeepCTM) to understand the relationship between the emissions and CTM concentrations.
Phase III: Constraint the emissions with the top-down method based on the observational data (surface AQS and satellite data) using the DeepCTM and the inverse modeling process.
2020 Emission data
CMAQ model with Deep CTM
Ambient & Satellite measurement data
2019 and 2020 Human Activity data
2019 Emission platform data

## Slide 4: 2020 Emission Data Development
Base Emissions: U.S. EPA’s 2019ge Emissions Modeling Platform (EMP) (as of September 2022)
COVID-19 EMP Development based on the human activity datasets
  Collect the human activity datasets for 2019 and 2020, and then compute the ratio of 2020 to 2019
  Apply the 2020/2019 ratio to activity-related emission inventory sources (annual or monthly)
  Calculate the 2020 COVID-19 annual totals, and then
  Compute monthly totals based on the 2020 monthly temporal profiles, and then export them in FF10 SMOKE inventory formats
  Updated the SMOKE run scripts to correctly process monthly total inventories
  Month2Day Temporal PROfiles (TPRO): onroad (RPD), airports, and oilgas (with oil production)
Updated Sectors: nonpt, ptegu, ptnonipm, np_oil_gas, pt_oilgas, np_solvent, airports, noroad, RPD, CMV
Exempted Sectors: Onroad (RPV, RPS, RPH,,,), Hourly CEMS, RWC, AgNH3, ptfires, afdust, and ptagfires

## Slide 5
2019 : 100.2 Quads
1 Quads = 1015 BTU
Vehicles, Airport, Vessel, Railroad
1
2
3
4
5
6

## Slide 6: Human Activity Data Collections
U.S. DOT Data :
Daily travel distance data (County, Daily)
March 2020 US flight data (US, Daily)
Freight Weight data (Mode , State ,Monthly)
U.S. EIA Data :
Electricity Generation data (Fuel type, State, Monthly)
Natural Gas Consumption (not for EGU) (State, Monthly)
Petroleum Sale End users (Fuel type, State, Yearly)
Petroleum Consumption (End user, Fuel type ,US, Monthly)
Net petroleum product (5 PADD regions, Monthly )
Petroleum Production supply (6 products, 5 regions, Monthly)
Electricity Usage (End users, State, Monthly)
INRIX Data:
Normalized Daily VMT data (Vehicle type, State, Monthly )
Flighttrader24 Data:
Flight tracked by Flightradar24 (Global, Daily)
Total number of temporal profiles developed (county/state, daily/month/annual, source): 5995 + no of county-vehicle VMT TPRO
Petroleum Administration for Defense Districts (PADD)

## Slide 7
EIA Data
(S=State level, M=Monthly, US=US total, R=Regions)
3) Petroleum sale by end-user and fuel types (S,A)
Petroleum consumption by end-user
and fuel types (US, M)
4) Petroleum Process data related
to Crude Oil (R, M)
Petroleum Supply by fuel types (R, M)
Electric Generation
Natural Gas Consumption
Petroleum Consumption:
Distillate fuel, Kerosene, Residual fuel, Coal, Propane, Biomass.
Gasoline, Petroleum Coke, propane, propylene, total petroleum
Other data that can not be identified by energy consumption or Production.
1) Electricity Generation by fuel (S, M)
2) Natural Gas Usage by end-user (S,M)
5) Electricity Usage by end-user (S, M)
Combustion or Consumption
Oil and Gas Production and supply
PTEGU or Electric Generation
SCC Mapping
Nature Gas usage : Boilers, Combustion, Industrial Process, Chemical Evaporation, Stationary Source fuel combustion (Residential, commercial, industrial), space Heater, Dryer, Roasting, Turbine, Heater
Petroleum product usage : Boilers, Combustion, Industrial Process, Chemical Evaporation, Stationary Source fuel combustion (Residential, commercial, industrial), space Heater, Dryer, Roasting, Turbine, Asphalt concrete,
Pt_oilgas, np_oilgas: Oil and gas Production, Exploration, product storage, transportation and
Marketing petroleum products, Refinery, Fugitive Emissions
Other : Chemical Manufacturing All process, Food and Kindred Products, Agriculture Production, and others
Energy-related sectors : ptegu, ptnonipm, pt_oilgas, np_oilgas, nonpt, solvent

## Slide 8
1) Electricity Generation
2) Natural Gas Consumption in Industry and residential
4) Petroleum supply
Energy-related Emission Source Monthly Trends

## Slide 9
Transportation: Onroad RPD
(S = state level, C = county level, M = monthly data , D = daily data, Vt = Vehicle type)
DOT VMTdata [D, C]:
County level, daily data 2019-2020, but no Vehicle type. but only total VMT, not Vt contribution.
EPA VMT data [M, C, Vt]:
County level, Monthly data, with eleven vehicle types, but only 2019, no 2020.
INRIX normalize VMT data [D, S]
State level, Daily data, three vehicle types, but only 2020 and no VMT contribution by vehicle types.
Goal: 2019 and 2020 monthly VMT data with Vehicle types (C, M)
We used the DOT VMT data to calculate the County level, monthly total of 2020 to 2019, But this data missing vehicle types contribution information.
We used EPA VMT data to address the vehicle type VMT contribution for 2020 February. The vehicle type contribution to VMT will be used with INRIX data.
The INRIX data are used to identify the 2020 VMT for individual vehicle types.
After applied the EPA VMT February data as standard, we generate the INRIX 2020 county level, monthly total VMT contribution by vehicle types.
The monthly total DOT VMT data can be separated into three vehicles by INRIX data vehicle contribution data.

## Slide 10: U.S. DOT VMT Changes
PV: Passenger Vehicle, LH: Long Haul, LF: Local Fleet

## Slide 11
Transportation: Airports
DOT
Airport-level Activity Reports, (C, M)
DOT, Bureau of Transportation Statistics:
Airline On-Time Data, (US, Daily, March 2020 only)
Flightrader 24
History data of commercial flights (Global)
Calculate the month-to-day temporal profile for US.
Individual airport Monthly landing and take-off counts:
Airport county level profile
State total level profile
US total profile
Airports points emissions
(C = county level, M = monthly data)

## Slide 12
Sectors | airports | ptegu | ptnonipm | pt_oilgas | AC4 Point draft | EPA 2020 point draft Aug 2022 | AC4_2020 vs EPA2020
2019 NOX (tons) | 140,837 | 1,028,545 | 866,977 | 442,842 | 2,479,201 |  | 1.39%
2020 NOX (tons) | 90,603 | 887,205 | 798,319 | 439,382 | 2,215,484 | 2,185,147 | 
NOX change (%) | 64.30% | 86.30% | 92.10% | 99.20% | 89.36% | 88.1% | 1.39%
2019 VOC (tons) | 58,511 | 29,912 | 763,440 | 184,092 | 1,035,955 |  | -7.11%
2020 VOC (tons) | 38,171 | 27,073 | 723,870 | 168,885 | 957,982 | 1,031,292 | 
VOC change (%) | 65.20% | 90.50% | 94.80% | 91.70% | 92.47% | 99.55% | -7.11%
2019 PM25 (tons) | 9,087 | 100,082 | 242,308 | 14,236 | 365,713 |  | -0.01%
2020PM25 (tons) | 5,985 | 87,940 | 227,804 | 13,906 | 335,631 | 335,671 | 
PM25 change (%) | 65.90% | 87.90% | 94% | 97.70% | 91.77% | 91.79% | -0.01%
2019 SO2 (tons) | 17,685 | 1,048,032 | 504,057 | 38,959 | 1,608,733 |  | -0.62%
2020 SO2 (tons) | 11,341 | 854,721 | 431,459 | 38,194 | 1,335,711 | 1,343,979 | 
SO2 change (%) | 64.10% | 81.60% | 85.60% | 98% | 83.03% | 83.54% | -0.62%
2019 CO (tons) | 516,605 | 484,817 | 1,363,324 | 234,232 | 2,598,978 |  | 5.13%
2020 CO (tons) | 335,270 | 428,567 | 1,272,253 | 228,987 | 2,264,875 | 2,154,426 | 
CO change (%) | 64.90% | 88.40% | 93.30% | 97.80% | 87.14% | 82.90% | 5.13%
2019 NH3 (tons) | 0 | 20,965 | 68,813 | 3,767 | 93,545 |  | -2.97%
2020 NH3 (tons) | 0 | 20,701 | 66,205 | 3,980 | 90,886 | 93,664 | 
NH3 change (%) | 0% | 98.70% | 96.20% | 105.70% | 97.16% | 100.13% | -2.97%
Preliminary COVID-19 2020 EMP Results

## Slide 13: Acknowledgement
Supported by NOAA Atmospheric Chemistry Carbon Cycle &Climate (AC4) project.
USEPA OAQPS provided latest 2019 Emission (2019ge version) Inventory data and other ancillary data.
  Alison Eyth (USEPA)
DOT Daily VMT travel data
INRIX State-level normalized daily VMT data by vehicle types

## Slide 14
Thank you and Questions?

## Slide 15
Support information slides

## Slide 16: Human Activity affected by COVID-19
Electricity Generation: Geothermal, Natural Gas, Coal, Biomass, Petroleum
Natural Gas Consumption: Residential, Commercial, Industry.
Petroleum Consumption (not for transportation): Distillate Fuel, Kerosene, Propane Residual Fuel, Coal, Biomass.
  End users: Residential, Commercial, Industry.
Petroleum Product supply: Crude Oil, Natural Gas, Distillate Fuel, Kerosene, Asphalt, Miscellaneous products.
Electricity Consumption: Residential, Commercial, Industry.
Transportation: Vehicles, Aviation, Vessel, Railroad

## Slide 17: Deep-Machine Learning [DeepCTM]
Study the impacts from the inputs (Emissions, Meteorology, Concentrations, and Time)
The efficiency of AQ simulations can be enhanced with ML-built emission-concentration relationship
(Xing et al., ES&T, 2020)
CNN: convolution network; LSTM: long short term memory; U-Net structure (2-layers); MLP: multiple layers of perceptrons with threshold activation; pReLU: the parametric rectified linear unit is used as the activation function
O3
NO2
Cinitial cond.= 2
Concatenate
CFlux transport= 2
U wind
V wind
2-meter temperature
PBL height
Wind speed
Short-wave radiation
convective velocity scale
humidity
CMeteorology= 6
VOC emission
NOx emission
CEmission = 2
LSTM
LSTM
LSTM
LSTM
LSTM
LSTM
U-Net
CNN
pReLU
CNN
pReLU
CNN
MLP
Height of terrain
Cgeography= 1
CNN
pReLU
CNN
pReLU
CNN
O3
NO2
CConcentration= 2

## Slide 18
DOT Freight data
(Monthly, State, Transport method)
Monthly Freight Weight by Railroad (S, M)
Freight Weight by Vessel (US, Canada, Mexico) (S, M), Port State.
Petroleum Sale by end user (non- highway, farm, vessel, railroad) by Diesel (S,A)
Petroleum consumption by end user (Industry) and Diesel (US, M)
State Level Monthly Profile
RAL_TRD
CMV_TRD_US CMV_TRD_Canada, CMV_TRD_Mexico
CMV_DIS_US,
RAL_DIS_US
NOR_DIS_US
FRM_DIS_US
Emission Sector Mapping
Railroad
CMV_c1c2_US
CMV_c3 _US
CMV_c1c2_CA
CMV_c3 _CA
CMV_c1c2_MX
CMV_c3 _MX
Nonroad
non highway (NOR_DIS), Agricultural Equipment (FRM_DIS),
Transportation: Railroad, Vessel, Nonroad
EIA nonroad data
(S = state level, M = monthly data, US = US total)

## Slide 19: Transportation: Railroad, Vessel, Nonroad

## Slide 20: U.S. DOT VMT Changes: County level

## Slide 21
Download the Daily and stay at home data from DOT website: https://data.bts.gov/Research-and-Statistics/Trips-by-Distance/w96p-f2qv
The file name is “Trips_by_Distance-2_org.csv”. The rows set are each day, county level (Date 2019/01/01-2020/12/31, State and FIPS) ; The columns are Number of Trips in various range, include (<1 miles, 1-3 miles, 3-5 miles, 5-10 miles, 10-25 miles, 25-50 miles 50-100 miles, 100-250 miles, 250-500 miles, >=500 miles, )
The Number of Trips times the middle point of travel distance range and calculate the daily county total travel distance. df["Total Miles Driven"] = df["Number of Trips <1"] * 0.5 + df["Number of Trips 1-3"] * 1.5 + df["Number of Trips 3-5"] * 4 + df["Number of Trips 5-10"] * 7.5 + df["Number of Trips 10-25"] * 17.5 + df["Number of Trips 25-50"] * 37.5 + df["Number of Trips 50-100"] * 75 + df["Number of Trips 100-250"] * 175 + df["Number of Trips 250-500"] * 375 + df["Number of Trips >=500"] * 500
After calculate the Daily County Total (DCT) VMT, we did the data QA/QC to replace the abnormal numbers in the DCT with monthly average data.
The data for each assigned the reference county code in the last column and use this reference county code to calculate the reference county DCT VMT. This ref DCT VMT data are used as full back data.
For each individual county: A. We checked the DCT VMT for each county in each month has the missing data less than 4 days (~10%), or we replace the them by reference county data. B. We checked the DCT VMT for each county in each month, use the 75% + 1.5IQR and 25%-1.5IQR to identify the abnormal numbers for each county every month, and use the monthly average (without outlier) to makeup this abnormal data. If the outlier is more than 4 days, we replace them by reference county data.
Generate the DOT DCT VMT for 2019 and 2020.
2020 VMT preparation I : Generate the DOT Daily County Total VMT

## Slide 22
The DOT VMT data do not have Vehicle Type information. The Vehicle type informations are in 2019 EPA VMT (13 types) and INRIX normalized VMT (3 types)
We prepared a table to map EPA VMT vehicle types to INRIX vehicle types. The right figures showed the 2019 VMT contribution by vehicle types in EPA and INRIX categories.
The INRIX is normalized data by 2020 Jan and Feb, so we assume 2019 EPA VMT data in Feb 2019 has the same vehicle types VMT contribution in 2020. Then denormalized for INRIX data, After that, we get the daily VMT contribution by three vehicle types of INRIX. After this process, we first generated INRIX Monthly State Total (MST) VMT by 3 vehicle types and than use this data (INRIX MST VMT) to calculate the Vehicle monthly contribution of monthly State VMT (RHS table).
Use the vehicle type monthly contribution data with DOT DCT VMT to calculate the Vehicle type monthly VMT data for 2020.
Before we process the Monthly VMT contribution by vehicle type, we figure out that the monthly ratio between 2020/2019 have some outliers (1-2%), we set 75% +2IQR and 25%-2IQR to remove the outliers and replace with state average. We removed the outlier and generate the state level monthly 2020/2019 ratio. This data was used for outlier or missing data.
The 2020VMT and 2019 VMT already separate to 3 vehicle types, and can use to calculate the vehicle types county level monthly ratio 2020/2019.
2020 VMT preparation II : Calculate the 2020/2019 County level VMT ratio by three Vehicle types
State level monthly ratio
INRIX Vt contribution

## Slide 23
Chart: Long Haul (LH) US avg
Chart: Local Fleet (LF) US avg
Chart: Passenger Vehicle (PV) US AVG
EPA VMT contribution by vehicle types in Feb (We assume 2019 Feb Vehicle type data are the same as 2020 Feb)
Mobile Onroad Daily VMT from INRIX normalized data
EPA 2019ge VMT contribution by vehicle types (vehicle type SCC code)
Standard period of INRIX
EPA 2019 FEB VMT mapping for Vehicle type contribution
After this process, we have the vehicle contribution in 2020, but there is NO INRIX 2019 data to calculate the ratio of 2020 to 2019. Thus, we used the DOT VMT data that have the total monthly (daily) VMT for 2019 and 2020.

## Slide 24
Aug16
Aug16
Aug16
California
Florida
North Carolina
DOT original data shows the August peak, this peak shows near Aug 16 in DOT’s daily travel data
Figures from DOT website
Figures from DOT website
Figures made by CTW
https://www.bts.gov/daily-travel
500mile +
250 mile -500mile