## Slide 1: Black carbon aging process simulation in the WRF-CMAQ coupled model
Yuzhi Jin1，Jiandong Wang1，David C. Wong2, and Chao Liu1
1 School of Atmospheric Physics, Nanjing University of Information Science and Technology, China.
2 Office of Research and Development, U.S. Environmental Protection Agency.
The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. EPA.

## Slide 2
Introduction
BC Aging Module Development
Case Description
New Model Evaluation
New Model Results Analysis

## Slide 3: Introduction：Black Carbon
Black Carbon (BC) : Produced from the incomplete combustion of carbonaceous fuels.
BC
Strong light absorption
Regional air pollution
Global radiative forcing
Direct radiative forcing
Indirect radiative forcing
Atmospheric stability
Secondary particulate matter

## Slide 4: Introduction：BC Aging Process
Optical properties
Mixing states
Potential impact
Cloud condensation nuclei (CCN)
Ice nuclei (IN) concentration
Dry and wet deposition ……

## Slide 5: BC Aging Module Development：New Species
Coated BC
Bare BC
New Model
Default Model
BC
 | Mode | Mode | Mixing state | Hygroscopicity
 | Aitken | Accumulation |  | 
Bare BC | “ABECI” | “ABECJ” | External mixing | hydrophobic
Coated BC | “ACECI” | “ACECJ” | Internal mixing | hydrophilic

## Slide 6: BC Aging Module Development：Aging Schemes
1. Set an e-folding conversion lifetime；
2. Focus on the change in the properties during the BC aging process and their physical processes；
Set the aging process related to specific atmospheric components;
Hydrophilicity change as an aging indicator;
3. Subdivide black carbon aerosols into finer units.
A two-dimensional size-BC proportion interval；
Particle-resolved models.

## Slide 7: BC Aging Module Development：Aging Schemes
1. Set an e-folding conversion lifetime；
2. Focus on the change in the properties during the BC aging process and their physical processes；
Set the aging process related to specific atmospheric components;
Hydrophilicity change as an aging indicator;
3. Subdivide black carbon aerosols into finer units.
A two-dimensional size-BC proportion interval；
Particle-resolved models.
Scheme1: 1.15 days.
（Cooke et al., 1999,2002; Chung and Seinfeld, 2002 ; Huang et al., 2013 ）
Scheme2: OH radicals concentration.
Where β is 4.6×10-12 cm3 molecule-1 s-1，𝛼 is 5.8×10-7 s-1.
（Liu et al., 2011; Huang et al., 2013）
OH aging scheme

## Slide 8: BC Aging Module Development：New Model

## Slide 9: Case Description：Model Setup
Two-way coupled WRF4.4.1-CMAQ5.4
Location: United States
Time: June 2010
Resolution: 12km, 35 vertical layers
Chemical Mechanism: “CB6r5-AERO7”
Assimilation Datasets: FNL, NAM, NARR
Physics processes | Schemes | References
Microphysical Process | Morrison 2–moment Scheme | Morrison et al., 2009
Planetary Boundary Layer(PBL) Physics Process | Asymmetric Convection Model 2 Scheme(ACM2) | Pleim, 2007
Cumulus Parameterization Process | Kain–Fritsch Scheme | Kain, 2004
Shortwave Radiation Process | RRTMG Shortwave Scheme | Iacono et al., 2008
Longwave Radiation Process | RRTMG Longwave Scheme | Iacono et al., 2008
Land Surface Physics Process | Pleim–Xiu Land Surface Model | Pleim and Gilliam, 2009
Surface Layer Physics Process | Pleim–Xiu Scheme | Pleim, 2006

## Slide 10: Case Description：Observational data
Carbonaceous Aerosols and Radiative Effects Study (CARES）
（Zaveri et al., 2012）
Data type | Data | Data description | Instrument/Technique
Meteorology | T | Temperature | Vaisala WXT-510
Meteorology | RH | Relative Humidity | Vaisala WXT-511
Meteorology | P | Pressure | Vaisala WXT-512
Meteorology | WS | Wind speed | Vaisala WXT-513
Meteorology | WD | Wind direction | Vaisala WXT-514
Gas concentration | O3 | O3 concentration | UV absorption
Gas concentration | SO2 | SO2 concentration | Thermo Model 43i
Gas concentration | NO | NO concentration | Chemiluminescence
Gas concentration | NO2 | NO2 concentration | Photolytic conversion CU GMAX-DOAS
BC | MBC | BC mass concentration | Sunset OC/EC
Optics properties | babs | Absorption coefficient | PSAP

## Slide 11: Based Model Evaluation

## Slide 12: New Model Results Analysis：Aging-related Variables
Aging rate ()
Scheme1
Scheme2
Aging timescale (τ)
= 1.00644×10-5 s-1 τ = 1.15 days (27.6h)
𝒌 (s-1)
τ (h)

## Slide 13: New Model Results Analysis：BC mixing state
Bare BC dominates near the emission sources, while Coated BC dominates in areas further away from the sources.
The number fraction of Coated BC (
=

## Slide 14: New Model Results Analysis：BC mixing state (cont’d)
The number fraction of coated BC shows a distinct increase during the local time period of 8:00-20:00.

## Slide 15: New Model Results Analysis：Optical properties
Absorption coefficient () (532nm)

## Slide 16: New Model Results Analysis：Optical properties (cont’d)
Considering BC aging process can reduce the MAC values.
BC mass absorption cross-section (MAC) (532nm)
Absorption coefficient
BC mass concentration

## Slide 17: New Model Results Analysis：Optical properties (cont’d)
“Grid-Point Equivalent Particles” (GPEP)
The Diameter of Particles (Dp)
The Diameter of BC Core (Dc)

## Slide 18: New Model Results Analysis：Conclusions
The new model, which takes into account the BC aging process, exhibits good performance in terms of aging-related variables, BC mixing state, and optical properties.
The scheme2 better reflects the spatiotemporal distribution of aging-related variables.
We will explore more suitable BC aging schemes in the future.

## Slide 19: THANKS Email: jin@nuist.edu.cn