## Slide 1: Graphics Processing Unit Assisted Computation for a Gas-Phase Chemical Solver in CMAQ
Khanh Do1,2,4, Jose Rodriguez Borbon1, George Delic3, Bryan Wong1,
Yang Zhang4, and Cesunica Ivey1,2,5
22nd CMAS Conference, Chapel Hill, NC, October 16th, 2023
1Department of Chemical and Environmental Engineering, University of California, Riverside, CA
2Center for Environmental Research and Technology, Riverside, CA
3Hiperism Consulting, LLC, Chapel Hill, NC
4Department of Civil and Environmental Engineering, Northeastern University, Boston, MA
5Now at Department of Civil and Environmental Engineering, University of California, Berkeley

## Slide 2: Motivation
3D air quality models are computationally intensive
  Solve for chemistry and transport
  Simulate entire CONUS domain < 12-km is computationally expensive
All air quality models are being executed on CPUs
Limited number of cores per CPU
  Intel consumer product: 24 cores (i9 13900k)
  Intel server: 60 cores (Xeon Platinum 8490H)

## Slide 3: Rectilinear Grid Model
sciproc
pa_output
hadv
zadv
hdiff
vdiff
cldproc
chem
phot
ros3
driver
All science processes are executed sequentially for every grid cell in the domain
The number of MPI threads corresponds to those grid cells being computed
aero
pa_irr

## Slide 4
Central processing unit (CPU)
  Very fast, smart, and low latency
  Very few cores, parallelization limitation
Graphics processing unit (GPU)
  Thousands of cores
  Speed up of massive independent workload
GPU is used to accelerate CMAQ
  Parallelize and vectorize independent loops for numerical intensive subroutines
  Increase efficiency and reduce simulation time
Intel Core i9 CPU
NVIDIA RTX 3090
Why GPU?

## Slide 5: Heterogeneous Computing
GPU program
  Step 1: send a copy of the data from the CPU host to the GPU device
  Step 2: launch a CUDA kernel (.cuf) for instruction to compute on the GPU
  Step 3: send the GPU-computed data (results) from the GPU device to the CPU host
Each step adds to the overall computing time of the system
Scheme of a computer with a GPU

## Slide 6: Development Process
Determine the slowest process in CMAQ
Create GPU-friendly data structures and algorithms
Design compilation compatibility with the CUDA
Perform code independent analysis
Target ROS3 solver for gas-phase mechanism
Port subroutines of ROS3 solver into the GPU
Optimize CUDA program
The slowest module among the five modules

## Slide 7: Flow Diagram of CMAQ-CUDAv1.0
The blue blocks are executed using the CPU (host), and the red blocks are executed using GPU (device)
GPU computing time (kernel) much faster than the CPU time
The overall simulation time is still slower than the original CMAQ

## Slide 8: CMAQ-CUDAv2.0
  Minimize data transfer and optimize parallel computing
  Vectorize & combine 4 subroutines ported on GPU to enhance transfer
The blue blocks are executed using the CPU (host), and the red blocks are executed using GPU (device)

## Slide 9: Performance of CMAQ-CUDA
CMAQ-CUDAv2.0
  Reduce significantly the data transferring
  Increase kernel time due to more arithmetic operations, series operations
  Perform better with larger computing block size (BLKSIZE)

## Slide 10: Simulation Errors (Spatial)
Two versions of CMAQ produce very similar concentrations across all the species
Domain mean biases are small
Maximum differences are ~0.8% for NO, ~5% for O3, and ~0% for SO2
O3
NO2

## Slide 11: Simulation Errors (Temporal)
Errors do not accumulate and grow
Largest NMB for O3 is < 3% across all sites
Normalized Mean Bias for O3 of 27 sites in Southern CA

## Slide 12: Simulation Errors
Domain NMB errors do not accumulate over prolonged simulation periods for all species
Largest domain NMB errors is < 1% across all species

## Slide 13: Error Analysis
Technical factors
Human errors
  Port a large number of codes to the GPU
  Vectorize dependence loops
Architecture differences
  Extremely small values (e.g., time step, concentrations) magnify the errors
  The ROS3 for CMAQ-CUDA is highly parallel to maximize loop vectorization
  Vector operation on GPU is different than CPU
Reduction algorithm for GPU computing

## Slide 14: Conclusions
GPU computing gains popularity with the CUDA library
Computer hardware improves
  Lift the communication bottleneck between the host and the device
  Faster GPU clock speed
GPU computing remains the model’s integrity
CMAS team develops a GPU version of CMAQ
  ODE solver can be generalized for other AQMs
  Quality control, maintenance, and support
Heterogeneous computing offers a promising future of the grid models

## Slide 15: Acknowledgments
NSF CDS&E (#2053560)
Duncan Quevedo for developing CMAQ-CUDAv3.0
Prithviraj Yuvaraj for supporting CMAQ-CUDA

## Slide 16
Scientists have been working to improve the performance of 3D air quality models
Algorithm optimization
  MPICH, OpenMP
  Improvements the chemistry solvers; still maintain the integrity
    Sparse Matrix Vectorized Gear (SVMGear) - slowest but most accurate
    Rosenbrock (ROS3) – based on GEAR method and faster than SMVGear
    Euler Backward Iteration (EBI) – fastest but least accurate
Hardware optimization
  Faster CPUs and more MPI processes and OpenMP threads
  Porting intensive codes on GPU
Machine learning
Motivation
Results
CMAQ-CUDAv2.0
Future Work
Background/
Objective
Results
CMAQ-CUDAv1.0
Methods

## Slide 17: Methods
We target ROS3 solver for gas-phase mechanism
  Handle well stiff ODEs
  Highly vectorizable independent loops
Porting subroutines of ROS3 solver onto the GPU
  Partial derivative, Jacobian matrix, LU decomposition, back substitution
Model configuration
  SAPRC-07 mechanism
  4x4 km resolution
  156x102x11 grids
  Southern California
Figure 6. The third and inner-most domain (blue boundary) with 4 km horizontal grid spacing covered the entire SCAQMD region (thick black lines).
Results
CMAQ-CUDAv2.0
Future Work
Background/
Objective
Results
CMAQ-CUDAv1.0
Methods

## Slide 18: Results and Discussion
ROS3 | RBFEVAL (ms) |  |  | RBJACOB (ms) |  |  | RBDECOMP (ms) |  |  | RBSOLVE (ms) |  | 
 | CTD | KER | CTH | CTD | KER | CTH | CTD | KER | CTH | CTD | KER | CTH
Version 1.0 2,100 BLKS | 3.8 | 2.5 | 0.39 | 12 | 14 | 13 | 11 | 11 | 9.8 | 9.9 | 1.6 | 11
CMAQ 2,100 BLKS | 0 | 4.0 | 0 | 0 | 12 | 0 | 0 | 38 | 0 | 0 | 4.1 | 0
Version 1.0 10,000 BLKS | 24 | 1.9 | 1.7 | 50 | 7.6 | 58 | 53 | 13 | 45 | 46 | 1.7 | 53
CMAQ 10,000 BLKS | 0 | 23 | 0 | 0 | 56 | 0 | 0 | 190 | 0 | 0 | 21 | 0
The actual GPU computing time (kernel) is much faster than CPU with the same number of arithmetic operations
The overall simulation time still slower than original CMAQ
  Suffered from the cost of data transfer between the host and device
  The gain from the kernel was offset by the data communication cost
Table 1. Computing time for RBFEVAL, RBJACOB, RBCECOMP, and RBSOLVE subroutines for CMAQ and CMAQ-CUDAv1.0. The time was measured in seconds and was the average of a CMAQ timestep for 2,100 and 10,000 BLKSIZE. CTD (copy to device) is the time for transferring data from host to device. CTH (copy to host) is the time for copying the results from the device to the host. KER (kernel) is the GPU computing time in milliseconds.
Results
CMAQ-CUDAv2.0
Future Work
Background/
Objective
Results
CMAQ-CUDAv1.0
Methods

## Slide 19: Future Work
CMAQ-CUDAv3.0 will significantly reduce data transfer between host and device
We will implement multi-GPU method

## Slide 20: Simulation Errors
Time series of O3 normalized mean bias for 27 locations over Southern California for vertical layers
NMB errors do not accumulate over prolonged simulation periods for all layers
Enhancement over the simulation duration spanning all layers

## Slide 21
Optional aqueous chemistry with kinetic mass transfer and Rosenbrock solver: AQCHEM-KMT
GAS-PHASE CHEMISTRY Chapter 8 from CMAQ Documentation: Gear type solvers are the most accurate
https://www.cmascenter.org/cmaq/documentation/4.4/CHEM_SOLVER_NOTES.txt